## Slide 1
FCC
PS
SPS
LHC
The e-e+ Future Circular Collider FCC-ee
Frank Zimmermann, CERN
Thanks to Michael BENEDIKT, Ilkay TÜRK ÇAKIR, Orhan ÇAKIR, Haluk DENIZLI, Kenan Abbas ÇİFTÇİ, Rena ÇİFTÇİ, Özgür ETIŞKEN, Salim OĞUR, Gokhan UNEL, Saleh SULTANSOY, Fatih YAMAN
UPHUK8, Bodrum, 5 September 2022
on behalf of the FCC collaboration and FCCIS DS team
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; iFAST, grant agreement no. 101004730, FCCIS, grant agreement 951754, and E-JADE, contract no. 645479
http://cern.ch/fcc

## Slide 2
FCC-ee
The FCC integrated program
inspired by successful LEP – LHC programs at CERN
2020 - 2040
2045 - 2060
2065 - 2090
FCC-hh
comprehensive long-term program maximizing physics opportunities
stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities
stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, with ion and eh options
complementary physics
common civil engineering and technical infrastructures, building on and reusing CERN’s existing infrastructure
FCC integrated project allows seamless continuation of HEP after completion of the HL-LHC program
a similar two-stage project CEPC/SPPC is under study in China

## Slide 3
Feasibility Study: 2021-2025
If project approved before end of
decade  construction can start
beginning 2030s
FCC-ee operation ~2045-2060
FCC-hh operation 2070-2090++
technical timeline of FCC integrated programme
F. Gianotti

## Slide 4
FCC-ee in a nutshell
High luminosity precision study of Z, W, H, and 21036 cm-2s-1/IP at Z (or total 1037 cm-2s-1 with 4 IPs), 71034 cm-2s-1 at ZH, 1.31034 cm-2s-1 at , unprecedented energy resolution at Z (<100 keV) and W (<300 keV)
Low-risk technical solution based on 60 years of e+e- circular colliders and particle detectors ; R&D on components for improved performance, but no need for “demonstration” facilities; LEP2, VEPP-4M, PEP-II, KEKB, DAΦNE, or SuperKEKB already used many of the key ingredients in routine operation
Infrastructure will support a century of physics
  FCC-ee  FCC-hh  FCC-eh and/or several other options (FCC-mm, Gamma Factory ..)
Utility requirements similar to CERN existing use
Strong support from CERN, partners, and 2020 ESPPU
Detailed multi-domain feasibility study underway for 2026 ESPPU

## Slide 5
FCC-ee parameters
Parameter [4 IPs, 91.1 km,Trev=0.3 ms] | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1400 | 135 | 26.7 | 5.0
number bunches/beam | 8800 | 1120 | 336 | 42
bunch intensity [1011] | 2.76 | 2.29 | 1.51 | 2.26
SR energy loss / turn [GeV] | 0.0391 | 0.37 | 1.869 | 10.0
total RF voltage 400/800 MHz [GV] | 0.120/0 | 1.0/0 | 2.1/0 | 2.5/8.8
long. damping time [turns] | 1170 | 216 | 64.5 | 18.5
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.64 | 1.49
vertical geom. emittance [pm] | 1.42 | 4.34 | 1.29 | 2.98
horizontal rms IP spot size [mm] | 10 | 21 | 14 | 39
vertical rms IP spot size [nm] | 34 | 66 | 36 | 69
beam-beam parameter xx / xy | 0.004/ 0.159 | 0.011/0.111 | 0.0187/0.129 | 0.096/0.138
rms bunch length with SR / BS [mm] | 4.32 / 15.2 | 3.55 / 7.02 | 2.5 / 4.45 | 1.67 / 2.54
luminosity per IP [1034 cm-2s-1] | 181 | 17.3 | 7.2 | 1.25
tot. integr. luminosity / yr [ab-1/yr] | 86 | 8 | 3.4 | 0.6
beam lifetime rad Bhabha / BS [min] | 19 / ? | 20 / ? | 10 / 19 | 12 / 46

## Slide 6
FCC-ee Design Outline
Double ring e+e- collider
Common footprint with FCC-hh
Asymmetric IR layout and optics to limit SR towards the detector
Large crossing angle 30 mrad, “virtual” crab-waist collision, four-fold superperiodicity: 2 or 4 IPs
SR power 50 MW/beam
Top-up injection requires booster synchrotron in collider tunnel
C=91.1 km

## Slide 7
For FCC-hh, two high-luminosity general-purpose experiments and two specialized experiments are foreseen, similar to
present LHC detectors
FCC-ee & hh would share the 4 experimental caverns
a case for four IPs & experiments
M. Dam, ECFA Det. R&D Roadmap, 2021, https://indico.cern.ch/event/994685/
Four different FCC-ee detectors to optimally address:
(1) Higgs factory program; (2) Ultraprecise electroweak & QCD physics; (3) Heavy Flavour physics; (4) Search for feebly coupled particles

## Slide 8
efficient RF power sources
(400 & 800 MHz)
efficient SC cavities
energy efficient twin aperture arc dipoles
I. Syratchev
A. Milanese
under study: CCT HTS quad’s & sext’s for arcs
800 MHz 5-cell Nb
prototype / JLAB, 2 K
F. Marhauser
400 MHz 1-,2- & 4-cell Nb/Cu , 4.5 K
FPC & HOM coupler, cryomodule, thin-film coatings…
M. Koratzinos
accelerator R&D examples

## Slide 9
FCC-ee Pre-Injector - Swiss CHART 2 program
Collaboration between PSI and CERN with external partners: CNRS-IJCLab (Orsay), INFN-LNF (Frascati), KEK/SuperKEKB as observer, INFN-Ferrara – radiation from crystal
P3: PSI e+ production experiment with HTS solenoid at SwissFEL
planned for 2024/25
Latest FCC-ee pre-injector layout
P. Craievich et al.
location? transfer lines?

## Slide 10
FCC-ee mock-ups for arcs and IR
Arc half-cell: most recurrent assembly of mechanical hardware in the accelerator (~1500 similar FODO)
Mock-up  Functional prototype(s)  Pre-series  Series
Building a mock-up allows optimizing and testing fabrication, integration, installation, assembly, transport, maintenance
Working with structures of equivalent volumes, weights, stiffness
Arc half-cell mock-up
IR mock-up
F. Carra et al.
M. Boscolo et al.
Step 1: Central IP vacuum chamber (test the cooling system and the vacuum system), AlBeMet162 & steel transition (study the shape of the transition, EBW process), Bellows (vacuum and thermal tests), Welding (EBW for elliptical geometry)
Step 2: Trapezoidal vacuum chamber with remote vacuum connection, first quadrupole QC1, cryostat, beam pipe and quadrupole and cryostat support, vibration & alignment sensors

## Slide 11
SuperKEKB / Belle II
world record luminosity of 4.71x1034 cm-2s-1 on 22 June 2022, by* = 1.0 mm in routine operation, also by* = 0.8 mm demonstrated in both rings – with FCC-ee-style “virtual” crab-waist collision scheme originally developed for FCC-ee (K. Oide)
Design: double ring e+e- collider as B-factory at 7(e-) & 4(e+) GeV; target luminosity x 1035 cm-2s-1; by* 0.3 mm; beam lifetime5 min; top-up inj.; e+ rate up to 2.5 1012 /s ; under commissioning
T. Browder et al., U. Hawaii, BNL, etc.

## Slide 12: 8-site baseline “PA31”
8 sites – less use of land, <40 ha instead 62 ha
Possibility for 4 experiment sites in FCC-ee
All sites close to road infrastructures (< 5 km of new road constructions for all sites)
Vicinity of several sites to 400 kV grid lines
Good road connection of PD, PF, PG, PH suggest operation pole around Annecy/LAPP
Number of surface sites | 8
LSS@IP (PA, PD, PG, PJ) | 1400 m
LSS@TECH (PB, PF, PH, PL) | 2143 m
Arc length | 9.6 km
Sum of arc lengths | 76.9 m
Total length | 91.1 km
PA: Experiment
PB: technical
PD: experiment
PF: technical
PG: experiment
PH: technical
PJ: experiment
PL: technical
J. Gutleber
optimized placement and layout

## Slide 13
Shaft depth:
A: 202 m
D: 177 m
G: 228 m
J: 251 m
B: 200 m
F: 399 m
H: 139 m
L: 253 m
FCC passes below Lake Geneva moraines
FCC passes above limestone
FCC inclined at 0.5% gradient to minimise depth of point F
Limestone unavoidable between G-H
FCC Long Section – PA31-1.0
John Osborne

## Slide 14
plans for high-risk area site investigations
  Jura, Vuache (3 Areas)
  Top of limestone
  Karstification and filling-in at the tunnel depth
  Water pressure
  Lake, Rhône, Arve and Usses Valley (4 Areas)
  Top of the molasse
  Quaternary soft grounds, water bearing layers
  Mandallaz (1 Areas)
  Water pressure at the tunnel level
  Karstification
  Bornes (1 Area)
  High overburden molasse properties
  Thrust zones
  Site investigations planned for 2024 – 2025:
  ~40-50 drillings, some 100 km of seismic lines

## Slide 15
sustainability and carbon footprint studies
Thanks to twin-aperture magnets, thin-film SRF, efficient RF power sources, top-up injection
luminosity vs. electricity consumption
highly sustainable Higgs factory
FCC-ee annual energy consumption LHC/HL-LHC
powered by mix of renewable & other C-free sources
optimum usage of excavation material
int’l competition “mining the future®”
J.-P. Burnet, FCC Week 2022
https://www.carbonbrief.org/
France & Switzerland: already
lowest electricity C content
in the world (90% C-free)
incl. CERN site & SPS
https://indico.cern.ch/event/1001465/

## Slide 16
sustainability compared with other Higgs factories
Patrick Janot
CLIC | ILC | C3 | FCC-ee | CEPC
0.8 | 0.9 | 0.9 | 1.1 | 2.0
TWh / year for the “Higgs factory” centre-of-mass energy
    √s = 240 GeV for CEPC/FCC-ee, 250 GeV for ILC/C3, 380 GeV for CLIC
CLIC | ILC | C3 | CEPC | FCC-ee
30 | 20 | 21 | 10 | 3.3
Energy consumption in MWh / Higgs
      becomes 2 MWh / Higgs for FCC-ee with 4 IPs
CLIC@CERN | ILC@KEK | C3@FNAL | CEPC@China | FCC-ee@CERN
2.1 | 7.8 | 8.5 | 6.1 | 0.24
0.14 ton CO2 / Higgs for FCC-ee with 4 IPs
Present carbon footprint for electrical energy in tons CO2 / Higgs
https://indico.cern.ch/event/1178975/

## Slide 17
future upgrades and uses
FCC-ee: not only Higgs, but Z and W factory (TeraZ); upgrade (1 BCHF);
optional direct s-channel Higgs
production at 125 GeV with monochromatization
civil construction & technical infrastructures shared with
[and prepare] 100 TeV hadron
collider FCC -hh – stage 2 of FCC integrated program (next slide)
numerous other possible extensions (ep/eA/AA, Gamma Factory, LEMMA-type m collider FCC-mm ? …, ERL upgrade ? … )
A. Faus-Golfe et al., Eur. Phys. J. Plus, 137 (2022) 31
F. Zimmermann et al., PAC’22, Bangkok, WEPOST009
e- Yukawa coupling

## Slide 18
preparing for FCC stage 2 (FCC-hh)
CERN budget for high-field magnets doubled in 2020 Medium-Term Plan (~ 200 MCHF over ten years)
Main R&D activities:
materials: goal is ~16 T for Nb3Sn, at least ~20 T for HTS inserts
magnet technology: engineering, mechanical robustness, insulating materials, field quality
production of models and prototypes: to demonstrate material, design and engineering choices,
industrialisation and costs
infrastructure and test stations: for tests up to ~ 20 T and 20-50 kA
Detailed deliverables and timescale being defined through Accelerator R&D roadmap under development
L. Bottura, F. Gianotti, A. Siemko
In parallel to FCC studies,
High Field Magnet development program as long-term separate R&D project

## Slide 19
FCC-Conceptual Design Reports:
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  CDRs published in European Physical Journal C (Vol 1) and ST (Vol 2 – 4) [Springer]
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 ,
  EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382
EPJ is a merger and continuation of Acta Physica Hungarica, Anales de Fisica, Czechoslovak Journal of Physics, Fizika A, Il Nuovo Cimento, Journal de Physique, Portugaliae Physica and Zeitschrift für Physik. 25 European Physical Societies are represented in EPJ, including the DPG.
Summary documents provided to EPPSU SG
  FCC-integral, FCC-ee, FCC-hh, HE-LHC
  Accessible on http://fcc-cdr.web.cern.ch/
FCC CDR published in 2018/19
>1350 contributors 41 from Turkey!) and >350 institutes (19 institutes from Turkey!),
a truly global effort as suggested by EPPSU 2013

## Slide 20
from ESPP Update 2020
      High-priority future initiatives:
      An electron-positron Higgs factory is the highest-priority next collider. For the longer term, the European particle physics community has the ambition to operate a proton-proton collider at the highest achievable energy. Accomplishing these compelling goals will require innovation and cutting-edge technology:
      “the particle physics community should ramp up its R&D effort focused on advanced accelerator technologies, in particular that for high-field superconducting magnets, incl. high-temperature superconductors”
      “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. Such a feasibility study of the colliders and related infrastructure should be established as a global endeavour and be completed on the timescale of the next Strategy update..”

## Slide 21
FCC Feasibility Study (FS)
2013 ESPPU requested FCC Conceptual Design four-volume report → 4 volumes delivered in 2018/19, describing the physics cases, the design of the lepton and hadron colliders, and the underpinning technologies and infrastructures. Fol-
2020 ESPPU→ 2021 Launch of FCC Feasibility Study (FCC FS) by CERN Council
Feasibility Study Report (FSR) expected by the end of 2025 , not only the technical design, but also numerous other key feasibility aspects, including tunnel construction, financing, and environment
FSR will be an important input to the next ESPPU expected in 2026/27.
FCC FS is organized as international collaboration.
The FCC FS and a possible future project will profit from CERN’s decade-long experience with successful large international accelerator projects, e.g., the LHC and HL-LHC, and the associated global experiments, such as ATLAS and CMS.
Organisational Structure of the FCC Feasibility Study
http://cds.cern.ch/record/2774006/files/English.pdf
Main Deliverables and Timeline of the FCC Feasibility Study
http://cds.cern.ch/record/2774007/files/English.pdf

## Slide 22
Post FS & ESPPU2027: Project Cost & Profile
Construction cost estimate for FCC-ee
(from CDR 2018, update in 2025)
Machine configurations for Z, W, H working points included
Baseline configuration with 2 detectors
CERN contribution to 2 experiments incl.
cost category | [MCHF] | %
civil engineering | 5.400 | 50
technical infrastructure | 2.000 | 18
accelerator | 3.300 | 30
detector | 200 | 2
total cost (2018 prices) | 10.900 | 100
Spending profile for FCC-ee
CE construction 2032 - 2040
Technical infrastructure 2037 - 2043
Accelerator and experiment 2032 – 2045
Commissioning and operation start 2045 -2048.

## Slide 23
Status of Global FCC Collaboration
30
Companies
34
Countries
147
Institutes
EC
H2020
Increasing international collaboration as a prerequisite for success: links with science, research & development and high-tech industry will be essential to further advance and prepare the implementation of FCC
FCC Feasibility Study: 58 fully-signed previous members, 17 new members, MoU renewal of remaining CDR participants in progress

## Slide 24
15 or 16 institutes from Turkey: AIBU, Bolu; Akdeniz U, Antalya; Ankara U, Tandogan/ Ankara; EgeU, Bornova-Izmir; Giresun U, Giresun; Isik U, Sile, Istanbul; Istanbul Aydin U, Istanbul; Istanbul U, Vezneciler-Istanbul;
Istinye U, Istanbul; IUE, Balcova-Izmir; IYTE, Urla-Izmir;
Kirrikale U; Okan U, Istanbul; PRU, Tuzla/Istanbul; TOBB ETU, Ankara; ULUDAG, Nilüfer-Bursa
Turkish members of FCC collaboration

## Slide 25
https://indico.cern.ch/event/405973/
Istanbul 2016
Antalya 2019
FCC workshops organized by
Turkish FCC community

## Slide 26
Publications by FCC groups in Turkey FCC theses at Turkish universities
  The 28 GeV Dimuon Excess in Lepton Specific 2HDM, A. Cici, S. Khalil, B. Niş, C. S. Un, arXiv:1909.02588v1 [hep-ph]
  Study on Anomalous Neutral Triple Gauge Boson Couplings from Dimension-eight Operators at the HL-LHC, A. Senol, H. Denizli, A. Yilmaz, I. Turk Cakir, O. Cakir., arXiv:1906.04589 [hep-ph].
  Sensitivity on Anomalous Neutral Triple Gauge Couplings via ZZ Production at FCC-hh, A. Yilmaz, A. Senol, H. Denizli, I. Turk Cakir, O. Cakir., arXiv:1906.03911 [hep-ph].
  Top quark anomalous FCNC production via $tqg$ couplings at FCC-hh, K.Y. Oyulmaz, A. Senol, H. Denizli, O. Cakir, Phys.Rev. D99 (2019) no.11, 115023. 10.1103/PhysRevD.99.115023.
  Testing for observability of Higgs effective couplings in triphoton production at FCC-hh, H. Denizli, K.Y. Oyulmaz, A. Senol., arXiv:1901.04784 [hep-ph]
  Linac and Damping Ring Designs for the FCC-ee, S. Ogur et al., Proceedings of International Particle Accelerator Conference (IPAC 2019), pp. 420-423, 2019
  FCC-ee: The Lepton Collider : Future Circular Collider Conceptual Design Report Volume 2, FCC Collaboration (A. Abada et al.)., Eur.Phys.J.ST 228 (2019) no.2, 261-623, 10.1140/epjst/e2019-900045-4.
  FCC-hh: The Hadron Collider : Future Circular Collider Conceptual Design Report Volume 3, FCC Collaboration (A. Abada et al.)., Eur.Phys.J.ST 228 (2019) no.4, 755-1107, 10.1140/epjst/e2019-900087-0.
  HE-LHC: The High-Energy Large Hadron Collider, FCC Collaboration (A. Abada et al.)., Eur.Phys.J.ST 228 (2019) no.5, 1109-1382. 10.1140/epjst/e2019-900088-6.
  FCC Physics Opportunities : Future Circular Collider Conceptual Design Report Volume 1, FCC Collaboration (A. Abada et al.)., Eur.Phys.J. C79 (2019) no.6, 474. 10.1140/epjc/s10052-019-6904-3.
  Probing anomalous tq\gamma and tqg couplings via single top production in association with photon at FCC-hh, K.Y. Oyulmaz, A. Senol, H. Denizli, A. Yilmaz, I. Turk Cakir, O. Cakir., Eur.Phys.J. C79 (2019) no.1, 83. 10.1140/epjc/s10052-019-6593-y.
  Probing top quark FCNC tq\gamma and tqZ couplings at future electron-proton colliders, O. Cakir, A. Yilmaz, I. Turk Cakir, A. Senol, H. Denizli, Nucl.Phys. B944 (2019) 114640. ,10.1016/j.nuclphysb.2019.114640.
  Probing the Effects of Dimension-eight Operators Describing Anomalous Neutral Triple Gauge Boson Interactions at FCC-hh, A. Senol, H. Denizli, A. Yilmaz, I. Turk Cakir, K.Y. Oyulmaz, O. Karadeniz, O. Cakir., Nucl.Phys. B935 (2018) 365-376, 10.1016/j.nuclphysb.2018.08.018.
  Light stops and fine-tuning in MSSM, A. Çiçi, Z. Kırca, C. S. Ün; , Eur. Phys. J. C (2018) 78: 60. https://doi.org/10.1140/epjc/s10052-018-5549-y
  Probing the Anomalous FCNC Couplings at Large Hadron Electron Collider , I. Turk Cakir, A. Yilmaz, H. Denizli, A. Senol, H. Karadeniz, O. Cakir. Adv.High Energy Phys. 2017 (2017) 1572053.
15) Top quark FCNC couplings at future circular hadron electron colliders , H. Denizli, A. Senol, A. Yilmaz, I. Turk Cakir, H. Karadeniz, O. Cakir. Phys.Rev. D96 (2017) no.1, 015024.
16) Probing Charged Higgs Boson Couplings at the FCC-hh Collider , I.T. Cakir, S. Kuday, H. Saygin, A. Senol, O. Cakir. , Phys.Rev. D94 (2016) 015024.
17) Single production of the excited electrons in the future FCC-based lepton–hadron colliders, Abdullatif Caliskan, Seyit Okan Kara., Int.J.Mod.Phys. A33 (2018) no.24, 1850141.
18) Layout and Performance of the FCC-ee Pre-Injector Chain, Salim Ogur et al., DOI: 10.18429/JACoW-IPAC2018-MOPMF034.
Pre-Booster Ring Considerations for the FCC e⁺e⁻ Injector, Ozgur Etisken, Fanouria Antoniou, Abbas Çiftçi, Yannis Papaphilippou, DOI: 10.18429/JACoW-IPAC2018-MOPMF002.
20) Bunch Schedules for the FCC-ee Pre-injector, Salim Ogur, Katsunobu Oide, Yannis Papaphilippou, Dmitry Shatilov, Frank Zimmermann. DOI: 10.18429/JACoW-IPAC2018-MOPMF001.
21) First Look at the Physics Case of TLEP , TLEP Design Study Working Group (M. Bicer et al.). , JHEP 1401 (2014) 164.
22) Excited muon searches at the FCC based muon-hadron colliders , A. Caliskan, S.O. Kara, A. Ozansoy. arXiv:1701.03426 [hep-ph]. Adv.High Energy Phys. 2017 (2017) 1540243.
23) Azimuthal Angular Decorrelation of Jets at Future High Energy Colliders , I. Hos, H. Saygin, S. Kuday. arXiv:1809.01505 [hep-ph].
Projections for Neutral Di-Boson and Di-Higgs Interactions at FCC-he Collider , S. Kuday, H. Saygın, İ. Hoş, F. Çetin., Nucl.Phys. B932 (2018) 1-14. 10.1016/j.nuclphysb.2018.05.002.
25) FCC Based Lepton-Hadron and Photon-Hadron Colliders: Luminosity and Physics, Y. C. Acar, A. N. Akay, S. Beser, H. Karadeniz, U. Kaya, B. B. Oner, S. Sultanso, arXiv:1608.02190 [physics.acc-ph].
26) Color Octet Electron Search Potential of the FCC Based e-p Colliders , Y. C. Acar, U. Kaya, B. B. Oner, S. Sultansoy, J. Phys. G 44, no. 4, 045005 (2017).
27) Resonant production of leptogluons at the FCC based lepton-hadron colliders, Y. C. Acar, U. Kaya, B. B. Oner, S. Sultansoy, arXiv:1511.05814 [hep-ph].
I . Turk Cakir, A. Şenol, A. T. Tasci and O. Cakir. “Probing Anomalous WW γ and WWZ Couplings with Polarized Electron Beam at the LHeC and FCC-Ep Collider”. World Academy of Science, Engineering and Technology International Journal of Chemical, Molecular, Nuclear, Materials and Metallurgical Engineering (2015) Vol:9, No:1.
I. Turk Cakir, B. Hacisahinoglu, S. Kartal, A. Yilmaz, A. Yilmaz, Z. Uysal, O. Cakir, "Search for Flavour Changing Neutral Current Couplings of Higgs-up Sector Quarks at Future Circular Collider (FCC-eh)". World Academy of Science, Engineering and Technology, Open Science Index 132, International Journal of Physical and Mathematical Sciences (2017), 11(12), 525-529.
30) I. Turk Cakir, M. Altinli, Z. Uysal, A. Senol, O. Yalcinkaya, A. Yilmaz, "The Search of Anomalous Higgs Boson Couplings at the Large Hadron Electron Collider and Future Circular Electron Hadron Collider". World Academy of Science, Engineering and Technology, Open Science Index 132, International Journal of Physical and Mathematical Sciences (2017), 11(12), 519-524.
31 F. Yaman et al., “Mitigation of electron cloud effects in the FCC-ee collider”, EPJ Techniques and Instrumentation volume 9, Article number: 9 (2022)
FCC-Turkey team extremely active and productive
PhD theses
Ozgur ETISKEN, Ankara University, “Pre-Booster Ring Design for FCC-e+e- Injector complex”, CERN/Ankara
Umit KAYA, Ankara University, “Search for Color Octet Electron (e8) at TeV Energy Scale Colliders”
Kaan Yuksel OYULMAZ, Bolu Abant Izzet Baysal University, “Upgrade and performance studies of CMOS sensors for future colliders”
Salim OGUR, Bogazici University, “Linac and Damping Ring Designs of the future Circular e+e- Collider of CERN”, CERN/Bogazici PhD April 2019 – lzter CERN fellow
…
MSc theses
Yunus Emre OKYAYLI, 2018, “Search for R-parity violation interactions of scalar leptons at future circular collider”, Istanbul U.
Gökhan HALİMOĞLU, 2018, “Measurement of lepton + jets at 100 TeV at future circular collider”, Istanbul U.
Rokia Omar Ali ALAMIN, 2017, “Anomalous heavy down type b' quark production at the future circular collider”, Kastamonu University
Burak HACIŞAHİNOĞLU, 2017, “Search for flavour changing neutral current couplings of higgs-up sector quarks at electron-proton colliders”, Istanbul U.
Murat ALTINLI, 2017, “Investigation of gauge boson anomalous couplings with higgs particle at electron-proton colliders”, Istanbul U.
Çağla ÇAĞLAR, 2019, “Search for quarkonium consists of E6 model predicted isosinglet quark at future colliders,”, Ege University
Alev Ezgi DEMİRCİ, 2017, “Production and decay channels of charged higgs boson at high energy hadron colliders”, Ankara U.

## Slide 27
FCC-ee e-cloud build up studies
Fatih Yaman

## Slide 28
FCC-ee e-cloud build up studies
Fatih Yaman

## Slide 29
FCC-ee e-cloud build up studies
Fatih Yaman

## Slide 30
linac and damping ring design
  S-Band structures.
  Results with misalignments and BPM errors.
Salim Ogur

## Slide 31
pre-booster design: SPS & greenfield
Ozgur Etisken

## Slide 32
injector & collider filling schemes
Salim Ogur

## Slide 33
Physics Studies
teams in Turkey are extremely productive !

## Slide 34
FCC opportunities for Turkey
ongoing collaborations
FCC-ee injector design (Ankara, Bogazici, IEU, Kirikkale.…)
FCC-ee beam dynamics studies (IYTE,…)
FCC detector studies (AIBU, Uludag, …)
FCC physics (Akdeniz, Ankara, Tandogan, EgeU, Giresun, Isik, Istanbul Aydin, Istanbul U, IEU, Okan, PRU, TOBB ETU, ULUDAG…)
potential further contributions
FCC civil engineering
FCC-ee vacuum system prototype (IEU proposal)
FCC-ee damping ring and booster designs (Ankara, Kirikkale, ...)

## Slide 35
The European Strategy Update 2020 has issued a high-priority request for a feasibility study of the FCC integrated programme, and suggestions for key technology R&D areas
Main activities of the FCC Feasibility Study: concrete local/regional implementation scenario in collaboration with host state authorities, accompanied by machine optimization, physics studies and technology R&D, performed via global collaboration and supported by EC H2020 Design Study FCCIS, to prove FCC feasibility by 2025/26
Long term goal: world-leading HEP infrastructure for 21st century to push the particle-physics precision and energy frontiers far beyond present limits.
Success of FCC relies on global participation
Strong participation from Turkey with many addt’l opportunities !
Summary and Outlook
Teşekkür ederim !

## Slide 36: FCC Week 2023
From 5 to 9 June 2023 in London
5 – 9 June