## Slide 1: Congratulations for 70th Anniversary of Turkish Physical Society and Korean Physical Society

## Slide 2
We enjoyed 2002 World Cup Semi-final Match
(Turkiye 3 : 2 Korea)
And
Korea thanks Turkish Army for one of 16-UN Forces
during Korean Conflict in 1950-1953

## Slide 3: Brief Facts about Korea
People & Language: Korean (~4,500 yrs in the area)
Area (South): ~100,000 km2 (~38,000 sq. mi.)
Population (South): 52 million
Recent History:
1945: Divided into North and South
1950~1953: Korean Conflict
1960~1970: Modernization (Migration to cities)
1970~1980: Industrialization (Heavy Industries)
1990~2022: High-tech oriented
Leading Industries:
Electronics, Automobile, Ship-building,
Steel, Chemicals, Construction
Economy: GDP = 1.8 T$ and 35.4 k$/capita in 2021
Religion: Christian (~30%), Buddhism (~30%)
Education: > 80% high-school seniors go to college
Seoul
Daejeon
Busan
Pohang

## Slide 4
PAL-XFEL (10.0 GeV) and
PLS-II (3.0 GeV Light Source)
Accelerator Facilities in Korea (2022)
KOMAC (100-MeV Proton Linac)
Rare Isotope Science Project (RISP)
(Under construction)
4GSR Project (KPS)
(Under construction)

## Slide 5: Status and Prospects of Pohang Accelerator Laboratory (PAL)
Won Namkung
PAL, POSTECH
September 5-7, 2022
UPHUK-VIII
Bodrum, Turkiye

## Slide 6: Aerial View of PAL
PLS-II
(3GeV/400mA)
PAL-XFEL (10.0 GeV)
1.1 km
170 m
280 m
3rd Generation Light Source

## Slide 7: Pohang Accelerator Laboratory Overview
POSTECH, a newly established university, proposed to construct
a synchrotron light source on its campus in 1988
PLS is a 3rd generation synchrotron radiation source:
- 2 GeV injector linac and storage ring with upgrade option to 2.5-GeV
- Construction Project: April 1988 ~ December 1994
- Funded by POSCO (60%) & Government (40%)
Upgraded to 3.0 GeV in 2011 (PLS-II)
PAL-XFEL (X-ray Free Electron Laser) was constructed in 2015
- World 3rd after SLAC (US) and SACLA (Japan)
PAL is donated to Government in 2018
KPS Project (4.0 GeV, 4GSR) is started with KBSI in Chung-ju (2021-2027)

## Slide 8
PAL-XFEL
Initial proposal was to use existing PLS linac
to be a leading group member in 2003
Revised proposal in 2010 for 10 GeV XFEL

## Slide 9
Undulator Line | HX | SX
Photon energy [keV] | 2.4 ~ 15 | 0.28 ~ 1.0
Beam Energy [GeV] | 4 ~ 11 | 3.0
Wavelength Tuning | Energy | Gap
Undulator Type | Planar | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 9.0
  Main parameters
  e- Energy 10 GeV
  e- Bunch charge 20-200 pC
  Slice emittance < 0.4 mm mrad
  Repetition rate 60 Hz
  Bunch length 5 fs – 50 fs
  Peak current 3 kA
  SX line switching Kicker Magnet
PAL-XFEL Layout and Parameters

## Slide 10
Parameter | Unit | Value
Energy | GeV | 10
Charge | pC | 200
No. of SLED |  | 42
No. of Acc. Column |  | 173
Cross Section of Acceleration. Column
Linac Tunnel

## Slide 11
Parameter | Unit | Value
No. of Undulator |  | 21
Length | m | 5
Period | mm | 26.0
Gap | mm | 8.3
Wavelength | nm | 0.1
Magnetic field | Tesla | 0.8124
K |  | 1.9727
Undulator Hall

## Slide 12: Hard X-ray Experiment Hutches

## Slide 13: Hard X-ray Experiment Station

## Slide 14
Bi(111) thin film (50 nm) on GaSb(111)/Si(111)
X-ray: 6 keV
X-ray size: ~ 60 x 60 um2
Laser: 800 nm, 100 fs
Detector: MPCCD 0.5M
- No timing jitter correction
- averaged by 50 trials of the time delay scan and normalized by GaSb(111) Bragg peak intensity
- Only slow time-drift correction
- Vibration Frequency : 2.7 THz
- Instrument Response: 137 fs (FWHM)
Hard X-ray FEL with Femtosecond Timing Jitter

## Slide 15
Ec = 9.7 keV
SASE bandwidth (FWHM) = 27 eV
Self-seeding bandwidth (FWHM) = 0.22 eV
Averaged pulse energy: ~850 μJ
FEL Pulse duration = ~ 20 fs
Hard X-ray self seeding
Nat. Photon. 15, 435 (2021)

## Slide 16
undulator section for lasing pump pulse
(8 undulators)
undulator section for lasing probe pulse
(13 undulators)
magnetic chicane
(delay control)
e-beam
pump X-ray
probe X-ray
e-beam
e-beam delay
pump X-ray (SASE)
probe X-ray (SASE)
delay
Undulator section
for lasing pump pulse
(9.5 keV)
Undulator section
for lasing probe pulse
(8.5 keV)
Probe (8.5 keV) ~257 mJ
BW ~9.5 eV (rms)
Pump (9.5 keV) ~224 mJ
BW ~10.9 eV (rms)
Machine study results (2022. 01. 15)
Two-color HX FEL pulse generation

## Slide 17: PAL-XFEL Machine Performance
Lattice design used three bunch compressor configuration
Machine stability is outstanding
Self-seeding and two-color generation are very promising
FEL position stability: < 10 % of beam size
FEL power stability: < 5 % rms
E-beam energy jitter: < 0.015 %
E-beam arrival time jitter: < 15 fs
FEL pulse energy: > 3.18 mJ at 7.13 keV
FEL beam pulse duration: 20 ~ 30 fs (FWHM)
Saturated FEL: up to 20.0 keV

## Slide 18: PAL-XFEL Statistics
Annual Plan of Operation (Days)
User Service
 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
User Beam-time | 120 | 140 | 160 | 170 | 180 | 190
Turn-on & Tuning | 123 | 110 | 73 | 67 | 70 | 57
Machine Study |  |  | 21 | 21 | 10 | 10
Maintenance | 109 | 102 | 98 | 97 | 92 | 95
 | Applied | Approved | Days of Service
2017 | 82 | 26 | 120
2018 | 84 | 45 | 140
2019 | 140 | 49 | 160
2020 | 118 | 51 | 170
2021 | 132 | 47 | 180
2022 | 131 | 53 | 190

## Slide 20
PLS-II
Energy upgrade: 2.5 => 3.0 GeV
Top-up operation
Normal conducting RF => Super conducting RF
One year for user beam-time interruption

## Slide 21: PLS-II Upgrade Storage Ring
○ Main goals
- Beam energy : 2.5 → 3.0 GeV
- Current : 200 → 400 mA
- Storage Ring Emittance : 18.9 → 5.8 nm
- Top-up Operation mode
- No. of Insertion Device : 10 → 20
- Superconducting RF cavities
PLS
PLS
DEC. ‘10
Dismantling
Re-installation
PLS-II
PLS-II
JAN. ‘11

## Slide 22: PLS-II Linac
Injector LINAC
Thermionic Electron Gun
17 Pulse Modulators (200MW, 7.5µs)
17 Klystrons (80 MW, 4µs)
16 Energy Doublers (gain=1.5)
46 Accelerating Sections
Length = 170m
3.0 GeV, full energy injection
2,856 MHz (S-band)
10 Hz, 1.5 ns, 1Å pulsed beam
Norm. emmittance: 150 µmrad
Gallery
Tunnel

## Slide 23: PLS-II Parameters
Beam Energy 3.0 GeV
Beam Current 400 mA
Lattice DBA
Superperiods 12
Emittance 5.8 nm∙rad
Tune 15.37 / 9.15
SRF Frequency 499.97 MHz
Circumference 280 m

## Slide 24
36 Beam-lines at PLS-II

## Slide 25
Number of Experiments and Users per Year

## Slide 26
User Sciences in PLS-II
Chart: Research Fields
 | 54 | 23 | 15 | 8
Chart: Energy Storage and Conversion
 | 55 | 15 | 10 | 10 | 5
Chart: User Affiliations
 | 60 | 25 | 15

## Slide 27
2020-2021 User Scientific Representative Achievements-I
Nanochemistry & Catalyst
Electrocatalyst
Li-ion Battery
Electrocatalyst
Electrocatalyst
Focused on Energy conversion and storage Materials
and
Nanochemistry
Solar cell
Memory device
Semiconductor
Nanochemistry
Electrocatalyst
Solar cell
Catalyst

## Slide 28
2022 User Scientific General Achievements-II
An increasing trend of Impact factor
Constant SCI Publications

## Slide 29
KPS (Korea Photon Source)
Users are increasing
Available Beam-lines are limited at 36
High-performance beams are in demand
There is no space left at PAL

## Slide 30
KPS
(Korean 4GSR)
Off-axis injection
3rd and 4th Generation Light Sources

## Slide 31: 3GSR vs. 4GSR (with challenging technology)

## Slide 32
- Preliminary study by PAL: 2017 ~ 2019 - CDR project: 2020 - Project start: 2021. 7 ~ 2027. 12 - Building by KBSI / Machine by PAL
Parameter | Units | PLS-II | Korean 4GSR
Electron energy | GeV | 3 | 4
Horiz. Emittance | pm | 5,800 | 58 (RB: 39 )
Vert. Emittance | pm | ~ 58 | ~ 5.8 (RB: 39 )
Bunch length (rms) | ps | 20 | 13 (50 with HC)
Circumference | m | 280 | 800
Harmonic # |  | 470 | 1332
RF frequency | MHz | 500 | 500
Beam stability @ ID (x/y) |  | < 4 / 2 | < 2.5 / 0.45
Injection mode |  | Top-up | Top-up
Parameter | Units | PLS-II | Korean 4GSR
Electron energy | GeV | 3 | 4
Horiz. Emittance | pm | 5,800 | 58 (RB: 39 )
Vert. Emittance | pm | ~ 58 | ~ 5.8 (RB: 39 )
Bunch length (rms) | ps | 20 | 13 (50 with HC)
Circumference | m | 280 | 800
Harmonic # |  | 470 | 1332
RF frequency | MHz | 500 | 500
Beam stability @ ID (x/y) |  | < 4 / 2 | < 2.5 / 0.45
Injection mode |  | Top-up | Top-up
Korea Photon Source (KPS) Project

## Slide 33: Major Parameters for KPS

## Slide 34: SR Lattice Structure (linear)
Natural evolution of ESRF-EBS and APS-U
ESRF-EBS type - Dispersion bump w/sextupoles. - Longitudinal gradient dipoles. - Phase advance of Δφx ~ 3π and Δφy ~ π between corresponding sextupole
APS-U type: Reverse bends in Q4, Q5, and Q8.
Massive use of combined function magnets
6.5 m straight section and 2 T center-bend (Ec=21 keV)
Minimum emittance @ 4 GeV

## Slide 35: Hybrid 7-bend Achromat

## Slide 36: Longitudinal Gradient Bending Magnet (LGBM)
EM version is selected for construction costs and total cost of operation during the lifetime.
3D field map with 1mm step size is calculated, and the multipole along the orbit is calculated.
Except the quadrupole component which comes from the edge focusing, higher order was negligible.
To match the design field, reluctance gap at the return yoke is implemented for each magnet section
Dipole and higher order multipole along the orbit.

## Slide 37
High photon beam performance from storage ring. - The best performance in the range of 10 ~ 40 keV. - Capability to generate photon beam up to 100 keV.
Considering well demonstrated technologies for the design. - Off axis injection with conventional injection scheme - General technologies for magnet and vacuum systems.
Synergy with PLS-II and PAL-XFEL. - Supporting full range of synchrotron radiation application.
Design Features

## Slide 38: Initial Beam-lines (10 units)
Beam-line | Beam Energy | Resolution | Source | Experimental Technique
① BioPharma-BioSAXS | 5~20 keV | SAXS: < 1 Å ΔE/E < 10-4 | IVU | ① Bio-SAXS
② Material Structure Analysis | 5~40 keV | ΔE/E < 10-4 | Undulator | ① XRD ② XAFS
③ Soft X-ray Nano-probe | 0.1~5.0 keV | sub-micro beam ΔE/E>1.5×10-4@1keV | EPU | ① XAS ② XPS
④ Nanoscale Angle-resolved Photoemission | 0.1~2 keV | < 100 nm ΔE/E < 10-4 | Undulator | ① Nano-ARPES
⑤ Coherent X-ray Diffraction | 3~30 keV | sub-micro beam | Undulator | ① XRD ② CDI
⑥ Coherent Small-angle X-ray Scattering | 4~40 keV | few nm ~ few μm ΔE/E < 2×10-4 | IVU | ① SAXS/WAXS ② XPCS
⑦ Real-time X-ray Absorption Fine Structure | 5~40 keV | Few μm | Undulator | ① XAFS
⑧ Bio Nano crystallography | 5~20 keV | < 1 Å | IVU | ① MX
⑨ High Energy Microscopy | 5 ~ 100 keV | resolution 0.1μm | Superbend | ① Projection imaging
⑩ Nano-probe | 5~25 keV | < 50nm 1~10 μm | IVU | ① Ptychography/XRF ② XRS

## Slide 39: Site Arrangement (Plan)

## Slide 40
Summary
A few visionary people initiated light source facility in Korea in late 1980s.
Successful constructions and user services at PAL have been recognized
There are more accelerator projects being undertaken recently.
The users’ quality is continuously improved, and we expect more impact results.
We need more technological development for effective domestic maintenance capability, for example, high-power klystrons, superconducting cavities, and cryogenic facilities.

## Slide 41
Acknowledgements
C. B. Kim: PAL-XFEL
I. T. Uom: PAL-XFEL
S. H. Shin: PLS-II
M. K. Kim: PLS-II
K. W. Kim: PAL
I. S. Ko: KPS
Thanks to
for their contribution

## Slide 43: First Publication by First User
Confirmation of the Existence of the Widom Line !
Science (Dec. 21, 2017)