## Slide 1
Plasma-based compression of electron beams
Kelly Swanson
R. Hessami, J. Park, A. Marinelli,
M. J. Hogan, B. O’Shea, C. Emma
Thursday, July 30, 2026
This work was supported by the U.S. Department of Energy under contract number DE-AC01-76SF00515. C. Emma and K. K. Swanson acknowledge support from the Department of Energy Early Career Research Program.

## Slide 2
This work was made possible by:
The FACET-II Advanced Accelerator Research Department, Beam Physics and Operations, and Test Facilities
The FACET-II Scientific User program, particularly E338, E300, E304 collaborations
Mario Galletti, Livio Verra, Riccardo Pompili, and all the operations staff at SPARC
SPARC
FACET-II
Notes: Novel accelerating schemes – drivers with transverse and longitudinal sizes comparable or shorter than the plasma wavelength at solid densities (0.1um)

## Slide 3: Extreme beams unlock unprecedented opportunities Dense electron beams with ultrashort durations and high peak currents are of interest to many applications but remain a challenge to generate.
Attosecond Light Sources
Emma et al., APL Photonics. 6, 076197 (2021)
Laboratory Astrophysics
Macchi, Pegoraro, Nature Photonics 12, 314 (2018)
TeV/m Advanced Accelerators
Rosenzweig et al., NIMA 653 11 (2011)
Strong field QED
Matheron et al., Communications Physics 6 141 (2023)
Cesar et al., Optica 10 1 (2023)
Ultrafast Quantum Dynamics
QED = quantum electrodynamics
Notes: Novel accelerating schemes – drivers with transverse and longitudinal sizes comparable or shorter than the plasma wavelength at solid densities (0.1um)

## Slide 4: Single attosecond pulses exhibit trade-offs between energy and wavelength, limiting attosecond science Ultrashort, high current bunches can help fill the gap between HHG and XFELs.
HHG
XFEL
High harmonic generation
X-ray Free Electron Laser
Duris, et al., Nat. Photonics 14, 30-36 (2020)
Royal Swedish Academy of Science, Nobel Price in Physics (2023)
Notes: Atomic motion happens on femtosecond timescales. Our probe beams? Ten times slower. We're watching molecular dynamics through a blurry lens.

## Slide 5: Advanced compression techniques enable electron beams with 1 μm bunch lengths and 100 kA peak currents
Swanson, et al., PRAB 29, 052802 (2026)

## Slide 6: Advanced compression techniques enable electron beams with 1 μm bunch lengths and 100 kA peak currents
Swanson, et al., PRAB 29, 052802 (2026)

## Slide 7: Plasma-based compression
Theory
Experiments
Next steps
1
2
3

## Slide 8: Plasma-based compression
Theory
Experiments
Next steps
1
2
3
Plasma-based compression
Swanson, et al., PRAB 29, 052802 (2026)

## Slide 9: Short, high-peak current bunches can be generated by manipulating the beam’s longitudinal phase space
Radiofrequency
cavity
Quadrupole triplet
Chicane
z
Eb
z
Eb
z
Eb
A (nearly) linear energy variation imprinted onto the bunch by an RF cavity combined with path length differences in a magnetic chicane result in compression.
φ
E
Chirp (h)
R56
Fully compressed when R56 ~ 1/|h|
h = O(%/mm)
Notes: Say in words what chirp is in MeV/mm

## Slide 10: Coherent synchrotron radiation in the chicane becomes more significant as bunches get shorter
z
Eb
z
Eb
CSR degrades the beam quality and limits final bunch duration.
CSR interacting with other parts of the beam
Lou, et al., Proc IPAC (2021)

## Slide 11: The longitudinal electric field in a plasma wakefield accelerator can impart chirps orders of magnitude larger than RF cavities
Plasma wakefield
z
Eb
z
Eb
z
Eb
Chirps x1000 larger possible in a plasma wakefield (%/um) compared with RF cavity (%/mm).
h = O(%/um)
Beam direction
Notes: Rotate image so moves left to right

## Slide 12: Larger chirps reduce the CSR limitations compared to conventional compression schemes
Plasma wakefield
z
Eb
z
Eb
z
Eb
Reduced CSR preserves beam quality and enables stronger compression.
CSR energy loss
Larger chirp smaller bend angles reduced CSR

## Slide 13: Simulations demonstrate potential and limitations of plasma-based compression
QPAD
Bmad – includes effects such as space charge, coherent synchrotron radiation
Energy (GeV) | 10
Charge (nC) | 1.5/0.5
Slice energy spread (% rms) | 0.1
Spot size (um) | 20
Duration (um) | 10
FACET-II beam parameters

## Slide 14: Short, high-peak current bunches can be generated by manipulating the beam’s longitudinal phase space
Energy (GeV)
Charge (pC)
Energy (GeV)
Charge (pC)
Wakefields imprint tunable, large amplitude chirps that enable compression to ultrashort bunches.
Swanson, et al., PRAB 29, 052802 (2026)
50 - 600 MeV/um tunable with plasma density
10 MeV/um
60 MeV/um

## Slide 15: Compression O(100 nm) possible with reasonable PWFA parameters
Chirp, slice energy spread, and beam emittance strongly impact the final bunch duration.
Swanson, et al., PRAB 29, 052802 (2026)
Large compression factor achieved with:
More chirp

## Slide 16: Compression O(100 nm) possible with reasonable PWFA parameters
Swanson, et al., PRAB 29, 052802 (2026)
Chirp, slice energy spread, and beam emittance strongly impact the final bunch duration.
Large compression factor achieved with:
More chirp
Small slice energy spread

## Slide 17: Compression O(100 nm) possible with reasonable PWFA parameters
Swanson, et al., PRAB 29, 052802 (2026)
Chirp, slice energy spread, and beam emittance strongly impact the final bunch duration.
z
z
Emittance-induced slippage
Large compression factor achieved with:
More chirp
Small slice energy spread
Small emittance

## Slide 18: Plasma-based compression can achieve extreme beam parameters unattainable with conventional techniques
Plasma-based compression
Swanson, et al., PRAB 29, 052802 (2026)

## Slide 19: Prebunched electron beams enable generation of ultrashort, x-ray pulses A plasma-driven attosecond x-ray source extends our ability to study electron dynamics on ultrafast timescales
HHG
XFEL
Plasma-driven attosecond x-ray source
Emma, et al., APL Photon. 6 076107 (2021)
Duris, et al., Nat. Photonics 14, 30-36 (2020)
A prebunched,-high current electron beam can generate attosecond x-ray pulses with mJ energies in a shorter undulator

## Slide 20: Plasma-based compression
Theory
Next steps
1
3
Experiments
2
SPARC_LAB, INFN FACET-II, SLAC

## Slide 21: SPARC delivers 100 MeV drive-witness electron bunches for plasma wakefield acceleration experiments
Energy (MeV) | 100
Charge (pC) | 500/40
Spot size (um) | 40
Duration (um) | 60/40
SPARC beam parameters
Pompili, et al., PRAB. 29 051602 (2026)
Notes: Bunch duration rms

## Slide 22: The witness beam energy spread provides an estimate of the chirp
Length (cm) | 13
Density (1015 cm-3) | 1-10
Capillary discharge parameters
O(0.1 MeV/um) chirp imprinted into the witness electron bunch.
)
Chirp estimated as:
z
Eb

## Slide 23: Undulator radiation provides first experimental evidence of plasma-based compression
Demonstrated witness bunch compression, confirmed by coherent undulator radiation scaling with chicane strength.
Period (cm) | 2.8
K parameter | 2.2
Length (periods) | 75
Resonant wavelength (nm) | 650
Undulator parameters
Publication in preparation
R. Hessami, WG6, 07/27 @ 4pm
Notes: Previous SPARC result (write but don’t say)

## Slide 24: Undulator radiation provides first experimental evidence of plasma-based compression
Demonstrated witness bunch compression, confirmed by coherent undulator radiation scaling with chicane strength.
Period (cm) | 2.8
K parameter | 2.2
Length (periods) | 75
Resonant wavelength (nm) | 650
Undulator parameters
300 nm estimated bunch duration from measured undulator spectra and simulations. Analysis ongoing!
Publication in preparation

## Slide 25: Bunch compression tunable with the plasma density
Lower plasma density results in lower chirp, requiring increased chicane R56 to reach equivalent compression.
Low density
High density
Notes: Made complicated by the fact that the witness energy decreases… densities = 1e15, 1e16

## Slide 26: Studied dependence of compression on witness charge
An increase in undulator radiation observed at lower witness charge suggests that beam loading suppresses the witness chirp.
Flattened longitudinal electric field
Publication in preparation

## Slide 27: First evidence of plasma-based compression
Special thanks to Mario Galletti, Livio Verra, Riccardo Pompili, and all the operations staff at SPARC!
C. Emma
Results good enough to commemorate with a (temporary) tattoo.

## Slide 28: Investigating plasma-based compression at FACET-II
Energy (GeV) | 10
Charge (nC) | 1.5/0.5
Slice energy spread (% rms) | 0.1
Spot size (um) | 20
Duration (um) | 10
FACET-II beam parameters
Different challenges: higher energy, longer beamline, increased accumulation of jitter
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Plasma
target

## Slide 29: Drive-witness separation controlled by varying the RF phase relative to the bunches
The longitudinal distribution of the drive and witness was measured using a transverse deflecting cavity
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Plasma
target
Notes: Higher resolution TCAV image

## Slide 30: Drive-witness separation controlled by varying the RF phase relative to the bunches
Scanned the witness position inside the wake to measure the longitudinal electric field and therefore infer the chirp
Tunable bunch separation
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Plasma
target
Notes: Higher resolution TCAV image

## Slide 31: Drive-witness separation controlled by varying the RF phase relative to the bunches
135
100
75
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Plasma
target
Scanned the witness position inside the wake to measure the longitudinal electric field and therefore infer the chirp
Notes: Higher resolution TCAV image

## Slide 32: The witness chirp is inferred by scanning its position in the wake
98 MeV/um
O(100 MeV/um) chirps measured in 40 cm-long plasma at density 4.4e16 cm-3.
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Li oven
90
108
126
144
162
180
Bunch separation (um)
Notes: Add simulations of phase space, remake CHER plot

## Slide 33: The witness chirp is inferred by scanning its position in the wake
98 MeV/um
Chirp tunable with the plasma density with work ongoing to match simulations and experiments.
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Li oven
90
108
126
144
162
180
Bunch separation (um)
Notes: Add simulations of phase space

## Slide 34: The witness chirp is inferred by scanning its position in the wake
With FACET-II beam parameters and 100 MeV/um chirp, compression down to 100 nm is possible.
98 MeV/um
Energy spectrometer
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Li oven
90
108
126
144
162
180
Bunch separation (um)
Notes: Add simulations of phase space

## Slide 35: Newly installed chicane and diagnostics allow first plasma compression experiments at FACET-II
Post-plasma chicane installed Feb 2026
Expected CSR spectrum
Emma, et al., PRL 134, 085001 (2025)
Compressed bunch duration retrieved from CSR spectrum.
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
Plasma target

## Slide 36: Changing the chicane R56 increases the CSR signal, similar to the SPARC experiment
Observed an increase in CSR signal on spectrometer consistent with a compressing witness. There is ongoing analysis to determine the compression factor.
Drive + witness
UV-Visible
spectrometer
Charge
monitor
L1
L2
L3
Transverse
deflecting
cavity
H2 static fill
C. Emma, WG3, 07/28

## Slide 37: Transverse effects in the plasma make it a challenge to reach maximum compression
Drive
Drive
Witness
x
y
x
y
Position
Witness
Angle
Drive and witness can enter the plasma with a transverse offset and angle
Plasma
Y. Ye, WG3, 07/27 @ 2:50pm

## Slide 38: Transverse effects in the plasma make it a challenge to reach maximum compression
x
y
Drive and witness can enter the plasma with a transverse offset and angle
Seed betatron oscillations
Growth in post-plasma witness slice energy spread and divergence due to betatron motion in the wake.
Drive
Position
Witness
Angle
Plasma
Pousa, et al., Sci Rep 9, 17690 (2019)

## Slide 39: Plasma-based compression
Theory
1
Experiments
2
Next steps
3

## Slide 40: 100 attosecond beams could be possible with plasma injection
Challenge | Solution | Plasma injection
Betatron slippage/emittance growth | Matching with density ramps | Injected matched
Emittance-induced slippage | Smaller emittance | nm-scale emittance
Chromatic aberrations in quadrupoles | Shorter bunch duration  smaller energy spread | um-scale duration
Coherent synchrotron radiation | Larger chirps  smaller bend angles | > 500 MeV/um
Higher order compression | Smaller bunch duration  smaller energy spread | um-scale duration
Notes: Simulating 100 TW laser pulse with 17 fs duration and 15 um spot size propagating through a 0.7 cm plasma with density 2e18 cm-3
 1 GeV beam with 60 MeV/um chirp

## Slide 41: Different plasma-injection schemes will be tested at FACET-II
Zhang, et al., Nat. Commun. 16, 10719 (2025)
Many plasma injection techniques for tunable, highly chirped electron beams are possible
Trojan Horse
Density downramp
Density downramp injection and Trojan horse will be tested in Fall 2026
Heinemann, thesis (2026); Hidding, et al., PRL 180, 035001 (2012)

## Slide 42: Conclusions
Plasma-based compression demonstrated at SPARC with continuing studies at FACET-II with both external and plasma injection
A post-chicane vacuum chamber enables a broad range of experiments with compressed beams including strong field QED, quantum dynamics, and attosecond science.
kswan@slac.stanford.edu
Post-chicane vacuum chamber
SIOM
LWFA FEL
Plasma-based compression at FACET

## Slide 43: Supplementary Slides

## Slide 44: Peak current of the compressed beam is also dependent on chirp, slice energy spread and emittance

## Slide 45: Impact of CSR reduced even when compress to short, high-current beams