## Slide 1: Dephasingless laser wakefield acceleration of electrons using a flying focus
Charlie Arrowsmith
Advanced Accelerator Concepts 2026, Los Angeles
26-31 July 2026
Notes: 25+5 mins

## Slide 2: Collaborators
K. G. Miller, M. V. Ambat, B. Boni, I. A. LaBelle, A. Martin, J. J. Pigeon, H. G. Rinderknecht, I. A. Settle,
J. P. Palastro, J. L. Shaw, D. H. Froula
Plasma and Ultrafast Laser Science and Engineering
A. Rigatti, J. Spaulding
Optical Manufacturing
S.-W. Bahk, I. A. Begishev, S. Bucht, N. Dauphin, C. Jeon, C. Mileham, S. Qin, R. Roides, M. Spilatro, B. Webb
Laser Technology Development Group, MTW and MTW-OPAL
Engineering
This material is based upon work supported by the Department of Energy [National Nuclear Security Administration] University of Rochester “National Inertial Confinement Program” under Award Number(s) DE-NA0004144 and the U.S. Department of Energy under Award DE-SC0021057.
J. Kendrick, M. Romonofsky, J. Szczepanski

## Slide 3: Moore’s law of laser-plasma accelerators
Energy gain doubled every 3-4 years
for 40+ years

## Slide 4: Dephasingless laser wakefield acceleration provides a credible path towards TeV-class electron beams in a single-stage, compact accelerator
Achieved by using a flying focus to drive a wakefield in plasma at the vacuum speed of light.
Projected to lead to a step-change increase in the electron energy producible in a sub-meter accelerator.
Initial proof-of-concept experiments have showed that dephasing can be eliminated (published in Nature Physics).
Future experiments are being planned to optimize the scheme in preparation to scale to the multi-GeV regime.

## Slide 5: Spatiotemporal pulse shaping is enabling a new generation of radiation sources, diagnostics, and laser–plasma interactions
Chromatic flying focus
Achromatic/ultrashort/ultrafast flying focus
M. Piccardo et al., Optica 12, 732-752 (2025).
A. Sainte-Marie et al., Optica 4, 10 (2017). D. H. Froula et al., Nat. Photonics 12, 5 (2018). D. Turnbull et al., Phys. Rev. Lett. 120, 225001 (2018). S. Smartsev et al., Optics Letters 44, 14 (2019).
2. Axiparabola
Creates an extended focus, f = f(r)
1. Echelon
Adds radial group delay using flat λ/2 steps
J. J. Pigeon et al., Optics Express 32, 1 (2024).
Inverse Compton Scattering (ultra bright and highly tunable)
  E. Gerstmayr et al., arXiv:2607.15805v1 (2026).
Radiation reaction and vacuum birefringence
  M. Formanek et al., Phys. Rev. A 105, L020203 (2022).
  M. Formanek et al., Phys. Rev. D 109, 056009 (2024).
Photon acceleration, vacuum electron acceleration and others…
  J. Howard et al., Phys. Rev. Lett. 123, 124801 (2019).
  D. Ramsey et al., Phys. Rev. E 102, 043207 (2020).
Two-color terahertz (THz) generation
  T. T. Simpson et al., Phys. Rev. Research 6, 013041 (2024).
  J. P. Pigeon et al., Nat. Comms. (accepted, 2026).
Laser wakefield acceleration
  J. P. Palastro et al., Phys. Rev. Lett. 124, 13 (2020).
  A. Liberman et al., Phys. Rev. Research 8 (2), L022001 (2026).
  C. D. Arrowsmith et al., Nat. Phys. (2026).

## Slide 6: A flying focus can be used to eliminate dephasing in a laser-plasma accelerator
Traditional laser wakefield acceleration (LWFA)
Plasma densities ~1017 cm−3 are used to reach multi-GeV energies.
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Gaussian pulse drives a wakefield at roughly the plasma group velocity
Blowout regime
(a0 ≳ 2)
W. Lu et al., Phys. Rev. ST Accel. Beams 10, 061301 (2007).

## Slide 7: A flying focus can be used to eliminate dephasing in a laser-plasma accelerator
Traditional laser wakefield acceleration (LWFA)
Dephasingless laser wakefield acceleration (DLWFA)
Plasma densities ~1017 cm−3 are used to reach multi-GeV energies.
Flying focus drives a wakefield at the vacuum speed of light
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Gaussian pulse drives a wakefield at roughly the plasma group velocity
Blowout regime
(a0 ≳ 2)
W. Lu et al., Phys. Rev. ST Accel. Beams 10, 061301 (2007). J. P. Palastro et al., PRL 124, 13 (2020). K. G. Miller et al., Sci. Rep. 13, 21306 (2023).

## Slide 8: A flying focus can be used to eliminate dephasing in a laser-plasma accelerator
Traditional laser wakefield acceleration (LWFA)
Dephasingless laser wakefield acceleration (DLWFA)
Plasma densities ~1017 cm−3 are used to reach multi-GeV energies.
Flying focus drives a wakefield at the vacuum speed of light
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Accelerator length = dephasing length | 
Maximum energy gain | 
Strength of the accelerating field | 
Gaussian pulse drives a wakefield at roughly the plasma group velocity
Plasma densities >1018 cm−3 can be used (>GV/cm accelerating fields).
Accelerator length | 
Maximum energy gain | 
Accelerator length | 
Maximum energy gain | 
Wakefield structure
Blowout regime
(a0 ≳ 2)
Ionization
front
Particle–in-cell simulation
(laser not shown)
W. Lu et al., Phys. Rev. ST Accel. Beams 10, 061301 (2007). J. P. Palastro et al., PRL 124, 13 (2020). K. G. Miller et al., Sci. Rep. 13, 21306 (2023).

## Slide 9: Shrinking multi-GeV laser-plasma accelerators
d ~ 12”
d ~ 4”
d ~ 24”
Next step
Next gen.
Facility (Pulse durations ≲ 25 fs) | Accelerator length (cm) | Predicted energy (GeV) | Shot cycle
MTW-OPAL (0.24 PW) | 0.7 | 0.9 | 1 / 20 mins
ELI-Beamlines HAPLS (0.5 PW) | 1.5 | 3 | 3.3 Hz
EPAC (1.5 PW) Expected 2027 | 4.4 | 6 | 0.1-10 Hz
Apollon (2 PW) | 6 | 9 | 1 / min
ZEUS (3 PW) Expected 2026 | 9 | 15 | 1 / min
CoReLS (4 PW) | 12 | 17 | 0.1 Hz
ELI-NP HPLS (10 PW) | 30 | 42 | 1 / min
Vulcan 20-20 (8 PW, long focal length) Expected 2030s | 23 | 34 | TBC
NSF-OPAL (25 PW) Expected 2040 | 73 | 105 | 1 / 5 mins
5 GeV in 3.5 cm (>10 cm for LWFA)
10 GeV in 7 cm (~30 cm for LWFA)
40 GeV in 30 cm using 10 PW
Pulse guiding not required (single beam)
More compact focusing optics (~f/10)

## Slide 10: Shrinking multi-GeV laser-plasma accelerators
Ritus-Narozhny conjecture:
QED no longer perturbative
when αχ2/3 ≳1 ().
A possible workhorse for 10’s of GeV electron beams for SF-QED
d ~ 12”
d ~ 4”
d ~ 24”
Next step
Next gen.
Facility (Pulse durations ≲ 25 fs) | Accelerator length (cm) | Predicted energy (GeV) | Shot cycle
MTW-OPAL (0.24 PW) | 0.7 | 0.9 | 1 / 20 mins
ELI-Beamlines HAPLS (0.5 PW) | 1.5 | 3 | 3.3 Hz
EPAC (1.5 PW) Expected 2027 | 4.4 | 6 | 0.1-10 Hz
Apollon (2 PW) | 6 | 9 | 1 / min
ZEUS (3 PW) Expected 2026 | 9 | 15 | 1 / min
CoReLS (4 PW) | 12 | 17 | 0.1 Hz
ELI-NP HPLS (10 PW) | 30 | 42 | 1 / min
Vulcan 20-20 (8 PW, long focal length) Expected 2030s | 23 | 34 | TBC
NSF-OPAL (25 PW) Expected 2040 | 73 | 105 | 1 / 5 mins
5 GeV in 3.5 cm (>10 cm for LWFA)
10 GeV in 7 cm (~30 cm for LWFA)
40 GeV in 30 cm using 10 PW
Pulse guiding not required (single beam)
More compact focusing optics (~f/10)

## Slide 11: Shrinking multi-GeV laser-plasma accelerators
Proposed NSF-OPAL Facility
“Alpha” beams: 2× 25 PW / 5 mins
“Beta” beam: 2 PW
Up to 4× multi-kJ long-pulse beams
Two target areas: highest intensity, flexible focus
OMEGA EP
OMEGA
100 GeV in 0.7 m at NSF-OPAL
d ~ 12”
d ~ 4”
d ~ 24”
Next step
Next gen.
Facility (Pulse durations ≲ 25 fs) | Accelerator length (cm) | Predicted energy (GeV) | Shot cycle
MTW-OPAL (0.24 PW) | 0.7 | 0.9 | 1 / 20 mins
ELI-Beamlines HAPLS (0.5 PW) | 1.5 | 3 | 3.3 Hz
EPAC (1.5 PW) Expected 2027 | 4.4 | 6 | 0.1-10 Hz
Apollon (2 PW) | 6 | 9 | 1 / min
ZEUS (3 PW) Expected 2026 | 9 | 15 | 1 / min
CoReLS (4 PW) | 12 | 17 | 0.1 Hz
ELI-NP HPLS (10 PW) | 30 | 42 | 1 / min
Vulcan 20-20 (8 PW, long focal length) Expected 2030s | 23 | 34 | TBC
NSF-OPAL (25 PW) Expected 2040 | 73 | 105 | 1 / 5 mins
5 GeV in 3.5 cm (>10 cm for LWFA)
10 GeV in 7 cm (~30 cm for LWFA)
40 GeV in 30 cm using 10 PW
Pulse guiding not required (single beam)
More compact focusing optics (~f/10)

## Slide 12: Roadmap to 100 GeV electron acceleration
J. P. Palastro et al., Phys. Rev. Lett. 124, 13 (2020). K. G. Miller et al., Sci. Rep. 13, 21306 (2023). J. J. Pigeon et al., Optics Express 32, 1 (2024). C. D. Arrowsmith et al., Nat. Physics, 1-6 (2026).
Optimized wake velocity matching
(5 J, 1 GeV)
Initial demonstrations of DLWFA
(5 J, 0.4 GeV)

## Slide 13: Design considerations for blowout-regime dephasingless laser wakefield acceleration
Objective: Propagate a laser pulse with a0 ~ 2 at v = c in a high-density plasma (ne > 1018 cm-3) for the longest distance possible.
Limited by laser energy
Limited by pulse duration to ensure c𝜏 < λp/2
𝜏 = 20 fs ⟶ ne ≲ 8×1018 cm−3
Notes: Having given a bit of background, now I’m going to talk about the initial proof-of-concept experiments that we performed last year. And I thought it would be helpful first to go through some of the steps that show how we arrive at suitable operating conditions

## Slide 14: Design considerations for blowout-regime dephasingless laser wakefield acceleration
< 15
Objective: Propagate a laser pulse with a0 ~ 2 at v = c in a high-density plasma (ne > 1018 cm-3) for the longest distance possible.
Limited by P
Limited by pulse duration to ensure c𝜏 < λp/2
𝜏 = 20 fs ⟶ ne ≲ 8×1018 cm−3
Frequency-domain Fresnel diffraction integral
v = 1.002c, L = 10 mm, R = 50 mm
f/15
f/10
f/5
1. Focal length decided by minimizing intensity modulations and keeping pulse duration short
Notes: Having given a bit of background, now I’m going to talk about the initial proof-of-concept experiments that we performed last year. And I thought it would be helpful first to go through some of the steps that show how we arrive at suitable operating conditions

## Slide 15: Design considerations for blowout-regime dephasingless laser wakefield acceleration
< 15
Objective: Propagate a laser pulse with a0 ~ 2 at v = c in a high-density plasma (ne > 1018 cm-3) for the longest distance possible.
Limited by P
Limited by pulse duration to ensure c𝜏 < λp/2
𝜏 = 20 fs ⟶ ne ≲ 8×1018 cm−3
Frequency-domain Fresnel diffraction integral
v = 1.002c, L = 10 mm, R = 50 mm
f/15
f/10
f/5
2. Minimize non-linear propagation effects and relativistic self-focusing
OSIRIS Particle-in-cell simulations
Fluctuations in size and shape of bubble
More stable for 20 fs pulses when ne ~ 5×1018 cm−3
P ≲ Pc/2 ⟶ ne ≲ 5×1018 cm−3
1. Focal length decided by minimizing intensity modulations and keeping pulse duration short
Notes: Having given a bit of background, now I’m going to talk about the initial proof-of-concept experiments that we performed last year. And I thought it would be helpful first to go through some of the steps that show how we arrive at suitable operating conditions

## Slide 16: Design considerations for blowout-regime dephasingless laser wakefield acceleration
< 15
Objective: Propagate a laser pulse with a0 ~ 2 at v = c in a high-density plasma (ne > 1018 cm-3) for the longest distance possible.
Limited by P
Limited by pulse duration to ensure c𝜏 < λp/2
𝜏 = 20 fs ⟶ ne ≲ 8×1018 cm−3
Frequency-domain Fresnel diffraction integral
v = 1.002c, L = 10 mm, R = 50 mm
f/15
f/10
f/5
2. Minimize non-linear propagation effects and relativistic self-focusing
3. Match the desired wakefield velocity as closely as possible
OSIRIS Particle-in-cell simulations
Calculations of the wakefield velocity (f/8 axiparabola)
Fluctuations in size and shape of bubble
More stable for 20 fs pulses when ne ~ 5×1018 cm−3
P0 ≲ Pc/2 ⟶ ne ≲ 5×1018 cm−3
= 8
Electrons catch up with laser
Wake velocity too slow
1×1018 cm−3
5×1018 cm−3
1×1019 cm−3
1×1018 cm−3
5×1018 cm−3
1×1019 cm−3
v = c
1. Focal length decided by minimizing intensity modulations and keeping pulse duration short
Notes: Having given a bit of background, now I’m going to talk about the initial proof-of-concept experiments that we performed last year. And I thought it would be helpful first to go through some of the steps that show how we arrive at suitable operating conditions

## Slide 17: Initial proof-of-concept experiments at LLE were performed last year
EL = 4 J, 21 fs
C. D. Arrowsmith et al., Nat. Physics, 1-6 (2026).

## Slide 18: Electrons at twice the dephasing-limited energy were observed
C. D. Arrowsmith et al., Nat. Physics, 1-6 (2026).
13 pC
11 pC
4.4 pC
0.1 pC
12 pC
5.7 pC

## Slide 19: Particle-in-cell simulations observed the same trend between plasma density and maximum electron energy
The imperfect velocity matching of the axiparabola caused periods of stalled acceleration.
C. D. Arrowsmith et al., Nat. Physics, 1-6 (2026).

## Slide 20: Control of the radial group delay is required to achieve perfect wakefield velocity matching
Aim
Using an axiparabola without an echelon can only get you so far...
The longer the accelerator, the more necessary an echelon becomes.
15 GeV projected
(if optimized)
Electrons catch up with laser
Electrons fall behind
Typical bubble radius ≈ few μm

## Slide 21: Fabricating flying focus optics in-house at LLE
1. Design
2. Fabrication
3. Metrology
J. J. Pigeon et al., Optics Express 32, 1 (2024).
Spherical substrate → Axiparabola
Flat substrate → Echelon

## Slide 22: Axiechelons can be made using the same fabrication technique
Echelon
Adds radial group delay without tilting phase fronts
Axiechelon
Combines an axiparabola and an echelon into a single optic
Axiparabola
Echelon
(nλ/2 steps)
Axiechelon
Coating to convert a spherical substrate into an axiechelon
Constant velocity flying focus (v = c), f/5
Radial mask
Oblique incidence makes the projection of steps elliptical
  Annuli of the beam may be split over multiple steps
  May have an effect of stretching the pulse
Precise alignment required
  Makes it difficult to swap out and try lots of configurations
Extended focal region and spatiotemporal couplings achieved with a single optic
  Easy to align and swap in and out during experiments

## Slide 23: Axiechelons can be made using the same fabrication technique
Echelon
Adds radial group delay without tilting phase fronts
Axiechelon
Combines an axiparabola and an echelon into a single optic
Oblique incidence makes the projection of steps elliptical
  Annuli of the beam may be split over multiple steps
  May have an effect of stretching the pulse
Precise alignment required
  Makes it difficult to swap out and try lots of configurations
Extended focal region and spatiotemporal couplings achieved with a single optic
  Easy to align and swap in and out during experiments
The first axiechelons have been made and are being characterized
Axiparabola
Echelon
(nλ/2 steps)
Axiechelon
Coating to convert a spherical substrate into an axiechelon
Constant velocity flying focus (v = c), f/5

## Slide 24: The axiechelon approach gives the fine control required to produce a perfectly luminal wake
K. G. Miller et al., Scientific Reports 13, 21306 (2023).
Desired wakefield velocity
Bubble shrinkage
term
Early time
Dephasingless
(constant focus velocity)
Dephasingless
(accounting for bubble shrinkage)
Late time
Focus velocity
Plasma group velocity
Traditional
(electrons dephase)

## Slide 25: Using adaptive optics for rapidly tunable flying-focus trajectories is a promising direction
Measuring flying focus velocities in real time remains a challenge
Optics can creep over time
Has not yet been implemented at high power
Markland, H. et al. Optics Letters 51, 676–679 (2026).
P. Blum et al., Optics letters 51, 9–12 (2025).

## Slide 26: Dephasingless laser wakefield acceleration provides a credible path towards TeV-class electron beams in a single-stage, compact accelerator
Initial proof-of-concept experiments have showed that dephasing can be eliminated using a flying focus (published in Nature Physics).
May be possible to drastically shrink multi-GeV accelerators. No pulse guiding. Shorter focal length optics.
Future experiments are being planned to optimize the scheme in preparation to scale to the multi-GeV regime.
Some outstanding experimental challenges:
Demonstration of high-charge, narrow-energy-spread beams, ideally free of dark current
Plasma source (~70 cm length required for 100 GeV flagship)
Transport and diagnostics (for 10-100 GeV electron beams)
Fabrication of large flying focus optics (12” diameter required for demonstrations at e.g. EPAC, ZEUS, CoReLS)