## Slide 1: SHORT-PULSE X-BAND PHOTOGUN: FROM FIRST DEMONSTRATION TO RECENT RESULTS & FUTURE DEVELOPMENTS
Gongxiaohui Chen
PETS
07/27/2026

## Slide 2: outline
Introduction to Structure wakefield acceleration (SWFA)
Two beam acceleration (TBA) at Argonne Wakefield Acceleration (AWA) facility
Motivation for short-pulse acceleration
Selected highlights of the X-band photogun (Xgun):
  Phase scans @ different gradients
  Understanding of the short-pulse operation and beam performance
  Longitudinal phase space (recent work)
Future developments

## Slide 3: Structure wakefield acceleration
CWA and TBA
Collinear Wakefield Acceleration (CWA)
drive beam
main beam
metal shell
dielectric
Two Beam Acceleration (TBA)
drive beam (train)
main beam
power extraction and transfer structure (PETS)
LINAC or gun
extracted RF pulse
Drive and main beam propagate in the same structure.
Energy is transferred locally from the wakefields of the leading bunch to a trailing bunch.
Drive and main beams propagate in separate beamlines and different structures.
RF power is extracted from the drive beam and transferred to the main beamline.

## Slide 4: Two beam acceleration (TBA)
Simulated RF pulse
A single TBA module
Structures (LINAC or gun) is powered by short RF pulses extracted from the PETS.
Main beamline:
Principle: coherent stacking of wakefield pulse produced by each bunch within a train.
At AWA, we are interested in the short-pulse operation, for a metallic corrugated PETS:
  8-bunch drive beam of 400 nC
  RF pulse: ~400 MW, 9 ns
Drive beamline:
PETS
LINAC or gun
drive bunch train
main beam
RF pulse

## Slide 5: AWA test facilities
TBA testbed
…
…
…
…
short RF pulse
Example#2 of TBA
Example#1 of TBA
Power Extraction & Transfer Structure (PETS)
Drive beamline:
Beam energy: ~63 MeV
Single bunch: ~50 nC
8-bunch train total charge: >400 nC
Main (“Xgun”) beamline:
Powered by the PETS with short RF pulses (9 ns).
Flexible beamline for R&D
High-power test stand:
Powered by the PETS with short RF pulses (9 ns).
Dedicated to structure high power conditioning

## Slide 6: Why Short-pulse?
Motivation
Monitor local H-field
evolution
Pulsed heating: high H-field induced temperature rise
Equation:
Under short pulse regime, highest temperature is ~75 °C, greatly lower than long pulse powered structure.
Breakdown insensitive acc. regime (hypothesis):
If BD initiates plasma, the short RF pulse may transmit through the structure and remain largely unaffected [1, 2]
Short Pulse vs. Long Pulse
[1] J. Shao et al., IPAC2022, doi: 10.18429/JACOW-IPAC2022-FROXSP2.
[2] D. Merenich et al., Phys. Rev. Accel. Beams, vol. 27, no. 4, p. 041301, Apr. 2024
Achieved >400 MV/m in an X-band photogun with a low breakdown rate under short-pulse operation.

## Slide 7
Selected highlight i:
phase scans at different gradients
Measured phase scans (charge vs. Xgun launching phase) @ different gradients: 60 MV/m to 320 MV/m
Simulation benchmarking
X-band photogun
…
Drive bunch train

## Slide 8: photoemission studies
Phase scans (or Schottky studies)
Simulation setup
Possible field () contributions acting on the cathode:
Both included in ASTRA
Modeled separately using a sinusoidal surface [1-2]
where,
: applied rf field
: space charge shielding field
: modeled 3D EM field introduced by surface roughness.
In ASTRA, bunch charge is evaluated as follows,
where,
: Schottky strength coefficients
: field on the cathode
[1] D. J. Bradley, et al., J. Phys. D: Appl. Phys., Vol. 10, (1977).
[2] G. S. Gevorkyan, et al., Phys. Rev. Accel. Beams 21, 093401 (2018).
Xgun
main sol.
ICT
BPM
Laser cross

## Slide 9: Schottky scans
@ 60, 100, 180, 250, 320 MV/m
Peak charge discrepancy only at high gradient.
Other emission mechanism involved (i.e. photo-assisted field emission)?
Ref data for simulation param (, , ) optimization
At all gradients, simulations include the shows a better agreement with the measurements.
Revealed a beam clipping issue at the Xgun exit.
Photo-assisted field emission might happen at high gradient.
In ASTRA, bunch charge is evaluated as follows,

## Slide 10
Selected highlight iI:
Operate the Xgun in Transient Regime
Understand the RF buildup process during the short pulse filling
Potential effects on the beam performance
X-band photogun
…
Drive bunch train

## Slide 11: RF build up process
E-field on cathode: 9 ns vs. “long” 50 ns
If driven by 9 ns pulse, Xgun is under-filled and staying in the transient state during the full RF duration.
E-field on cathode is changing cycle by cycle.
Broad high-gradient operational window.
350 MV/m @ ~7.6 ns
Zoom-in
around the mostly filled region
Zoom here
G. Chen, et al., arXiv: arXiv:2503.09575. doi: 10.48550/arXiv.2503.09575.
(peak)

## Slide 12: RF build up process
Spatial evolution of E-field: 9 ns vs. “long” 50 ns
RF
RF
RF
E_cathode (2 ns to 3 ns)
On-axis Ez (2 ns to 3 ns)
E_cathode (7 ns to 8 ns)
On-axis Ez (7 ns to 8 ns)
E_cathode (35 ns to 36 ns)
On-axis Ez (35 ns to 36 ns)

## Slide 13
Recent work:
Longitudinal phase space (LPS)
Measured bunch lengths
Projected emittance, slice emittance
X-band photogun
…
Drive bunch train

## Slide 14: Recent beam test
Beamline in 2025
ε measured w/ multi-slit (2025 data)
Given the current resources, a deflecting cavity (TDC) was installed into the beamline. We try to characterize the longitudinal phase space (LPS):
  Bunch lengths at different injection phases
  Slice emittance measurement
YAG
Quads
Quads
TDC
YAG &
Multi-slit plates
X-band photogun
Spectrometer
dipole
main solenoid
ICT
BPM
PETS
Drive bunch train

## Slide 15: LPS phase space measurement
Preliminary σz and ε
Quads
TDC
Spectrometer
dipole
YAG
beam
Multi-slit plates
LPS and σz @ different phases:
Projected ε and slice ε:
Projected ε
sliced ε
Analysis ongoing…

## Slide 16
future work: New LINAc development
Introduction to the design concept
Preliminary design

## Slide 17: Short-pulse powered LINAC
On-going effort
Backward wave (BW) single cell
Forward wave (FW) single cell
BW matching cell
Rectangular-to-circular adapter
H-plane power divider & FW matching slots
E-plane power divider
Short RF pulse
Beam direction
(a)
(b)
(c)
(d)
(e)
(f)
Design concept:
To maximize the energy gain, a compact LINAC with longer accelerating length is needed.
We proposed a two-half BW-FW structure to extend the structure length, with each section optimized for high vg and high r.
Concept
[1] G. Chen, et al., Proceedings of IPAC’26, 2026. doi: 10.18429/JACoW-IPAC2026-TUV3301.

## Slide 18: future work and Conclusion
New photogun and solenoid design.
Near term (3 MeV10 MeV): Add an in-house conventional linac to reach 10 MeV, and quantify beam performance. With one PETS powering both the X-gun and linac.
Long term (50 MeV): Add a second “PETS-linac” module for further energy scaling.
Xgun upgrade
LINAC
Xgun
Power splitter
Phase shifter
Short-pulse operation is promising, with gradients >350 MV/m demonstrated in the X-gun.
Short-pulse operation also introduce challenges, such as rapid filling time, and potential transient effects in underfilled structures.
The ultimate goal is 100 pC with 100 nm emittance.
Xgun (3 MeV) 10 MeV 50 MeV
Thank you!

## Slide 19: backup

## Slide 20: Phase scan + beam trajectory

## Slide 21: Closer look on Ez (on-axis)
Early filled stage (~2.5 ns)
RF
Standing wave (SW) cavity:
Selected snapshots
“0-mode” like distribution
Clear Deviation from the pure SW Cavity.
Clear Deviation from the pure SW Cavity.
Before reaching to steady states, different coupling between sections causes non-uniform RF power flow, making some sections respond to the RF faster while others lag, showing a delayed or “0-mode”-like field patterns.
G. Chen, et al., arXiv: arXiv:2503.09575. doi: 10.48550/arXiv.2503.09575.

## Slide 22: Closer look on Ez (on-axis)
Mostly filled stage (~7.5 ns)
When the Xgun is under-filled in the transient states, the EM field distribution varies cycle-by-cycle. This transient behavior is different from pure SW cavity.
This transient effect needs to be considered in beam simulations.
RF
Selected snapshots from #88 RF bucket
Ez phases 88°–96°
RF buckets #80, #88, #96, & steady-state

## Slide 23: Beam simulation workflow
Include the transient field map
Dynamic field mapping method, simulation setup:
  Update field map every ~0.2 ps (1° at X-band).
  Use 3D field map
  Zero thermal emittance; no solenoid; ignore space charge
In the following work, we focus on characterizing beam properties (kinetic energy, transverse emittance, and bunch length) with the influence only from transient RF field.

## Slide 24: An example of beam tracking
With dynamic field mapping
Launch the beam from #88 bucket at the launching phase of 185°.
Update field map every 0.2 ps. On-axis Ez (red curve) plotted for reference.
Track the bunch to the gun exit, and record the results (i.e. kinetic energy in this example).
Then repeat this process for launching phase 0° to 360° → next slide
kinetic energy

## Slide 25: Beam performance summary
Kinetic energy, emittance, bunch length
Small effect.
The value of the min emittance is similar as SW cavity (nearly no change). However, the phase is different.
Very small effect.
kinetic energy vs. launching phase
emittance vs. launching phase
bunch length vs. launching phase
G. Chen, et al., arXiv: arXiv:2503.09575. doi: 10.48550/arXiv.2503.09575.

## Slide 26: Lps data calibration
E and time calibration
Notes: ICT4 gate: 190, 210 nC
XICT gate: 30, 135 pC