## Slide 1
Recent Advances in Plasma Wakefield Acceleration at FACET-II
Advanced Accelerator Concepts 2026
Doug Storey | FACET-II | SLAC National Accelerator Laboratory
July 27, 2025
Facility for Advanced
Accelerator Experimental Tests

## Slide 2: Beam driven PWFA at SLAC - FFTB
FFTB: 1999-2006
Energy doubling of 42 GeV electrons in the SLAC linear accelerator
High energy gain - but not a discrete bunch
Blumenfeld et al., Nature 445, 741 (2007)

## Slide 3: Beam driven PWFA at SLAC - FACET
FFTB: 1999-2006
FACET: 2010-2016
Litos, et al., Nature 515, 92 (2014)
Litos, et al., PPCF 58, (2016)
Two bunch PWFA
Multi-GeV energy gain, few-% transfer eff.

## Slide 4: FACET-II – A facility for precision PWFA studies
SLAC linac further divided
FACET-II: Demonstrate single stage plasma wakefield acceleration at collider-relevant energy scale
  Single or double bunches from a new RF photo-injector
  RF linac and bunch compressors for precise control of longitudinal phase space
LCLS-II Accelerator
LCLS Accelerator
FACET-II

## Slide 5: FACET-II provides 10 GeV beams for PWFA studies
Single or double bunches at 10 GeV
𝒪(10𝜇m) emittance, 𝒪(100kA) peak currents
SLAC National Accelerator Laboratory
FACET-II Technical Design Report SLAC-R-1072

## Slide 6: FACET-II experimental area
Collimators
Magnetic chicane
YAG
screen
Final focus quadrupoles
EOS
Spectrometer quadrupoles
Spectrometer dipole
Cherenkov spectrometer
Transverse deflecting cavity
Long plasma sources
YAG
screen
Gas jet
Two-bunch energy profile
Longitudinal profile
No plasma
PWFA beams
Li plasma profile
2D longitudinal phase space
Drive
Witness
Drive
Witness
Drive
Witness
Drive
Witness
Witness
Drive
J. Park, WG5 Th 15:20
E. Ros, WG5 M 17:20
Notes: Jinseo – Virtual TCAV

## Slide 7: Plasma sources at FACET-II: Li oven plasma source
Lithium oven vapor source:
Beam or laser ionized plasma source
Nominal plasma density of cm-3 over 40cm length
~10 cm density ramps defined by Li/He boundary
Li Oven
Bypass line
Picnic Basket
Laser Extraction
Spectrometer Bend
Upstream DPS and final focus quads
XTCAV
US Be
window
DS Be
window
Downstream DPS and reimaging quads
Li Oven / Bypass line

## Slide 8: Plasma sources at FACET-II: Laser ionized hydrogen plasma
Ariniello, R., V. Lee, and M. D. Litos, Optics Express 33.25 (2025): 52019-52034.
Laser-ionized unconfined H2 gas
Tandem lens shapes intensity and phase
On-axis density at 5x1016 cm-3 over 80 cm
Longitudinal laser intensity measurement confirms lens design and beam-based measurement confirms plasma length

## Slide 9: Topic #1
Multi-GeV PWFA with high beam quality and efficiency

## Slide 10: FACET-II Goal: PWFA with high efficiency and high beam quality
  Multi-GeV energy gain, with 10’s-% energy transfer efficiency, and beam quality preservation
Joshi et al., PPCF 60, 034001 (2018)
  What do we need to achieve this goal?
  Peak current of drive and witness bunches (10 kA)
  Witness (and drive) bunches matched to the plasma density
  Drive and witness transversely aligned, and with the correct bunch separation

## Slide 11: The beam alignment problem – How do you measure it?
Collimators
Magnetic chicane
YAG
screen
Final focus quadrupoles
EOS
Spectrometer quadrupoles
Spectrometer dipole
Cherenkov spectrometer
Transverse deflecting cavity
Plasma source
YAG
screen
Upstream BPM
Downstream BPM
  Energy slice-BPM measurements
  Collimators select energy slice
  BPMs measure IP trajectory of that slice
Y. Ye, WG3 M 14:50
Energy-slice IP trajectories
Novel slice BPM dispersion measurement allows for measurement and optimization of critical beam properties
Plasma entrance

## Slide 12: The beam alignment problem – How do you fix it!
Collimators
YAG
screen
Final focus quadrupoles
EOS
Spectrometer quadrupoles
Spectrometer dipole
Transverse deflecting cavity
Plasma source
YAG
screen
Upstream BPM
Downstream BPM
Sextupole Magnets
  Sexutpole magnets in dispersive region of chicane
  Adjust sextupole strength and position to align energy slices
  12 degrees of freedom to tune!
Drive
Witness
Plasma
Witness
Drive
Plasma
ML
Cherenkov spectrometer
Machine learning enables more efficient bunch alignment in this high-dimensional search space

## Slide 13: Maximizing drive‑to‑wake energy transfer with ML beam tuning
ML-tuning achieved up to
    Single bunch: 1.6 nC @ 10 GeV
    7.7 J energy transferred to the plasma
Statistics across subset of dataset with same compression:
  = 6.1 ± 0.5 J and = 38 ± 3%
  GeV
= 7.7 J
= 48%
Approaching the energy-transfer scale required for efficient staging applications
Image credit: Y. Ye, SLAC
Depleted energy spectrum
Credit: S. Rego,
Ecole Polytechnique
Notes: Note – HALHF - 80% efficiency, 4 GeV drive, 8 nc  25J transferred to the wake. Factor of 3 higher than achieved here.

## Slide 14: Plasma-based ML optimization of two bunch PWFA
ML tuning on PWFA performance:
  Objective: Maximize total energy transfer efficiency (drive  witness)
Result: 5x improvement in
Next steps to improve performance
  Include additional linac settings as model inputs (phase, BPM readings, etc)
  Expand actuators (DOFs): sextupoles + FF quads + correctors
ML optimization is now part of routine PWFA tuning, enabling faster, repeatable operation
Credit: S. Rego, Ecole Polytechnique

## Slide 15: Optimizing beam loading to reduce energy spread
Next step – use collimators to shape the witness profile to optimize beam loading
  By flattening the wake:
Overloading in QPAD simulation
Overloaded
Collimated
Credit: T. Dalichaouch, UCLA/SLAC
Can achieve <1% energy spread on witness after proper bunch shaping

## Slide 16: Multi-GeV acceleration with high field-uniformity and efficiency
Stable witness acceleration across shots with comparable incoming beam parameters
  Driver: 1.2 nC, 6-8 kA, Witness: ~250 pC
  Plasma: 40cm long lithium plasma, 4e16 cm-3
Energy gain, | (4.1 ± 0.3) GeV
Gradient, | (10 ± 1.0) GeV/m
Energy spread | (0.58 ± 0.06) %
Field uniformity, | (2.0 ± 0.2) %
Instantaneous efficiency, | ~20-30 %
Total efficiency, | (4.9 ± 0.5) %
 | (4.1 ± 0.3) GeV
 | (10 ± 1.0) GeV/m
Energy spread | (0.58 ± 0.06) %
 | (2.0 ± 0.2) %
 | ~20-30 %
 | (4.9 ± 0.5) %
Precision PWFA studies at collider-relevant energy scale

## Slide 17: PIC simulations are guiding future progress
  QPAD simulations used to better understand loading, matching, etc
  Performed by T. Dalichaouch (UCLA/SLAC)
  Simulation matches experimental setup
  With plasma density ramps
  Similar LPS and emittances, but with azimuthal symmetry
Credit: T. Dalichaouch, UCLA/SLAC
Excellent agreement between PIC sims and experimental results

## Slide 18: Pushing the energy-transfer efficiency beyond
New tools have pushed our total efficiency to ~10% while maintaing sub percent energy spread
Pushing the bounds of energy transfer efficiency, while maintaining high quality acceleration
(a)
(b)
(a)
(b)
Preliminary

## Slide 19: Work towards matching and emittance preservation
Transverse offset of the witness bunch leads to emittance growth
  PWFA studies at 11016 cm-3 ( goes from 160 µm to ~300 µm)
At this reduced plasma density:
  Witness energy gain of 1.2 GeV
  Beam divergence increased to ~ 100 µrad (factor of 5 over incoming)
Witness
Drive
4.41016 cm-3
11016 cm-3
20 µm transverse offset of the witness
Credit: T. Dalichaouch, UCLA/SLAC
Y. Ye, WG3 M 14:50

## Slide 20: Drive beam depletion in laser-ionized hydrogen plasma source
Ariniello et al., arXiv:2511.15143 (2025)
Lee et al., PRAB 29, 041001 (2026)
Multi-joule energy transfer demonstrated in the laser ionized plasma source
5.6 J and = 37 ± 3% in an all-optical plasma source
Energy depletion of particles to below 1 GeV

## Slide 21: High-performance PWFA in laser-ionized hydrogen plasma
V. Lee, WG3 Tu 14:10
Large energy gain
Large total efficiency
High overall quality
Large energy Gain
Large total efficiency
High overall quality
High quality and high efficiency witness acceleration in an application-relevant plasma source

## Slide 22: Optical probing of plasma wakes via dark field shadowgraphy
Observation of plasma wakes to diagnose wake structures in PWFA and exotic regimes
Beam direction
PWFA regime
PWFA regime
H. Zhang, WG3 Th 14:50
Credit: S. Rego, Ecole Polytechnique

## Slide 23: Optical probing of plasma wakes via dark field shadowgraphy
Beam direction
Wakeless regime
Observation of plasma wakes to diagnose wake structures in PWFA and exotic regimes
Wakeless regime
H. Zhang, WG3 Th 14:50
Credit: S. Rego, Ecole Polytechnique
Minimal wake structure behind the beam
Notes: Applications to ion channel laser, e+ acceleration

## Slide 24: Topic #2
Ultra-high brightness plasma injectors and brightness transformers

## Slide 25: Plasma-wakefield injector boosts energy and brightness
Meter-scale static fill H2 gas, with H2 gas jet
Three stage brightness booster:
  Stage 1: Plasma lens
  Stage 2: Density downramp injection
  Stage 3: Plasma Accelerator
Gas-jet in static fill
10 GeV Driver
Gas jet
Density
downramp
~2.8m
Zhang et al., Nat. Comms. 16, 10719 (2025)

## Slide 26: Plasma-wakefield energy and brightness booster
Meter-scale static fill H2 gas, with H2 gas jet
Three stage brightness booster:
  Stage 1: Plasma lens
  Stage 2: Density downramp injection
  Stage 3: Plasma Accelerator
Zhang et al., Nat. Comms. 16, 10719 (2025)

## Slide 27: High transformer ratio acceleration of the injected bunch
10 GeV incoming electron bunch
  Charge: nC
  Emittance: mm mrad
  Energy spread:
  Current: kA
Outgoing beams:
  Injected charge: up to ~40 pC
  Emittance: mm mrad
  Energy spread:
  Current: ??
Plasma injected bunches accelerated up to 30 GeV with transformer ratio greater than 2
C. Zhang, WG3 Tu 13:30
Extension of this idea:
  TeV electron beams from Plasma Acceleration via Regenerative Cascading
Zhang and Joshi , arXiv:2607.07979 (2026)

## Slide 28: Brightness transformer with high conversion efficiency
Use the measured energy spectrum to infer the current profile from a physics informed model of the plasma acceleration process
Zhang et al., Nat. Comms. 16, 10719 (2025)
Brightness of injected beams up to 38x brighter than incoming bunch

## Slide 29: Stable density downramp injection – next steps
New fixed length plasma source tested
Modulated downramp injection
Xu et al., Nat. Comms. 13, 3364 (2022)
Generating stable, low-emittance, pre-bunched beams in a plasma wakefield accelerator
Credit: C. Zhang, UCLA

## Slide 30: Trojan Horse injection for ultra-bright electron beams
Collinear Trojan Horse injection
  nm rad-scale emittance
  Application towards future light sources
Reconfiguration of the FACET-II experimental area underway!
First collinear Trojan Horse injection experiments will take place this fall
Habib and Heinemann, et al., Ann. Phys. 2023, 353, 2200655
N. Thomas, WG3 M 13:50
E. Hartmann, WG5 M 14:50
B. Hidding, WG6 M 16:40, WG3 Th 14:30, …
Habib et al., Nat. Comms. 14, 1054 (2023)
New FACET IP layout

## Slide 31: Energy chirp in PWFA beams enable compression to <100 nm duration
z
Eb
z
Eb
z
Eb
Chicane
89 MeV/um
Plasma chirper
Compression of plasma-chirped witness beams  increased CSR emission as compression is increased
Plenary: K. Swanson, Th 10:45
R. Hessami, WG6 M 16:00

## Slide 32: PWFA studies at FACET-II
Multi-GeV acceleration with high beam quality and efficiency at collider-relevant energy scales
  ~10% energy efficiency with sub percent energy spread
  Next step – emittance preservation!
Ultra-high brightness plasma injectors and brightness transformers
  Transformer ratios >2
  >38x brightness boost

## Slide 33: Many thanks to all my collaborators
SLAC Advanced Acceleration Research Department team:
  S. Crisp, T. Dalichaouch, K. Downham, A. Edelen, C. Emma, S. Gessner, C. Hast, J.P. Gonzalez Aguilera, M. Hogan, P. Kicsiny, A. Kinderman, A. Knetsch, C. Lin, J. Park, S. Perez, I. Rajkovic, D. Storey, K. Swanson, Y. Ye, J. Wang, B. O’Shea
  Z. Buschmann, R. Loney, M. Parker, G. Yocky
Plus many more contributions:
    FACET-II is supported in part by the U.S. Department of Energy under contract number DE-AC02-76SF00515

## Slide 34: Thank you!
Questions?

## Slide 35: Extra materials

## Slide 36: TeV electron beams from Plasma Acceleration via Regenerative Cascading
TeV beams from a two-stage sub-kilometer plasma accelerator

## Slide 37: FACET-II provides 10 GeV beams for PWFA studies
FACET-II Technical Design Report SLAC-R-1072
Positron Damping Ring (not installed)
Two ways to produce 2 bunches at the experimental area for PWFA studies:
Single chirped long bunch, collimated to produce lower current drive and witness
FINAL FOCUS
To PWFA
Jaw Collimators
Notch Collimator
SYAG
Drive
Witness

## Slide 38: FACET-II provides 10 GeV beams for PWFA studies
FACET-II Technical Design Report SLAC-R-1072
Positron Damping Ring (not installed)
Two ways to produce 2 bunches at the experimental area for PWFA studies:
Two bunches off the photo cathode, co-accelerated through the linac
Energy
Time
Energy [GeV]
Drive
Witness
EOS Temporal Profile
TCAV Long. Phase Space
Drive
Witness
Drive
Witness

## Slide 39: PWFA in the laser-ionized hydrogen plasma source
51016 cm-3 laser ionized plasma, 80 cm length
Credit: V. Lee, CU Boulder

## Slide 40: Post plasma diagnostics
gammas
e-
Plasma
sources
Spectrometer Quadrupoles
Spectrometer
Dipole
UV Spectrometers
Electron and Gamma Screens
C. Emma et al., PRL 134, 085001 (2025)
Imaging electron spectrometer
Betatron radiation diagnostics
UV and XUV spectrometers
  Compton Spectrometer upcoming, covering a range of 180 keV-28 MeV
P. San Miguel Claveria et al., AAC (2022)
D. Storey et al., PRAB 27 051302 (2024)

## Slide 41: Laser pre-ionization of Lithium plasma
Pre-ionization increases PWFA performance over relying on beam ionization
  ~1 mm wide plasma channel
  Increased participating drive charge
  Increased witness acceleration and total efficiency
 | Laser Ionized | Beam Ionized
Energy gain, | (4.0 ± 0.2) GeV | (3.7 ± 0.2) GeV
Field uniformity, | (2.3 ± 0.2) % | (3.4 ± 0.6) %
Total efficiency, | (5.5 ± 0.5) % | (4.6 ± 0.3) %
Witness charge capture, | (68 ± 6) % | (64 ± 4) %
 | Laser Ionized | Beam Ionized
 | (4.0 ± 0.2) GeV | (3.7 ± 0.2) GeV
 | (2.3 ± 0.2) % | (3.4 ± 0.6) %
 | (5.5 ± 0.5) % | (4.6 ± 0.3) %
 | (68 ± 6) % | (64 ± 4) %

## Slide 42: Longitudinal Phase Space delivered to the plasma
Control of the LPS is critical for:
  Ensuring proper bunch spacing
  Optimizing driver intensity for efficient energy transfer
  Beam loading of the wake for minimizing witness energy spread
Achieved through combination of RF phases, collimators, cathode laser pulse separation
LPS measured via transverse deflecting cavity before the plasma
Range of Longitudinal Phase Space Profiles
Drive
Witness
Collimation
Drive
Witness