## Slide 1: High temporal resolution THz streaking of high brightness relativistic electron beams
By Maximilian Lenz
Advanced Accelerator Concepts
July 27 2026
Notes: The main topic I would like to talk about is THz streaking as a longitudinal bunch length diagnostics
but also another laser based beam diagnostic we performed at UCLA

## Slide 2: Motivation
Laser electron beam synchronization
Longitudinal bunch length diagnostics
Inverse Compton Scattering
Animation by Brian Schaap
Dielectric Laser Accelerator
Mei et al. Ultrafast Science 2023
Ultrafast Electron Diffraction Dexter Johnson (2017)
Notes: Let me motivate this:
Lasers are finding more and more applications in accelerators and beam interactions
We need reliable tools to measure out the timing between laser and electron beam

## Slide 3: PEGASUS beamline
Photogun
1.6 cell S-band
Solenoid
ICT
Linac 11 cell S-band
Dipole spectrometer
Quadrupoles
Vacuum chamber
Charge: 1fC-3nC
Energy: 3-10MeV
Bunch length:
Highly modular, student operated
THz streaking
THz
Ota, M., et al. IRMMW-THz 2022
Electro – Optic Sampling
Rest frame
Lab frame
Notes: Before I introduce the two THz experiments we did at Pegasus let me first show you Pegasus
Here is a schematic of Pegasus
It’s a highly modular beamline and parts are changing all the time
  Even this figure from three years ago is outdated
Fully student run. Pietro always shows this picture when he talks about his students. Shows how he truly sees us…
Photo gun produces a few MeV electron beams
Linac then allows us to further accelerate, compress or deaccelerate the beam

## Slide 4: Electro-Optic Sampling (EOS)
Electro-Optic effect
  Birefringence
e-beam
vacuum
chamber
ZnTe
CMOS camera
polarizer
polarizer
Notes: This has been performed many times but what’s unique is that we directly hit the crystal

## Slide 5: Transverse and longitudinal information
Fluorescence without probe ZnTe crystal is a screen by itself
Measurement of transverse and longitudinal field profile
E-beam fluorescence
ZnTe damage
Measured
Analytic
Longitudinal slice
Transverse slice

## Slide 6: EOS on e-beam fields
Signal observable at
Electron bunch lengths measured (Jitter Limited)

## Slide 7: THz streaking
Electromagnetic fields induce a force on the beam
Place beam on gradient of the THz field
        Streaking of the beam
THz vs RF
Higher frequencies Stronger gradients
Short interaction length
  Diagnostic at single position
Laser synchronized
Notes: Overlap a THz wave with an electron beam
Propagate through a field enhancing structure
Wave induces a Lorentz force on the particles that deflects them
If we place the beam on the zero crossing of the wave it gets streaked
Allows us to map out this longitudinal profile transversely on a screen

## Slide 8: THz source setup
Mg:LiNbO3 crystal
Grating – imaging configuration for phase matching
780 nm,
100 fs, 10 mJ
QWP
OAP f=2”
OAP f=4”
Pellicle
Wollaston
Compressor
Amplifier
CCD
Ti:Sapph laser system
THz
EOS line
Notes: Many iterations of this setup

## Slide 9: THz streaking – Experimental Setup
RF
Photogun
THz signal on ZnTe
Pinhole
Quads
Solenoid
Vacuum Box
Different streaking structures
        Adjustable position in x, y, z and tilt around x-axis
OAP with 3mm hole: Overlap of beam and THz
THz off
THz on

## Slide 10: THz streaking – Calibration
Notes: What we now need is to understand this longitudinal to transverse mapping

## Slide 11: THz Streaking Structures
Tsinghua Structure
Confined waveguide mode
Dispersive
  Increases phase velocity
  Stretches waveform
Ucla structure
Parallel plate waveguide TEM mode
No dispersion
Easier fabrication and simulation
  Parameters were optimized numerically
750
One half
Front view
Waveguide section
50
Yuemei Tan (Tsinghua university)
Front view
Model
100
Waveguide section

## Slide 12: Streaking gradients

## Slide 13: Road to 1fs electron beams
Attosecond bunchlengths would be a major milestone!
  UED, FELs, Compton sources
Maxson et al., PRL 118, 154802 (2017)
L. Zhao. Phys. Rev. X 8, 021061 (2018)
THz streaking
F. Qi et al., Phys. Rev. Lett. 124, 134803 (2020)
Snively, E. C., et al. Phys. Rev. Lett. (2020)
Yang, Yining, et al. arXiv:2508.03946 (2025).
H. W. Kim et al., Nat. Phot., 14, 245 (2020)

## Slide 14: Road to 1fs electron beams
UV pulse on cathode
  Samples less phases on linac
        Linear compression
        More space charge
UV pulse on cathode
  Non-linearities in linac Advantageous!
  Less space-charge
        Simulation: 0.6fs current spikes
100m Pinhole
Virtual cathode
camera
Notes: Keep short if we’re short on time!

## Slide 15: Temporal Resolution
Deconvolve streaked signal with background
  FWHM
Noise analysis: 1.3fs resolution
        0.3fs resolution after averaging!
THz off
THz on
4.2 fs

## Slide 16: Summary
Electro-optic sampling of e-beam coulomb fields
  Simple laser-beam arrival time diagnostic
  Multi-shot diagnostic
  Temporal resolution limited to 300 fs
THz streaking of ultrashort electron beams
  Development of a high power THz source
    30J, 0.5% conversion efficiency
  Record streaking gradient of
  2fs bunch lengths measured with femtosecond resolution
Pegasus 2026?

## Slide 17: Acknowledgements
Collaborators Tsinghua University
  Renkai Li, Yining Yang, Yuemei Tan
Work supported by NSF grant PHY-1734215 and DOE grants DE-SC0009914 and DE-SC0021190
Pietro Musumeci
Brian Schaap
Renkai Li

## Slide 18: Thank you! Questions?

## Slide 19: Temporal Resolution Limit
Beam arrival time jitter of
        Multi-shot scans are limited in arrival time
Single shot methods
  Performed on the THz FEL but not for direct beam diagnostics
ZnTe (and other EO crystals) are fundamentally limited
Casalbuoni, S., et al. – PRAB 2008
THz FEL diagnostics

## Slide 20: Mg:LiNbO3 THz source
In LiNbO3 :
Vastly different velocities
Tilted pulse fronts
  Image grating into crystal
Notes: Been demonstrated to have the best balance between conversion efficiency and damage threshold

## Slide 21: Calibration
Find extrema positions
Take projections
Find peak of projections
Reconstruct waveform from extrema

## Slide 22: Streaking Power at different beam energies
Streaking power
  Mismatch between theory and experiment Clipping within structure
Reached structural limitations
2.4mm
Notes: Go over quickly

## Slide 23: THz Streaking - Conclusion and outlook
Developed THz source for THz streaking
  of pulse energy at 0.5% generation efficiencies
Record streaking gradient of
  Limited by the structure itself
Non-linear ballistic compression 2fs beam structures measured
Different Streaking geometries
Pegasus 2026?

## Slide 24: Outlook – Double tapered PPWG
Increase horizontal focusing?
  PPWG has no horizontal focusing element
  Enclosed waveguide will increase dispersion
    Pulse stretching
    Change in phase velocity Shorter interaction length
Possible solution: Double tapered parallel plate waveguide

## Slide 25: Outlook – Breaking the streaking power limits
Very low dispersion!
  For refrerence:
    Tsinghua structure:
field enhancement
  Tsinghua structure:
measured at
gradients possible
Rohrbach, David, et al. "Wideband dispersion-free THz waveguide platform." Scientific Reports 13.1 (2023): 15228.
Iwaszczuk, Krzysztof, et al. "Terahertz field enhancement to the MV/cm regime in a tapered parallel plate waveguide." Optics express 20.8 (2012): 8344-8355.

## Slide 26: DT-PPWG test at UCLA
UCLA designed structure
  Slit width:
  Gap size:
  Far away from optimal
Resin printed and coated with copper tape
Better fabrication capabilities at SLAC than UCLA

## Slide 27: Outlook – Perpendicular Streaking geometry
Increase vertical focusing?
  Clipping of beam
Possible solution: perpendicular geometry
  Stronger force
  Shorter interaction length
Copropagating case: Magnetic fields counter electric fields
Perpendicular geometry: B is along No magnetic field effect
Baek, In Hyung, et al. "Real-time ultrafast oscilloscope with a relativistic electron bunch train." Nature communications 12.1 (2021): 6851.

## Slide 28: Outlook – Perpendicular streaking
Longer bunches can be captured
Better single shot capabilities
No spectrometer required
Baek, In Hyung, et al. "Real-time ultrafast oscilloscope with a relativistic electron bunch train." Nature communications 12.1 (2021): 6851.

## Slide 29: Outlook – Perpendicular streaking
Dephasing effects Beam should sample less than half a cycle
  Fabrication challenge
With significant field enhancement
THz source can be simplified
  Simple ZnTe/GaP crystal for THz generation
Tilted Pulse Front THz source
Mg:LiNbO3