## Slide 1: Compact THz Streaking Framework for Robust Longitudinal Diagnostics in Advanced Accelerators
Gerard Lawler1, Banan Yamani2, Matthias Nabinger3, Micha Dehler1, Evan Ericson1, Nicole Hiller1, Michael Nasse3, Alexander Molodozhentsev2, Rasmus Ischebeck1
1 Paul Scherrer Institute 2 Extreme Light Infrastructure 3 Karlsruhe Institute of Technology
Notes: Leverage PSI expertise in longitudinal diagnostics and to develop and improve THz diagnostics for scalable beamline implementations

## Slide 2: Motivation
https://agenda.infn.it/event/50880/contributions/288551/attachments/146220/222591/EuPO_Marinelli.pdf
PACRI European funded project to develop key plasma accelerator technologies for Europe’s future research infrastructures, such as EuPRAXIA and Extreme Light Infrastructure (ELI)
SWISSELITE: Swiss Contributions to Technological Advancements at ELI Beamlines

## Slide 3: RF Deflecting cavity
https://indico.cern.ch/event/1335148/contributions/5663218/attachments/2769854/4825803/PolariX_CLIC_Mini_Week.pdf
Marchetti, B., Grudiev, A., Craievich, P. et al. Experimental demonstration of novel beam characterization using a polarizable X-band transverse deflection structure. Sci Rep 11, 3560 (2021).
State of the art PSI PolariX TDS
Meters on beamline
https://indico.cern.ch/event/1380440/contributions/6176576/attachments/2969104/5224846/CAS24_longitudinal_BI.pdf

## Slide 4: RF Deflecting cavity
https://indico.cern.ch/event/1335148/contributions/5663218/attachments/2769854/4825803/PolariX_CLIC_Mini_Week.pdf
Marchetti, B., Grudiev, A., Craievich, P. et al. Experimental demonstration of novel beam characterization using a polarizable X-band transverse deflection structure. Sci Rep 11, 3560 (2021).
State of the art PSI PolariX TDS
Meters on beamline
https://indico.cern.ch/event/1380440/contributions/6176576/attachments/2969104/5224846/CAS24_longitudinal_BI.pdf

## Slide 5: Proof of concept geometries
Resonant structures manufactured and tested in collaboration with Karlsruhe Institute of Technology (KIT) @ FLUTE (Ferninfrarot Linac- und Test-Experiment)
Inverse Split Ring Resonator (ISRR)
Tilted-slit Resonator (TSR)
Glukhov, Sergei, et al. "Simulations of the compact transverse deflecting system for ultra-short electron bunch diagnostic." Proc. IPAC’23 (2023): 4887-4890.

## Slide 6: What changed?
Not necessarily max Q
Focus on want stronger streaking field for the same incident THz energy, shunt impedance, and longer interaction length
RF TDS | THz Resonator
Higher Q beneficial | Higher Q increases field enhancement
Narrowband | THz pulse may be broadband
Filling time not critical | Filling time may exceed pulse duration
Goal to maximize voltage | Goal to maximize kick per available THz energy

## Slide 7: Why THz?
RF systems challenging in certain situations
Existing laser systems when RF difficult (e.g. KIT right)
Short pulse synchronization
Treat THz less like optical diagnostic and more like mini-RF systems
MeV energy electrons
Schaefer, Jens, et al. "Split-ring resonator experiments and data analysis at FLUTE." Proc. 14th International Particle Accelerator Conf.(IPAC’23). 2023.

## Slide 8: THz Generation
Experimental chamber proceeded by photogun, magnetic optics, and collimator followed by dipole + screens
High Q resonator -> RF like behavior with field enhancement >50 in gap
Approx 10 urad/fs streaking strength
Experimental chamber
Dipole magnet
Schäfer, Jens, et al. "Split Ring Resonator Experiment-Simulation Results." Proc. IPAC’21 (2021): 888-891.

## Slide 9: Entering New Regime
Underlying diagnostic logic still recognizable as RF streaking
Micron gap aperture
THz higher in frequency so imprint more on beam of same length
RF TDS | THz Resonator
Linearized streak | Highly nonlinear
Single 0 crossing | Multiple visible cycles
Simple observable | Complex image morphology
RF infrastructure | Laser systems
cm gap | micron gap

## Slide 10: Visualization
Linear energy chirp allows dispersive section to see multiple cycles

## Slide 11: FLUTE data
In FLUTE data we get linear energy chirp from S-band photogun
THz phase delay dependent morphology
TSR
ISRR

## Slide 12: FLUTE data
In FLUTE data we get linear energy chirp from S-band photogun
THz phase delay dependent morphology
TSR
ISRR

## Slide 13: FLUTE data
In FLUTE data we get linear energy chirp from S-band photogun
THz phase delay dependent morphology
TSR
ISRR

## Slide 14: Failure of existing observables
Complex shapes lead to difficult comparison
For three example densities p1, p2, p3
Each pair has the same distance in L1, L2
https://www.stat.cmu.edu/~larry/=sml/Opt.pdf
L1

## Slide 15: Morphology based image comparison
Earth Mover’s Distance (EMD) calculate minimum “work” used to transform distributions optimally
Common in machine learning
Projections into lower dimensions can be used
https://sbl.inria.fr/doc/Earth_mover_distance-user-manual.html
Zhang, J., Ma, P., Zhong, W., & Meng, C. (2023). Projection-based techniques for high-dimensional optimal transport problems. WIREs Computational Statistics, 15(2), e1587. https://doi.org/10.1002/wics.1587

## Slide 16: Intuition
EMD AKA Wasserstein metric linearity unlike L1, L2, or chi^2
Gives more reliable positioning jitter reduction
Faster algorithms for EMD noisier but on average still effective

## Slide 17: Applications for THz streak
Low noise

## Slide 18: Applications for THz streak
Moderate noise

## Slide 19: Applications for THz streak
High noise

## Slide 20: Experimental images
Example longitudinal data for TSR
2.87 ps

## Slide 21: Theory + simulation
Experimental error limited to angular resolution in 10s of fs, improvements possible with EMD
2.87 ps

## Slide 22: Modified EMD
1 dimension calculation for streak

## Slide 23: Scalability Needs
Laser Undulator-Illuminated Source (LUIS) in phase 0
Phase 1 10^5–10^7 incoherent soft X-ray photons per pulse
Phase 2 high-flux coherent XUV 10^9–10^11 photons per pulse

## Slide 24: Higher energy beams
100 MeV case w/ RF TDS on way to 300 MeV ELI case
24.71 pC, 308.24 MeV, beam
THz TDS cavity 0.3 THz, 4.9 MV, 49 MV/m
Notes: Activity 2.1.2. Feasibility study and Conceptual design of the laser-based THz TDS setup
  Participants: ELI, PSI / Lead: PSI
Deliverable 2.1.2 (D2) Conceptual design of the integrated THz TDS setup
Milestone 2.1.2 (M2) Scope of work and list of components of the integrated THz DS setup, including laser, dielectric structure and relevant diagnostics.

## Slide 25: Higher energy beams
100 MeV case w/ RF TDS on way to 300 MeV ELI case

## Slide 26: Segmented THz structures
Primarily to increase effective interaction length
With previous performance 1-2 cm needed
Zhang, Dongfang, et al. "Segmented terahertz electron accelerator and manipulator (STEAM)." Nature photonics 12.6 (2018): 336-342.
Notes: Improve upon horn geometry and coupling with CST Microwave Studios optimization

## Slide 27: Preliminary implementation
Conceptual design ongoing but clamped structure shows promise
10s mm linear dimensions

## Slide 28: Conclusions
THz resonators can reproduce familiar RF streaking concepts in smaller package
Understanding which assumptions survive and which do not is an ongoing process and translating PolariX TDS performance remains goal
New regime benefits from advanced image-processing methods for interpreting more complicated morphology
Promising scalable solution for compact research infrastructure such as Eupraxia at ELI
Notes: Leverage PSI expertise in longitudinal diagnostics and to develop and improve THz diagnostics for scalable beamline implementations

## Slide 29: Conclusions
THz resonators can reproduce familiar RF streaking concepts in smaller package
Understanding which assumptions survive and which do not is an ongoing process and translating PolariX TDS performance remains goal
New regime benefits from advanced image-processing methods for interpreting more complicated morphology
Promising scalable solution for compact research infrastructure such as Eupraxia at ELI
Questions?

## Slide 30: Further References
Floettmann K., PRSTAB,6, 034202 (2003)
Glukhov, Sergei, et al. "Simulations of the compact transverse deflecting system for ultra-short electron bunch diagnostic." Proc. IPAC’23 (2023): 4887-4890.
He, Xie, et al. "Terahertz-Driven Two-Dimensional Mapping for Electron Temporal Profile Measurement." Acs Photonics 12.6 (2025): 3064-3072.
Lenz, Maximilian, et al. "High temporal resolution THz streaking of high brightness relativistic electron beams." arXiv preprint arXiv:2605.00125 (2026).
Migliorati M. et al, Physical Review Special Topics, Accelerators and Beams 16, 011302 (2013)
Qi, Hong, et al. "Self-synchronized ultrafast electron beam diagnostics using a split-ring resonator driven by multicycle THz pulses." Nuclear Engineering and Technology 57.6 (2025): 103434.
Qi, Yingpeng, et al. "Theoretical studies of the THz compression of low-to-medium energy electron pulses and the single-shot stamping of electron–THz timing jitter." New Journal of Physics 23.6 (2021): 063052.
Schaefer, Jens, et al. "Split-ring resonator experiments and data analysis at FLUTE." Proc. 14th International Particle Accelerator Conf.(IPAC’23). 2023.
Schäfer, Jens, et al. "Split Ring Resonator Experiment-Simulation Results." Proc. IPAC’21 (2021): 888-891.

## Slide 31: Bonus: Wasserstein metric Properties
n_pixels = 80
pixel_pitch = 1.0
sigma_beam = 7.0 # broad beam
noise_level = 0.01 # moderate noise
max_shift = 1.0 # maximum sub-pixel shift

## Slide 32: Bonus: Wasserstein metric Properties
n_pixels = 80
pixel_pitch = 1.0
sigma_beam = 7.0 # broad beam
noise_level = 0.002 # moderate noise
max_shift = 1.0 # maximum sub-pixel shift

## Slide 33: Bonus: Wasserstein metric Properties
n_pixels = 80
pixel_pitch = 1.0
sigma_beam = 7.0 # broad beam
noise_level = 0.001 # moderate noise
max_shift = 1.0 # maximum sub-pixel shift

## Slide 34: Bonus: Wasserstein metric Properties
n_pixels = 80
pixel_pitch = 1.0
sigma_beam = 7.0 # broad beam
noise_level = 0.00001 # moderate noise
max_shift = 1.0 # maximum sub-pixel shift