## Slide 1
Alex DeSimone
7/30/2026
Emittance Growth and Sensitivity Analysis of a Transverse Deflecting Cavity-Based Dechirper

## Slide 2: Transverse deflecting cavities (TDCs)
Nonlinearities are not a concern:
TDCs operate at zero-crossing phase and
TM110
Transverse kick, longitudinal acceleration
TDC operation in mode:
  Reference particle experiences no forces at zero-crossing phase
  Transverse kick based on longitudinal position
  Longitudinal acceleration based on transverse position
Courtesy of H. Xu
Color-coded for energy
Notes: TDC figure ref.: WEP091 Haoran Xu

## Slide 3: Principle of TDC-based chirping
Accelerating cavities can operate on-crest
Chirp control scheme:
  Introduce coupling
  Angular deflection becomes horizontal displacement through drift
  Second TDC accelerates based on , which is determined by chirp adjusted
  Second drift and third TDC remove remaining and coupling
Beam
z
z
z
z
z
z
z
z
z
z
z
z
1. coupling
4. Remove couplings
2.
3. -acceleration w/ coupling
chirp control

## Slide 4: Principle of TDC-based chirping
Accelerating cavities can operate on-crest
Chirp control scheme:
  Introduce coupling
  Angular deflection becomes horizontal displacement through drift
  Second TDC accelerates based on , which is determined by chirp adjusted
  Second drift and third TDC remove remaining and coupling
Beam
z
z
z
z
z
z
z
z
z
z
z
z
1. coupling
4. Remove couplings
2.
3. -acceleration w/ coupling
chirp control
, so changing doesn’t change sign of chirp

## Slide 5: Negative identity drift (NID) transport
Forming NID sections:
  Form NID in using two quads ( and )
  and defocus , so focuses to prevent large vertical beam size
  are arbitrary
Transport produces correct and correlations for dechirping
Beam
Color-coded for initial
Beam head has
Transport between TDCs must be modified for :

## Slide 6: TDC-based dechirping using NIDs
Principle of dechirper:
  Introduce coupling
  First NID transport ensures correct coupling orientation
  Chirp by accelerating based on (beam head has )
  coupling removed in second NID transport
  coupling with last TDC
z
Beam
z
z
z
z
z
z
z
z
z
z
z
Color-coded for energy
NID
NID

## Slide 7
Simulation study of dechirper in preparation for experimental demonstration

## Slide 8: Simulation of optimal Gaussian beam
Initial beam parameter | Value
Initial beam parameter | Value
Chirp
The dechirper can adjust chirp positively, but introduces emittance growth
Simulations were done in General Particle Tracer (GPT)

## Slide 9: Identifying dominant emittance growth mechanism
For an unchirped Gaussian beam:
  Transverse emittance growth is <3% w/ and w/o space charge
  from higher-order effects is substantial
LPS w/o space charge
LPS w/ space charge
LPS w/o space charge
For an optimal Gaussian beam:
  Transverse emittance growth is <3% w/ and w/o space charge
  Space charge is dominant source of longitudinal emittance growth
LPS w/ space charge
In experimental plan,

## Slide 10: Identifying dominant emittance growth source
TDC1
TDC3
TDC2
Beam
NID1
NID2
Second-order transport
Output
Linear transport
Combination linear and 2nd-order matrix tracking:
Identification of dominant 2nd-order terms in dechirper:
One 2nd-order element at a time reveals source of
NID1 is dominant source of emittance growth
NID1’s and are dominant terms
NID1’s horizontal-longitudinal series contributions
Matrix-based tracking was done in Python
Contributions at end of NID1

## Slide 11: Analytical emittance growth results and mitigation options
Longitudinal transport equations counting only dominant terms:
Emittance growth mitigation strategies:
Reduce TDC strength (reducing chirp control range)
Add sextupoles to compensate nonlinearities in transport
Compensates longitudinal terms by using horizontal-longitudinal coupling

## Slide 12: Emittance growth mitigation results
Adding sextupole to dechirper:
  One sextupole in NID can compensate nonlinear effects in and
Reducing :
  From analytical results, should reduce exponentially with
Emittance growth is reduced, but not eliminated
Emittance growth is largely eliminated, but maintaining requires longer beamline

## Slide 13: Emittance growth mitigation results
Adding sextupole to dechirper:
  One sextupole in NID can compensate nonlinear effects in and
Reducing :
  From analytical results, should reduce exponentially with
Emittance growth is reduced, but not eliminated
Emittance growth is largely eliminated, but maintaining requires longer beamline
Emittance growth is expected in the dechirper’s experimental demonstration, but its sources and mitigation strategies have been identified

## Slide 14
Sensitivity Study of Dechirper

## Slide 15: Engineering-informed sensitivity study
AWA engineering considerations:
All TDCs will have same phase and voltage variations
No feedback control
NID quadrupole gradients will vary independently
Element parameter | Control range
TDC phase | 
TDC voltage | 
NID quadrupole gradient | 
Element parameter | Control range
TDC phase | 
TDC voltage | 
NID quadrupole gradient | 
Ideal transport case
Variations of <10% in beam parameters can be expected in experiment due to engineering constraints
No particle losses seen
~4% max. variation in

## Slide 16: Comparison of and TDC phase control
AWA has phase control, but a narrower control range is possible:
Tighter phase control drastically improves emittance growth, but not chirp control

## Slide 17
Start-to-End Simulation of Dechirper

## Slide 18: Start-to-end simulation of dechirper
Beamline settings | 
Focusing quad strengths | [-0.39, 0.38, -0.42] Tm-1
Slope matching quad strengths | [-0.64, 0.91] Tm-1
, , | [1.1, 2.2, 1.1] m-1
NID quad strengths | [1.0, 1.0, 1.0] Tm-1
Beamline settings | 
Focusing quad strengths | [-0.39, 0.38, -0.42] Tm-1
Slope matching quad strengths | [-0.64, 0.91] Tm-1
 | [1.1, 2.2, 1.1] m-1
NID quad strengths | 
Injector settings | 
Qtot | 100 pC
Gun phase | 50 from zero-crossing
BF sol. current | 550 A
Matching sol. current | 203 A
at | 83.5
Injector settings | 
Qtot | 100 pC
Gun phase | 
BF sol. current | 550 A
Matching sol. current | 203 A
 | 83.5
22.8 m
23.8 m
23.0 m
L1
L2
L3
Cathode at Z = 0.0 m
Accelerating section
10.0 m
Focusing quads
Slope matching quads
13.6 m
L5
30.0 m
BF solenoid
Matching solenoid
26.9 m
NID quads
13.9 m
14.1 m
Chirping TDC
Realistic beam was simulated with injector and transverse matching quadrupoles
Diagnostic section and upgraded injector will be simulated before experimental run

## Slide 19: Emittance and beam envelope up to dechirper entrance
Max. not pictured
Envelope evolution and matched phase spaces:
  Matching solenoid set to minimize at injector exit
  not pictured due to scale difference ()
Five matching quads
Transverse emittance evolution:

## Slide 20: Start-to-end dechirper simulation results
Dechirper performance:
  Emittance growth of realistic beam approximately agrees with results for Gaussian beam
  In experiment, emittance growth of ~10% can be expected in all directions
  Linearity of longitudinal phase space unchanged ()
The dechirper is expected to effectively control chirp without severe emittance growth

## Slide 21: Summary
TDC-based chirper/dechirper experimental preparation is underway (run in September)
Dominant emittance growth sources and related mitigation strategies were identified
A sensitivity study was done to quantify expected beam parameter variations due to engineering constraints
A start-to-end simulation indicated effective chirp control with 10%-level emittance growth in all directions

## Slide 22: Acknowledgements
Northern Illinois University
Gongxiaohui Chen
Scott Doran
Gwanghui Ha
Wanming Liu
Rachel Margraf-O’Neal
John Power
Eric Wisniewski
Los Alamos National Laboratory
Thomas Kim
Quinn Marksteiner
Haoran Xu
Nikolai Yampolsky

## Slide 23: Mitigating emittance growth with a sextupole
#sextupole("wcs","z", 2.495, .1, 5.82856); #6.67313
Space charge off
Space charge on

## Slide 24: Emittance growth by reducing