## Slide 1: The EEX-enabled microbunching experiment at the Argonne Wakefield Accelerator
James Rosenzweig
For UCLA-NIU-ANL-LANL-SLAC collaboration
AAC 2026 – July 30, 2026

## Slide 2: Motivation
The emittance exchange (EEX) process shows great promise for longitudinal beam shaping
  Applications in wakefield acceleration
  Basis of new types of coherent light source
Coherent soft X-rays obtained by converting transverse modulations to longitudinal?
  Many unexplored physical effects – open field for investigation

## Slide 3: AAC application: beam shaping for wakefield accelerators
High transformer ratio PWFA and DWA demonstrated
R. Roussel, et al., Phys. Rev. Lett. 124, 044802 (2020)
Recent work on multi-leaf collimator to refine process (ML emphasis)
Power of collimation + EEX methods is demonstrated
Note residual correlations
N. Majernik, et al., Phys. Rev. Accel. Beams 26, 022801 (2023)
Transverse
Longitudinal

## Slide 4: How does EEX work?
Step 1. Momentum dispersion in x (and t)
Step 2. Dipole mode cavity for converting t to x’. Note that Panofsky-Wenzel theorem indicates x-dependent acceleration, giving correlated DE across the beam
Step 3. Remove the correlation between the x and DE exploiting the x x(t) correlation using a fundamental mode cavity. Small voltage
Step 4. Remove momentum dispersion with dogleg
NB: Doglegs must be sextupole corrected
NB: Transformation done correctly exchanges horizontal and longitudinal emittance. Longitudinal is quite large!

## Slide 5
Emerging application: ASU CXFEL employs EEX
Photoinjector
9.3 GHz
1 kHz
150 MV/m
5 MeV energy
1 pC
200 fs
ICS Interaction Point
In overtaking geometry
Electron diffraction for nanopatterning
3 Linacs
9.3 GHz
1 kHz
75 MV/m
60 MeV max
Ebeam optics match to EEX
Emittance exchange EEX
ICS laser: Trumpf DIRA 400
1030 nm Yb:YAG
400 mJ/shot at 1 kHz
<50 fs pulse with nonlinear compression
X-rays to hutch
Solenoids
Ebeam dump
Courtesy: W. Graves
Laser undulator gives low energy operation (<46 MeV)

## Slide 6
CXFEL Soft X-ray Parameters
Photon energy | 250 | 1000 | 2500 | eV
X-ray wavelength | 4.9 | 1.2 | 0.49 | nm
Average flux at 1 kHz | 8.0E+11 | 1.1E+11 | 4.4E+10 | photons/sec
Average brilliance | 1.3E+15 | 1.2E+16 | 7.3E+16 | ph/s/mm^2/mrad^2
Peak brilliance | 1.2E+28 | 5.6E+28 | 1.4E+29 | ph/s/mm^2/mrad^2
RMS source size | 0.9 | 0.5 | 0.3 | um
RMS source divergence | 440 | 188 | 117 | urad
X-ray flux per shot - energy | 32 | 18 | 18 | nJ
Photons per pulse | 8.0E+08 | 1.1E+08 | 4.4E+07 | Photons/shot
Pulse length FWHM | 9.1 | 4.6 | 1.9 | fs
Bandwidth FWHM | 0.18 | 0.09 | 0.08 | %
RMS timing jitter | <10 | <10 | <10 | fs
Repetition rate | 1000 | 1000 | 1000 | Hz
Electron beam energy | 14 | 29 | 46 | MeV
Goals extending to sub-nanometer coherent light

## Slide 7
This collaboration has embraced an experimental opportunity at the AWA
Test the physics limiations of the EEX microbunching itself

## Slide 8: Micro-bunching with EEX at the AWA
Start at longer period modulations
  Collimation-based systems; ASU uses electron diffraction
  E. A. Nanni, W. S. Graves, D. E. Moncton Phys. Rev. Accel. Beams 21, 014401 (2018)
  Diagnostic systems within reach?
  Establish operation in optical-IR – 800 nm
Explore physical limits of process in existing setup
  Optical nonlinearities
  Collective effects: space-charge, coherent synchrotron radiation (CSR)
First analysis of physics and experimental challenges
  Study charge, wavelength, optics dependencies
  Initial experimental scenario can be scaled in charge

## Slide 9: Overview of Experimental Approach
HPS at TEM Grid exit
HPS at Demagnifier exit
HPS at TEM Grid entrance
LPS at EEX exit
TDC
FMC
AWA Injector
Goal: generate sub-micron longitudinal density modulation using (asymmetric) emittance exchange (EEX) beamline at the AWA
44 MeV, 2 pC electron beam
Observation of z-modulation
3

## Slide 10: The beginning: low charge (1 pC) operation chosen
Optimized phase space quality; minimized collective effects
0.1 pC
1 pC
10 pC
Low charge for many reasons! Emittance, EEX CSR and space-charge, nonlinearities
Courtesy G.Ha

## Slide 11: Emittance: quad scans
April 2026
July 2025
x
y
x
y
,
e-
Non-optimized:
2025: old RF gun
2026: large laser on cathode
Courtesy R. Magraf-O’Neal

## Slide 12: Measuring micron-scale beam features
Filter .32% (~.3 pC)
Colorscale_max
=1000
= 71 μm
= 39 μm
Filter 3.2% (3pC)
= 89 μm
= 63 μm
Colorscale_max
=12000
Smallest beam sizes measured at AWA are 30-40 μm
YAG thickness (100 μm) can reduce resolution
Collective effects
Emittance/beam-optics limits
Courtesy R. Magraf-O’Neal

## Slide 13: Micro-patterning: CXFEL uses diffraction
Use of optimized electron
diffraction with structured
Si (100) crystal
A complex process.
To begin, simplify…
Picking out undiffracted population

## Slide 14: TEM grid used for micro-patterning at micron level
First step: 44 MeV electrons scatter on gold TEM grid with 12.5-62 𝜇m periodicity wire array,. Simulated in GEANT4
Follow with demagnification using quad triplets
Beam image after 5 cm
GEANT4 simulations

## Slide 15: Bonus: emittance measurement with TEM grid
First at high energy, 44 MeV (compare to UCLA Pegasus at ~4 MeV)
Image 50 cm after grid shows angular spreading after collimation
  Is it too much spreading? Shorten drift
  How high of emittance is measurable?
Beamlet spread gives
4D phase space

## Slide 16: Recent analysis more detailed
Close coupling (5 cm) of grid and YAG detector – bremsstrahlung directly excites YAG emission
Problem for initial validation of the transverse modulation
Boundary condition for emittance measurements
Electron beam pattern
Emission at YAG surface
Courtesy Jack Phillips

## Slide 17: Demagnification section Modulation befor and after demagnification
3 microns x periodicity ->0.8 nm in z periodicity w/EEX
Demagnification section
We have simulated up to 8.3x demagnification. More demag occurs in EEX
Courtesy Buse Naz Temizel Ozdemir

## Slide 18: Sextupole Correction of 2nd order non-ideal behavior
A sextupole at DL2 entrance
2nd order contribution on
A sextupole in DL2
2nd order contribution on
Placed 2 sextupoles at the best candidate locations;
Sextupole at DL2 entrance mainly affects z-series, with less impact on xz-series.
Sextupole inside DL2 affects xz-coupling more.
Combining both sextupoles enables control of all dominant second-order terms.
2 sextupoles together
2nd order contribution on
2nd order contribution on
No sextupoles
z:
xz:
FMC
TDC
Isolates degradation from collective effects

## Slide 19: Effect of Beam Charge on Bunching Factor and LPS
LPS for different charge levels
4 pC
5 pC
6 pC
Bunching factor for different charges
7 pC
9 pC
10 pC
1 pC
-
2 pC
-
3 pC
-
Bunching factor remains measurable at higher beam charge
Scanned charge to see its effect on the modulation. Notable distortions above 3 pC
To do: remove correlations
Courtesy Buse Naz Temizel Ozdemir

## Slide 20: Fundamental mode cavity development
Single cell, 300 kV for correction . Power only10-20 kW
Joint design effort (LANL/ASU/UCLA) with UCLA fabrication. Synergistic with LANL development
Electric ield profile
Novel coaxial coupler

## Slide 21: Sextupole design
Like FMC, fields are weak, but apertures are large (2 inch beampipe in EEX
  Need only ~60 T/m2
  Current limited, changing coil geometry

## Slide 22: Measuring microbunching
3 micron modulation yields 800 nm microbunching
  Coherent radiation measurement
  Copious existing optics/detectors
Use CTR; method well established
  Far IR to optical
  800 nm and harmonics at VISA
~1E6 800 nm photons for this expt.
Coherent radiation
  UCLA-Kurchatov undulator
A. Tremaine, et al. Phys. Rev. Lett. 81, 5816 (1998)
First high gain SASE microbunching diagnosed with CTR

## Slide 23: Coherent undulator radiation
UCLA undulator – 1E8 photons!
Harmonics and gain to be investigated

## Slide 24: AWA experiment on EEX-based micro-bunching
Critical test of new ultra-compact light source schemes
Beam dynamics analysis well underway
  CSR and nonlinearities limits
  Space-charge with GPT (also
Interesting challenges in beam size measurements
  Micron scale beams with large full ROI
  Radiation and collective effects active
EEX-based experiments beginning
  Demagnification
  Emittance measurements
  New hardware
  EEX commissioning
Exciting program; heavy student involvement. Open collaboration
Thanks to US DOE BES for suppor t