## Slide 1
Virtual Diagnostic For Longitudinal Phase Space Prediction at FACET-II
SLAC National Accelerator Laboratory
AAC 2026, UCLA
Presenter: Jinseo Park, PI: Claudio Emma
Notes: I’ll now start my presentation on recent progress of longitudinal phase space prediction, a k a virtual TCAV.

## Slide 2: Motivation Principle of Operation Results / Application Current Research Direction

## Slide 3: Longitudinal Phase Space
Head  ζ  Tail
E
Bunch Separation
E Spread
Driver Length

## Slide 4: FACET-II S20 XTCAV Overview
bunch
Dipole
(Vertical Kick ∝ 1/p)
DTOTR2
ζ
ζs
E
TCAV On(φ=90°)
SYAG
TCAV
(Horizontal Kick∝ζ)
IP
bunch
bunch
Notes: So, how do we measure longitudinal phase space at facet-two? We use XTCAV! I’m sure quite a few people in this room knows how to use it, but I’ll quickly revisit the basics.
After some betatron phase advance, ideally 90 degrees, the electrons arrive at DTOTR2, one of the OTR screens in front of the dump.
There are similar schemes at BC11 and at BC14, although not as widely used by the users.

## Slide 5: Shot-to-Shot LPS Variation
Figure provided by C. Emma

## Slide 6: Motivation Principle of Operation Results / Application Current Research Direction

## Slide 7: Training Set Preparation
Toggler: Removes x-y Correlation, first order effect of orbit, etc.
n x 250 x 850
TCAV DAQ w/
Toggler
Preprocessed LPS Data
(~n/3) x 100 x 150
Model Data
TCAV Cal.
(um / deg)
Multiset Training

## Slide 8: Inference Model Image Model
Normalized PVs → Image Encoding
[0, 1]#PV → [0,1]EncodingDimension
Example:
Random Forest (RF) Regressor
Image Encoding → Image
[0,1]EncodingDimension → Image
EncodingDimension = 12-20
Example:
Convolutional Variational Autoencoder (CVAE)
440x1
EPICs PV Acquisition
Filter PVs
(Before IP Only)
Bypass PVs
(Disconnected, …)
Normalization
220x1
220x1
Inference Model
16x1
Image Model
200x200
Postprocessing

## Slide 9: Benefits of 2-Lv. Modularization
Backward Compatibility
PV Regularization
DTOTR2 Correction only applies to Image Model
PV Correction only applies to Inference Model
Notes: There are some easily recognizable benefits of having this kind of two level modularization.

## Slide 10: Perceptron VS CVAE
Notes: Here, I’ll briefly explain the reason I picked cvae instead of the better known perceptron.

## Slide 11
Dimension Reduction
Interpolatability
PCA vs CVAE
Notes: Unlike perceptron,
A standard autoencoder is deterministic (Input A always equals Latent Point B). A Variational Autoencoder (VAE) is probabilistic. Instead of mapping an input to a single point in the latent space, it maps it to a distribution (a mean and a variance).
While Principal Component Analysis (PCA) only looks for linear relationships, an autoencoder uses non-linear activation functions (like ReLU or Sigmoid). This allows it to learn incredibly complex, curved relationships in your data—which is why it can "package" 200 features into 16 dimensions so much more effectively than simple math could.

## Slide 12: Hyperparameter Optimization: Image
Notes: The latent dimension, or the number of components used for encoding, does have an optimum, which varies slightly depending on the dataset.

## Slide 13: Inference: Random Forest
Single feature(PV) is compared each branch
Outputs latent encoding for the image model
https://www.geeksforgeeks.org/machine-learning/random-forest-regression-in-python/

## Slide 14: Sample Density Weighting
Ex: Sinusodialer Data E338_15552 → E338_15507 (8 Hrs Apart)
Without Density Weighting:
Notes: It should be noted that the model used here is trained on a training set which is taken 8 hours after taking the data.

## Slide 15: Sample Density Weighting
Ex: Sinusodialer Data E338_15552 → E338_15507 (8 Hrs Apart)
With Density Weighting:

## Slide 16: Hyperparameter Optimization: Inference
model = RandomForestRegressor(
n_estimators=500,
max_depth=15,
min_samples_leaf=2,
random_state=42,
n_jobs=-1
)

## Slide 17
Dimension Reduction
Interpolatability
Image: CVAE
Notes: Unlike perceptron,
A standard autoencoder is deterministic (Input A always equals Latent Point B). A Variational Autoencoder (VAE) is probabilistic. Instead of mapping an input to a single point in the latent space, it maps it to a distribution (a mean and a variance).
While Principal Component Analysis (PCA) only looks for linear relationships, an autoencoder uses non-linear activation functions (like ReLU or Sigmoid). This allows it to learn incredibly complex, curved relationships in your data—which is why it can "package" 200 features into 16 dimensions so much more effectively than simple math could.

## Slide 18: Filtering/Bypassing PVs
Downstream PV
Reconfigured PV
Disconnected PV
Rank | Feature Name | Importance Score | Sector / Component
1 | BLEN_LI20_3014_BRAW | 0.2989 | LI20 Bunch Length
2 | BLEN_LI14_888_BRAW | 0.128 | LI14 Bunch Length
3 | BPMS_LI14_801_X | 0.1278 | LI14 Beam Position (X)
4 | PMT_LI20_3070_QDCRAW | 0.0957 | LI20 Photomultiplier
5 | BPMS_LI20_2445_X | 0.0607 | LI20 Beam Position (X)
6 | BPMS_LI20_2445_Y | 0.0223 | LI20 Beam Position (Y)
7 | BLEN_LI11_359_BRAW | 0.0159 | LI11 Bunch Length

## Slide 19: Real Time SYAG Integration
Train Without Collimator
Insert Collimator
Read SYAG Shadow
Apply LPS Shadow

## Slide 20
Under-compressed
BC14 BLEN = 9000
head
tail
Notch
Jaw
Notes: I can arbitrarily increase the shadow cast by collimators, but that does not have much physical basis to reason upon.

## Slide 21: Motivation Principle of Operation Results / Application Current Research Direction

## Slide 22: Model Output

## Slide 23: Current Profile Prediction

## Slide 24: Current Profile Prediction
Current profile in Python, Matlab formats

## Slide 25: Offline Analysis: Plasma Interaction
Drive to Wake Energy Transfer
Notes: Another analysis I worked on is to correlate Energy Transfer into Plasma, also known as ELOSS, using virtual TCAV. As you can see from the scatter plot, this is a much tougher job because while it is expected for ELOSS to correlate positively with longitudinal peak current, the horizontal distribution of the beam may still jitter shot to shot.

## Slide 26: Correlation Studies
Bunch Compressor Orbit
LI11
LI14
LI20
L1
L2
L3

## Slide 27: Anomaly Detection
AAC 2026 E327: Virtual Diagnostic For Phase Space Prediction And Customization at FACET-II
Persistent problem across the entire ML world:
Building Trust!
When models give us bad predictions….. Why?

## Slide 28: Anomaly Detection
AAC 2026 E327: Virtual Diagnostic For Phase Space Prediction And Customization at FACET-II
Anomalies not immediately visible by checking any individual readout…
The inference model catches it in real time!

## Slide 29: Real Time Confidence
AAC 2026 E327: Virtual Diagnostic For Phase Space Prediction And Customization at FACET-II
Topological distance between training set and the current state, measured in real time

## Slide 30: Motivation Principle of Operation Results / Application Current Research Direction

## Slide 31: LCLS XLEAP application
Li, Siqi & Zhang, Zhen & Alverson, Shawn & Cesar, David & Driver, Taran & Franz, Paris & Isele, Erik & Duris, Joseph & Larsen, Kirk & Lin, Ming-Fu & Obaid, Razib & O'Neal, Jordan & Robles, River & Sudar, Nick & Guo, Zhaoheng & Vetter, Sharon & Walter, Peter & Wang, Anna & Xu, Joseph & Marinelli, Agostino. (2024). “Beam à la carte”: Laser heater shaping for attosecond pulses in a multiplexed x-ray free-electron laser. Applied Physics Letters. 125. 10.1063/5.0233468.

## Slide 32: Also Check Out…

## Slide 33: Summary
Acknowledgments
SLAC: D. Storey, R. Hessami, K. Larsen, R. Robles, K. Swanson, C. Emma, A. Marinelli, Y. Ye, A. Kinderman, C.-E. Lin, T. Dalichaouch, D. Kalvik, A. Knetsch, S. Gessner, S. Corde, S. Rego, Z. Buschmann, R. Loney, J. Yocky,
A. Edelen, D. Cesar, A. Reed
Experimental Collaborations with: E-300, E-338
Special Thanks to: S. Amberkar, N. Majernik
Thank you for your attention
Virtual Diagnostics accurately predicts LPS from nondestructive diagnostics.
Prediction Confidence can be used for Real Time Anomaly Detection.

## Slide 34: VTCAV: Virtual Diagnostic For Longitudinal Phase Space Prediction
440x1
EPICs PV Acquisition
Filter PVs
(Before IP Only)
Bypass PVs
(Disconnected, …)
Normalization
220x1
220x1
Inference Model
16x1
Image Model
200x200

## Slide 35: Bunch Length Feedback System
L1 BLEN Count
L1 Energy BPM
L2 BLEN Count
L2 Energy BPM