## Slide 1: Multi-GeV Electron Combs from a Plasma Wakefield Accelerator
Work supported by DOE-HEP
Simulations done using OSIRIS and QPAD
on Perlmutter@NERSC
Chaojie Zhang
(on behalf of the E300 Collaboration)
July 30, 2026
AAC 2026, UCLA, Los Angeles
See arXiv:2607.08069 for more details

## Slide 2: What to expect
We show the experimental generation of multi-GeV electron combs:
a multi-GeV electron beam consisting of more than 10 microbunches
microbunch charge: several pC; energy spread down to 0.5% rms
up to 0.26 GeV (7%) energy spacing between adjacent spectral peaks
microbunches should be sub-fs in duration and separated in time
————————————————————————————————————————
mechanism: beam-induced ionization injection of helium electrons into a lithium plasma wake, with longitudinal mapping due to gentle density gradients
measured
inferred

## Slide 3: Plasma accelerators keep improving: energy, brightness, stability
Energy reached O(10) GeV
Zhang et al, Nat Commun (2025)
Picksley et al, PRL (2024)
Stability and reproducibility
Wang et al, Nature (2021)
Lindstrøm et al, PRL (2021)
Beams bright enough to drive an EUV FEL

## Slide 4: A less-explored feature of plasma accelerators: in-situ beam shaping
Internally injected electrons in a plasma accelerator can be tailored in situ, on fs timescales, by manipulating the injection process.
Examples:
nm pre-bunched beams from modulated downramp injection
Xu et al, Nat Commun (2022)
spiral e- bunch from ionization injection using LG lasers
Xu et al, PRAB (2022)
multi-color beam from two-color ionization injection
Zeng et al, PRL (2015)
recently demonstrated in experiment
Angella et al, PRL (2026)

## Slide 5: Multi-color beam generated in a PWFA (the FACET E217 experiment)
Periodic pinching of the drive bunch ionizes the helium dopant gas in a lithium plasma
Injection happens every half betatron wavelength
N. Vafaei-Najafabadi et al, Phil. Trans. R. Soc. A (2019)
Li
He
Experiment

## Slide 6: A long driver means a long injection phase
N. Vafaei-Najafabadi et al, Phil. Trans. R. Soc. A (2019)
Long Gaussian driver
  pinching slice moves along the beam —>
  changes ionization phases —>
  injects long, overlapping bunches
Microbunches are separated in energy,
but not necessarily in time.
~10 µm microbunches

## Slide 7: Revisiting E217 at FACET-II: two changes uncover new physics
The experiment was performed at FACET-II using the 1.5 nC, 10 GeV beam (March 2024)
The drive beam is over-compressed to generate a double-spike structure
  Leading spike ionizes lithium; subsequent charge drives the wake; trailing spike ionizes helium
  The narrow current spike limits the ionization/injection phase —> ultrashort bunches
Non-uniform plasma
  40-cm lithium vapor, bounded (and doped) by helium gas
  Longitudinal mapping during injection places microbunches at different phases

## Slide 8: The physics explained by PIC simulations
narrow ionization phase

## Slide 9: Ionization-injected beams show distinct energy peaks
no injection
with injection (drive beam waist at optimal location, z=10 cm)

## Slide 10: A beam consisting of more than 10 microbunches
20 shots (out of 100 consecutive shots)
An example shot showing clear energy bunching

## Slide 11: Spacing between adjacent peaks turns over at the highest energies
We observe the spacing turning over above ~4 GeV
Expected: highest-energy peaks = earliest injected = largest spacing, monotonic
The turnover means those bunches are loading the wake and reducing the local field
Significant loading requires multi-kA currents → sub-fs bunch lengths at O(10) pC → they cannot fully overlap in time

## Slide 12: Without strong loading, the spacing rises monotonically — as expected
Simulation with reduced injected charge; bunch length ~0.1 µm, separation up to ~0.9 µm

## Slide 13: Longitudinal phase space (LPS) mapping during injection
Helium electrons selectively ionized over a ~21 cm region are mapped into a ~6 µm-long beam (~35,000x mapping factor)
The LPS mapping order is controlled by the density gradient
  We can manipulate the LPS of the injected beam on fs scales by tailoring the plasma on cm scales.
What does this mean?

## Slide 14: Summary
We show the experimental generation of multi-GeV electron combs:
a multi-GeV electron beam consisting of more than 10 microbunches
microbunch charge: several pC; energy spread down to 0.5% rms
up to 0.26 GeV (7%) energy spacing between adjacent spectral peaks
microbunches should be sub-fs in duration and separated in time
————————————————————————————————————————
mechanism: beam-induced ionization injection of helium electrons into a lithium plasma wake, with longitudinal mapping due to gentle density gradients
enables fs in-situ beam shaping by tailoring the plasma on cm scales
measured
inferred

## Slide 15: Backup: Drive beam waist scan
The amount of charge injected depends on the driver’s waist location (betatron oscillation envelope)
Energy peak contrast increases with injected charge, indicating beam loading effects