## Slide 1
Laser-Based Collimation of Beam Halo Electrons via Compton Scattering
Ching-En Lin
AAC26
2026 Jul 28

## Slide 2: Motivation: Collimation Challenges
Fast instabilities cause catastrophic collimator damage.
SuperKEKB has already experienced catastrophic collimator damage.
FCC-ee collimators may not survive a fast instability.
Richard Cowan, FCC Week 2026

## Slide 3: Laser Collimation as a Defense-in-Depth Layer
An additional, non-material layer to reduce the load on conventional collimators.
The closer the collimator jaws are to the beam, the more impedance issues, and they are more susceptible to damage.
F. Zimmermann, AIP Conf. Proc. 472, 103–117 (1999).
normal collimator
laser collimator

## Slide 4: Laser Collimation Concept
Donut-laser scattering separates halo electrons from the main beam.
halo electrons
donut laser
main bunch
beam dump
magnet dipole

## Slide 5: E344: Laser-Collimation Test at FACET-II
OAP
Axicon
Built on the established E320 platform
FACET-II enables a near-term test of laser collimation.
Notes: E320 is a nonlinear QED experiment in which a high-intensity laser collides with an electron beam. It has already established the interaction geometry, synchronization, diagnostics, and experimental workflow. E344 mainly adds the beam-shaping optics needed to test laser collimation.

## Slide 6: Laser Requirements: FCC-ee vs FACET-II

## Slide 7: Comparison of Optical Schemes
Property | High-NA axicon + OAP | Low-NA axicon + focusing optic | Spiral phase plate + high-NA OAP
Ring radius | broadly tunable | broadly tunable | tied to diffraction scale
Ring thickness | thin | thick | moderate
Radius/thickness independent control | good | good | limited
Peak intensity | high | low | high
Main-ring energy concentration | high | moderate-high | moderate
On-axis suppression | good | moderate | excellent
Input beam size sensitivity | low for radius | low for radius | high
Notes: For FCC-ee, it is possible to generate a light-sheet beam or other tailored beam profiles. It is also possible to use multiple laser beams.

## Slide 8: Ray-Tracing Simulation
1+1D simplified ray tracing
3D ray-tracing
Notes: The thickness of the ring at focus is determined by two main factors: (1) the diffraction limit and (2) astigmatism.
If one wants a thicker ring or other beam structures, phase-retrieval methods such as the Gerchberg–Saxton (GS) algorithm can be used.

## Slide 9: Ray-Tracing Simulation
β
α

## Slide 10: Donut-Beam Profile Measurement
Target radius: 125 μm
Measured radius: 131 μm
Difference likely from residual alignment error
Notes: 800nm CW Fiber laser

## Slide 11: Scattering Probability
Notes: Klein–Nishina formula has relatively weak scaling with laser photon or electron energy.

## Slide 12: Scattering Probability
~1% Scattering Probability for Single Electron
Notes: Need to consider the electron beam size: σx ≈ 46 μm, σy ≈ 23 μm.

## Slide 13: Choosing the Ring Radius
An Axicon w. m Maximizes a Clear Proof-of-Concept Signal.
Notes: Since the interaction length is about 35mum, and the laser spatial profile does not change much over this range, numerical calculations verify that the scattering probability for a 30 deg incident angle differs from that for 0 deg by only a few percent.

## Slide 14: Toward Collider-Scale Laser Collimation
High-Repetition-Rate Operation
Cavity-enhanced laser system ∼30 MHz interaction rate
Efficient pulse recycling
(30W pump laser?)
Flexible Laser Profiles
Light sheet · LG modes · Multiple beams · Target intensity profiles via phase masks

## Slide 15: Conclusion
Notes: Klein–Nishina formula has relatively weak scaling with laser or electron energy.

## Slide 16: References
[1] S. Terui et al., “Collimator challenges at SuperKEKB and their countermeasures using nonlinear collimator,” Phys. Rev. Accel. Beams 27, 081001 (2024). https://doi.org/10.1103/PhysRevAccelBeams.27.081001
[2] R. Cowan et al., “Mechanical Design of FCC-ee Collimators,” presented at FCC Week 2026, Helsinki, Finland (2026). https://indico.cern.ch/event/1552126/
[3] F. Zimmermann, “New final focus concepts at 5 TeV and beyond,” AIP Conf. Proc. 472, 103–117 (1999). https://doi.org/10.1063/1.58898
[4] F. Zimmermann and T. O. Raubenheimer, “Controlling e+/e− circular collider bunch intensity by laser Compton scattering,” in Proc. IPAC’22, Bangkok, Thailand, pp. 1695–1698 (2022). https://doi.org/10.18429/JACoW-IPAC2022-WEPOST010
[5] C. Munting, P. Kicsiny, E. Barbi, N. Gonzalez, S. Gessner, and I. Drebot, “Laboratory Tests of Laser Control of Electron Beams for Future Colliders,” arXiv:2601.19865 [physics.acc-ph] (2026). https://arxiv.org/abs/2601.19865
This work is supported by the SLAC LDRD Program and by U.S. Department of Energy under contract DE–AC02–76SF00515.