## Slide 1: A Scintillator-Based High Repetition Rate Diagnostic for Multi-Energy Proton Beam Imaging & Probing
Veronica Contreras
Advanced Accelerator Concepts - 2026

## Slide 2
Acknowledgements
Collaborators
  Dr. Paul T. Campbell
  Dr. Yong Ma
  Dr. Anatoly Maksimchuk
  Dr. Heath LeFevre
  Dr. Milos Burger
  Dr. Qian Qian
  Jeremy Rebenstock
  Che-Hao Chang
  Ryuya Yamada
  Prof. Alec Thomas
  Prof. Karl Krushelnick
  Prof. Carolyn Kuranz
  Prof. Louise Willingale
ZEUS Engineering & Data Team
  Grant Young
  Richard Anthony
  Will Likes
  Qing Zhang
ZEUS Laser Team
  John Nees
  Galina Kalinchenko
  Bixue Hou
  Gregg Sucha
  Rick Van Camp
  Jeff Xia
  Yana Kleimenova
This work is funded by the U.S. Department of Energy NNSA Center of Excellence under cooperative agreement number DE-NA0004146 and by the National Science Foundation through award number 2408410. This research was conducted at the ZEUS facility which is supported by the National Science Foundation under award 2126181.

## Slide 3
Proton deflectometry
Laser
Thin foil
Electron cloud generates a sheath field
Time-of-flight provides image sequence on film layers
Quasi-static electric or magnetic fields deflect protons
Detector stack
TNSA proton beam is accelerated in the electric sheath field:
Laminar acceleration  good spatial resolution
Short acceleration time  good temporal resolution
Maxwellian-like spectra
Force on a charged particle
M Borghesi et al, Rev Sci Inst, 74, 1688 (2003); Laser and Part Beams, 20, 269 (2002); Slide design: L. Willingale
high energy
(early in time)
lower energy
(later in time)
Sample RCF stack
Notes: Ps temporal resolution
Maxwellian – time –resolved data

## Slide 4: Proton detectors
    High spatial resolution5
    Can be used in a stack for time-resolved measurements (similar to RCF)
    Can have thick active layer
Scintillator
5H. Tang, et al, Rev. Sci. Instrum. 91, 123304 (2020)
Single-Use Detectors
Reusable Detectors
    Optical density radiation dose
    Can use a stack for time-resolved measurements
    Requires replacement after each shot
    Requires scanning before analyzing
Radiochromic Film
Not Suitable for High Rep-Rate
Suitable for High Rep-Rate
    Multi-use
    Requires removing from vacuum and scanning after each shot
Image Plate
    Stringent vacuum requirements
    Not suitable for time-resolved proton imaging
MCP
    Detection efficiency ~100%
    Requires replacement after each shot
    Time-consuming etching process before scanning and then analyzing
CR-39
Notes: Thicker active layer means drop in the spatial resolution because you have more overlapping deflections
Thicker active layer also means that you have a drop in your temporal resolution because youre capturing more energies on that specific layer so you have a wider range of times you’re looking at.

## Slide 5
High rep rate proton beam profiling diagnostics
M. J. V. Streeter, et. al, Nature Communications 16, no. 1 (2025).
Single detector concepts
  Aurand et. al
    Al grid filter
    Interpolate beam profile
  Mariscal et. al : PROBIES (Proton Beam Imaging Energy Spectrometer)
    3D-printed repeated grid pattern
    Requires high confidences in print precision / repeatability
    Interpolate beam profiles
  Streeter et. al
    EJ 440, thin phosphor detector
Aurand, B., et al. Laser and Particle Beams 33, no. 1 (2015).
D. A. Mariscal, et. al, Rev. Sci. Instrum. 94, 023507 (2023)

## Slide 6
High rep rate proton beam profiling diagnostics
M. Huault, et al, High Power Laser Science and Engineering, Vol. 7, e60. (2019); M. Huault, et. al, IEEE Trans. on Instrumentation and Measurement 73 (2024).
Multi-detector concepts
  Green et. al
    Varied wavelength scintillating stack
  Huault et. al
    Accordion-style scintillator stack, image from the sides
    Requires light-tight shielding to capture scintillator images
J. Green, et al, SPIE Proc. 8079, 807991 (2011).

## Slide 7
Glowing On-shot Scintillator Stack for Imaging Protons (GOSSIP)
High-repetition rate
Allows for beam profile, pointing, and divergence measurements
Time-resolved interaction information
Image above stack  maximizes horizontal resolution
3D-printed housing
Simple & reconfigurable
Proton Source
Pinhole
To TPS
Scintillator Stack
Mirror
GOSSIP Image
Proton Source
Scintillator Stack
Camera
Top half, full beam imaging
Side beam imaging
Full beam imaging

## Slide 8: Experiments with GOSSIP
ZEUS January 2025
  Flat foil targets
  GOSSIP (top half) + TPS
  EJ 204 scintillators
    Scratches scatter light
ZEUS TA2 April 2025 Liquid sheet targets
  Full beam on GOSSIP
  EJ 440 scintillators
    Signal balance required
ZEUS TA1 March 2026 Proton probing
  1 camera / detector
  First demonstration of fs HRR proton probing on scintillators at ZEUS
  Scattering between layers is significant
3.3 MeV
4.6 MeV
3.3 MeV
4.6 MeV
3.3 MeV
4.6 MeV
1.5 MeV
1.5 MeV
5.6 MeV
1.5 MeV
5.6 MeV
1.5 MeV
Raw GOSSIP Data
3.2 MeV
3.2 MeV

## Slide 9
ZEUS TA1: Proton Probing Experiment
Experiment Aims
Characterize proton beam on GOSSIP with TEM grid
Achieve high shot rate proton probing measurements at ZEUS with GOSSIP

## Slide 10
ZEUS TA1: Proton Probing Experiment Setup
Delay
Stage
Beam Path
f/3
OAP
Proton
Beam
GOSSIP
S1: 3.3 MeV
S2: 3.7 MeV
S3: 5.3 MeV
f / 60, 30 J, 40 fs
f / 3, 5.5 J, 30 fs
Targets
f/60 beam: 6m foil
f/3 beam: TEM grid or 125m wire mounted 2mm behind

## Slide 11
Post-processing
6.5 cm
6.5 cm
Protons
GOSSIP
Targets
In-chamber setup
Light
shielding
ZEUS TA1: Proton Probing Experiment Setup

## Slide 12
Shot A
Shot B
ZEUS TA 1: Proton Probing Experiment Results - Characterization

## Slide 13
Investigating the observed image blurring effect in the data
Shot A
Narrow peak  better localization of proton signal
Broader peak  increased blur
Mesh-plane position [mm]
Normalized LSF
Line Spread Function
Take the same, well-defined mesh edge near the center of each detector image
Resulting fit is used to calculate the line spread function
Fit an error function to the measured edge spread function
Notes: This slide investigates the origin of the image blur we observe.
For each detector layer, I selected the same well-defined mesh edge near the center of the image.
An error function was fit to the measured edge spread function, and the resulting fit was used to calculate the line spread function and modulation transfer function.

## Slide 14
 | Lateral Range
3.7 MeV (Layer 2) | 3.0°
5.3 MeV (Layer 3) | 1.8°
Modeling in TRIM
Image blurring effect is partially due to small-angle scattering in the detectors.
Measured LSF FWHM compared with TRIM-predicted broadening
Measured LSF FWHM
Baseline resolution
TRIM-predicted scattering by L1 on L2
TRIM-predicted scattering by L1+L2 on L3
3.2 MeV
3.7 MeV
5.3 MeV
Notes: To understand what causes this image degradation, we modeled proton transport through the detector stack using TRIM.
TRIM is a monte carlo code that predicts the lateral spread of protons as they traverse the detector materials. Both the lateral range and lateral straggle increase the size of the proton distribution on the scintillator, reducing image sharpness.
The lateral range = average lateral distance from the central beam axis
Lateral straggling = average deviation from the lateral range
TAKEAWAY: The experimental broadening measured by the ESF, LSF, and MTF is consistent with the scattering predicted by the TRIM simulations, indicating that scattering within the detector stack is a dominant contributor to the loss of spatial resolution.

## Slide 15
Low energy (PW: ~12J, TW: ~2 J)
Preliminary Proton Probing Results: 3.3 MeV
x at mesh (µm)
y at mesh (µm)
x at mesh (µm)
y at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)

## Slide 16
Low energy (PW: ~12J, TW: ~2 J)
Preliminary Proton Probing Results: 3.3 MeV
x at mesh (µm)
y at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)
Original wire
Original wire
Original wire
Original wire
x at mesh (µm)
y at mesh (µm)
x at mesh (µm)
x at mesh (µm)
x at mesh (µm)
Original wire
Original wire
Original wire
Original wire

## Slide 17
Preliminary Proton Probing Results: 3.3 MeV
Parameters:
Low energy
PW: 12J, TW: 2 J
High Energy
PW: 31J, TW: 5.5 J
High energy Snapshot:
PW: ~31J, TW: ~5.5 J

## Slide 18: Time-resolved data snapshot
t0 + 40 ps
t0 + 34 ps
t0 + 5 ps
t0 - 1 ps
Shot A
Shot B
Layer 2: 3.7 MeV
Layer 1: 3.3 MeV

## Slide 19
Conclusions
GOSSIP – Glowing On-shot Scintillator Stack for Imaging Protons
  3D-printed, simple, easily reconfigurable holder
  Allows for simultaneous beam profile, pointing, and divergence measurements
  Stack can provide time-resolved interaction information with sufficient proton beam energy
Measurements taken at ZEUS with
  Grids for diagnostic characterization
  fs proton deflectometry
Next steps
  Field inversion for probe data

## Slide 20: Questions
Email: vacontre@umich.edu

## Slide 21
Image blurring effect is due to small-angle scattering in the detectors.
Shot A
Narrow peak  better localization of proton signal
Broader peak  increased blur
Mesh-plane position [mm]
Normalized LSF
Line Spread Function
Take the same, well-defined mesh edge near the center of each detector image
Resulting fit is used to calculated the line spread function
Fit an error function to the measured edge spread function
Notes: This slide investigates the origin of the image blur we observe.
For each detector layer, I selected the same well-defined mesh edge near the center of the image.
An error function was fit to the measured edge spread function, and the resulting fit was used to calculate the line spread function and modulation transfer function.

## Slide 22: Scattering-induced image blur
Experimental Data
ZEUS TA 1: Proton Probing Experiment Results - Characterization
Shot A
ESF:
As edge becomes less sharp, transition broadens  loss of spatial resolution
LSF:
Narrow peak  better localization of proton signal
Broader peak  increased blur
MTF:
Higher MTF at a given spatial frequency  finer image detail
Mesh-plane position [mm]
Normalized Intensity
Mesh-plane position [mm]
Normalized LSF
MTF
Spatial frequency [lines/mm]
Notes: This slide investigates the origin of the image blur we observe.
For each detector layer, I selected the same well-defined mesh edge near the center of the image.
An error function was fit to the measured edge spread function, and the resulting fit was used to calculate the line spread function and modulation transfer function.

## Slide 23
ZEUS TA1: Proton Probing Characterization for Scattering

## Slide 24
Shot A
ZEUS TA 1: Proton Probing Experiment Results - Characterization
Contrast tells how well the detector can distinguish adjacent mesh wires and openings
Contrast
Average over a small region
Identify peaks and valleys
Calculate contrast for each period (wire)

## Slide 25
Horizontal
ZEUS TA 1: Proton Probing Experiment Results - Characterization
Layer | Mean Contrast | Standard Deviation
1 | 0.245 | 0.101
2 | 0.235 | 0.077
3 | 0.283 | 0.102
Horizontal Results Summary
Contrast
Vertical
Layer | Mean Contrast | Standard Deviation
1 | 0.225 | 0.093
2 | 0.240 | 0.106
3 | 0.232 | 0.052
Vertical Results Summary
Notes: The differences in mean contrast are fairly modest
contrast varies substantially across each detector, motivating the spatial heat-map analysis instead of relying on a single average value.

## Slide 26
ZEUS TA 1: Proton Probing Experiment Results - Characterization
Local contrast measurements show non-uniform imaging performance across each scintillator layer.
Measured contrast can be influenced by:
  Proton scattering within the detector stack
  Camera imaging conditions (e.g., ND filtering/camera settings)
  Local detector response
Together, the horizontal and vertical analyses suggest that the measured contrast depends on the orientation of the mesh features.
Contrast
Layer | Mean Contrast | Standard Deviation
1 | 0.245 | 0.101
2 | 0.235 | 0.077
3 | 0.283 | 0.102
Horizontal Results Summary
Layer | Mean Contrast | Standard Deviation
1 | 0.225 | 0.093
2 | 0.240 | 0.106
3 | 0.232 | 0.052
Vertical Results Summary

## Slide 27
Layer 1: 3.2 MeV (+ 5.7 ps)
Layer 2: 3.7 MeV (+ 12.5 ps)
Layer 3: 5.3 MeV
ZEUS TA1: Proton Probing Experiment Setup

## Slide 28: GOSSIP design
Values from TRIM
J. F. Ziegler, et. al, Nuclear Instruments and (2010).