## Slide 1: A laser-based high average yield neutron source for medical applications
Károly Osvay
Advanced Accelerator Concepts
UCLA, LA, USA 28th July, 2026

## Slide 2
Motivation
https://www.mdpi.com/journal/applsci/special_issues/7KCJK80OJJ
Neutron
High penetration in material
Direct interact with nuclei
The number of neutron facilities sources is decreasing
reactors are aging, and closing down.
big sources are delayed.
Specialities of a laser-based neutron source
neutrons are generated in ultrashort bunches
the ”machine” (laser) and the ”source” can be separated
the laser is not a nuclear device

## Slide 3
A room for laser-based neutron sources
Many emerging applications call for neutron sources with
a yield of 106 n/s - 1010 n/s;
relaxed safety and security (compared to reactors);
compact, efficient;
reliable.
Mirfayzi et. al., Jpn.J.Appl.Phys. 64 (2025) 010002

## Slide 4
Specialities of a laser-based neutron source
neutrons are generated in ultrashort bunches;
the ”machine” (laser) and the ”source” can be separated;
the laser is not a nuclear device.
Many emerging applications call for neutron sources with
a yield of 108 n/s - 1011 n/s;
relaxed safety and security (compared to reactors);
compact, efficient;
reliable.
A room for laser-based neutron sources

## Slide 5
Photonuclear
Accelerate electrons
Brehmstralung and high Z converter: (,n)
Highest efficiency experiment
Günther et al., Nat. Com.13 (2022) 170
2.9×107 n/J
~ 105 n/s
Neutron spectra: continous
Papp et al., Photonics 9 (2022) 826
Pomerantz et al., PRL 113 (2014) 184801
Laser-based neutron sources
Multi-J (PW)-class lasers – current situation

## Slide 6
Laser-based neutron sources
Multi-J (PW)-class lasers – current situation
PhotoFusion
Accelerate ion (proton, deuterium)
Make fusion: Be(p,n), Li(p,n), D(d,n) (T)d,n)
Highest efficiency experiment
69×107 n/J
2×106 n/s
Günther et al., Nat.Com. 13 (2022) 170
Pitcher-catcher:
Complicated, but higher neutron yield
Neutron spectra: continous or quasi-monochromatic
Kleinschmidt et al, Phys.Plasmas 25 (2018) 053101
Alvarez et al., Phys.Procedia 60 ( 2014) 29
Alejo et al., Il Nuovo Cimento 38 C (2015) 188

## Slide 7
State-of-the-art laser-based neutron sources
Canova et al., HPLSE 13 (2025) e79

## Slide 8
Strategies ”en large”
for a laser driven particle (neutron) source
Use T(P)W lasers from single shot mode
Contrast issues
Curiosity-driven research
Full understanding physics
Proof-of-principle experiments
Increase laser repetition rate
Target development
NLTL approach
Existing 100 W lasers
Peak intensity issues
Physics with low pulse energy
Continuous operation
Neutron yield for application regime > 107 n/s
Data aquisition, monitoring and control
High repetition rate target development
Increase pulse energy
Both paths would lead to a laser accelerator based particle source…
… with differences especially in early stage

## Slide 9
Study of ion acceleration by few-cycle pulses from ultrathin foils
Ter-Avetisyan et al., PPCF 65 (2023) 085012
Singh et al., Sci.Rep. 12 (2022) 8100
Challange 1
What are the properties of ion acceleration by few-cycle lasers pulses?
Large number of low energy protons
(above 100keV: 1010/shot)
Small beam divergence (<65mrad for protons > 250 keV)
Small emittance 0.00032 π-mm-mrad

## Slide 10
Challenge 2
Match the material of the catcher to the ion spectra for
The highest neutron yield
Characterisation of ion acceleration
most common: cut-off (attractive, but… )
Practically what matters (NOT only for neutron generation!)
mean kinetic energy
bunch energy (conversion from laser to total particle energy)
Higginson et al., Nat.Commun. 9 (2018) 724
d(d,n)3He
Osvay et al., EPJ Plus 139 (2024) 574

## Slide 11
Two liquid jets collide from two glass nozzles
Pulsation damping system for stability
Recirculation system for continous operation
Thicknesses measured in vacuum (!)
Thinnest liquid sheet is 190 nm
Füle et al., HPLSE 12 (2024) e37
Challenge 3
High repetition rate target systems
Development of a colliding jet liquid leaf system

## Slide 12
Temporal contrast
Peak intensity in focus: 2×1019 W/cm2 (a0~2.2)
Pulse energy: ~80 mJ (105 mJ in laser)
Laser pulse duration: 8.4 fs (measured in vacuum, after OAP, with disp scan)
Focal spot FWHM: 2.9×2.6 µm2
S3 laser (1 kHz, OPCPA) of ELI-ALPS parameters measured on target
*peak at +-22ps is a post-pulse from the variable density filter in the diagnostics arm, not in the main output
Central wavelength: 826nm
artifacts

## Slide 13
Neutron generation – experimental setup

## Slide 14
Low-Energy Ion Acceleration beamline
for high average power ion beam
Unique Specs
Single-shot – kHz repetition rate
On target, TL pulse duration: 4 fs – 12 fs
On target, energy: 12 mJ – 80 mJ
Angle of incidence: 2° - 75°
Solid-state targets, XYZ stages Liquid sheet (H2O, D2O): 200 nm – 1 m
Thomson Parabola Spectrometers, e- (in prog.) Back-reflection diagnostics
Markov-chain Monte-Carlo optimisation for an ion parameter (at a laser pulse energy, liquid, thickness, and ion; <15 min)
60mJ, D2O, d+, 760nm, cutoff
80mJ, H2O, p+, 300nm, bunch energy
Ter-Avetisyan et al., PPCF 65 (2023) 085012
Singh et al., Sci.Rep. 12 (2022) 8100
Füle et al, HPLSE 12 (2024) e37
Varmazyar et al, Comm.Phys. 8 (2025) 350
Peak ion beam Performance
Ion (p+,d+) cutoff: > 2.5 MeV (±6% rms)
Ion average current ~20 μAmp
Ion peak current ~20 kAmp (1011 ions/pulse)
Ion beam divergence: <5°
Emittance: 0.00032 π-mm×mrad
Regular stable operation: > 6 h
T. Gilinger’s talk, WG2 Thu 16:20

## Slide 15
Neutron energy spectrum Measured outside At the source
Neutron angular distribution
DIAGNOSTICS – neutron
Two independent systems
Outside the chamber
Plastic scintillators: LILITH M, XL systems
Liquid scintillator: PHRS system
Quasi-monoenergetic
Osvay et al., EPJ Plus 139 (2024) 574

## Slide 16
Control and log of (almost) all parameters upon operation
Bunch energy of deuteron
Cutoff energy
deuterons
Neutron event
LILITH
Liquid Scint
Stability
of liquid jet

## Slide 17
7×107 n/s
Neutron generation at 1kHz repetition rate dPE neutron converter
1.5×107 n/s
Neutron generation: 450nm D2O leaf + 1mm C2D4
2×107 n/cm2/s
> 1013 n/cm2/s
Ageing (burning) of the dPE
Peak yield detected at 1kHz :
Average yield over 1 hour at 1kHz :
Average neutron flux at 1kHz :
Peak neutron flux rate / shot:
Irradiation demonstrated: 3×100 min/day (exchange of dPE)

## Slide 18
Neutron generation at 1kHz repetition rate D2O neutron converter
Peak neutron flux rate / shot:
Average neutron flux at 1kHz :
Average yield over 1 hour at 1kHz :
Peak yield detected at 1kHz :
4×107 n/s
4×107 n/s, 1.7% rms
Neutron generation: 410nm D2O leaf + 0.5 mm D2O
~108 n/cm2/s
> 1013 n/cm2/s
Irradiation demonstrated: 210 min continous
Osvay et al., patent pending

## Slide 19
Pitcher-Catcher scheme
Neutron Performances
Catcher: rotating dPE, flowing D2O
Peak neutron yield (kHz): 108 n/sec
Peak neutron flux-rate: 1013n/cm2/shot
Operation (±3% rms): > 6 h @10 Hz
Regular operation: >2 Gy/h, @ 1kHz
LEIA-n(eutron) beamline
D+ acceleration
d(D,n)3He fusion
Neutron spectrum and angular distribution
Applications & user experiments
Radiobiology of ultrashort, fast neutron pulses
Neutron-induced therapy
Medical isotope production
Material science for IFE
Osvay et al., EPJ Plus 139 (2024) 574
Stuhl et al, PRR 7 (2025) 023137
Osvay et al., in prep
Osvay et al., Sci.Rep. 14 (2024) 25302
Plastic scintillators EJ-240, 4 pcs.
Liquid scintillator EJ-309, 4 pcs.
Bubble-detector neutron spectrometer

## Slide 20
Experimental chamber…
…. Zebrafish embryos in
a vacuum tight container
Neutron dose simulation
Apoptotic cell density measurement after irradiation
PI: Katalin Hideghety
First radiobiology experiments with laser-generated fast neutrons

## Slide 21: Direct Production of >99.95% Radioisotopic Pure Cu-64 from Natural Zinc Targets
Comparison of neutron spectra of different kinds of sources
Comparison of neutron spectra of different kinds of sources
PI: Jeremy Brown

## Slide 22
Background Corrected Gamma-Spectra
511 keV Photopeak Half-Life
Direct Production of >99.95% Radioisotopic Pure Cu-64 from Natural Zinc Targets

## Slide 23
State-of-the-art
High average power ion acceleration
Neutron yield per second
Estimated or calculated
Measured!
Real practical breakthrough is expected for once the average power
of high peak power lasers reaches kW level – foreseen in 3-5 years.

## Slide 24
Summary
Neutron generation from dPE @ 1 kHz, 80 mJ (2024)
- at 1 kHz (continous)
- 450 nm D2O leaf + 1mm C2D4
Neutron generation from D2O @ 1 kHz, 80mJ (2025)
- at 1 kHz (continous)
- 420 nm D2O leaf + D2O
Future work:
- optimisation directly for neutron yield
- increase stability (below 1%)
- increase trouble-free continous operation (>6 h)
- use high(er) average power laser(s)
Peak yield: 7×107 n/s
~107 n/s, 3x100min
Peak yield: 4×107 n/s
4×107 n/s, hours

## Slide 25
J. Csontos, K. Hideghéthy, A. Ebert, P.P. Geetha, A. Mohácsi, R. Molnar, R. Polanek, T. Somoskői, R.E. Szabó, Sz. Tóth
B. Biró, L. Csedreki, Z. Elekes, Z. Halasz, A. Fenyvesi, Zs. Fülöp, L. Stuhl
Hungarian Government: ITM 1096/2019. (III.8.)
National Research, Development and Innovation Office
NKFIH-877-2/2020, NKFIH-476-4/2021, NKFIH-476-16/2021
Multiscan 3D H2020 project: 101020100
B. Bencsik, E. Buzás, K. Farkas, T. Gilinger, Z. Jäger, M. Karnok, A. Kovács, A. Mohácsi, P. Varmazyar
J. Brown, H. Huang, S. Juodkazis
D. Gailevicius, M. Grigalavicius, M. Vengris