## Slide 1
synchronized
secondary fs X-rays
(betatron, ICS, brems)
Coherent Smith-Purcell Radiation
from plasma-accelerated electrons:
a synchronized strong-field THz radiation source
Advanced Accelerator Concepts (July 30, 2026)
grating
Mike Downer, R. Rudzinsky, Z. Ouyang, J. Brooks, B. Dinh, L. Zhang, A. Raka, E. Martinez, R. Zgadzaj
The University of Texas at Austin
M. LaBerge, Y.-Y. Chang, A. Debus, J. M. Klopf, F. M. Herrmann, P. Ufer, S. Schöbel, T. E. Cowan, A. Irman, U. Schramm
Helmholtz-Zentrum Dresden-Rossendorf (HZDR)
1
2
1 S. J. Smith and E. M. Purcell, Phys. Rev. 92, 1069 (1953)
2 R. Rudzinsky et al., Optica 13 (5), 810-821 (2026)
Previous AAC 2026
presentations:
• Rudzinsky, The role of CSPR for LWFA beam diagnosis, WG5 Tu 13:50
• Rudzinsky, CSPR from plasma-accelerated electron bunches, M poster
• Martinez, Reconstructing LWFA e-bunch longitudinal profiles from CSPR, Tu poster.
SPR
𝜎z
N-electron-bunch
CSPR:
𝜆 > 𝜎z
• Raka, Reshaping CSPR from fs LWFA e-bunches into strong-field THz pulses, M poster.

## Slide 2
Nonlinear phononics: controlling matter w. THz light
1) Strong THz pulse (≳ 1 GV/m) resonantly drives
IR-active lattice vibration QIR to high amplitude.
ETHz
1
2) Anharmonic lattice potential rectifies that vibration into displace-
ment along another structural coordinate QR, producing a tran-
sient crystal with different electronic & magnetic properties.
1
2
2
Nicoletti & Cavalleri, Adv. Opt. Phot. 8, 403- (2016)
• laser-based
• accelerator-based
Strong THz sources:
Types of fs probes:
• optical
• X-ray
• electron
• insulator → metal
• antiferromagnet → magnetically disordered
• normal → superconducting
• charge-ordered → charge-disordered
• ferroelectric polarization reversal
e.g.
QIR
QR
Ferroelectric polarization
reversal in LiNbO3 via strong
resonant excitation of IR-
active phonon.
Mankowsky, PRL 118, 197601 (2017)
+P
-P
strong THz
probes of
structural
change, if synchronized with THz pump

## Slide 3
 | Laser-Driven Sources |  | RF Accelerator-Driven Sources |  |  | fs CSPR
THz property | Mid-IR [1,2] (Organic X-tals) | Near-IR [3-5] (TPF, LiNbO3) | RF: FELBE/TELBE [6,7] U37 U100 U300 |  |  | LWFA-driven [8] (this work)
wavelength [µm] | 30-3000 | 120-3000 | 5-40 | 18-250 | 120-3000 | 5 -30
frequency [THz] | 0.1 - 10 | 0.1 - 3 | 7.5 - 60 | 1.2 - 17 | 0.1 – 2.5 | 10 - 60
time-synched to... | drive laser |  | drive e-bunch and secondary X-rays |  |  | 
scale | tabletop |  | large user facility |  |  | tabletop
[1] Vicario, PRL 112, 213901 (2014)
[2] Gollner, APL Photonics 6, 046105 (2021)
[3] Hebling, JOSA B 25, B6 (2008)
[4] Tóth, Light Sci. Appl. 12, 256 (2023)
[5] Kroh, Opt. Express 30, 24186 (2022)
Existing strong-field THz sources & fs LWFA-driven CSPR
[6] Green, Sci. Rpts. 6, 22256 (2016)
[7] Helm, Eur. Phys. J. Plus 138, 158 (2023)
[8] Rudzinsky,
Optica 13, 810 (2026)
• configurable
• transportable
Preliminary comparison
Tilted Pulse Front (TPF)
Near-IR

## Slide 4
Coherent SPR (CSPR)...
300
3
30,000
3,000
30
10
0.3
THz band
Infrared
Visible
mm-wave
...from RF accelerators:
•
ps
...from LWFAs:
•
s
*
4
Rudzinsky et al.,
Optica 13, 810 (2026)
*

## Slide 5
calibrated/
measured
CSPR energy
e-spectra
SPR
(µm)
CSPR Experimental
Results at 𝜆 = 10 µm
basic CSPR
theory
+ Fresnel
diffraction
grating
skim
11
Rudzinsky et al., Optica 13, 810-821 (2026)
Q ≈ 0.4 nC
e-
diamond
window
pyro-
electric
detector
8 mrad
2.5 cm
d = 10 µm
The good agreement with calculated
energy shows that the SPR is
fully coherent at 𝜆 ≈ 10 µm.

## Slide 6
CSPR pulses have complicated space-time structure...
For CSPR pulses to be useful for
strong-field THz experiments, we
must remove these chirps.
grating
window
e-bunch
1.5 m
• angular chirp
• transverse spatial chirp
• longitudinal chirp
9.83
µm
10.17
µm
10 µm
Lgr = 2.5 cm
d = 10 µm
ps
Doing so requires
precise phase control
• Radiation must be highly coherent
⇒
• Losses must be minimized
1st step

## Slide 7
PRISM
fs e-
bunch
grating
OAP 1
OAP 2
4f SPR dechirper
OAP 1 maps each
to a point in
its focal plane.
OAP 2 maps the set of points
to a set of collimated beams that
converge in its Fourier Plane (FP).
Prism combines beams
to a common path...
...thereby removing angular
& transverse spatial chirp,
but leaving longitudinal chirp.
FP
Inverse
Czerny-Turner
spectrometer
See Raka poster for
analysis of prism.
transverse

## Slide 8
4f SPR transverse dechirper: numerical example
PRISM
Longitudinally
Chirped Pulse
window
4f collimator parameters:
• OAPs: cm; 10 cm clear aperture;
(protected gold)
• Prism: Ge; apex angle 28˚; AR-coated;
0.9 energy throughput
Ray-tracing / Fourier optics simulation
⇒
⇒
Output pulse parameters:
• collimated, 3 cm diam.
• duration: ~ 40 ps
• chirp: -7.4 ps2
• energy: 15 µJ
CSPR source parameters:
• grating length : 12.5 mm
• groove spacing: 10 µm
• collection angles: 90˚, 0˚
• collected cone: 15 mrad
e.g. 2.5 cm diam. window 50 cm from grating
• collected energy: 17.5 µJ
• collected : 9.85 - 10.15 µm
(86% throughput)

## Slide 9
Compressing -7.4 ps2, 40 ps pulses at 𝜆0 ≈ 10 µm
☐ several m. of e.g. Ge, ZnSe needed
☐ high absorption losses + TOD
☐ not available at high THz frequencies
☐ insufficient positive GDD
☐ insufficient positive GDD at small separations
Options in principle:
Bulk GDD > 0 THz-transparent material
Chirped Mirrors
Prism Compressor
Martinez “stretcher”
→
☐ readily achieves positive 5-10 ps2
☐ manageable loss, TOD
(compressor for GDD < 0 input)
✗
✗
✗
✗
✗
✓
✓
(steps beam ↓)
Pick-Off
Mirror
40 ps
OAP 5
FINAL
FOCUS
(tilts beam ↑)
-7.4 ps2
Martinez, IEEE J. Quant. Electron. 23, 1385 (1987)

## Slide 10
Martinez compressor: numerical example
(steps beam ↓)
Pick-Off
Mirror
OAP 5
FINAL
FOCUS
(tilts beam ↑)
Input pulse parameters:
D ≈ 6 cm; 𝜏 ≈ 40 ps; GDD ≈ -7.4 ps2
(f = 20 cm; NA = 0.15)
• Energy: 4.5 < ℇ < 7 µJ (25-40% total thru-put)
Simulated output beam parameters:
• Duration: 0.6 < 𝜏 < 1 ps (FWHM, intensity)
• Final Focus: 0.6 < I0 < 1.6 x 1016 W/m2
2 < Epeak < 4 GV/m
( µm)
ℇ = 15 µJ; 𝜆 ≈ 10 µm;
Compressor parameters:
• Gratings: 100 lines/mm (1st order); R ≈ 0.8 each;
2-pass throughput 0.4 – 0.5
• OAPs 3,4: same as for OAPs 1,2
• 3 Flat Mirrors: R ≈ 0.98 each

## Slide 11
e-
 | Laser-Driven Sources |  | RF Accelerator-Driven Sources |  |  | fs CSPR
THz property | Mid-IR [1,2] (Organic X-tals) | Near-IR [3-5] (TPF, LiNbO3) | RF: FELBE/TELBE [6,7] U37 U100 U300 |  |  | LWFA-driven [8] (this work)
Pulse duration [ps] | 0.1 - 10 | 0.3 - 10 | 1 - 5 | 2.5 - 30 | 0.5 - 10 | 0.6 -1
Pulse energy [µJ] | < 100 | < 14,000 | < 2 | < 2 | < 10 | 5 – 7 c
Epeak [GV/m] a | < 4 | < 0.5 | < 3 b | < 0.5 | < 0.18 | 2 - 4
Rep. rate | 10 - 1000 | 10 - 105 | 13 x 106 | 13 x 106 | 0.5 x 106 | 1 – 10 d
Existing strong-field THz sources & fs LWFA-driven CSPR
Further comparison
a Peak focused field for Gaussian pulse focused to beam waist w0 = 2𝜆.
b Varies with 𝜆; value for 𝜆 = 10 µm is 1 GV/m, assuming 2 µJ energy.
c 3D grating & SPR collection geometries can potentially approach mJ energy
e-
T. Zhang, R. Ischebeck, et al., “Boosting the efficiency of narrowband
THz radiators via 3D emission-collection,” PR-AB 28, 054501 (2025)

## Slide 12
 | Laser-Driven Sources |  | RF Accelerator-Driven Sources |  |  | fs CSPR
THz property | Mid-IR [1,2] (Organic X-tals) | Near-IR [3-5] (TPF, LiNbO3) | RF: FELBE/TELBE [6,7] U37 U100 U300 |  |  | LWFA-driven [8] (this work)
Pulse duration [ps] | 0.1 - 10 | 0.3 - 10 | 1 - 5 | 2.5 - 30 | 0.5 - 10 | 0.6 -1
Pulse energy [µJ] | < 100 | < 14,000 | < 2 | < 2 | < 10 | 5 – 7 c
Epeak [GV/m] a | < 4 | < 0.5 | < 3 b | < 0.5 | < 0.18 | 2 - 4
Rep. rate | 10 - 1000 | 10 - 105 | 13 x 106 | 13 x 106 | 0.5 x 106 | 1 – 10 d
Existing strong-field THz sources & fs LWFA-driven CSPR
Further comparison
a Peak focused field for Gaussian pulse focused to beam waist w0 = 2𝜆.
b Varies with 𝜆; value for 𝜆 = 10 µm is 1 GV/m, assuming 2 µJ energy.
c 3D grating & SPR collection geometries can potentially approach mJ energy [Zhang et al., PR-AB 28, 054501 (2025)]
d LWFAs operating at 100 Hz exist [Eichner et al., Opt. Lett. 50, 4890 (2025)].
LWFAs operating at 1 kHz are under development:
• Rovige et al., Phys. Rev. Accel. Beams 23, 093401 (2020)
• Salehi et al., Phys. Rev. X 11, 021055 (2021)].

## Slide 13
SUMMARY
• Few-fs LWFA bunches ( µm) propagating over planar metal gratings of
period recently generated ps SPR pulses at up to 30 THz (𝜆 down to 10 µm).
The measured energy µJ proved the high coherence of the radiation.*
* Rudzinsky et al., Optica 13, 810 (2026)
• Simulations show that selected cones of the CSPR “fan” can be de-chirped, compressed
to 𝜏 < 1 ps, and focused to Epeak ~ several GV/m using standard CPA optics.
• Since these pulses
1) originate from a table-top source; 2) readily reach tens-of-THz frequency; and
3) are intrinsically synchronized with the fs LWFA e-bunch & its secondary X-rays,
they offer unique capabilities for ultrafast high-field THz spectroscopy that complement
existing laser-based and RF accelerator-based THz sources.
Funding:
U. S. Dept. of Energy, Office of HEP (DE-SC0011617)
Helmholtz Association (Matter & Energy)
Presented scheme not optimized; many improvements possible.

## Slide 14
1st Generation SPR
Experimental Setup
• 1% N2-doped He
• cm-3
• 0.5 nC
• 450 MeV
• 1 mrad
• 3 µm
coarse
adjustment
fine
jitter
measure-
ment
10
Rudzinsky et al., Optica 13, 810-821 (2026)

## Slide 15
Edward M. Purcell
1912-1997
Smith-Purcell Radiation (SPR)
S. J. Smith and E. M. Purcell, “Visible light from localized surface charges moving across a grating,”
Phys. Rev. 92, 1069 (1953).
Stephen J. Smith
1925-2017
(EMP PhD student)
PRIDE* fan:
*Purcell Radiation
Into Directions
according to Energy
Angular distribution
of SPR energy (1 e-):
Brownell, Phys. Rev. E 57, 1975 (1998)
grating efficiency
factor
evanescent field length:
Dispersion relation:
measured from e- propagation direction
distance from e- to grating
Angular distribution
of SPR energy ( e-):
Brownell, Phys. Rev. E 57, 1975 (1998)
e-
5
mm
For GeV electron
and µm:
longitudinal
bunch-profile
diagnostic
band