## Slide 1
Ultrashort Pulse Generation and High Power Machine Protection in a Fiber Laser for Advanced Accelerator Applications
1Lawrence Berkeley National Laboratory
2University of California, Berkeley
AAC 2026, UCLA
M. Logantha1,2, F. Kong1, A. Amodio1, M. Chen1, D. Wang1, Q. Ji1, J. van Tilborg1, J. Osterhoff1, C. G. R. Geddes1, C. B. Schroeder1,2, Q. Du1, T. Zhou1

## Slide 2: Broadband spectral combining enables ultrashort, high average power fiber lasers
[1] T. Zhou et al. Optics Letters 21, 4422 (2017)
[2] W. Chang et al. Optics Express 21, 3897 (2013)
[3] T. Zhou et al. Optics Express 23, 7442 (2015)
  Broadband spectral combing enables 10s of fs pulse generation at high average power
power
amplifiers
l1
spatial
combiners
temporal
stackers
spectral
combiners
pulse compressor
stretchers and
pre-amplifiers
spectral
splitter
l2
l3
output
oscillator
…
Accelerator
Laser Parameter | Expected Spec
Laser driver Energy | 150 mJ
Pulse duration | ~ 40 fs
Rep-rate | ~ 5 kHz
Average power | 1 kW
Notes: Part of a more extensive plan

## Slide 3: Complex High Power System Architectures Require a Multi-layer Machine Protection Scheme
Protection point #1 for GHz laser oscillator
Protection point #2 for large-core amp stage (single pulse burst @20kHZ)
Prevent unwanted changes in seeding and pump conditions of high-power laser amplifiers can damage system
Solution: FPGA-based, multilayer, distributed protection system
***Machine protection currently in operation
Notes: Unwanted changes in seeding and pump conditions of high power laser amplifiers can result in damage to the system. We have designed and implemented an FPGA-based, multilayer, distributed protection system, via rapidly sensing errors in signal amplitude, duration, and timing, and stopping seed pulses and pump lasers, critical for multi-spectral-channel high power laser amplifier operation.
High power pulse can damage components, spike or loss of seed loss, misfire, overfire, monitor pulse amplitude using monitoring point throughout system , set up detecteion range

## Slide 4: Spectral combining addresses gain narrowing in fiber lasers to achieve ultrashort pulses as energy and power is scaled
5nm(150dB gain)
50nm(input)
spectral bandwidth is limited to 5nm (300fs) in high energy fiber system without gain narrowing compensation
Yb3+ cross section has ~100nm(30fs) bandwidth
but gain narrowing limits amplified bandwidth
Paschotta, Quantum Electronics 1997
Coherent spectral combining of multiple fiber channels overcomes
gain narrowing by:
Spectrally splitting and amplifying each spectral channel independently before combining
S. Chen, 2021
Notes: What is gain narrowing,
Compare ti sapg bandwidth +pw

## Slide 5
Prior work: Shortest pulse (~42fs) from spectrally combined ~100nm Yb:fiber system
Single-stage amplification and broadening
~20ps stretched pulse duration
Previous proof of concept 42fs and current work on spectrally combining Yb:fiber system
Current work: 40-70fs via spectral combining ~100nm
High-gain (80dB), high dispersion
~1ns stretched pulse duration/spectral channel
5
Current Spectral Combiner
S. Chen et al, Optics Express, 2023
Notes: We have built a three-spectral-channel, multi-stage fiber chirped pulse amplification (FCPA) laser system aimed at combining these spectral channels and achieving ~40fs compressed pulses after ~70dB gain. To reach transform-limited pulse durations, we have modeled the systemic dispersion at various orders from pulse propagation through a fiber-based stretcher, fiber amplifiers, and a grating compressor, and designed compensation schemes. We have also built an automated spectral phase mapping and optimization loop using programmable pulse shapers, and further achieved optimally compressed pulses from one spectral channel. We have demonstrated phase-locking of all three spectral channels using FPGA-based feedback controls, and are currently investigating coherent spectral combination and pulse compression.

## Slide 6: Experimental setup and result of high gain, broadband spectral combining
Spectral Combining Experimental Setup
Spectrum amplitude and phase control
Phase-locking mechanism
Diagnostic for phase-locking
Plot of combined spectrum output of broadband, high-gain SMFA before compressor
Wavelength (nm)
Power (Normalized)
Notes: Digital controls needed to achieve spectral combining:
Optimize spectral intensity and phase in each spectral channel
Synchronize phase and timing to correct coherence mismatch between spectral channels
Active phase-locking in real-time to reach ultrashort pulsewidth
Spectrum amplitude control is used to optimize amplification for each spectral band over multiple stages of amplification
Spectral phase control is used to optimize pulse compression at the final stage
Piezo-shifters to phase-lock the pulse bursts for each spectral channel in time. We use active feedback

## Slide 7: Challenges to achieve high gain, broadband, spectral combining
Solution:
Implement FPGA-based active feedback loop with Stochastic Parallel Gradient Descent (SPGD) algorithm to detect coherent, overlapping spectra
Wavelength (nm)
Power (Normalized)
Challenge 1
Digital controls needed to achieve spectral combining in temporal domain
Challenge 2
Compensate for complex residual dispersion in system
Complex residual dispersion
Solution:
Build physics model to gain system-level dispersion insight
Utilize feedback and phase mapping methods with programmable shaper in each spectral channel
Fiber stretcher
Multi-stage Fiber Amplifiers
Grating Compressor
Interference

## Slide 8: Experimental Results: real-time active phase-locking 3 spectral channels at 20kHz
Interference at leakage ports used to phase-lock 3 spectral channels in time domain with SPGD algorithm
Wavelength (nm)
Power (Normalized)
Interference
Power Intensity ( a.u.)
Time (ms)

## Slide 9: Optimal compression over broadband spectrum requires system-level dispersion accounting
~100m of fiber stretcher
Active Yb:fiber
Grating Compressor
Complex residual dispersion
Passive Yb:fiber
Physics model built to calculate system-level residual dispersion
Initial compressor angle configured for only broadband spectrum
Autocorrelation traces of spectral channel B and C (non optimal compressor condition for broadband operation)
Model showed large residual dispersion difference between spectral channels
Model incorporates major positive and negative dispersion in system:
Time (
Time (
GDD (ps^2)
GDD (ps^2)

## Slide 10: Optimal compressor configuration found with developed dispersion model to achieve broadband compression
Time (
Time (
CH.B
CH.C
Measured Autocorrelation Traces
Before physics model (55 deg AOI)
CH.B
CH.C
After physics model (47 deg AOI)
Residual higher order dispersion remains after optimal compressor configuration
Time (
Time (
Notes: Physics model block diagram introduction

## Slide 11: Programmable phase shaper used to tune spectral phase for broadband pulse compression at singular compressor configuration
Nonoptimal Pulse Compression
Autocorrelator Measurement
Python-based feedback/mapping processing for programmable shaper
Corrected laser pulse
Step 1: 2D spectral phase mapping with reduced amplifier system to avoid damage at high gain
Step 3: Manual fine tune shaper with all amplifiers
Step 2: Feedback loop with shaper and reduced amplifier system with Autocorrelator
Time (
Time (

## Slide 12: Phase mapping and feedback results for fine tune spectral phase for dispersion compensation to reach near-transform limit pulse durations
Plots of GDD vs TOD phase mapping in spectral CH.C
Plots of TOD vs FOD phase mapping in spectral CH.C
Autocorrelator Pulsewidth Contour Map
Autocorrelator Amplitude Contour Map
1080 fs  270 fs
1650 fs  300 fs
CH.C: 215 fs (TF 200fs) final pulse width

## Slide 13: Achieved 78 fs spectral combined and compressed pulse from 2 channels after 80dB gain and ns chirping
Individually optimized channels after physics model and phase shaper feedback tuning
Combined 2 spectral channels after optimal phase-locking

## Slide 14: Recap
  Built 3-spectral-channel, multi-stage fiber chirped pulse amplification laser system
  Demonstrated spectral combining of 2 high-gain spectral channels to achieve 78fs
  Modeled systemic dispersion and built automated spectral phase mapping and optimization loop using programmable pulse shapers
  Designed and implemented an FPGA-based, multilayer, distributed protection system
  Next steps:
  Optimally combine and compress 3 high-gain spectral channels
    Spectrally combine high-power fiber system at multi-mJ level
Notes: Part of a more extensive plan

## Slide 15
Acknowledgement
This work is support by:
DOE Office of High Energy Physics, contract no. DE-AC02-05CH11231
Gordon and Betty Moore Foundation