## Slide 1: 100mJ Spatially and Temporally Combined Femtosecond Fiber Laser System Enabling Next Generation Laser Plasma Accelerators
Christopher Pasquale1,*, Yanwen Jing1, Tayari Coleman1, Bowei Yang1 , Bohan Zhou1, Michael Garner1 Alexander Rainville1, Mathew Whittlesey1,Qiang Du2 and Almantas Galvanauskas1
1Gerard Mourou Center For Ultrafast Optical Science, University of Michigan
2Lawrence Berkely National Laboratory
*chrispas@umich.edu

## Slide 2: Collaborators:
Tong Zhou
Jens Osterhoff
Cameron Geddes
*Lawrence Berkeley National Laboratory, USA
Mingshu Chen (currently at *)
Francisco Leon Ascencio
Siyun Chen
Mohammed Azzouz
Gerard Mourou Center for Ultrafast Optical Science, University of Michigan, USA
Optical Engines
Don Sipes
Brian Schulz

## Slide 3
Long-term: Discovery science with
multi-100’s kW average & multi-TW peak
Secondary-radiation and particle sources for:
  -Medicine/Biology
  -Material science/Laboratory Astrophysics
  -Homeland security/SNM Detection
Near-term: Practical applications with
multi-kW average & multi-TW peak
GeV Electron Beams at kHz Repetition Rates
Interaction with Electron Beams
for kHz-rate 𝛾 Photon Sources
Interrogation of Nuclear Materials
kHz-rate Secondary Radiation & Particle Sources
Need for High Intensity (10s J/10s fs) and Average Power (10s kHz rep. rates) Femtosecond Pulse Laser Drivers
~6.5 J, 130fs, ~50kHz
~ 325kW average &
~50TW peak
with >25% WPE

## Slide 4
Current UPSL status and future scientific needs are highlighted in the recent DOE, NSF and DOD co-sponsored BRN Workshop on Laser Technology:
Progress in High Intensity (10s J/10s fs) and Average Power (10s kHz rep. rates) Femtosecond Pulse Laser Drivers
https://science.osti.gov/-/media/ardap/pdf/2024/Laser-Technology-Workshop-Report_20240105_final.pdf

## Slide 5
Coherently combined fiber laser array
Coherently combined fiber lasers offer:
Scalability to 100s of kW & 1-10J
30-100 fs pulses at 10-100kHz repetition rates
>30% wall-plug efficiency
Compactly integrated, robust and reliable laser drivers
Spatial-domain coherent beam combining (CBC): power and energy scaling
Time-domain coherent combining (CPSA): power and energy scaling with ~100 times reduced array size
Spectral-domain coherent spectral combining (LBNL) to reduce pulse durations to ~30-50fs
Nonlinear amplification/compression approaches (UM) to reduce pulse durations to ~20-50fs
>1J in 50-100fs from >100 fiber amplifier channels
>1J in 10-50fs from >100 fiber amplifier channels
Efficient, high power, ultrafast fiber lasers offer path to future plasma accelerators, secondary-radiation sources
Mode-locked pulse train
Stacking burst
formation
Power & energy amplification
Spatial splitting & combining
Increasing pre-pulse contrast
Coherent pulse stacking
Pulse compression
Pulse stretching & dispersion control

## Slide 6: Need for Coherent Pulse Stacking Amplification (CPSA)
CPSA
Traditional CPA Limits single fiber energy to a few percent of stored energy
Time domain coherent combining allows ‘extension’ of chirped pulse duration
  Allows extraction of all stored energy
CPSA Extends CPA by ~100x, allowing for full energy extraction and array size reduction
…
1
2
3
81
80
79
CPA

## Slide 7: Coherent Pulse Stacking Amplification technique
Input Burst
Output
Pulse
1
2
3
9
8
7
4
5
6
CPSA uses Gires-Tournois Interferometer (GTI) cavities with controllable reflectivity, phase and length1,2,3,4
Flexible design of GTI cavities allows for stacking arbitrary number of pulses
  Rule of thumb: N cavities stack 2N pulses
Multiplexing of cavities allows for close approximation of 2N cavity stacking while drastically reducing number of cavities
81 → 1 pulse stacking experimentally demonstrated at low power5
  stacking efficiency up to 90% (theoretical 98%)
  <0.8% RMS stability
This sets the benchmark for high-power temporal combining experiments
Input Burst
Output
Pulse
Intermediate Burst
…
1
2
3
81
80
79
1
9
81
72
…
Peak Power (A.U.)
1.34 x 350fs
SHG Intensity (A.U.)
[5] Manuscripts in preparation
[1] T. Zhou, et. al., Optics Express, vol. 23, no. 6, p. 7442, 2015
[2] John Ruppe, PhD Thesis, University of Michigan, 2017
[3] Hanzhang Pei, PhD Thesis, University of Michigan, 2021
[4] Mathew Whittlesey, PhD Thesis, University of Michigan, 2023

## Slide 8: Scaling to Joule-class performance will require cascading many amplifier stages
Key Technological Milestones Achieved to Validate this Architecture:
  Demonstrated up to ~10mJ per each 85µm core chirally-coupled-core (CCC) fiber amplifier. CCC fibers operate in a fundamental spatial mode, and are optimized for monolithic integration of fiber-laser subsystems1
  Demonstrated Coherent Pulse Stacking Amplification (CPSA) extracting up to ~9mJ with ~300fs compressed pulse durations1
  Demonstration simultaneous spatial-domain Coherent Beam Combining (CBC) and coherent time-domain combining (CPSA) at up to 7mJ per channel (with 4 channels)2
[1] A. Rainville et al. , Optica 11, 1540 – 1548 (2024)
[2] A. Rainville et al. , CLEO 2023, paper SF3H.6
Example architecture of a Joule-class CBC-CPSA fiber laser system

## Slide 9: Current work is to achieve ~100mJ CBC-CPSA performance milestone
2. Enable first fiber laser driven LPA experiments
  Goal is to achieve 50MeV electron acceleration
  This will require achieving ~30fs pulse durations with post-compression
1. Explore/validate operation of 112 channel cascaded strongly saturated amplifier stages
  Demonstrate managing pulse burst reshaping along and across strongly saturated amplifiers
  Demonstrate managing nonlinear phase accrual along multiple amplifier stages
Example architecture of a Joule-class CBC-CPSA fiber laser system
10mJ/0.1kW amp.
10mJ/0.1kW amp.
Current ~100mJ/10kHz 12-channel demonstrator
Two major objectives for this demonstrator:

## Slide 10: 12-Channel Spatially and Temporally Combined (CBC-CPSA) Fiber Laser System

## Slide 11: Spatially and Temporally Combined Fiber Laser Array System
1GHz Fiber Oscillator
Amplitude Modulator
Phase Modulator
AOM 1
AOM 2
SM
Amp
SM
Amp
LMA Amp
AOM 3
CCC
Amp.
Stretcher
SM
Amp
…
Compressor
GTI Stackers
Modulated Burst, 81pulses, 1MHz
~1ns Stretched Pulses
1GHz, 75fs Pulses
Amplified Burst, 1-10mJ, 1-10kHz
Stacked Pulse
Compressed Pulse
Downcount to 100kHz
Downcount to 20kHz
Downcount to 1-10kHz
~1mJ
Channel 1
Channel 12
Splitting Optics
Combining Optics
…
Spatially Combined Amplifiers
AOM 4
Suppress ASE

## Slide 12: Spatially and Temporally Combined Fiber Laser Array System
1GHz Fiber Oscillator
Amplitude Modulator
Phase Modulator
AOM 1
AOM 2
SM
Amp
SM
Amp
LMA Amp
AOM 3
CCC
Amp.
Stretcher
SM
Amp
…
Compressor
GTI Stackers
Modulated Burst, 81pulses, 1MHz
~1ns Stretched Pulses
1GHz, 75fs Pulses
Amplified Burst, 1-10mJ, 1-10kHz
Stacked Pulse
Compressed Pulse
Downcount to 100kHz
Downcount to 20kHz
Downcount to 1-10kHz
~1mJ
Channel 1
Channel 12
Splitting Optics
Combining Optics
…
Spatially Combined Amplifiers
AOM 4
Suppress ASE
LMA Amp
…
Phase
Control
Amplitude Control & Downcounting
Master Clock
Stacker
Stabilization
EOM Bias
Stabilization
CBC Phase Control
FPGA
1MHz -> 100kHz Downcounting
Peak Power Metric
Burst Shaping

## Slide 13: Design of 100mJ CBC System
Key Subsystems:
  Splitter – splitting into 12 equal seed burst with phase control
  Amplifier Array – fiber laser amplifiers, capable of 10mJ @ 10kHz
  Combiner – Efficient recombining of output beams, requires high beam stability
  Control System – measure system output and provide feedback for phase control
HR
HR
PBS
PBS
λ/2
λ/2
λ/4
λ/4
HR
50/50
Fiber Laser Amplifier
Fiber Laser Amplifier
PD
Control System
Piezoelectric Actuators
Beam Sampler

## Slide 14: Amplifier Module Design
Temperature Along Active Fiber at 300W Pumping
Position From Fiber Input [cm]
Chart: Amplifier Module Output Energy for 250uJ Seed
| 0 | 3.01 | 13 | 23.9 | 36.299999999999997 | 48.8 | 61.1 | 72.7 | 84.8 | 96.5 | 109 | 120 | 131 | 141 | 150
1kHz | 0 | 0 | 0 | 0.32149 | 1.1583 | 2.5235 | 4.1691 | 5.8133 | 7.3106 | 8.397 | 9.2044 | 9.7622 | 10.0852 | 10.32 | 10.5109
2kHz | 0 | 0 | 0 | 0.36113 | 1.1157 | 2.1961 | 3.4351 | 4.6976 | 5.9748 | 7.0904 | 8.2208 | 9.1163 | 9.7475 | 10.2026 | 10.5256
3.3kHz | 0 | 0 | 0 | 0.34792 | 0.91603 | 1.7132 | 2.6072 | 3.5379 | 4.5068 | 5.4169 | 6.4005 | 7.2666 | 7.9566 | 8.6025 | 9.2924 | 9.4686 | 10.0264 | 10.4668 | 10.8192
5kHz | 0 | 0 | 0 | 0.30388 | 0.734 | 1.3095 | 1.9319 | 2.5719 | 3.2296 | 3.9636 | 4.6536 | 5.3142 | 5.8426 | 6.4445 | 6.9877 | 7.1051 | 7.663 | 8.2502 | 8.8961 | 9.5126 | 10.0264 | 10.4375 | 10.7458
8kHz | 0 | 0 | 0 | 0.22409 | 0.51051 | 0.87516 | 1.269 | 1.692 | 2.1229 | 2.5526 | 3.0763 | 3.4741 | 3.8587 | 4.2299 | 4.6145 | 4.7206 | 5.1184 | 5.5427 | 6.02 | 6.4974 | 6.9217 | 7.3726 | 7.7969 | 8.1947 | 8.6057 | 8.9903 | 9.335 | 9.64 | 9.9185
10kHz | 0 | 0 | 0 | 0.20258 | 0.45802 | 0.76189 | 1.1069 | 1.4504 | 1.8203 | 2.1741 | 2.5426 | 2.8787 | 3.2149 | 3.4792 | 3.7434 | 3.7874 | 4.1104 | 4.4774 | 4.8884 | 5.2848 | 5.7252 | 6.1362 | 6.5179 | 6.8702 | 7.2372 | 7.5602 | 7.8832 | 8.1474 | 8.4263
Designed, fabricated, tested and characterized amplifier module performance
Compact design of amplifier modules facilitates higher channel counts
RMS Stability <0.5%

## Slide 15: Optomechanical Design of 100mJ System
Splitting Array / Phase Control
Power Amplifiers
Beam Combiner

## Slide 16: Scaling to 100mJ: 12 channel beam combining system
Splitting Array / Phase Control
Power Amplifiers
Beam Combiner / Diagnostics

## Slide 17: Progress Towards Demonstrating 100mJ Coherently Combined Beam
1mJ/fiber amplifier:
  Spatial combining efficiency 90%
  RMS Stability 0.40% (1 min)
3mJ/fiber amplifier:
  Spatial combining efficiency 85%
  RMS Stability 0.45% (1min)
6mJ/fiber amplifier
  Spatial combining efficiency 78%
  RMS Stability 0.75% (1min)
Demonstrated 55mJ at 2kHz in coherently combined beam
  Highest reported CBC fiber laser energy to date

## Slide 18: Equal Nonlinearity Burst Shape in a Single High Energy Amplifier
Extracting all stored energy from amplifiers results in each pulse in the burst seeing different gain
B-integral leads to strongly varying phase across equal amplitude burst
  Disrupts prescribed phase profile, reducing stacking efficiency
Can design burst shape with each pulse having equal B-integral at output
Burst is shaped using EOM and AOM’s throughout system
Φnl [rads]
Time [ns]
Strongly Varying
Nonlinear Phase
Time [ns]
Equal Amplitude Burst Shape
Intensity [A.U.]
Intensity [A.U.]
Analytical Equal Nonlinearity
Burst Shape
Flat (and minimized)
Nonlinear Phase Profile
Φnl [rads]
Time [ns]
Time [ns]
Representative Energies in a 12 channel single amplification stage
250uJ/ch
10mJ/ch
7mJ Equal Nonlinearity Burst Shape
Experimental Result

## Slide 19: Equal Nonlinearity Burst Shape in Cascaded High Energy Amplifiers
4mJ
250uJ/ch
10mJ/ch
10uJ
Representative Energies for seeding 12 high energy amplifiers
Ein = 250uJ, Eout = 1mJ
Ein = 250uJ, Eout = 1mJ
Well Matched Fiber
Poorly Matched Fiber
Seeding many high energy amplifiers will require extracting significant energy from preamplifier
  We must now account for varying B-integral in preamplifier
We can design burst shape such that pulses accrue equal nonlinearity across both amplification stages
Amplifier characteristics must be matched.
  Running 9/12 fibers well matched: η ~ 80%
  Running 11/12 fibers well matched: η ~ 90%
Combined 55mJ Burst Shape

## Slide 20: Intrabusrt Pulse Reshaping
Without in-burst saturation control
With in-burst saturation control
Experimental Validation of In-burst Saturation Control in a 6mJ, 10nm amplifier
Saturation of broadband gain causes variation of spectra (and chirped pulse shape) along stacking burst
Chirped pulse shape determines spectral phase accrual
Can be pre-compensated with high-speed amplitude modulator
Previously demonstrated ability to compensate this effect for 300fs BL pulses
Siyun Chen, PhD Thesis, University of Michigan, 2021
Amplitude Modulator
Phase Modulator
Stretcher
SM
Amp
Amplitude Modulator
Phase Modulator
High Speed Modulators will control pulse amplitude and phase profiles

## Slide 21: Temporal Combining
12-channel CBC+CPSA Results:
  1mJ/fiber @ 2 kHz
  CBC efficiency: 90%
    ~20W for temporal combining
  Stacking efficiency: 80.2%
1mJx12 Channel Stacking
Higher energy experiment ongoing:
  Single-channel results:
    E=3mJ stacking efficiency: 70.4%
    E=6mJ stacking efficiency: 52.3%
Further steps to improve performance:
  Optimization of equal nonlinearity burst shape
  Implementing control of shape of individual pulses within burst
Stacking Output Comparison
Notes: For 1mJx12ch combining, the stacking efficiency now is related to how much power in the stacker:
P=3W stacking efficiency: 80.2%
P=20W stacking efficiency: 60.8%
Rms stability:
1mJ (0428wfm3): 0.961%
3mJ (0604wfm5): 3.572% (another 3mJ shot on the same day has 1.648%)
6mJ (0714wfm3): 4.402%
No data for 1x12
2.105% for 1mJx12 when 60mW into stacker

## Slide 22: Compression
1 mJ/fiber:
  Pulse duration: 301fs (1.05x TL)
3 mJ/fiber:
  Pulse duration: 294fs (1.13x TL)
6 mJ/fiber:
  Pulse duration: 337fs (1.17x TL)
  Further optimization is required
    TOD is not fully compensated

## Slide 23: Enabling Fiber Laser Driven Laser Plasma Acceleration
Planned fiber-laser driven laser plasma acceleration experiments at Michigan will use ~50mJ in 30fs pulse
With a new post compression technique, we anticipate reducing pulse duration to ~30fs
Multi-focal phase-plate beam splitter
Multi-pass Cell
Chirped mirror compressor
t
t
➔ >50mJ/30fs
t
LPA Experiments
Multi-focal phase-plate beam recombiner
t
➔ 50-100mJ/300fs
Talk by T. Coleman in WG1 on 7/27/2026

## Slide 24
Summary of the State-of-the-Art in Ultrashort Pulse Coherently Combined Fiber Laser Arrays
Coherent beam combining (CBC) of 61 parallel fiber CPA channels using ~40µm core PCFs produced after combiner[1] :
  ~500µJ (8.2µJ/channel) at 2 MHz for <300fs pulses
  Would need >12 000 channels for ~10J of combined energy
CBC of 16 parallel fiber 6ns CPA + 8-pulse divided pulse amplification (DPA) using ~81µm PCF-rods produced in a combined beam[2] :
  ~48mJ (~3mJ/channel) at 20kHz for 158fs pulses
  Would need ~3300 channels for ~10J of combined energy
(Our work) CBC of 12 parallel fiber channels + 81-pulse CPSA using ~85µm 3C fibers produced in a combined beam [3] :
  ~55mJ (~6mJ/channel) at 2kHz for ~300fs pulses
  With projected ~10mJ/channel would need ~1000 channels for ~10J of combined energy
[2] Henning Stark et al. Opt. Lett. 48, 3007-3010 (2023)
[3] A. Rainville et al. , Optica 11, 1540 – 1548 (2024)
[1] Ihsan Fsaifes at al. Opt. Express 28, 20152-20161 (2020)
From [1]

## Slide 25
Future 1-10J Drivers Must Transition from Table-Top Laboratory Prototypes to Fully Integrated Systems
81 pulse stacker
Initial design for a 10 GeV LPA driver (supported by DARPA MuS2 and DOE SBIR Phase II Projects)
Collaboration between UM, LBNL and Optical Engines
~2200 fiber amplifiers sleeved into <20 cm OD water-cooled tube

## Slide 26: Summary
Fiber lasers offer an efficient, scalable path to 100's of kW ultrafast lasers with Joules of energy per pulse
Broad application areas ranging from secondary radiation sources (in the near term), to the future colliders (in the long term)
Demonstrated up to 55mJ in spatially combined beam, highest from CBC fiber laser system
Further developments in progress:
  Continuing to scale spatially combined energy to >100mJ
  Demonstrating high efficiency temporal combining with 100mJ
  Development of new post compression technique for 30fs pulses to enable fiber laser driven LPA experiments
Spectrally combined 200mJ system under construction at Berkeley National Lab supported by DOE ECRP and Moore Foundation Funding
Conceptual system design work carried out under DARPA MuS2 program to validate feasibility of compact and robust coherently-combined fiber laser drivers
3C fibers fabricated at nLight Inc.
This work is supported by the DOE Advanced Accelerator Stewardship grants FP00013287 and FP00016549.