## Slide 1: Investigation of transverse instability in efficient plasma-based accelerators
Arohi Jain, Navid Vafaei-Najafabadi
Stony Brook University
1

## Slide 2: Efficiency vs Instability
Goal: Plasma stages must achieve high power-transfer efficiency while preserving beam phase-space quality ( emittance energy spread)
Threat (BBU): For long-distance laser/plasma wakefield acceleration, strong plasma focusing forces resonantly amplify small transverse offsets into large transverse oscillations This is a critical issue of large emittance in prospective plasma-based colliders
Trade-off: Lebedev et al., suggested- BBU is unavoidable at high efficiency, mitigation (like BNS damping) compromises collider-level beam quality
Trailing bunch
Beam-breakup (BBU) instability growth
Lebedev et al., PRAB(2017)
Instability E Energy spread

## Slide 3: Beam loading for achieving low energy spread
Simulation design criteria
The system targets a blowout cavity radius to support collider-relevant charges nC at a loaded accelerating field GV/m. Driver: sustain a highly stable plasma cavity over meter-scale propagation allowing the beam-breakup dynamics to be isolated from wake evolution Trailing bunch: Trapezoidal current profile flattens the field and minimize energy spread
Simulation design criteria
M. Tzoufras et al., PRL(2008)
Jiayang Yan PhD thesis (2025)
Parameters
Plasma: Driver beam: Trailing bunch: 0.1% Offset m
Parameters
Driver
Trapezoidal trailing bunch
GV/m
A.Jain et al., PRR(2026)

## Slide 4: The code HiPACE++
3D, QS PIC for plasma acceleration
Runs on GPU and (multi-core) CPU
Open-source:https://github.com/Hi-PACE/hipace
Documentation: https://hipace.readthedocs.io/en/latest/
Main features:
  Multiple beams and plasma species to simulation beam-driven wakefield acceleration
  A laser envelope solver to simulate laser-driven wakefield acceleration
  Mesh refinement for efficient computation
  An advanced explicit field solver for increased accuracy
  Diagnostics compliant with the openPMD standard
  Arbitrary profiles for the beams and plasma profiles
  Readers from files for the beam and laser profiles
S. Diederichs et al., Comput. Phys. Comm. 278: 108421 (2022)

## Slide 5: Modelling beam-breakup instability
Transverse motion of beam slice centroid
Driving force
Driving force
Adiabatic damping due to energy gain
Ion restoring force
Precise determination of transverse wake function is crucial for accurate modeling of transverse instabilities in a plasma accelerator
Centroid
Bunch head position

## Slide 6: Wake potential model
Transverse wake function
Short-range wake theorem
Transverse wake function
Longitudinal wake function:
generated by the trailing beam
Driving force
Driving force
Wake potential superposition
Wake potential superposition
With trailing bunch
Without trailing bunch
Our wake potential model is valid for both LWFA and PWFA

## Slide 7: Wake potential model shows excellent agreement with simulation
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]
Stupakov et al., PRAB(2018)
Lebedev et al., PRAB(2017)
A factor-of-four error can lead to a substantial overestimate of the accumulated transverse instability.
Transverse force
Transverse force
Previous Models
Lebedev: Stupakov: High charge witness beam significantly deforms the bubble boundary, resulting in significant error in this model
Previous Models
Wake potential model
Our model naturally incorporates exact, deformed boundaries without any fitting parameters.
Wake potential model

## Slide 8: Bunch slice centroid evolution
Transverse motion of centroid
Driving force
Driving force
Transverse wake function
Transverse wake function
The agreement remains strong over a meter of propagation at 10 GeV/m
Wake potential formalism captures the transverse beam dynamics with predictive accuracy
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]

## Slide 9: Analytical modelling of efficiency and instability
Transverse wake function
, – Slope of for
Transverse wake function
Wake-to-trailing-bunch energy transfer efficiency
Ratio of extracted energy to the maximum energy available in the wake. How effectively beam loads the wake. How effectively extracts the available wake energy.
Ratio of extracted energy to the maximum energy available in the wake. How effectively beam loads the wake. How effectively extracts the available wake energy.
Beam loading efficiency
Driving force
Driving force
Transverse motion of centroid
Instability-
Efficiency-
Jiayang Yan PhD thesis (2025)
A. A. Golonov et al.,PPCF (2021)
M. Tzoufras et al., PRL (2008)

## Slide 10: Mapping the High-Efficiency, High-Stability Operating Window
Physically inaccessible
Bunch Length
Loaded field
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]

## Slide 11: Mapping the High-Efficiency, High-Stability Operating Window
Charge
Efficiency levels
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]

## Slide 12: Mapping the High-Efficiency, High-Stability Operating Window
Stability thresholds defined by the maximum slice centroid ratio
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]

## Slide 13: Mapping the High-Efficiency, High-Stability Operating Window
1x growth
, 0.8 nC,
3x growth
, 1.1 nC,
A. Jain arXiv:2607.10497 (2026) [under review in PRAB]

## Slide 14: Preservation of the beam quality over a meter-long plasma
Emittance below 500 nm rad
Energy gain up to 16.5 GeV
Relative energy spread <1.5 %
T. J. Mehrling et al., PRL (2018)
Ion motion (dotted lines)
Well-known mechanism for bounding BBU growth in plasma accelerators Phase Mixing: Nonuniform focusing along the trailing bunch causes different slices to accumulate differing betatron phases, reducing the BBU growth rate. Ion response introduces additional transverse forces modifying projected beam quality in configurations with limited centroid growth. Ion motion bounds the emittance growth of 3× while a baseline emittance increase in 1x
,

## Slide 15: Laser driven simulation set up
Trapezoidal bunch
Laser Pulse
1x growth
, 0.9 nC,
Parameters
Plasma channel: Plasma length= 20 cm Driver laser : m, fs, m Trailing bunch: 0.1% Offset m
Parameters
GV/m

## Slide 16: Preservation of the beam quality in 20 cm long plasma
Emittance below 500 nm rad
Relative energy spread ~1%
Energy gain up to 2 GeV
Relative energy spread ~1%
Energy gain up to 2 GeV

## Slide 17: Conclusions
Simulation Validation: Full 3D PIC simulations show excellent quantitative agreement with our analytical transverse force and centroid predictions over a meter-long plasma.
Parametric Mapping: The analytical model maps energy-extraction limits directly against stability thresholds to isolate a highly stable operating window.
Beam Quality Preservation: We successfully map out a highly stable, high-efficiency operating space over a 1 m acceleration distance, simultaneously demonstrating:
  Near 80% energy transfer efficiency
  Sub-500 nm rad transverse emittance preservation
  Up to 16.5 GeV energy gain with < 1.5% relative energy spread
Bypassing the Barrier: Our study demonstrates that the efficiency-instability trade-off is not an absolute limit. It can be systematically managed and circumvented by pairing precise wake potential modeling with tailored beam loading.
Future Work: This wake-potential formulation provides a path to integrate additional, self-consistent plasma effects like ion motion.

## Slide 18
Thank you

## Slide 19
Backup slides

## Slide 20: Ideal Beam Loading: Achieving Low Energy Spread and High Efficiency for Future Compact Colliders
pC
* See backup slides for detailed simulation parameters
Trapezoidal current profile is needed for flattening accelerating field
Two-color injection experiment at ATF offers a path towards such collider quality trapezoidal beam [1]
Such a beam also enables high energy extraction efficiency (43% in current simulation, theoretically >90% [2])
Current Profile
Electron beam driver
Injected trapezoid
[1] A.Jain et al., PRR(2026)
[2] M. Tzoufras, Phys. Rev. Lett 101, 14 (2008)

## Slide 23: Backup: details of previous work
Driver
Injector
Ion. level | (Driver) | (Injector)
Kr7+ -> Kr8+ | 1.87 | 0.06
Kr8+ -> Kr9+ | 3.10 | 0.16
Kr9+ -> Kr10+ | 3.78 | 0.20
Kr10+ -> Kr11+ | 4.51 | 0.23
Ion. level |  | 
Kr7+ -> Kr8+ | 1.87 | 0.06
Kr8+ -> Kr9+ | 3.10 | 0.16
Kr9+ -> Kr10+ | 3.78 | 0.20
Kr10+ -> Kr11+ | 4.51 | 0.23
Generated beam
Driver
Injector
Injected beam
A. Jain, et al., Phys.l Rev. Research 8.2 (2026): 023213.

## Slide 24
m, 20 GeV acceleration of the beam

## Slide 25: Mapping the High-Efficiency, High-Stability Operating Window
Bubble closure constraint: ensuring cavity does not collapse before the end of the bunch./Physically inaccessible
Bunch Length
Loaded field