## Slide 1
AAC 2026, July 27, 2026, UCLA
Design and progress of a 150 mJ, 40 fs, 5 kHz
fiber-laser accelerator driver
Tong Zhou, Qiang Du, Fanting Kong, Mahek Logantha, Mingshu Chen, Alessio Amodio, Dan Wang, Qing Ji, Jeroen van Tilborg, Carl Schroeder, Almantas Galvanauskas*, Jens Osterhoff, Cameron Geddes
Lawrence Berkeley National Laboratory
* University of Michigan

## Slide 2
  LPA based applications and light sources need kHz+ rates
  kHz+ rates can enable precision LPAs via feedback control
  New laser requirements for future kHz+ LPAs
High average power capability (up to 100’s kW)
High wall-plug efficiency (10s%)
Current Ti:sapphire lasers limited
Laser parameter | In progress | kBELLA* (GeV e-) | 10 kHz driver | 5 GeV driver
Energy | ~0.2J | 3J | 3J | 10J
Pulse duration | ~40fs | 30fs | 30fs | 30fs
Rep-rate | 5 kHz | 1kHz | 10kHz | 50kHz
Average power | ~1kW | 3kW | 30kW | 500kW
Laser plasma acceleration (LPA)
High average power (kW+) and high rep-rate (kHz+) lasers are needed
for new precision LPAs, light sources, and RF accelerator upgrades
Community Planning Priorities (DOE & National Academies)
  Need new laser technology beyond kHz rep-rate!
Promising: Fiber laser, Tm:YLF bulk, Yb:YAG bulk
  LACE Principle
  Complex pulse structure at SNS
  LACE at SNS, ORNL
Laser-based beam manipulation & stripping at RF accelerator facilities:
kHz+ lasers can enable laser Compton scattering for bunch intensity control in RF accelerators, e.g. FCC-ee
Laser-assisted stripping (LACE) overcomes power limits of current foil-based e- stripping. It needs: kW+ class power, MHz pulses in macro-pulses

## Slide 3
Coherently-combined fiber lasers can provide high power, rep-rate, energy, and efficiency
Commercial fiber laser
from IPG Photonics
(120 kW CW, WPE>45% )
61-fiber-laser combining system (1kW, ~250fs)
- Fsaifes et al. Opt. Express 28, (2020)
32mJ, 158fs, 640W combining 16 fibers
10mJ, 120fs, 1kW combining 16 fibers
- Stark et al. Optics Letters 48, 3007 (2023)
- Stark et al. Optics Letters 46, 969 (2021)
Fiber laser: most efficient high power laser & compactly integrable
Coherent combined fiber lasers rapidly developing worldwide, enabling high energy and power
LBNL, U Michigan, collaborators established scalable, multi-dimensional fiber combining architecture for high power, rep-rate, energy, efficiency
100-200 mJ, 1 kW demonstrators at multi-kHz rep-rates are in progress at UM (built) and LBNL
nLIGHT’s 300 kW tiled-aperture combined fiber laser
- Physics Today 77 (1), 2024
Demonstrated:
Temporally combined 81 pulses
Spatially combined 81 beams
Spectrally combined to 42 fs
Spatial-temporal combining (4x81) to 27mJ at 9.5 mJ/channel, kHz
- A. Rainville, et al. Optica 11.11 (2024)
- Q. Du, et al. Opt. Express 29.4 (2021)
- S. Chen, et al. Opt. Express 31.8 (2023)
- A. Rainville, et al. CLEO 2023, pp. SF3H.6

## Slide 4
A 150 mJ, 40 fs, 5 kHz demonstrator is in progress at LBNL,
directly enabling kHz LPA and scalable to higher energy
Coherently combine fiber laser pulses in space, time, and spectrum:
Temporal pulse stacking: Stack ~100 pulses in time to extract all stored energy (10 mJ per fiber)
Spatial beam combining: Power and energy scaling (>250 mJ from 3x9 fibers)
Spectral combining: Simultaneous energy/power scaling and pulse duration reduction (from >100 fs to 30-50 fs)
Architecture scalable to 10 J & 100s kW, >30% wall-plug efficiency, capable of compact system integration
spectral
combining
temporal
combining
pulse
compressor
(150mJ output)
3x - 4x
2x - 3x
fs oscillator
amp & pha modulator
Yb fiber amp
nonlinear fiber amp
pulse compressor
pulse stretcher
spectral splitting
pulse shaper
pulse modulator
spectral filter
pulse modulator
beam splitter
Final fiber amps
(>250mJ total)
beam combining
phaser
Yb fiber amp
fiber amp
fiber amp

## Slide 5
The 150mJ, 5kHz demonstrator is a fiber CPA system operating with
full bandwidth of Yb:fiber gain spectrum
Spectral broadening with a gain-managed nonlinear amplifier (GMNA)
75 nm gain bandwidth (Yb), <40 fs FWHM duration, (quasi-square spectrum)
3 spectral channels, 1020-1053 nm (A), 1049-1075 nm (B), 1070-1095 nm (C)
Programmable pulse shapers spectrally synthesized to provide full band, high-res. shaping (spectral phase & intensity)
Distributed spectral filtering to mitigate gain narrowing
40µm photonic-crystal fiber pre-amplification
(1st stage)
Backbone component is the 85µm core, high energy fiber amplifier
Out-of-plane MLD grating compressor design
- M. Logantha, et al. CLEO 2026, pp. JTU-220

## Slide 6
  Today’s large-core fiber amplifiers: free-space pump light coupling
  They need to be monolithically integrated and modularized for high energy systems (robust, compact, alignment-free, low-cost  scalable)
  We developed world’s largest-core (>85µm) and highest energy (10mJ) monolithically integrated fiber amplifier (CCC-CPTEC)
  Next step: Full monolithic integration for further scalability (~1cm transverse size of current module  ~1mm )
Integrated large-core fiber amplifier modules are developed
– key for scaling to high energy systems
Thermally stable at high power
- Chen, M. Chen, et al. CLEO 2026, pp. SM4H-4.

## Slide 7
85µm core integrated fiber amplifier tested for final amplification;
Spatial diffractive beam combining in progress
…
- T. Zhou, et al, Opt. Lett. (2017); - T. Zhou, et al. Opt. Lett. (2018); - R. Wilcox, US Patent (2019);
- D. Wang, et al, Opt. Express (2021); - Q. Du, et al, Opt. Express (2021)
Modeling shows high energy is achievable in different spectral channels
We developed novel diffractive pulse combining that can combine many ultrashort-pulse laser beams with two diffractive optical elements (DOE)
Previously combined eight 120-fs beams with maximum efficiency >90%
9-beam, high power DOE combiner in the 150 mJ demonstrator in progress

## Slide 8
Temporal coherent pulse stacking (CPS) enables extraction of full stored energy
in fiber; CPS accommodates ultrashort pulses <50 fs
T. Zhou, et al. Opt. Express 23, 7442 (2015)
A. Rainville, et al. Optica 11.11 (2024)
4+4 cavities to stack 81 pulses
L. Cooper, et al. CLEO 2023, pp. SF1N.6
T. Zhou, et al. Photonics West 2024, pp. PC1286503
8-cavity, 81-pulse, broadband pulse stacker in progress at LBNL
Modeling & experiment showed broad bandwidth (supporting as short as ~30 fs) can achieve excellent stacking with low dispersion optics

## Slide 9
Concept of broadband spectral combining with pulse shaping proved;
Current work shows the approach works in the 150 mJ demonstrator
In next presentation by Mahek Logantha
Proof-of-principle demo (20dB gain, 20ps chirped pulse): Record short pulse (42fs) from fiber combination systems
Coherently-spectrally synthesized pulse shaping achieves full-band spectral control
S. Chen, et al. Opt. Express 31, 12717 (2023)
T. Zhou, et al. US Patent (2025)
Current work: Extend the approach in the 150 mJ demonstrator system (high gain/energy, high dispersion)
First test: spectral combining before large-core fiber stages (80 dB gain, 800 ps chirped pulse), 2 channels
Achieved close to transform limit (TL), combined & compressed pulse (78fs vs 73 fs TL)

## Slide 10
100-200 mJ, 1 kW fiber laser demonstrators are in progress: step-stones towards high energy and power
12-Channel system has been built at UM:
27-Channel system (3 spectral bands) in progress at LBNL:
3 spectral bands
<10 mJ
>30fs
10 kW
>1 MHz
(beam shaping, full SNS stripping)
DOE Stewardship
DOE ECRP
& Moore
10 kW Class
50 kW Class
Type
Energy
Duration
Power
Rep-rate
Research (funded)
0.1 J
100 fs
1 kW
10 kHz
Research (mostly funded)
0.15 – 0.2 J
40 fs
1 kW
5 kHz
Facility
1 J
30 fs
10 kW
10 kHz
Facility
3 J
30fs
30 kW
10 kHz
<2 mJ
>50fs
2 kW
>1 MHz
(50% SNS stripping)
<60 mJ
>30fs
60 kW
>1 MHz
(beam shaping, future high intensity facility stripping)
OR:
OR:
OR:
…
System
engineering needed
- 2:50pm presentation by Christopher Pasquale

## Slide 11
Summary
This work is supported by DOE Office of High Energy Physics, including the Accelerator Stewardship program, and the Gordon and Betty Moore Foundation.
kW+, kHz+, efficient lasers needed for new precision LPAs, light sources, and RF accelerator upgrades
LBNL, UM, and collaborators established scalable fiber combining architecture, up to 10 J, 100s kW
A 150 mJ, 40 fs, 5 kHz fiber demonstrator is in progress at LBNL, directly enabling kHz LPA, scalable
100-200 mJ, 1 kW fiber laser demonstrators are in progress at UM (built) and LBNL: step-stones towards high energy and power
Coherent combining in space, time, and spectrum: Simultaneous energy/power scaling and pulse duration reduction
Developed integrated large-core fiber amplifier (scalability), tested record high energy (10 mJ)
Temporal & Spatial combining tested broadband operation supporting the demonstrator
Spectral combining tested large bandwidth, dispersion, and gain; Validated for the demonstrator