## Slide 1: Self-loading LWFAs using two-color ionization injection with flying-focus lasers
July 27, 2026
Evan Trommer, Arohi Jain, Navid Vafaei-Najafabadi
Stony Brook University

## Slide 2: Synthesis
An important area of focus with LWFAs is the acceleration of high charge (>100 pC) beams with sub-1% energy spreads and low transverse emittances (100 nm-rad) for future collider applications
A “flying-focus plasma photoinjector” can utilize spatiotemporal coupling of a laser’s fields to generate an e- beam with a trapezoidal shape, ideal for beam loading, with high amounts of charge
Applying this concept with experimentally-relevant laser parameters can generate an asymmetric e- beam with nearly 200pC of charge and 100s of nm-rad emittance
Schroeder, C. B., et al., Journal of Instrumentation 18.06 (2023): T06001.
Bulanov, S. S., et al., Journal of Instrumentation 19.01 (2024): T01010.

## Slide 3: Two-color ionization injection uses a second laser to generate the electron beam inside the wake
A high-intensity drive laser () drives a nonlinear plasma wake
A co-propagating laser with a shorter wavelength and lower a0 can be focused inside the wake as it is formed
The focused injector further ionizes the gas; electrons with low transverse momenta can be trapped with low emittance
The range of ionization is very short, so only a small amount of charge is injected
L. L . Yu et al., Phys. Rev. Lett. 112, 125001
C. B. Schroeder et al., Optica Publishing Group paper JSIII_1_3. (2015)

## Slide 4: Flying focus produces lasers with long intensity ranges
Flying focus can be used to create intensity profile with a traveling focus spot. This acts as a dynamic ionization front for our usage
The minimum spot size can be tuned to lengths , allowing us control the amount of charge injected
D. Froula et al., Phys. Plasmas 1 March 2019; 26 (3): 032109.
Simulated FF laser intensity profile in a vacuum with

## Slide 5: A flying focus laser can generate a near-trapezoidal beam inside a blown-out wake
The linear charge density of a beam generated by a flying focus laser:
e- beam
driver
trailing
e- beam
Ideal beam loading
load field value
maximum wake radius
slope of electric field
M. Tzoufras et al., Phys. Rev. Lett. 101, 145002 (2008)
Jiayang Yan, PhD Thesis (2024)
A. Jain, et al., Phys. Rev. Research 8.2 (2026): 023213.

## Slide 6: The e-beam could be produced in an LWFA stage, then accelerated in a PWFA stage
Instead of staging this process, can we inject and ideally load a beam in one stage?
Driver
Injector
Injected beam
Injection stage
Acceleration stage (20 GeV)
After acceleration
A. Jain, et al., Phys. Rev. Research 8.2 (2026): 023213.
Injected beam
Before acceleration
Notes: Slice energy spread is 1e-4

## Slide 7: We want to verify this method with an experiment
ATF @ BNL, the only lab with a TW-class CO2 laser, requires upgrades to enable sub-ps pulse (ongoing)
BELLA at LBNL could be well-suited for pursuing an experiment based on this method, before upgrades at BNL complete
Two systems: hundred-terawatt (HTW) and petawatt (PW) with laser. The injector would need to be frequency-tripled ()
 | BELLA HTW System | BELLA PW System
 | 50 TW | 1PW
 | 800 nm | 800 nm
 | 40 fs | 40 fs
 | BELLA HTW System | BELLA PW System
 | 800 nm | 800 nm
In this presentation, we will show preliminary results with some idealized scenarios based on these parameters

## Slide 8: Particle-in-cell simulations drive our studies
OSIRIS is our primary PIC code for studying flying focus lasers with ionization physics
Using Quasi-3D geometry with azimuthal modes
This material is based resources of NERSC facility, operated under Contract No. DE-AC02-5CH11231.

## Slide 9: Choosing optimal driver parameters
See: Navid Vafaei-Najafabadi WG1 Tue 5:20!
To drive a nonlinear wake while not ionizing some chosen gas
Trapping mechanics are optimized for large potentials
Since the size of the wake scales with the laser spot size, we want
To keep the blown out structure of the wake, we require sufficient ponderomotive force and pulse length:

## Slide 10: HTW laser can drive a nonlinear wake at
wake properties

## Slide 11: Designing the FF injector for the HTW bubble
Ionization levels |  | 
O5+ -> O6+ | 0.171 | 0.063
O6+ -> O7+ | 3.051 | 1.141
O7+ -> O8+ | 3.742 | 1.385
Ionization levels |  | 
O5+ -> O6+ | 0.171 | 0.063
O6+ -> O7+ | 3.051 | 1.141
O7+ -> O8+ | 3.742 | 1.385
Loading the beam where
To achieve ideal beam loading, we match the initial linear charge density and choose a viable combination of
Injector
Expected beam

## Slide 12: The beam generated has trouble flattening the field
We are observing an overloading effect, which will harm the energy spread!

## Slide 13: The beam has good shape and emittances but poor energy spread
Average emittances once beam is fully injected:
Emittance evolution
Last slice emittance
The injector creates a nice trapezoid which has reasonable agreement with theory. The total charge is consistent with calculations.
Energy spread evolution
Last slice energy spread
Average energy and energy spread once beam is fully injected:

## Slide 14: Why is our beam not ideally loading?
(1) our estimated wake properties are incorrect
Our load field and position appear correct with our inputs and model
Our may be over-estimated, meaning we designed the beam with too much charge
(2) The injector properties in simulations do not match expected values
is not constant over the focus range
Measured doesn’t exactly match simulation input

## Slide 15: Potential parameters for using a PW driver
Driver parameters
Using the PW system would allow us to operate at higher densities with laser bubbles, though higher emittances are expected
Injector parameters
Expected beam parameters

## Slide 16: Summary of results
Identified possible experimentally-relevant parameters to perform a flying-focus ionization injection experiment at a facility with high-power NIR lasers
Identified main limitations with the 1st/3rd harmonic setup
  Need relatively high to ionize gas with the injector pulse
  Still able to achieve high charge and near-trapezoidal profile with moderate transverse emittances
Work is continuing on revising the setup for a HTW injection stage and simulating a PW injection stage

## Slide 17: Thank you for listening!

## Slide 18: Backup slides

## Slide 19: Backup plots
Slice emittance over time
Slice energy spread over time

## Slide 20: Backup plots

## Slide 21: Requirements for electron trapping with ionization injection
For a particle ionized inside the bubble, it is “trapped” if:
If is small, which is determined by the injector’s , then the condition relaxes:
Small for the injector is important for the trapping condition and for emittance (discussed later on)

## Slide 22: Wake evolution and trapping may affect beam profile
Trapping dynamics may impact the shape of the beam
Electrons are born off-axis:

## Slide 23: A flying-focus laser can generate a near-trapezoidal beam inside a blown-out wake
The linear charge density of a beam generated by a flying focus laser:
For a wake with a parabolic potential,
(1) Amount of charge ejected from the ions by the moving focused laser. Note that , is the ion level before ionization
(2) Encompasses motion of the focus spot in the co-moving coordinate with constant
(3) “Compression factor” describes compression of electrons as they are trapped in an accelerating phase
A. Jain et al., Phys. Rev. Research https://doi.org/10.1103/q36y-6jqn (2026)

## Slide 24: Extra Slides: Threshold Ionization calculations
Ionization levels |  | 
O5+ -> O6+ | 0.171 | 0.063
O6+ -> O7+ | 3.051 | 1.141
O7+ -> O8+ | 3.742 | 1.385
N4+ -> N5+ | 0.106 | 0.039
N5+ -> N6+ | 2.0368 | 0.7649
N6+ -> N7+ | 2.5577 | 0.9549
F6+ -> F7+ | 0.258 | 0.094
F7+ -> F8+ | 4.3476 | 1.6198
F8+ -> F9+ | 5.1905 | 1.9258
Ne7+ -> Ne8+ | 0.37 | 0.134
Ne8+ -> Ne9+ | 5.9584 | 2.2128
Ne9+ -> Ne10+ | 6.9893 | 2.5867
Ionization levels |  | 
O5+ -> O6+ | 0.171 | 0.063
O6+ -> O7+ | 3.051 | 1.141
O7+ -> O8+ | 3.742 | 1.385
N4+ -> N5+ | 0.106 | 0.039
N5+ -> N6+ | 2.0368 | 0.7649
N6+ -> N7+ | 2.5577 | 0.9549
F6+ -> F7+ | 0.258 | 0.094
F7+ -> F8+ | 4.3476 | 1.6198
F8+ -> F9+ | 5.1905 | 1.9258
Ne7+ -> Ne8+ | 0.37 | 0.134
Ne8+ -> Ne9+ | 5.9584 | 2.2128
Ne9+ -> Ne10+ | 6.9893 | 2.5867
Ionization levels |  | 
Ar13+ -> Ar14+ | 1.9428 | 0.6989
Ar14+ -> Ar15+ | 2.3128 | 0.8309
Ar15+ -> Ar16+ | 2.5027 | 0.8969
Ar16+ -> Ar17+ | >10 | >10
Xe24+ -> Xe25+ | 1.3839 | 0.485
Xe25+ -> Xe26+ | 1.4609 | 0.5119
Xe26+ -> Xe27+ | 4.0236 | 1.4209
Xe27+ -> Xe28+ | 4.2926 | 1.5148
Kr23+ -> Kr24+ | 2.2658 | 0.7989
Kr24+ -> Kr25+ | 2.6557 | 0.9369
Kr25+ -> Kr26+ | 2.7817 | 0.9799
Kr26+ -> Kr27+ | >10 | 4.9525
Kr27+ -> Kr28+ | >10 | >5
Ionization levels |  | 
Ar13+ -> Ar14+ | 1.9428 | 0.6989
Ar14+ -> Ar15+ | 2.3128 | 0.8309
Ar15+ -> Ar16+ | 2.5027 | 0.8969
Ar16+ -> Ar17+ | >10 | >10
Xe24+ -> Xe25+ | 1.3839 | 0.485
Xe25+ -> Xe26+ | 1.4609 | 0.5119
Xe26+ -> Xe27+ | 4.0236 | 1.4209
Xe27+ -> Xe28+ | 4.2926 | 1.5148
Kr23+ -> Kr24+ | 2.2658 | 0.7989
Kr24+ -> Kr25+ | 2.6557 | 0.9369
Kr25+ -> Kr26+ | 2.7817 | 0.9799
Kr26+ -> Kr27+ | >10 | 4.9525
Kr27+ -> Kr28+ | >10 | >5

## Slide 25: Current profile monitor: COTR
M. LaBerge et al., Nat. Photon. 18, 952–959 (2024)

## Slide 26: Backup: details of previous work
Driver
Injector
Ion. level | (Driver) | (Injector)
Kr7+ -> Kr8+ | 1.87 | 0.06
Kr8+ -> Kr9+ | 3.10 | 0.16
Kr9+ -> Kr10+ | 3.78 | 0.20
Kr10+ -> Kr11+ | 4.51 | 0.23
Ion. level |  | 
Kr7+ -> Kr8+ | 1.87 | 0.06
Kr8+ -> Kr9+ | 3.10 | 0.16
Kr9+ -> Kr10+ | 3.78 | 0.20
Kr10+ -> Kr11+ | 4.51 | 0.23
Generated beam
Driver
Injector
Injected beam
A. Jain, et al., Phys.l Rev. Research 8.2 (2026): 023213.

## Slide 27: Extra Slides: 3D Nonlinear Theory
In the “small bubble” regime,
Jiayang Yan, PhD Thesis (2024)