## Slide 1: C. McCombs1, T. Benahmed2, A. Sinn2, M. Thevenet2, N. Cook3, R. Lehe1, C. B. Schroeder1 1Lawrence Berkeley National Laboratory, USA 2Deutsches Elektronen-Synchrotron (DESY), Germany 3RadiaSoft LLC, USA
AAC - July 28, 2026
CHEQUP: an open-source hydrodynamics framework for plasma-channel formation

## Slide 2: Preforming a plasma channel guides the laser in Laser Wakefield Acceleration (LWFA)
For laser-plasma acceleration: the laser driver needs to maintain at tight spot size over tens of centimeters of gas
This can be done by generating a plasma channel, ahead of the laser driver, that operates as an optical fiber (needs low on-axis plasma density)
One way to generate appropriate plasma channels is the HOFI technique: a secondary, lower-intensity laser pulse creates a hot plasma on axis, which then expands radially
Laser driver

## Slide 3: Modeling the formation of plasma channel
Laser driver

## Slide 4: Hydrodynamic simulations of the nanosecond-scale expansion have been performed in the past
(Code: HELIOS, Group Oxford)
Shalloo, Robert J., et al. "Hydrodynamic optical-field-ionized plasma channels." Physical Review E 97.5 (2018): 053203.
(Code: FLASH, Group Oxford)
Picksley, A., et al. "Meter-scale conditioned hydrodynamic optical-field-ionized plasma channels." Physical Review E 102.5 (2020): 053201.
Picksley, A., et al. "All-optical GeV electron bunch generation in a laser-plasma accelerator via truncated-channel injection." Physical Review Letters 131.24 (2023): 245001.
(Code: COMSOL/HYQUP, Group DESY):
Mewes, Steven Mathis, et al. "Demonstration of tunability of HOFI waveguides via start-to-end simulations." Physical Review Research 5.3 (2023): 033112.
(Code: SPARC, Group UMd):
Miao, Bo, et al. "Benchmarking of hydrodynamic plasma waveguides for multi-GeV laser-driven electron acceleration." Physical Review Accelerators and Beams 27.8 (2024): 081302.
(Code : FLASH, Group Radiasoft):
Cook, Nathan M., et al. "Hydrodynamic modeling of plasma channel systems for laser plasma accelerators." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1079 (2025): 170610.
This work builds on these previous efforts, to create an open-source, GPU-compatible simulation tool (CHEQUP).

## Slide 5: Castro-based HOFI Expansion with QUasineutral Plasma (CHEQUP)
Hydrodynamics code, built on Castro
Castro: an open-source, massively parallel compressible-hydrodynamics code with adaptive mesh refinement, built on the AMReX library (developed at LBNL) and maintained by the AMReX-Astro collaboration for astrophysical flows (supernovae, X-ray bursts)
CHEQUP extends Castro with plasma-channel physics: two temperatures, ionization/recombination, e–ion and e–neutral collisional coupling, electron conduction
Open-source: github.com/chequp-org/chequp/ Documentation: https://chequp.readthedocs.io/en/latest/
Runs on multi-CPU or multi-GPU systems
Supports mesh refinement and adaptive timestep
Multiple element support: Hydrogen, Helium, Nitrogen, Argon
Supported geometries: 1D / 2D / 3D Cartesian and 1D / 2D (r–z) cylindrical;

## Slide 6: CHEQUP solves two-temperature fluid equations for an arbitrary species mix
One velocity, two temperatures: all species advect with a single fluid velocity v (quasineutral, no charge separation); electrons carry their own temperature Te, all heavy particles (neutrals + ions) share Th. Electrons are not a separate fluid, ne follows from the ion charge states.

## Slide 7: Additional Physics: Multi-species impact ionization and three-body recombination
Hot electrons impact-ionize the neutral gas, expending energy and cooling the plasma

## Slide 8: Additional Physics: Collisional thermalization between electrons and heavy particles
Te >> Th. Electron–heavy equilibration takes ~nanosecond, so a single temperature would misrepresent the pressure that initiates the shock.

## Slide 9: Additional Physics: Electron thermal diffusion
Electron thermal diffusion carries heat beyond the ionized core, pre-heating and ionizing surrounding gas. Without it, the channel is too narrow and the on-axis density too high.

## Slide 10: Compatibility with other community codes

## Slide 11: Benchmark CHEQUP vs COMSOL/HYQUP
Excellent agreement in channel density and pressure between CHEQUP and COMSOL/HYQUP
Small differences between ion density and pressure could be attributed to absence of ion temperature diffusion in Chequp (captured in COMSOL/HYQUP)

## Slide 12: Example demonstrating Adaptive Mesh Refinement capabilities
R-Z simulation of HOFI channel expansion on GPU
Courtesy of T. Benahmed (DESY)

## Slide 13: Example demonstrating 3D capabilities
Inputs: multiple transverse laser intensity profiles along propagation
Calculates ionization fraction, electron temperature
Interpolates ionization and temperature along propagation
Output: 3D channel expansion for use in PIC

## Slide 14: Conclusion
CHEQUP is an open-source, GPU-compatible simulation toolkit, available to the community
CHEQUP includes important physics for HOFI channel formation
CHEQUP can be combined with other open source codes for a complete start-to-end simulation

## Slide 15
Thank you
This work was supported by the U.S. Department of Energy, Office of Science, Office of High Energy Physics under Contract No. DE-AC02-05CH11231, by funds from the UC Multi-Campus Research Programs and Initiatives of the University of California, Grant Number M23PR5854, and used the computational facilities at the National Energy Research Scientific Computing Center (NERSC).