## Slide 1
UNIVERSITY OF MARYLAND AT COLLEGE PARK
Dept. of Physics
Dept. of Electrical and Computer Engineering
Institute for Research in Electronics and Applied Physics
Kilohertz Guiding and Laser Wakefield Acceleration in Optically Generated Plasma Channels
G. Brewster, J.E. Shrock, E. Rockafellow, A.J. Sloss, S.W. Hancock, N. Tripathi, L. Railing, F. Sorkin, M. Gupta, C. Lazzarini, J. Šišma , A. Špádová, M. Jech, I. Zymak, S. Lorenz, G. Grittani, and H.M. Milchberg
Institute for Research in Electronics and Applied Physics and Department of Physics, University of Maryland, College Park, Maryland 20742, USA
Supported by DARPA under the Muons for Science and Society (MuS2) program
Notes: - I just wrapped up my first year of graduate school and this is my first conference, first presentation, and I will be talking about the first experiment I was apart of

## Slide 2
Waveguiding Regimes: kHz-mJ s vs. Joule-Class
(a)
(a)
Electron density
Index of refraction
core
cladding
Hydrodynamic channel formations depends on:
Ambient density
Plasma temperature
Plasma width
Notes: - Hydrodynamic channel formation depends on:
- Ambient density
- Plasma temperature
- Plasma width
- Joule-class experiments that push for GeV electrons have different experimental constraints compared to kHz operation

## Slide 3
Waveguiding Regimes: kHz-mJ s vs. Joule-Class
(a)
Narrow:
Short:
High plasma density:
  <10% core/cladding density contrast
Application driver: high average flux / dose rate over many shots
mJ kHz drivers
(a)
Wide:
Long:
Low plasma density:
  >100% core/cladding density contrast
Application driver: maximum single shot energy (GeV-class)
Joule-class Hz drivers
Electron density
Index of refraction
core
cladding
Hydrodynamic channel formations depends on:
Ambient density
Plasma temperature
Plasma width
Notes: - GO through and compare
- Go line by line and compare width, length, density regime, and application

## Slide 4
Two-color interferometry experimental setup @ UMD : SHG & THG of Ti:Sapphire
400 nm interferogram
267 nm interferogram
Bessel Focus
Few Micron Channel Formation Experiments @ UMD
Notes: - In preparation for our experiment at ELI Beamlines we conducted plasma channel characterization experiements at UMD
- We have a kHz system in-house with very similar specs to the auxillary beam that we were to use at ELI
- We set up a pump-probe two-color interferometry experiement to measure the plasma channel evolution in time

## Slide 5
Few Micron Channel Formation Experiments @ UMD
High plasma density regime
Neutral density contrast of <10% confirms channel will support waveguiding in kHz regime
Delay
Notes: - Here are some preliminary results from that setup
- The blue curve shows a greater than 10% contrast between neutral density on-axis vs. off, which indicated to us that this setup could be used for waveguiding at a kHz

## Slide 6
Few Micron Channel Formation Experiments @ UMD
High plasma density regime
Neutral density contrast of <10% confirms channel will support waveguiding in kHz regime
Delay
No clear density shock formation
High plasma density balanced by extremely narrow channel
Channel characterization experiments ongoing
Notes: - High plasma density is likely being balanced by the extremely narrow channel

## Slide 7
ELI Beamlines: L1 Laser Systems & ALFA Chamber
(a)
C.M. Lazzarini et al., PoP 31, 030703 (2024)
E.C. Erdman et al. Appl. Opt. 65, 2628-2634 (2026)
L1 Allegra System
  Broadband OPCPA, 1 kHz, 820 nm, 45-50 mJ, <15 fs pulses
FSYNC Auxiliary System
  Broadband OPCPA, 1 kHz, 820nm, 10-12 mJ, <15 fs pulses
Synchronization of two OPCPA systems
Notes: - Now I will transistion to discussing the experiement at ELI Beamlines
- The drive beam we used is the L1 allegra system
- This is a broadband OPCPA system running at a kilohertz with 45-50 mJ on target when running full amplification
- the channel forming line, FSYNC, is also a broadband OPCPA system at a kilohertz
- The two systems share a supercontinuum seed which allows for picosecond scale synchronization between the two systems

## Slide 8
ELI Beamlines: L1 Laser Systems & ALFA Chamber
(a)
L1 Allegra System
  Broadband OPCPA, 1 kHz, 820 nm, 45-50 mJ, <15 fs pulses
FSYNC Auxiliary System
  Broadband OPCPA, 1 kHz, 820nm, 10-12 mJ, <15 fs pulses
Synchronization of two OPCPA systems
First picosecond scale synchronization of L1-Allegra and FSYNC!
C.M. Lazzarini et al., PoP 31, 030703 (2024)
E.C. Erdman et al. Appl. Opt. 65, 2628-2634 (2026)
Notes: - While at ELI, we conducted the first sychronization of the two systems to the picosecond scale

## Slide 9
Experimental Layout – ALFA Chamber
Notes: - Here is a diagram of the layout in ALFA chamber at ELI
- Note the very tight geometry and the use of the axicon telescope
- Due to the tight geometry, we needed a way to extend the Bessel focus downstream so that we did not focus into the drilled mirror that allowed the drive beam to pass through
- We implemented what we call an 'axicon telescope' using custom diffractive axicons
- MORE WILL BE SAID ABOUT THIS IN THE NEXT SLIDE

## Slide 10
Experimental Layout – ALFA Chamber
Drilled Mirror
Custom Gas Jet
420 mrad refractive axicon
Notes: - As I mentioned, the setup was very tight as you can see from this picture taken during in-air alignment

## Slide 11
Tight Geometry Solution: Axicon Telescope
Axicon Telescope Ray-trace
Diffractive optics designed, simulated, & fabricated @ UMD!
Notes: - Here is the axicon telescope mentioned before in a diagram
- Note this diagram uses refractive axicons for clarity, but we used diffractive optics
- the steep approach angle required to make the plasma channel would have focused onto the drilled hole with the geometry constraints
- The use of the axicon telescope allowed us to extend the focus further downstream while saving us energy by not masking the beam

## Slide 12
ELI Beamlines Custom Gas Jet
(a)
Supersonic nozzles designed by ELI Beamlines
Extended neck enables use in tight geometry
1 mm and 2 mm versions employed
Simulated density profiles for different distances above 1 mm nozzle
Schematic courtesy of S. Lorenz
Notes: - Here is the custom gas jet we used, designed by ELI Beamlines personnel
- We implemented both a 1mm and 2mm version
- NOW ONTO PRELIMINARY RESULTS FROM THIS EXPERIMENT

## Slide 13
Guiding Results
(a)
Guiding achieved at low power (up to ~1 cm) and high power (up to 2 mm)
  Air
  N2
  He/N2
Observed from 100s ps ~ 100s ns
Short delay achievable due to low contrast requirement
Guiding diagnostic under-resolved
Long-lived low-power guiding in air-density plasma/neutral structure
Notes: - We first set out to achieve a proof of guiding with our plasma channel at LOW POWER in AIR
- the guiding diagnostic is under-resolved, however we were able to show clear proof of guiding out to extended delays at low-power

## Slide 14
Guiding Results
(a)
Guiding achieved at low power (up to ~1 cm) and high power (up to 2 mm)
  Air
  N2
  He/N2
Observed from 100s ps ~ 100s ns
Short delay achievable due to low contrast requirement
Guiding diagnostic under-resolved
High power guiding
Alignment of channel (blue crosshair) and high-power mode (red crosshair)
Notes: - Here is an example of guiding at high - power
- the blue crosshair shows the axicon vertical position as we scan to find the drive beam

## Slide 15
Guiding Results
(a)
High power guiding
Alignment of channel (blue crosshair) and high-power mode (red crosshair)
Unguided mode
Partial coupling shows both unguided and guided light
Guided mode
Notes: - Here are a few clear examples of an unguided mode, a partially guided mode as we approach overlap, and a fully guided mode

## Slide 16
Guiding Results
(a)
High power guiding
Alignment of channel (blue crosshair) and high-power mode (red crosshair)
Preliminary LWFA results:
Analysis ongoing
LWFA in N2 and N2-doped He
Steady-state operation w/ differential pumpting
Production of >30 MeV electron bunches
Substantial reduction in ebeam divergence and jitter
Notes: - NOW ONTO SOME PRELIMINARY ACCELERATION RESULTS
- The analysis is ongoing
- we were able to obtain steady-state kilohertz operation with a differential pumping system installed
- initial analysis shows production of ~30 MeV electron bunches and very stable pointing and jitter

## Slide 17
High Stability Beams
(a)
Conditions:
Higher density N2
2 mm channel
Quasimonoenergetic beams likely from beam loading
Few-mrad divergence with ~mrad pointing stability
Series of 100 consecutive bursts (not single shots) with ~45 mJ on target
Notes: - Here is an example of high beam stability
- This is 100 consecutive bursts and not single shots

## Slide 18
High Stability Beams
(a)
Conditions:
Higher density N2
2 mm channel
Quasimonoenergetic beams likely from beam loading
Few-mrad divergence with ~mrad pointing stability
100 additional bursts at the same conditions
Notes: - Here we show the electron beam profiles
- this is an ROI of the cameras, and this is NOT following a centroid
- the electron beam and the guided mode are very stable
- a few miliradian divergence

## Slide 19
Ionization Injected Beams
(a)
Use of N2 dopant in helium produces beams with multiple spectral peaks, consistent with short-pulse and guided ionization injection
Notes: - Here we show evidence of ionization injection with multiple spectral peaks

## Slide 20
High Energy Beams
(a)
Real signal in high-energy region!
2 mm N2 channel, high energy parameter space
Highest energy beams observed in pure channels
Notes: - Lastly we see our high energy result with tails up to 40-50 MeV
- ANALYSIS is still ongoing

## Slide 21
Summary
(a)
Important points:
Guided kHz monoenergetic electron beams
  Substantial reduction in electron beam divergence & jitter
Steady state kHz operation achieved w/ differential pumping
>30 MeV electron bunches
Preliminary results with very little optimization explored