## Slide 1: A-STAR a wakefield accelerator for high-repetition rate XFELs
W. Jansma, S. Lee1, M. Kasa, A. Nassiri, B. Popovic, M. Qian, S. Sorsher, N. Strelnikov2, K. Suthar, E. Trakhtenberg, G. Waldschmidt (APS/ANL)
S. Doran (HEP/ANL)
M. Fedurin, K. Kusche (ATF/BNL)
Siy3, N. Behdad, J. Booske (University of Wisconsin)
S. Baturin4, P. Piot5, W.-H. Tan6 (Northern Illinois University);
1) now at LANL, 2) at Amazon, 3) at Quaise Energy, 4) at ITMO University, 5) at HEP/APS/ANL, 6) at SLAC
Presenter: A. Zholents, APS/ANL
A
A
A
A
A
A
A
A
A
A
July 30, 2026
AAC’2026 UCLA

## Slide 2
LCLS-II sets a new standard for the X-ray laser, delivering millions of X-ray pulses per second to scientific users to tackle questions that had previously been impossible to address
“The increase (from 120 Hz to 1 MHz) has already made an amazing change,” Dakovski said*). “Not only is the data coming in faster and with clarity we haven’t seen before, it actually helps us see how the materials are transforming over time. We can watch how energy flows through the material and how the atomic components interact. We can create frame-by-frame ‘movies’ of the dynamic processes.”
*) https://www6.slac.stanford.edu/news/2025-08-07-united-states-just-got-new-x-ray-laser-toolkit-study-natures-mysteries

## Slide 3
Could we replace the SRF linac with more affordable compact accelerator?
1. Plasma-based wakefield accelerators driven by electron or laser beams
The bunch length is not much smaller than the plasma wavelength 
Operating at a high repetition rate is challenging 
2. Structure-based accelerators driven by external RF sources
C3 - the cryogenically cooled copper C-band linac
The CompactLight design study: leveraging the latest innovations in X-band linac and undulator technologies
Long RF pulse -> low repetition rate 
3. Two-beam wakefield accelerator -> CLIC (X-band 50 Hz, 312 bunches)

3. EuPRAXIA: combines structure-based and plasma-based -> low repetition rate 

## Slide 4
e-gun
1 GeV SRF linac
200 kHz
Beamlines
Accelerator for drive and witness bunches
.
Array of collinear wakefield accelerators
XFEL undulators and beamlines
4.5 GeV
Undulators
End stations
Switch yard
Multi-user tender-to-hard X-ray free electron laser facility
High wall plug power efficiency
CWAs do not need electrical power (almost)
Undulators do not need electrical power (almost)
Photon energy ℏ𝜔 versus undulator parameter 𝐾 calculated for FNAPU with a period of 12.6 mm.
Wavelengths from 1.5 keV to 10 keV. This range includes 𝐾-edges of 18 atoms from silicon to zinc.

## Slide 5
Collinear wakefield acceleration using one drive and one witness bunch is well suited for a high repetition rate operation
… because the wakefield needs to exist only for a short time!
The corrugated waveguide is used to obtain a wakefield
tail, attenuated
head
RF power envelope at the end of a 0.5 m long section of CWA operating at 180 GHz. The wakefield decays due to dissipation in the walls.
drive
witness
<<
4 ps
Cu
SS
Using sub-THz frequency and lossy material is beneficial for obtaining short pulses, and possibly high breakdown fields
Calculated using
10 nC and 20 kHz
RF power dissipation

## Slide 6
Shaped drive bunch to obtain a high accelerating field for a witness bunch and an equal deceleration rate for almost all electrons in the drive bunch
1) K. Bane, P. Chen, P. Wilson, Proc. of the Part. Acc. Conf. (PAC1985), Vancouver, Canada, p.3524–3526, 1985.
Transformer ratio
L
q0=10nC
( l=1.7 mm )
loss factor
acc
dec
A "doorstep" charge distribution1

## Slide 7
loss factor in CGS units
kick factor in CGS units
Lorentz force (cause of BBU)
where
Thus
maximum accelerating field
head
tail

## Slide 8
Adaptive energy chirp is used to facilitate BNS damping of BBU instability
1) K. Bane, P. Chen, P. Wilson, Proc. of the Part. Acc. Conf. (PAC1985), Vancouver, Canada, p.3524–3526, 1985.
Transformer ratio
L
q0=10nC
( l=1.7 mm )
loss factor
acc
dec
A "doorstep" charge distribution1

## Slide 9
Snapshots of the drive bunch longitudinal phase space taken at different locations along the A-STAR
distance from the beginning of A-STAR
Energy chirp = 15%
Energy spread = 0
Charge distribution
beginning
ending

## Slide 10
Two 0.5 m long modules of the collinear wakefield accelerator connected in series with the “quadrupole wiggler” removed on the left
Corrugated waveguide
Transition section
FODO focusing structure”
3-mm bore diameter quadrupoles play a decisive role in suppressing BBU instability
Implementation of BNS damping

## Slide 11
quadrupole’s pole tip field at saturation (1.6 T is assumed )
Upper bound for the maximum accelerating field in the structure-based collinear wakefield accelerator is defined by BBU
𝑎 = 1 mm,
𝑞0 = 10 nC,
R = 5,
we calculate 𝐸acc ≈ 90 MV/m.
Using practical constraints

## Slide 12
von Mises stress (MPa)
Bunch repetition rate is defined by the heat load and the tensile stress
This CWG section experiences the highest heat load
Corrugation rib
Corrugation groove 41 MPa
10 kHz bunch rep. rate was used in this example

## Slide 13
Electroformed copper can have much higher tensile stress threshold than ordinary copper (Hall-Petch effect) such as 100 kHz bunch repetition rate could be within the reach.
M. Wang, et. al., Nat. Commun. 13, 5581 (2022).
Courtesy Morris Wang, UCLA
Electroforming is used to make the corrugated waveguide

## Slide 14
Proprietary micro-machining process
Tooth Height 252.7 mm; error 1.5 mm RMS
Tooth Width 175.9 mm; error 2.0 mm RMS
High-Quality Surface Finish
using optical comparator
Aluminum mandrel production
Mandrel inspection and straightening
Electroforming
EDM of outside diameter
100 mm
followed by second straightening
Precision cut of edges
followed by aluminum etching
chamber with five 10-cm long tubes after brazing (currently use three);
low temperature brazing at 360 oC
14
Electroforming of an axially symmetric corrugated waveguide

## Slide 15
Test samples are wire EDM cut to expose the internal corrugations for dimensional analysis
Magnified longitudinal profile of corrugations
249.3 mm
340.7 ± 5mm
Tooth Cross-Section
Groove Cross-Section
angular cut
straight cut
Measurements indicate excellent fabrication quality
Average height of the corrugations of 249.7 mm was determined.
Example of a fabricated corrugated waveguide
Notes: A Keyence VR3200 3D surface profiler was used to perform high-precision metrology for the dimensional analysis of electroformed corrugated waveguide samples.

## Slide 16
300 mm
Setup of the experiment at ATF

## Slide 17
Fabrication of transition section between accelerator modules
Integrated offset monitor horn antenna, 1.10 mm × 0.45 mm
33 mm
TM01 coupler horn antenna, 0.72 mm × 1.78 mm
5.6 mm

## Slide 18
vg = 0.57c
vg = 0.55c
design:
measured:
1.5 ps
TM01
(L=34 mm)
f, GHz
no HOM
Interferogram
Design: 180 GHz
Measurement of CWG: Frequency & group velocity
Michelson interferometer

## Slide 19
head
tail
Calculated results for a 5 ps, 130 pc bunch with a flattop peak current distribution and 65 keV slice energy spread. Off crest acceleration by 6.0 degree. Tube length=74.12mm
diagnostic screen
e)
f)
Corrugated Waveguide
Energy (MeV)
d)
Tube with a smooth wall
h)
head
tail
c)
g)
b)
Energy (MeV)
diagnostic screen
a)
Measurement
Reconstruction using theoretical wakefield
Measurement of the electron beam self energy modulation

## Slide 20
Future work:
measurement of the electrical breakdown threshold and the rate of the breakdown events
development of the electroformed copper with a high tensile stress threshold

## Slide 21
Conclusion
BBU instability constrains the accelerating gradient in A-STAR to 90 MV/m.
All principal A-STAR components were fabricated and tested on the bench and with the electron beam. Work as designed.
As is, the A-STAR is expected to operate with the bunch repetition rate of 20 kHz. With more R&D, achieving 100 kHz could be feasible.
In the A-STAR project, we prioritize a full utilization of the drive-bunch energy in one stage and achieving a high bunch repetition rate, rather than a high accelerating field. Even so, A-STAR is designed for a real-estate acceleration rate of 90 MeV/m using 10 nC drive bunches.

## Slide 22
Bunch “train” structure
0.5 ns
Linear collider CLIC
312 bunches
20 ms
XFEL user’s preference
(1 – 50) ms
X-ray pulses
collect data pulse-by-pulse

## Slide 23
50,4611
36,4209
23,3625
93.7 MV/m
117 MV/m
77.7 MV/m
Witness bunch energy (MeV)
Option | Transformer Ratio | Eacc (MV/m) | Maximum Energy (MeV) | Acc. Length (m) | Bunch rep. rate (kHz) | Efficiency %
1 | 3.2 | 117 | 3625 | 23 | 10 | 57
2 | 4.2 | 93.7 | 4209 | 36 | 15 | 100
3 | 5.1 | 77.7 | 4611 | 50 | 22 | 161
Drive bunch:
Charge = 10 nC
Initial energy = 1 GeV
Final energy = 0.1 GeV
Witness bunch:
Charge = 0.15 nC
Initial energy = 1 GeV
Final energy, see Table
Accelerator length (m), final energy (MeV)
reference option
Comparison of options for obtaining high energy witness bunch

## Slide 24
Animation
Head
Head

## Slide 25
Calculations of a steady state temperature are performed using 20 kHz bunch repetition rate and assuming reduced copper conductivity s = 2.3e7 S/m (instead of 5.9e7 S/m)
Heat load
Vacuum chamber
Water
temperature 25.6 oC
Average power dissipation on 0.5 m long CWG at 20 kHz bunch repetition rate is 1050 W