## Slide 1
WIN, Brighton, June , 2025
Muon Collider
D. Schulte
On behalf of the International Muon Collider Collaboration
Funded by the European Union (EU). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

## Slide 2: Muon Collider Concept
2
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
The main challenge is the short muon lifetime τ = γ x 2.2 μs
Up to 100 ms at collision energy

## Slide 3: IMCC International Muon Collider Collaboration
3
Collaboration formed 2022, currently hosted by CERN
61 full partner institutes, more in the process
From all regions
EU co-funded design study MuCol started 2023
Strong recommendation from P5 «This is our muon shot»
Interest in hosting at FNAL
US partners are in the process of joining
US Muon Collider Inauguration Meeting in August 2024 at Fermilab (about 300 participants)
Forming national organisation to participate
Addendum to CERN-DoE agreement in preparation
Already strong US contribution to IMCC ESPPU documents
Work at universities started
Obtained several grants also at labratories
IMCC will carry out the R&D together and develop options to host the collider at CERN or at Fermilab and potentially also other sites

## Slide 4: IMCC Partners
4
IEIO | CERN
FR | CEA-IRFU
 | CNRS-LNCMI
 | Ecoles des Mines St-Etienne
DE | DESY
 | Technical University of Darmstadt
 | University of Rostock
 | KIT
UK | RAL
 | UK Research and Innovation
 | University of Lancaster
 | University of Southampton
 | University of Strathclyde
 | University of Sussex
 | Imperial College London
 | Royal Holloway
 | University of Huddersfield
 | University of Oxford
 | University of Warwick
 | University of Durham
 | University of Birmingham
 | University of Cambridge
NL | University of Twente
FI | Tampere University
 | HIP, University of Helsinki
LAT | Riga Technical University
CH | PSI
 | University of Geneva
 | EPFL
 | HEIA-FR
BE | Univ. Louvain
AU | HEPHY
 | TU Wien
ES | I3M
 | IFIC/CSIC
 | ICMAB
China | Sun Yat-sen University
 | IHEP
 | Peking University
 | Inst. Of Mod. Physics, CAS
 | University of CAS
KO | Kyungpook National University
 | Yonsei University
 | Seoul National University
India | CHEP
IT | INFN
 | INFN, Univ., Polit. Torino
 | INFN, LASA, Univ. Milano
 | INFN, Univ. Padova
 | INFN, Univ. Pavia
 | INFN, Univ. Bologna
 | INFN Trieste
 | INFN, Univ. Bari
 | INFN, Univ. Roma 1
 | ENEA
 | INFN Frascati
 | INFN, Univ. Ferrara
 | INFN, Univ. Roma 3
 | INFN Legnaro
 | INFN, Univ. Milano Bicocca
 | INFN Genova
 | INFN Laboratori del Sud
 | INFN Napoli
Mal | Univ. of Malta
EST | Tartu University
PT | LIP
SE | ESS
 | University of Uppsala
CA | Université Laval
US | Iowa State University
 | University of Iowa
 | Wisconsin-Madison
 | University of Pittsburgh
 | Old Dominion
 | Chicago University
 | Florida State University
 | RICE University
 | Tennessee University
 | MIT Plasma science center
 | Pittsburgh PAC
 | Yale
 | Princeton
 | Stony Brook
 | Stanford/SLAC
 | …
DoE labs | FNAL
 | LBNL
 | JLAB
 | BNL
Brazil | CNPEM
Signed MoC (61), requested MoC, contributor

## Slide 5: ESPPU Submission Content
5
Assessment
Present green field designs and technologies
International collaboration
Parameters, lattice and component designs, beam dynamics, cost, …
R&D plan
Including scenarios and timelines
Magnets, muon cooling, detector, …
The muon cooling technology and test facility is critical for this
Implementation Considerations
Civil engineering studies/considerations (for CERN and for FNAL)
Cost and power consumption scales
Parameter tables, scaled from green field
  Will develop detailed lattice designs after ESPPU
Schedule (strongly linked to R&D Plan)
Aim for initial stage by around 2050
Back-up document (406p, 450 signatories)

## Slide 6: Key Parameters
6
Param. | Unit | Site independent |  | CERN 2 tunnels |  | CERN 1 tunnel | 
Sqrt(s) | TeV | 3 | 10 | 3.2 | 7.6 | 3.2 | 7.6
L/IP | 1034 cm-2s-1 | 1.8 | 17.5 | 2 | 10 | 0.9 | 7.9
Int L | ab-1 | 1 | 10 | 1 | 10 | 1 | 10
Accumulation time | years | 2+2.8 | 2+2.9 | 2+2.5 | 2+5 | 2+5.6 | 2+6.3
C | km | 4.5 | 11.4 | 4.8 | 8.7 | 11 | 11
Bdipole | T | 11 | 14 | 11 | 14 | 4.8 | 11
Collider dipole technology |  | Nb3Sn | HTS | Nb3Sn | HTS | NbTi | Nb3Sn or HTS
Accumulation time: Time to obtain the integrated luminosity with two IPs.
Ramp-up over the first three years 5%, 205%, 70% of nominal.

## Slide 7: Muon Collider CTEs
7
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
- Proton pulse accumulation and compression
- Graphite target
- Target solenoid
- Muon cooling design
- 6D cooling solenoids
- 6D cooling RF cavities
- Final cooling solenoids
- Pulsed magnets and
power converters
- RCS RF system
- Collider ring dipoles
- Final focus quadrupoles
- Machine-detector interface
- Neutrino flux
Identified and prioritized with community
Other areas need now also to be addressed
(some work started)

## Slide 8: Site
Challenge:
Obtain negligible neutrino flux
Achieved:
Detailed modelling
First good orientation found
Mover system concept
FLUKA and RP studies
Mover system design
Arc mitigation concept
Site study at CERN for experimental insertion
Key conclusions:
Are close to a solution
More work to be done
Fermilab site study
t1
t2

## Slide 9: Physics and Detector Concepts
Two detector concepts are being developed
MUSIC
(MUon Smasher for Interesting Collisions)
MAIA
(Muon Accelerator Instrumented Aperatus)

## Slide 10: Beam-induced Background
Challenges:
Muon decay can give important background
40 000 muons/m/bunch crossing
1/3 of energy in electrons and positrons
Detailed studies with FLUKA
Conclusions:
Can do the physics
  Also thanks to HL-LHC technology
But room for improvement
Radiation level similar to HL-LHC
Achievements:
Two conceptual detector designs
Simulation studies with background also from machine
Studies of different lattices
Reconstruction algorithms
Physics studies

## Slide 11: Proton Complex
Challenge:
2 MW, 5 GeV, 5 Hz,
5 x 1014 protons/pulse
Proton pulse accumulator and compressor rings
Achieved:
Accumulator and combiner ring lattices
First collective effects studies promising
One or two bunches in compressor, to be decided
Key conclusions:
Can compress 2 MW, 5 GeV proton beam to two 2 ns bunches, then merge them
  Optimisation in compressor ring for collective effects ongoing
For 4 MW need 10 GeV beam
Cool beamline to avoid ion loss from black body radiation

## Slide 12: Target
Achieved:
Initial 2 MW graphite target conceptual design, pion yield optimised
HTS solenoid and shielding concept developed
Study of proton removal ongoing
Challenges:
2 MW, 5 Hz, 400 MJ/pulse target
Can we replace mercury with graphite?
Key conclusions:
Yield, magnet shielding, target stress, cooling, radiation are OK
Components survive 2 MW beam
Higher power alternatives to study:
  Graphite
  Liquid metal

## Slide 13: High-field Magnet Technology
NbTi (niob-titanium, operating at 2-4 k)
is standard, used in LHC limited to O(8 T)
Nb3Sn (niobium-tin, operating at 2-4 K)
Can reach O(16 T)
Difficult technology, needs to mature further
Expensive
Used in some points for HL-LHC
Foreseen for FCC-hh also in arcs
HTS (high-temperature superconductor, operating up to 20 K)
Different options exist, e.g. REBCO
In solenoids > 30 T demonstrated
Still expensive and technology challenges
Applications in other fields, e.g. medical, fusion reactors, power generators for wind energy, engines, …
Cut through a cable with superconductor embedded in copper, so some remains conductivity in case of a quench
REBCO Tape
Superconducting magnets reach highest fields, three main technologies for the cables

## Slide 14: Magnets
14
20 T large aperture target solenoid
6D cooling solenoids
- Pulsed magnets and
power converters
14 T, 14 cm HTS collider ring dipoles
40 T small aperture final cooling solenoids

## Slide 15: Muon Cooling Lattice Design
better
better
Previous design (MAP)
Goal
Achieved
Challenge:
Novel, complex lattice with cavities and absorbers in solenoids
Achieved:
Much improved lattice design
Improved simulation tools: BDSIM and RFtrack
Key conclusions:
Can in principle reach or exceed performance target
Much improved longitudinal, may be useful for collider ring
Study of collective effects important

## Slide 16: Muon Cooling Technology
MAP proved gradient
Initial RF designs
More RF design ongoing
Challenges:
NC RF cavities in magnetic field (30 MV/m)
HTS magnets (up to 40 T in final cooling)
Bright beam hard on absorbers and windows
  Can evaporise liquid hydrogen
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
First window tests performed with protons
Use of H2 gas where required
Key conclusions:
Ready to ramp-up effort, in particular prototyping and experimental work, also beamdynamics

## Slide 17: RCS Designs
Key conclusions:
1.3 GHz TESLA-type cavities work
Emittance transport is OK
Cost and power is OK
Need to connect to initial linacs
Achieved:
Lattices for all site independent RCSs
Beam propagation through complex
Conceptual design of magnets and power converters
Optimised design together with RF
Challenge:
Uses fast-pulsed normal magnets
5 Hz pulses of O(1-10ms)
6-35 km circumference
Cost
Recover energy from magnetic field
High bunch charge
Maintain beam quality
RCS | E [J/m] | Loss [%] | P [MW]
SPS 1 | 5447 | 1.1 | 1.9
LHC 1 | 5678 | 1.6 | 12.8
LHC 2 | 5752 | 6.3/2 | 26.6

## Slide 18: Collider Ring
Key conclusions:
Should improve energy acceptance should somewhat
OK with energy spread predicted in muon cooling
Mover system does not compromise beam in regular arcs
Achieved:
Magnet shielding design
Magnet conceptual designs
Cryogenics concept
Lattice reaches target beta-functions but not yet full target energy acceptance
First studies of mover system impact on beam
Challenges:
500 W/m loss, magnet strength, lattice design with beta 1.5-5 mm, 0.1% beam energy spread
Cryogenic loads at different temperatures
Shielding (30-40 mm)

## Slide 19: Site Specific Designs
Started studies for concrete site at CERN and Fermilab, looks very promising
Fermilab:
One RCS in Tevatron tunnel,
three RCS in one site-filler tunnel
CERN:
One RCS in SPS and two in LHC
Construct facility on CERN land
Adjusted parameters (3.2 and 7.6 TeV, 10 TeV maybe possible)

## Slide 20: Cost and Power Scale
Design of many collider areas/components has progressed
but uncertainties remain
No overall optimisation
HTS cost model
Power estimate based on conceptual designs and scaling from know components, e.g.
Simulations of fast-ramping magnets and power converter
Detailed scaling for RCS cavities

## Slide 21: Timeline and R&D Programme Proposal
Timeline is driven by R&D
Most ambitious example to define R&D programme priorities
Muon collider next flagship after HL-LHC
Other options
In Europe after a higgs factory
In the US to become leader at the energy frontier
R&D timeline drivers
Superconducting magnets
  Collider ring with no HTS dipoles for first stage
Muon cooling demonstration
  RF cavities, solenoids, absorbers, integration, demonstration with beam
Decision on demonstrator
Initial final demonstrator

## Slide 22: R&D Plan Deliverables and Resources

## Slide 23: Muon Cooling Demonstrator
Key conclusions:
Installation of demonstrator at CERN appears possible with limited cost (O(10kW)) proton beam
Expensive solution with O(80 kW) would allow future upgrade
Fermilab has approved a study
RF test stands are critical and urgent
Consistent with implementation timeline
Achieved:
Defined the scope and concept, made initial cost estimate, investigated three promising locations at CERN
Staged timeline to implement demonstrator
SLAC is moving forward building a 3/1.3 GHz test stand
Challenge:
Demonstrate muon cooling technology in stages
Critical for timeline
Construction
Project
preparation
R&D plan

## Slide 24: Magnets
24
Normal-conducting RCS pulsed magnets
HTS pancakes 4 mm tape
HTS final cooling solenoid mechanical design
First HTS winding tests
Target HTS solenoid
Achieved:
Systematic dipole/solenoid performance prediction (LTS and HTS)
  Aperture, field, cost, stress, loadline, protection, …
HTS solenoid designs (6D cooling, final cooling, target)
Normal-conducting fast-pulsed dipoles (HTS as alternative)
Technically limited R&D timeline developed
REBCO, 20 K
MuCol HTS conductor
Operating current: 61 kA
Did adjust collider ring field
Key conclusions:
Design work is basically done
Opportunity to ramp up effort (engineering designs, building models, …)
With sufficient resources HTS solenoids and Nb3Sn dipoles could be ready for decision in 10-15 years, consistent with implementation timeline
HTS dipoles likely take longer

## Slide 25: Way Forward
Continue to execute the Design Study
Defined R&D plan, with deliverables and resources estimates for the next 10 years
Identify resources, sharing of work between partners
Synergy with other particle physics and accelerators
Muons, neutrinos, …
Strong synergy with societal applications exist
HTS magnets for fusion reactors, wind power generators, motors, material science, health applications
Power converter
RF in magnetic field can be relevant for fusion
…
Design of 10 MW HTS wind generator
Early career experts are very motivated by the required and possible innovations
Examples:
Collaboration on target solenoid/fusion with F4P, ERUOFusion, GaussFusion, ENI
Common EU request with Infineon for power converter

## Slide 26: Conclusion
Muon collider has a compelling physics case
R&D progress is increasing confidence that the collider is a unique, sustainable path to the future
Much improved design, no showstopper identified, but more work to be done
Need to ramp up the momentum globally
Full start to end modelling
Actual hardware development
HTS solenoid and other magnet development
Preparation of the muon cooling demonstrator
Strong synergies with other fields ranging from particle physics to societal application exist
Fusion reactors
High-field solenoids
Power converter
…
Many thanks to the collaboration for all the work
Our web page: http://muoncollider.web.cern.ch
If you want to join: muon.collider.secretariat@cern.ch

## Slide 27: Reserve

## Slide 28: R&D Plan Deliverables and Resources
Totals:
Duration 10 years
Accelerator: 300 MCHF material, 1800 FTEy
Detector: 20 MCHF material, 900 FTEy

## Slide 29: Magnet R&D Impact
L. Bottura

## Slide 30: Practical Examples
Fusion for Energy (ITER EU Domestic Agency)
  Framework agreement and first addendum in final negotiation
  Contribution to the design of the HTS target solenoid, relevant to the central solenoid of DTT
EUROFusion (next step European fusion reactor)
  Framework agreement signed in 2023, first addendum signed in 2024
  Contribution to the design of the HTS target solenoid, relevant to the magnets of a Volumetric Neutron Source proposed as next step in the European fusion strategy
Gauss Fusion (one of the leading EU fusion start-ups)
  Consultancy agreement signed in 2023
  CERN contribution to the design of the LTS/HTS GIGA stellarator magnets, based on advances in the HTS target solenoid
ENI (oil and gas energy giant)
  Framework agreement and first addendum signed in 2024
  Collaboration on the conceptual design and project proposal for the CERN construction of a large bore HTS solenoid (20@20 model coil) relevant to the muon collider and fusion
IFAST-2 proposal to INFRA-2025-TECH-01-02 (CERN, INFINEON, PSI)
  Proposal of fast pulsed power cell + magnet system sent to IFAST-2 coordination for ranking at TIARA
  Industrial interest in rapidly pulsed and large energy/power supplies
L. Bottura

## Slide 31: European Accelerator R&D Roadmap
31
http://arxiv.org/abs/2201.07895
Reviews in Europe and the US found muon collider promising
Requires important innovation
European Strategy for Particle Physics Update (ESPPU) supported muon collider R&D in 2020
CERN Council charged Laboratory Directors Group (LDG) to develop Accelerator R&D Roadmap
Directors of institutes, e.g. INFN Frascati, PSI, DESY, RAL, CERN, …
LDG formed five panels, one on Muon Collider
Muon Collider panel developed an R&D Roadmap with the help of the global community until end of 2021

## Slide 32: Muon Collider Roadmap CT
32
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
- Proton driver
bunch compression
- Graphite target
- Target solenoid
- Muon cooling design
- 6D cooling solenoids
- 6D cooling RF cavities
- Final cooling solenoids
- Pulsed magnets and
power converters
- RCS RF system
- Collider ring dipoles
- Final focus quadrupoles
- Machine-detector interface
Identified and prioritized with community
Other areas need now also to be addressed
(some work started)

## Slide 33: MuCol Timeline
LDG anticipated input to next ESPPU by 2026
The ESPPU has been advanced to early 2025
2026
2024
2025
2023
2027
ESPPU submission
ESPPU recommendation

## Slide 34: Muon Cooling Challenges
34
Energy loss = cooling
Multiple scattering = heating
High field solenoids minimise beta-function and impact of multiple scattering

## Slide 35: ESPPU Submission March 2025
Collaboration produced ESPPU input:
Short, ten-page report (10p)
Addendum to answers specific questions from ESPPU (18p)
Back-up document (406p, 450 signatories)
  Assessment of collider status based on progress of R&D
  R&D Plan
  Final polishing is ongoing, you Urgently sign up to support

## Slide 36: IMCC International Muon Collider Collaboration
36
Roadmap: http://arxiv.org/abs/2201.07895
Develop high-energy muon collider as option for particle physics:
Implement globally defined accelerator R&D roadmap (2022) to justify CDR phase
Mid-term roadmap review found 75% of goal achieved
Provided ESPPU with
Assessment of muon collider concept, technologies and work progress
An R&D plan for the next 10 years
Implementation considerations (including site, timeline, …)
Back-up document (406p, 450 signatories)
Will inform other strategy processes
Focus on feasibility of 10 TeV with 10 ab-1 (site independent)
Explore initial stage by 2050, maybe around 3 TeV with 1 ab-1 or lower luminosity 10 TeV
Explore implementation at specific sites reusing infrastructure
Param. | Unit | 3 TeV | 10 TeV
L/IP | 1034 cm-2s-1 | 1.8 | 17.5
Int L | Ab-1 | 2.2 | 1.8
fr | Hz | 5 | 5
C | km | 4.5 | 11.4
Bdipole | T | 11 | 14
Collider techn. |  | Nb3Sn | HTS

## Slide 37: Muon Cooling Technology
MAP proved gradient
Initial RF designs
More RF design ongoing
Challenges:
NC RF cavities in magnetic field (30 MV/m)
HTS magnets (up to 40 T in final cooling)
Bright beam hard on absorbers and windows
  Can evaporise liquid hydrogen
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
40 T final cooling solenoid conceptual designs exist
55 T might be possible
Key conclusions:
Ready to ramp-up effort, in particular prototyping and experimental work, also beamdynamics
First window tests performed with protons
Use of H2 gas where required

## Slide 38: Muon 6D Cooling Cell
Key conclusions:
Key challenge is force from magnetic field
Concept to connect flanges developed
Iterations to improve overall and components design also considering beam dynamics is required/ongoing
Conceptual design ready in a few months
Achieved:
Cooling cell engineering design almost ready
Solenoid models for use in beamdynamics optimisation
Challenge:
Integrated 6D cooling cell
HTS solenoid designs
STEP 6: Connect 6x Coils with pins (half Cold Mass)
L. Rossi et al.
L Bottura et al.

## Slide 39: RCS Designs
Key conclusions:
1.3 GHz TESLA-type cavities work
Emittance transport is OK
Need to connect to initial linacs
Achieved:
Lattices for all site independent RCSs
  Strong synchrotron motion
  Including hardware specifications
Beam propagation through complex works
Challenge:
Uses fast-pulsed normal magnets
5 Hz pulses of O(1-10ms)
6-35 km circumference
Cost and power efficient acceleration
High bunch charge
Maintain beam quality
Lattice: A. Chance et al.
Long. dynamics: H. Damerell et al.
RF: Alexej Grudiev et al.
Power converter: F. Boattini et al.
Magnets: L. Bottura et al.

## Slide 40: Fast-ramping RCD Dipoles
Key conclusions:
High recovery efficiency for RCSs (98-99%)
Ready for experimental optimization/models/protoypes
Achieved:
Conceptual design of magnets and power converters
Optimised design together with RF
Power converters can switch sign of magnets without changing direction of voltage on capacitors
Challenge:
Fast ramping normal magnets (1-10 ms) with efficient energy recovery in power converter (200 MJ stored in magnets)
RCS | E [J/m] | Eiron [J/m] | Ecopper [J/m] | Loss [%] | P [MW]
SPS 1 | 5447 | 10 | 52 | 1.1 | 1.9
LHC 1 | 5678 | 9.2 | 80.6 | 1.6 | 12.8
LHC 2 | 5752 | 63.4 | 298 | 6.3/2 | 26.6
Energy in magnets, losses per cycle and total power at 5 Hz including cooling
Power converter: F. Boattini et al.
Magnets: L. Bottura et al.

## Slide 41: Collective Effects
Key conclusions:
Impedances in RCSs and collider ring can be taken care of by design
Beam-beam can be handled by 20 turn feedback
Resistive wall in muon cooling is OK
Further key detailed studies: beam loading, longitudinal and transverse space charge in 6D cooling, impedance of cooling absorbers
Achieved:
Initial studies for proton complex
Assessed impedances (beam screen and RF cavities) in RCSs and collider ring
  Studying counter-rotating beam impedance
Studies started on muon cooling
Goal:
Identify collective effects intensity bottlenecks

## Slide 42: Lattice Designs
42
Lattice design is progressing well

## Slide 43: Collider Ring Magnets
Challenge:
High-field collider ring magnets with large aperture
Key conclusions:
Dipoles appear feasible:
  NbTi at 4 K, 4.8 T, 16 cm aperture
  Nb3Sn at 4 K, 11 T, 16 cm aperture
  HTS at 20 K, 14 T, 14 cm aperture
Quad in dipole best combined solution
Experimental programme is now essential
Achieved:
New method developed to identify field limit, depending on technology, temperature, cost, aperture, considering current, stress and protection (quadrupoles, dipoles, combined function magnets)
Different conceptual dipole designs (block coil, cos-theta)
Combined function design ongoing