## Slide 1
Measurement of Muon Anomalous Precession Frequency in the Muon Experiment at Fermilab
Yonghao Zeng, on behalf of the Muon collaboration
June 10, 2025 | WIN 2025 | University of Sussex, Brighton, UK

## Slide 2
Final Results of Muon g-2 from Fermilab
All datasets have been fully analyzed
Run-4/5/6 result announced at Fermilab on June 3rd 2025
Perfectly consistent with previous measurements
Most precise determination of with 127 ppb accuracy
Presented in the previous talk by Joe Price

## Slide 3
Outline
Anomalous precession frequency measurement at FNAL
  Principles
  Analysis flow
Analyses combination
Systematic uncertainties
Summary
B

## Slide 4
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum

## Slide 5
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum

## Slide 6
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum

## Slide 7
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum

## Slide 8
Spin Precession in a Magnetic Storage Ring
Master Formula
,
Magic Momentum
This talk
Next talk by René Reimann

## Slide 9
Principle of Measurement
Weak decay violates parity symmetry
  Positrons are preferentially emitted along the direction of anti-muon spin

## Slide 10
Principle of Measurement
Positron energy spectrum encodes muon spin-momentum correlation
  The most energetic positrons are those emitted along the muon’s momentum

## Slide 11
Principle of Measurement
Positron energy spectrum encodes muon spin-momentum correlation
  The most energetic positrons are preferentially emitted along the direction of muon spin

## Slide 12
Principle of Measurement
We measure the energy and time of decay positrons
signal is encoded in the wiggle plot:
Time-modulation of energy spectrum

## Slide 13
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
E, t
E’, t’
Pilup only
Reconstruction

## Slide 14
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Enhancing statistical power through asymmetry-weighted events
T-methed
  A(E) = 1
  With a threshold of 1.65 GeV
A-method
  Extract A(E) from energy bin scan (50 MeV bin size)
  With a lower cut of 1 GeV

## Slide 15
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Simple 5-parameters model only captures the exponential decay and oscillation
Must account for beam oscillations, detector effects and muon losses

## Slide 16
Coherent Betatron Oscillation (CBO)
CBO enters the data through coupling between detector acceptance and muon decay position. It dominated Run-1/2/3 systemactic uncertainty
Beam Motion
Detector Acceptance
Distorted Wiggle Plot

## Slide 17
Coherent Betatron Oscillation (CBO)
A radio-frequency (RF) was applied to the electrostatic quadrpole plates to suppress CBO effect in Run-5/6
New!
No Additional RF on ESQ
Additional RF on ESQ
CBO enters the data through coupling between detector acceptance and muon decay position. It dominated Run-1/2/3 systemactic uncertainty

## Slide 18
Coherent Betatron Oscillation (CBO)
A radio-frequency (RF) was applied to the electrostatic quadrpole plates to suppress CBO effect in Run-5/6
New!
CBO enters the data through coupling between detector acceptance and muon decay position. It dominated Run-1/2/3 systemactic uncertainty
The CBO-induced bias: 1.7 ppm (Run-2)  0.1 ppm (Run-xyRF)
CBO-induced bias as a function of fit start time

## Slide 19
Coherent Betatron Oscillation (CBO)
VS.
A large CBO (thus a large bias) that can be well modeled, vs. a small CBO (thus a small bias) that is harder to model accurately
No-RF
RF
CBO separation via sliding window technique

## Slide 20
Coherent Betatron Oscillation (CBO)
Non-parametric approaches developed: Gaussian Process Regression (GPR), Spline
New!
GPR
Spline
A large CBO (thus a large bias) that can be well modeled, vs. a small CBO (thus a small bias) that is harder to model accurately

## Slide 21
Residual Slow Effect
Time-dependent phase change leads to a bias:
The detector effect because of SiPM gain sag
Gain Correction in Run-1/2/3:
  In-Fill Gain (IFG): caused by initial flash
  Short-Term Double Pulse (STDP): caused by single pulse
Energy-dependent Phase
IFG, recovery time ~
STDP, recovery time ~
Early-to-late

## Slide 22
Residual Slow Effect
Still remained in Run-4/5/6
20 ppb ~ 40 ppb effect on , 10 ppb ~ 20 ppb uncertainty
New!
Identified: Intermediate-Term Double Pulse (ITDP)
  Similar to STDP, but longer time scale, recovery time ~
  Specialized hardware study

## Slide 23
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Simple 5-parameters model only captures the exponential decay and oscillation
Must account for beam oscillations, detector effects and muon losses
The function expands to between 7 and 50 parameters

## Slide 24
Analyses Combination
Acquisition clocks are hardware blinded, analysis is software blinded
Four major datasets based on the presence or absence of RF: Run-noRF, Run-xRF, Run-5xyRF, and Run-6xyRF
5 analysis groups, 20 methods in total
7 analyses are used in the average

## Slide 25
Systematic Uncertainties
With respect to Run-2/3:
  Largest uncertainties are still CBO and Residual Slow Effect
  Rest of the systematics are stable over datasets
  Total systematic uncertainty for Run-4/5/6 is 30 ppb with 114 ppb statistical uncertainty

## Slide 26
Summary
The most precise determination of is given with an unprecedented precision of 124 ppb
I’ve presented the analysis flow of and improvements on CBO and Residual Slow Effect
Next, you will hear about magnetic field measurement from René Reimann

## Slide 27
THANK YOU FOR YOUR ATTENTION!
collaboration meeting @ July 2023, Liverpool, UK

## Slide 28
Backup

## Slide 29
Muon g-2 Experiment at Fermilab
8 GeV protons on target for pion production
Transport line for collection from decay
stored in a magnetic storage ring
Presented in the previous talk by Joe Price

## Slide 30
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum

## Slide 31
Calorimeters
24 calorimeters uniformly placed around the inner side of the storage ring
Each calorimeter has 6x9 PbF2 crystals coupled with SiPMs
SiPMs collect Cerenkov light from decay positrons
Extract energy and time from pulse fitting

## Slide 32
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
E, t
E’, t’
Pilup only

## Slide 33
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Raw Data
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
Raw ADC pulses are fitted with empirical pulse templates. Each positron generates a pulse in one or more SiPMs
Two approaches:
  Local fitting: ﻿fit each individual crystal pulse separately
  Global fitting: fit ﻿multiple crystal traces ﻿simultaneously
E, t

## Slide 34
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Raw Data
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
1296 SiPMs are time aligned with a laser pulse sent before beam injection, with ~50 ps accuracy
E, t’
Beam Injection
End of Beam
Sync Laser
Time

## Slide 35
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Raw Data
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
1296 SiPMs gain are calibrated by Laser Calibration System in different time scale
E’, t’
Beam Injection
End of Beam
Sync Laser
In-Fill Laser
Out-of-Fill Laser
Time

## Slide 36
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Raw Data
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
Cluster SiPM pulses into individual positron candidate for Local approach
Time resolution as a function of cluster energy
Goal: reduce the dead-time of clusters, thus reduce pileup events
Considered energy-dependent resolution
Reduced the level of pileup by a factor of four

## Slide 37
Analysis Flow
Data Acquisition
Reconstruction
Data Weighting
Wiggle Fitting
Raw Data
Pulse Fitting
Time Correction
Gain Correction
Clustering
Pileup Correction
Pileup occurs when two or more positrons arrive too close in time/space
Empirically construct pileup spectrum from data
Pilup only
Trigger
Shadow
P(ileup) = T+S

## Slide 38
A-method Weights
Optimal:

## Slide 39
Sliding Window for Individual Calorimeter

## Slide 40
Intro to GPR
A Gaussian Process is a collection of random variables (indexed by continuous time or space), of which, any finite number have a joint Gaussian distribution
Regression is described as given some observed data (training dataset), finding a function that represents the data as close as possible, then using the function to make predictions at new data points
A GP can help to make predictions, by inputing the prior assumption and observed data, then generating posterior prediction

## Slide 41
GPR
Alpha-beta representation: model and  model and
A Gaussian Process is a collection of random variables (indexed by continuous time or space), of which, any finite number have a joint Gaussian distribution.
200 bootstrap wiggle plots provide 200 times sliding window fits. Each specific sliding window point has a Gaussian distribution, and joint distribution between points follow a joint Gaussian distribution.

## Slide 42
Evidence of residual slow term:
The fitted muon lifetime will drift with energy and fit start time
In Run-4/5/6, we found that most residual slow term are caused by the Intermediate-Term Double Pulse (ITDP effect).
Short-term double pulse (STDP) effect: caused by single pulse, recovery time ~15 ns
In-fill gain (IFG) effect: caused by initial flash, recovery time ~6 us
What we have:
What we miss:
Intermediate term double pulse (ITDP) effect: caused by single pulse, recovery time ~6 us (same as IFG)
Residual Slow Effect

## Slide 43
Validation and measurement of residual slow effect
Specialized hardware study
for measuring the ITDP effect (gain sag amplitude and recovery time).
Laser gain monitor data
Use existed in-fill laser data to validate the hardware measurement result
dataset | (correction on/off, in ppb) | Systematics (in ppb)
noRF | 38.5 | 20.6
xRF | 38.7 | 19.2
xyRF-5 | 35.3 | 16.8
xyRF-6 | 27.3 | 11.0
dataset |  | Systematics (in ppb)
noRF | 38.5 | 20.6
xRF | 38.7 | 19.2
xyRF-5 | 35.3 | 16.8
xyRF-6 | 27.3 | 11.0
Summary of residual slow term correction effect on and systematics uncertainty.
Systematics uncertainty
Residual Slow Effect

## Slide 44
Dependency on Energy
Gain sag mostly occurs at early-time
High energy events are underestimated: low energy event becomes more, high energy event becomes fewer

## Slide 45
Muon Losses
Muon Losses: a fraction of muon drifts out of storage ring over time and hit multiple calorimeters

## Slide 46
Mutiple Parameters

## Slide 47
Consistency Checks
Calo Scan
Start Time Scan
Energy Bin Scan

## Slide 48
Spin Precession in a Magnetic Storage Ring

## Slide 49
Spin Precession in a Magnetic Storage Ring
Lab Frame
Rest Frame
Rate of spin precession with respect to momentum