## Slide 1
Optoelectronics & Microelectronics
CERN’s unique know-how derived from years of designing, testing and installing microelectronics exposed to harsh environments.
Notes: 1988- creation of microelectronics group
most exposed to harsh environment?

## Slide 2: CERN’s unique position
Design and integration of high performance and extreme radiation tolerant ASICs and optoelectronic modules
Long history of pushing the limits of mixed-mode circuit design for large detector systems
Broad range of testing and qualification capability for radiation hardness of ASICs and optoelectronic modules
Notes: In university they are developping thing just one channel to write a paper where we want to develop a system .
Pushing limit of a full system, operationnal in a large system.

## Slide 3
Time tagging resolution
Number of rad-hard chips installed in the LHC
Low power density
Extremely radiation tolerant
Opto & Micro-electronic know-how at CERN
Up to G-rad
<100mW/
cm2
≫ 1M
~ 10ps

## Slide 4
Lorem ipsum
Key competence: Radhard electronics
To withstand the level of radiation present in the collision points, unique expertise designing and integrating high performance and extreme radiation tolerant ASICs has been built. Broad range of testing and qualifying capability for radiation hardness of ASICs. Designed in large collaborative team
what
tech specs
Hands-on radhard design competences
 Know-how to accelerate your radhard design
Operating fast and large complex systems composed of thousands of components in ns time precision
 Know-how in building large, ultra fast systems
Access to a large database and network of qualified COTS
 Know-how of many radhard components / suppliers
apps
added value
Medical imaging
Hadron therapy beam monitoring
Non-destructive testing
Aerospace
Nuclear facilities
Expertise on the full range of effects induced by radiation:
  TID Total Ionising Dose on ASICS behavior
  Single event effects
  Displacement damage
Radhard by design using standard technologies
Expertise in the testing procedures
Selection and qualification of COTS (Commercial Off-The-Shelf)
Notes: Design of rad hard hybrid pixel detectors
Design of rad hard monolithic detectors
Design of rad hard optical links
Design and integration in complex systems including Front-End electronics, mechanical structure and cooling devices
deep

## Slide 5
Lorem ipsum
Key competence: Mixed-mode electronics
At CERN, we need our chips to be extremely reliable (several years of continuous operation) and low maintenance (difficult to access when installed). Therefore, designers are pushing the limits of mixed-mode circuit design for large detector systems with 100 millions of parallel operation channels requiring ns timing synchronisation.
what
tech specs
Vast experience with use of mixed-mode electronics in closed and extreme harsh environments
 Know-how on operation of fast systems exposed to radiation
Experience with use of multi channel operation designed for minimum maintenance
 Know-how for robust integration and design
apps
added value
Medical imaging
Hadron therapy beam monitoring
Non-destructive testing
Aerospace
Nuclear facilities
4 large CERN experiments using mixed mode circuits that proved to work continuously for already 12 years under high radiation with minimum maintenance.
Power constraints (<100mW/cm2)
ns time precision moving to 100 ps time precision
Micro spatial resolution
Notes: Nino-hptdc
fastIC- PicoTDC
100millions of channels
Design of rad hard hybrid pixel detectors
Design of rad hard monolithic detectors
Design of rad hard optical links
Design and integration in complex systems including Front-End electronics, mechanical structure and cooling devices
deep

## Slide 6
Lorem ipsum
Key competence: Monolithic pixel chips design
what
tech specs
apps
added value
Proton Computed Tomography
Particle track reconstruction for space studies
High speed imaging for low energy X-ray
Monolithic Active pixel Sensors detectors are high granularity tracking detectors, which provide unambiguous and precise hit information in the harsh environment close to the interaction point. The sensitive volume and part or the full readout circuitry is combined in ONE piece of silicon.
Sensor design:
  Timing resolution ns
  Radhard: TID 10s of Mrad
Circuit design:
  Low consumption: 20nA /ampli
Read out architecture:
  High rate: Mega counts /mm2/sec
Practical, solution oriented know-how
 You safe time in implementation of new pixel chips
Know-how of integration of sensors and circuits
 Leverage CERN know-how to help simplification and
cost reduction of your detector designs.
Notes: Temps de reaction très rapide.
Suggestion de modifs dans la techno
Know-how pour concevoir les capteurs HEP, réaction très rapide à la touche de particle et genere charge à l’interieur de la surface
Conception du capteur: Tcad et aussi Magdalena Muncker (CLIC) pour simulations
Conception du circuit
Architecture de lecture
Construction d’u système complet de plusieurs metres carrés
Combinaison MAPS + lecture de type Medipix? Exemple capteurs en technos 45nm et read out en 65nm cf présentation Fossum

## Slide 7
Lorem ipsum
Key technology: Robust DCDC converters
At CERN, we need DCDC converters in places with high magnetic fields and high radiation levels. Therefore we design and manufacture fully integrated magnetic field and radiation tolerant DCDC Point-Of-Load (POL)converters, enabling distribution at a higher voltage and lower current inside the detector.
what
tech specs
DCDC converters designed to operate in magnetic and/or radiation environments
 Increase reliability and robustness
Fully integrated, compact, high density designs
 Suitable for applications with limited space
apps
added value
Power distribution where radiation and magnetic field tolerance is required such as: Avionics, Space, Safety, Medical equipment, Electric transportation
Input voltage 2.5 or 12V
Continuous 4A load capability
Switching frequency in the range of 1 to 4 MHz
Synchronous Buck topology with continuous mode operation.
High bandwidth feedback loop for good transient performance.
Radiation tolerant:
      TID upto >200Mrad(Si).
      Displacement damage up to 2e15 N/cm2
      Single event effects immunity
Notes: (smaller cables)
Bpol2v5 en prototype.
Photo FEAST et bPOL
Additionl specs:
Protection Over-Current (OVC) and Over-Temperature (OTP).
Protection Input Under Voltage Lock Out(ULVO).

## Slide 8: DC-DC Converters A radiation and magnetic field tolerant DC-DC Point-Of-Load (POL) enables distribution at higher voltage with local on-detector conversion to the voltage required by the electronics, considerably decreasing the current in the cables.
bPOL12V
Input voltage 5.5 to 12 V
Continuous 4 A load capability
Adjustable switching frequency 1-3 MHz
Synchronous Buck topology with continuous mode operation
High bandwidth feedback loop (150 kHz) for good transient performance
Protection Over-Current (OVC) and Over-Temperature (OTP)
Protection Input Under Voltage Lock Out (ULVO)
Radiation tolerant: TID up to >150 Mrad(Si)
bPOL12V also available as a standalone licensable ASIC
APPLICATIONS
Point Of Load in distributed power systems where either radiation tolerance or magnetic field tolerance, or both, are required.
bPOL48V
Input voltage 17 to 48 V
Output current up to 10 A
Integrated 5 V and 12 V regulators for the power stage
Adjustable switching frequency 0.5-3 MHz
High bandwidth feedback loop (100 kHz) for good transient performance
Protection Input Under-Voltage Lock Out (ULVO) and Over-Temperature (OTP)
Radiation tolerant: TID up to > 50 Mrad(Si)
GaN-based power stage (also available as a standalone licensable ASIC)
APPLICATIONS
Point Of Load in distributed power systems where radiation tolerance is required.

## Slide 9
Lorem ipsum
Key technology: High speed optical links
In CERN experiments, inner tracking detectors require low-mass, high speed radiation tolerant optical links to read out data from the detectors and to send synchronisation signals and commands to the detectors.
what
tech specs
Compact
 Suitable where little space is available
Radhard
 Designed for harsh environment
High speed:
 Transfers large amount of data
apps
added value
Aeropsace
Safety
Nuclear power plants
Rad hard: 1MGy total dose
Wide temperature range :−35°C to 65°C
Fast and bi-directional:2.56 Gb/s in the downstream towards the detector; and 5.12 or 10.24 Gb/s in the upstream away from the detector
Compact optical transceiver : 1transmiter and up to 4receivers
  20 mm x 10 mm x 2.5 mm
Notes: Versatile link name of the module
GBT family
Compact
multichannel

## Slide 10
Lorem ipsum
Key Technology: Timing, trigger and control system
apps
added value
In the LHC experiments at CERN, the Timing, Trigger and Control (TTC) system is responsible for delivering the TTC commands from the central processor to the detector sub-partitions. The TTC-Passive Optical Network (PON) project was born from the idea of making use of the well-developed by the telecom industry FTTx/PON technology to propose an upgrade to the current off-detector TTC system, overcoming some of its limitations.
Network:
  Wavelength multiplexing
  Passive network, split ratio up to 1:128
  Network status online monitoring (current, optical power, eye diagram, propagation time)
Downstream:
  ~10Gbps
  Stability < 10ps rms
  Low latency
  BER<10-12
what
tech specs
High Split Ratio
 up to 128 nodes
Very short gaps between upstream frames (25ns)
 maximizing total bandwidth upstream
Extremely stable and robust against line errors
     <10ps rms and Forward Error Correction scheme
Complete Online Monitoring:
 continuous tracking of network status
 predictive maintenance
Telecommunications
Clock Distribution Networks
Upstream:
  Time Domain Multiplexing
  No arbitration
  Short GAP between bursts
  Downstream synchronous
Notes: It consists of a point-to-multipoint Bidirectional optical communication system in which the master can send data at 10 Gbps to up to 128 slave nodes . Upstream, the 2.4Gbps bandwidth is shared by the number of slaves. Each of them having a frame of 125ns (100ns of burst + 25ns of gap).

## Slide 11
Lorem ipsum
Key technology: Medipix chip family
A family of pixel detector read-out chips for particle imaging and detection developed by a consortium lead by CERN. Medipix works like a camera, detecting and counting each individual particle hitting the pixels. This enables high-resolution, high-contrast, noise hit free images. The Medipix chip family aims at frame based imaging and spectroscopic x-ray imaging.
what
tech specs
Colour imaging
 Detect various components
Designed for particle tracking
 Very high resolution
Can be used on wide range of detection devices
 Very broad applicability
apps
added value
Medical imaging
Electron Microscopy
Non-destructive testing
Particle track reconstruction
Charge summing and allocation scheme – mitigating charge sharing
2 thresholds per 55µm pixel each with 5 bits of local adjustment
High gain mode (HG, lower linearity, lower noise) or low gain mode (LG)
Configurable counter depths: 2 x 1-bit, 2 x 4-bit, 2 x 12-bit, 1 x 24-bit
Continuous or sequential data acquisition and readout

## Slide 12
Lorem ipsum
Key technology: Timepix chip family
By using ASICs that can accurately measure time, one can directly reconstruct the 3D track of passing charged particles. Timepix is a family of pixel detector read-out chips for particle imaging and detection developed by a consortium lead by CERN. The Timepix family is designed for detection with nanosec resolution with a data driven architecture (last version).
what
tech specs
Designed for particle tracking
   High resolution
Can be used on wide range of detection devices
 Very broad applicability
apps
added value
Electron Microscopy
Particle track reconstruction
Two main measurement modes: (1) simultaneous 10 bit ToTand 18 bit TOA and (2) 10 bit event counting and 14 bit integral TOT
TOT monotonic for large positive charges
Fast TOA for time stamping with a precision of 1.56 ns
Data driven readout: dead time free, for a maximum hit rate of 40 Mhits/s/cm^2
Shutdown/wake-up features for power pulsing tests on a full system

## Slide 13
 |  |  | Timepix2 | Timepix3 | Timepix4
Tech. node (nm) |  |  | TSMC 130 | IBM 130 | TSMC 65
Year |  |  | 2018 | 2013 | 2019
Pixel size (μm) |  |  | 55 | 55 | 55
# pixels (x x y) |  |  | 256 x 256 | 256 x 256 | 448 x 512
Sensitive area |  |  | 1.98 cm2 | 1.98 cm2 | 6.94 cm2
Number of sides for tiling using WB |  |  | 3 (85.6% active area) | 3 (86.7% active area) | 2 (93.7% active area)
Number of sides for tiling using TSV |  |  | 3 (85.6% active area) | 3 (91.6% active area) | 4 (99.3% active area)
Front-end |  | positive (h+) | High Gain (25mV/kh+) Logarithmic Gain (19mV/kh+) | High Gain (45mV/kh+) (Volcano >0.3MeV/pixel) | High Gain (35mV/kh+) Low Gain (20mV/kh+) Logarithmic Gain
 |  | negative (e-) | High Gain (25mV/ke-) | High Gain (45mV/ke-) | High Gain (35mV/ke-) Low Gain (20mV/ke-)
Minimum detectable charge |  |  | ~600 e- | ~500 e- | ~500 e-
Operation Modes | Tracking (Event arrival time and/or energy) | Readout | Full Frame-based (Sequential or Continuous R/W) | Data-driven (48-bit packet per pixel hit) | Data-driven (64-bit packet per pixel hit)
 |  | Event Data | TOT and TOA; TOT or TOA | TOT & TOA | TOT & TOA
 |  | TOT energy resolution | ~0.75keV (FWHM Si) | ~2KeV (FWHM Si) | ~1KeV (FWHM Si)
 |  | TOA bin size | 10ns (@100MHz) | 1.56ns (On-pixel TDC @40MHz) | 195ps (On-pixel TDC @40MHz)
 |  | TOA dynamic range | 2.62ms (@100MHz) | 409.6µs (14b@40MHz) | 1.63ms (16b@40MHz)
 |  | Max Rate | <1x106 hits/cm2/s | 43x106 hits/cm2/s | 358x106 hits/cm2/s
 |  | Max Pix Rate | 33 Hz/pixel | 1.3 KHz/pixel | 10.8 KHz/pixel
 | Imaging (Event counting) | Readout | Full Frame-based (Sequential or Continuous R/W) | Zero-suppressed (with pixel addr) (Sequential R/W) | Full Frame-based (Continuous R/W)
 |  | Counter depth | 10-bit or 14-bit | Counting (10-bit) or iTOT (14-bit) | 8-bits or 16-bits
 |  | Frame rate | 4.9 kfps @10-bit 32x100Mbps 3.5 kfps @14-bit 32x100Mbps | 1.62 kfps @48-bit 8x640Mbps | 89.2 kfps @8-bit 16x163Gbps 44.8 kfps @16-bit 16x163Gbps
 |  | Max Count Rate | ~35 x 109 hits/cm2/s | ~82 x 109 hits/cm2/s | ~800 x 109 hits/cm2 /s
Maximum Readout bandwidth |  |  | 3.2Gbps (32 x 100MHz) | ≤5.12Gbps (8x SLVS@640 Mbps) | ≤163.84Gbps (16x @10.24 Gbps)
Power consumption |  |  | 450mW/cm2 (nominal) 165mW/cm2 (low power mode) | 625mW/cm2 (nominal) 108mW/cm2 (low power) | 700mW/cm2 (nominal) 200mW/cm2 (low power)
Paper |  |  | https://www.sciencedirect.com/science/article/pii/S1350448719305165 | https://iopscience.iop.org/article/10.1088/1748-0221/9/05/C05013 | https://www.sciencedirect.com/science/article/pii/S0168900222007811
Hybrid pixel detectors were developed to respond to a need at the LHC: particle tracking in high rate environments.
Single particle counting detectors have been widely used in education, space science, materials analysis and X-ray applications

## Slide 14
FastIC+
FastIC (65nm CMOS) is a chip for the read-out of fast radiation detectors providing particle time of arrival and energy information. The chip has applications in medical and biomedical fields, e.g. for
Time-of-Flight Positron Emission Tomography (PET), mass spectrometry or fluorescence detection in biological samples.
Fast Timing
detectors
Front-End
Multi Channel
ASIC
Time-to-
Digital-
Conversion
FastIC (65nm, 2020)
SiPMs, MCPs, PMTs
Multichannel readout ASIC that has incorporated a fast front-end, discriminators and analog signal processing chain and a Time-to-Digital (TDC) with a time bin of 25ps.
Enables compact system integration and low power consumption.
Singled ended, differential & summation of 4 single-ended channels (+/-) to explore benefits of segmentation of detector areas;
Large range of input capacitances;
Large dynamic range (with positive and negative polarity readout).
To the best of our knowledge FastIC+ is the first digital readout ASIC achieving ctr<100ps fwhm
Notes: Technical and financial collaboration between CERN (KT funded) and University of Barcelona (ICCUB) (Grant FPA2016-80917-R)
Technological advancement in detector and Front-End technology
Progress in SiPMs and MCPs
New TDC development @ CERN: picoTDC (~3 ps bin).
FastIC: new Front-End chip in 65 nm CMOS technology
Multipurpose chip: SiPMs, MCPs, etc
Single ended (pos/neg), differential and active summation
Binary (linear / non-linear ToT) and Analog output
First submission scheduled for Q2 2020: 8 channels

## Slide 15
FastIC+
Paper: https://arxiv.org/abs/2506.11655

## Slide 16: PicoTDC
Technology CMOS 65 nm
# Channels 64 or 32 differential channels.
Time binning 3 ps or 12 ps (programmable),
with very low jitter (<1ps) and high stability (~1ps).
Reference 40 MHz
Dynamic range 204 µs (13 bit @ 40 MHz)
Power ~1.5 – 0.5 W
Large on-chip data buffering capability.
Option of triggering with programmable latency and time window.
Support for overlapping trigger windows.
Option of using channel 0 as timing channel and trigger generator channel.
High performance time to digital converter ASIC chip for use in applications requiring precise time-tagging of electronic signals. E.g. electron and photon detection in medical imaging, laser ranging, life science or material research.
Paper:
PicoTDC: a flexible 64 channel TDC with picosecond resolution https://doi.org/10.1088/1748-0221/18/07/P07012
Tech Brief:
https://kt.cern/sites/default/files/technology/picotdc/tech-brief/picotdc_0.pdf