## Slide 1
Characterizing Earth siblings
RISTRETTO/VLT: a demonstrator for PCS/ELT
N. Blind
C. Lovis (PI), B.Chazelas, M. Shinde, I. Dinis, L. Genolet, I. Hughes, M. Sordet, R. Schnell, S. Rihs, A. Crausaz, L. Hoerner, N. Restori, B. Wehbe, J.-R. Delorme, J. Kühn

## Slide 2
© Erwan Le Roux
The lighthouse?
No! The bug flying around!
 Contrast > 108
Is it a firefly? Or a butterfly?
Systems
R&D
Techniques
Science
What we try to do...
We look at…
Notes: THE firefly because we know it is here from its gravitational pull on the lighthouse!

## Slide 3
Spectrograph nearly finished
This is challenging, but the technology is there for 8m class.
So, we build it.
: a demonstrator for PCS/ELT
See Bruno Chazelas poster
Science
PDR
FDR
PAE
SAR
Front-End: system architecture review in Feb. 2026
Science ~ Q4 2031

## Slide 4
NDLR - This is not PCS. PCS does not even have a logo.
Permanent improvement of Technology Readiness Level
Research
TRL1
Basic principle
TRL2
Technological concept
TRL3
Proof of concept
Development
TRL4
Lab validation
TRL5
Validation in relevant environment
TRL6
Demonstration in relevant environment
Deployment
TRL7
Prorototype demo in operationnal environment
TRL8
System complete and qualified
TRL9
System proven in opetration
Scalability
Dx
TRL
PCS/ELT
: a demonstrator for PCS/ELT

## Slide 5
NDLR - This is not PCS. PCS does not even have a logo.
Permanent improvement of Technology Readiness Level
Research
TRL1
Basic principle
TRL2
Technological concept
TRL3
Proof of concept
Development
TRL4
Lab validation
TRL5
Validation in relevant environment
TRL6
Demonstration in relevant environment
Deployment
TRL7
Prorototype demo in operationnal environment
TRL8
System complete and qualified
TRL9
System proven in opetration
Rebound effect
Emerging science
TRL
Technologies
« Industry »
Systems
« Development »
Techniques
« Research »
Science
Scalability
Dx
PCS/ELT
: a demonstrator for PCS/ELT

## Slide 6
Technologies
« Industry »
Systems
« Development »
Techniques
« Research »
Science

## Slide 7
Technologies
Systems
Techniques
Science
High Contrast
High Angular Resolution
Spectroscopy

## Slide 8
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
eXtreme Adaptive Optics

## Slide 9
Technologies
« Industry »
Systems
« Development »
High Contrast
Spectroscopy
Large telescope
eXtreme Adaptive Optics
VLT (8m)
ELT (39m)
Techniques
High Angular Resolution
Notes: Big leap forward
Bigger difference than Hubble vs VLT

## Slide 10
Technologies
« Industry »
Systems
« Development »
High Contrast
Spectroscopy
Large telescope
eXtreme Adaptive Optics
VLT (8m)
ELT (39m)
Techniques
High Angular Resolution
Notes: Big leap forward
Bigger difference than Hubble vs VLT

## Slide 11
Technologies
Systems
Techniques
High Contrast
Spectroscopy
eXtreme Adaptive Optics
Real Time Calculator
Wave Front Sensor
D1-2
D4
Photon-counting, fast detectors
D2
High Angular Resolution
Coronagraph
Integral Field Unit
Optimal
controller
D2
7
5
Deformable mirror
D2
7
3
5
Large telescope

## Slide 12
Technologies
Systems
Techniques
High Contrast
Spectroscopy
Large telescope
eXtreme Adaptive Optics
Deformable mirror
Real Time Calculator
Wave Front Sensor
D1
D2
D4
Photon-counting, fast detectors
D2
High Angular Resolution
Coronagraph
Integral Field Unit
Optimal controller
D2
New Wave Front Sensor on-sky demo
Muskan Shinde talk today@13:45
New optimal controller on-sky demo
Isaac Dinis talk today@14:10
5
5
Concepts demo at PAPYRUS/OHP during summer 2025

## Slide 13
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
Coronagraph
Integral Field Unit
eXtreme Adaptive Optics
eXtreme Adaptive Optics

## Slide 14
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
Integral Field Unit
eXtreme Adaptive Optics
eXtreme Adaptive Optics
Coronagraph
D0-1

## Slide 15
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
Integral Field Unit
eXtreme Adaptive Optics
Micro Lens Array & slicer
Single-mode fiber bundles
Mode selective photonic lantern
Coronagraph
eXtreme Adaptive Optics

## Slide 16
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
Integral Field Unit
eXtreme Adaptive Optics
Micro Lens Array & slicer
2PP 3D printing
Photolitography, etching
Segmented DM
D0
Mode selective photonic lantern
Single-mode fiber bundles
3
5
4
Coronagraph
eXtreme Adaptive Optics
D0

## Slide 17
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
eXtreme Adaptive Optics
Micro Lens Array & slicer
D0
Single-mode fiber bundles
D0
Fiber bundle & V-groove
Multicore fiber
Mode selective photonic lantern
7
6
Integral Field Unit
Coronagraph
eXtreme Adaptive Optics
D0

## Slide 18
Technologies
Systems
Techniques
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
eXtreme Adaptive Optics
Micro Lens Array & slicer
Single-mode fiber bundles
D0
D0
Mode-selective
photonic lantern
D0
3
Multimode to singlemode
multiplexing
Integral Field Unit
Coronagraph
eXtreme Adaptive Optics
D0

## Slide 19
Technologies
« Industry »
Systems
« Development »
Techniques
« Research »
High Contrast
High Angular Resolution
Spectroscopy
Large telescope
Coronagraph
Techniques
« Research »
High Contrast
eXtreme Adaptive Optics
Phase Induced Amplitude Apodizer and Nuller
High transmission, high dispersion coronagraphy at 2λ/D
PIAA: a double aspherical pupil reshapping lens
(similar to a reversed laser beam shaping lens)
IFU: making use of 2-photon polymerization 3D-printing with 100nm accuracy for single-mode fiber coupling
Singlemode fiber bundle
3D printed micro-lens array
T = 70%
Contrast ~ 3x10-5
125um
750um
Star
Planet
Blind et al., A&A, 704 (2025) A141
D0
6

## Slide 20
Technologies
Systems
Techniques
Large telescope
Spectrograph
Spectroscopy
Single-mode fiber
High Contrast

## Slide 21
Technologies
Systems
Techniques
Spectrograph
Single-mode fiber
Detectors & cryogeny
D0
Vacuum
D0
D0
Diffraction element
D0
>5
Ruled grating
Wet etching grating
Volume Phase Holographic
Virtually Imaged Phased Array
e.g. NIGHT
e.g. RISTRETTO
e.g. NIRPS
7
5
7
7
7
7
Spectroscopy

## Slide 22
Technologies
Systems
Techniques
Spectrograph
Single-mode fiber
Detectors & cryogeny
D0
D0
Diffraction element
D0
>5
Ruled grating
Wet etching grating
Volume Phase Holographic
Virtually Imaged Phased Array
e.g. NIGHT
e.g. RISTRETTO
e.g. NIRPS
7
5
7
7
7
Detector unit for astronomical applications at UNIGE --- Ludovic Genolet talk today@16:40
Spectroscopy

## Slide 23
EKARUS@ASIAGO – 2027-…
PAPYRUS@OHP - 2020-03/2026
Research
TRL1
Basic principle
TRL2
Technological concept
TRL3
Proof of concept
Development
TRL4
Lab validation
TRL5
Validation in relevant environment
TRL6
Demonstration in relevant environment
Deployment
TRL7
Prorototype demo in operationnal environment
TRL8
System complete and qualified
TRL9
System proven in opetration
Need for a sky access and an XAO-assisted platform in Europe
5
Science
ADC
PDR
FDR
PAE
Integration of RISTRETTO R&D in EKARUS
7
A. Alagao, B. Neichel, V. Chambouleyron, J.-F. Sauvage, R. Fétick, T. Heritier, T. Fusco

## Slide 26
Manufacture
Characterizing Earth siblings
Coronagraph
D0
Integral field Unit
D0
Large telescope
D2
Real Time Calculator
D4
Deformable Mirrors
D2
Atopsheric Dispersion Corrector
D1
Singlemode Fibers
D0
Spectrograph
D0
Spectroscopy
Detectors
D0
Fast EMCCD
D2
Wavefront sensor
eXtreme Adaptive Optics
High contrast
High angular resolution
Micro Lens Array
D0
Techniques
Science
Systems & hardware
Aspheres
Liquid Crystals
Metasurfaces
Lithography,
Etching

## Slide 27
Requirements driven by Prox Cen b case
8-10m telescope
7-spaxel coronagraphic IFU
620-840nm VIS high-resolution spectrograph
2 λ/D = 37mas
    Mounted on an 8m telescope
    Stand-alone XAO
    Spectrograph: R ~ 135.000, λ=620-840nm
    IFU: 7-spaxels, coupled to Single Mode Fibers
Planet coupling > 50% at 37mas
Contrast coupling < 10-4
Total transmission > 5%
XAO with NIR (850-1800nm) WFSs
3s-pyramid prototype