## Slide 1: European Solar Telescope: A New Frontier for Swiss Science and Technology
Svetlana Berdyugina
IRSOL / USI
Consortium:
USI, IRSOL, FHNW, SUPSI, HEIG-VD, ETHZ/EAWAG, ZHAW, UNIBE, PMOD/WRC, ETHZ/CSCS
Swiss Innovation for Astrophysics and Planetary Science (SIAPS), January 20-22, 2026, Bern

## Slide 2: European Solar Telescope (EST)
Next-generation telescope for the 21st century solar physics
  4.2-m aperture, Gregorian optical configuration
  MCAO, Active M1, Adaptive 0.8m M2, open dome, 44m tall
  Multi-wavelenghth high-resolution spectropolarimetry (7 imaging spectropolarimeters in 4 channels 350–1800 nm)
Roadmaps:
ESFRI Roadmap 2016: EU Research Infrastructure
AstroNet Roadmap 2022-2035: EST is of high priority for ground-based observations (on par with CTA)
SCNAT Astronomy Community Roadmap 2024 Update for 2029-2032: “Participation of Switzerland in EST should be secured.”

## Slide 3: Observatorio del Roque de Los Muchachos, La Palma

## Slide 4: Swiss solar telescope vs EST: “A quantum leap”
IRSOL: 0.45m + Swiss technology EST: 4.2m

## Slide 5: The Sun: Closest star that supports Life on Earth
SDO/HMI 6173 A
GREGOR, 1.5m, 7055 A

## Slide 6: The Dark Energy of the Sun: Magnetic Fields
Jan 18, 2026: X1.9 Flare, lasted 6h!
SDO/AIA 131 A
Jan 19, 2026: G4, Kp=8.7, 24h+

## Slide 7
EST Scientific Goals
1
2
1
3

## Slide 8: Technological Challenges
1. Heat
  4m mirror: ~12 kW
  Heat stop in F1 reduces it to 300 W:
    Reflector: ~98% is rejected (outside FOV)
    Absorber: active cooling by liquid
    T ~ +4C of the ambient level
Chriselle et al. (2022), DKIST, 4m, off-axis

## Slide 9: Technological Challenges
2. Atmospheric Turbulence
  Phase errors of a few micrometers in the optical, within 20 km of the Earth atmosphere
  Single-conjugate AO (CAO): isoplanatic angle of a few arcsec << FOV
  EST Multi-conjugate AO (MCAO): 5 DMs, FOV Ø~1’, res 0.03’’ (~20km on the Sun)
Schmidt D., et al. (2017), BBSO, 1.8m, off-axis

## Slide 10: Technological Challenges
3. Polarimetric sensitivity
  Standard polarimetric precision ~ 0.1%, accuracy > 1%, modulation < 30 Hz
    Induced spurious polarization due to seeing (>100 Hz) and evolution of solar features
  IRSOL’s ZIMPOL polarimetric precision & accuracy ~ 0.001%
    Fast modulation: 42 kHz using FLC or PEM
    Slow modulation: < 1Hz beam swapping using a rotating retarder
    System calibration every ~20 min to remove cross-talks using polarizers and retarders in the beam
4. Sensors for high-precision polarimetry
  Synchronous demodulation on the ZIMPOL CCD (custom electronics & software, SUPSI)
  ZIMPOL for biopharmaceutic studies of chiral enantiomers using polarimetry
    Joint Patent ETHZ & IRSOL (2019)
    NG Sensor – Innosuisse project 2025-2027 by SUPSI, IRSOL, ENANTIOS AG.

## Slide 11: Technological Challenges
5. Multi-Dimensional data
  Multi-dimensional data cubes: [x,y,λ,(I,Q,U,V),t]
  Not all dimensions can be sampled simultaneously
    FPI: Scanning in λ and modulating Stokes (I,Q,U,V)
     fast 2D [x,y] imaging
    SlitSpec: Scanning in x and modulating Stokes (I,Q,U,V)
     fast 2D [x, λ] imaging (or IFU mosaic)
    Evolution of [<I,Q,U,V> at (x,y,λ)]t in t  goal to reduce t

## Slide 12: Technological Challenges
5. Multi-Dimensional data
  Multi-dimensional data cubes: [x,y,λ,(I,Q,U,V),t]
  Not all dimensions can be sampled simultaneously
    FPI: Scanning in λ and modulating Stokes (I,Q,U,V)
     fast 2D [x,y] imaging
    SlitSpec: Scanning in x and modulating Stokes (I,Q,U,V)
     fast 2D [x, λ] imaging (or IFU mosaic)
    Evolution of [<I,Q,U,V> at (x,y,λ)]t in t  goal to reduce t
6. Data rate
  Currently: ~ few TB/day raw data (Level 0), << TB processed data (Level 1: calibration & image reconstruction)
  EST: 1-2 PB/day raw data, ~6-10 ExaB/30yrs  CPU/GPU and storage, AI applications

## Slide 13: Swiss EST Partnership
Consortium:
22 groups (incl 12 Profs) at 10 universities and research institutes / facilities:
USI, IRSOL, FHNW, SUPSI, HEIG-VD, ETHZ/EAWAG, ZHAW, UNIBE, PMOD/WRC, ETHZ/CSCS
Academic Interest:
Swiss groups in space physics, astrophysics, Earth science
Industrial Interest:
CSEM, ARCoptix, Ateleris, Enantios
Collaborators:
MeteoSwiss,
CERN-ESCAPE, SKAO
www.sviss.ch/est/
Swiss Virtual Institute for Solar Science
SVISS

## Slide 14: Swiss Contribution to the EST
D1 - Instrumentation:
TELPOL calibration unit, HPPOL modulators, New Generation Sensor (NGS)
D2 - Swiss Node DC at CSCS: Data management, storage, processing, prototyping,etc.
Telescope Instruments DC

## Slide 15: Thank You!