## Slide 1: Possible remote sensing instruments for the next decades
Nicolas Thomas

## Slide 2: CaSSIS integration at Uni Bern
11.5 μrad/px
18 kg; 17.3 W

## Slide 3
MY36_014886_164
Acquisition: 03/25 Emission: 10.804 Latitude: 18.6196
Filters: PAN-RED-NIR-BLU Loc. Sol. Time: 12:53:10 Longitude: 77.3691
Incidence: 16.015 Ls: 22.31 Near: Jezero crater
Phase: 14.762 Target ID: - Mars2020 – Perseverance rover

## Slide 4
Map of Oxia Planum – the landing site for ExoMars. Unit definition performed using CaSSIS data (inter alia).

## Slide 5: Phobos
Target of JAXA’s MMX

## Slide 6: Comet Interceptor
A joint mission to a dynamically new comet
3I/ATLAS seen from Mars by CaSSIS

## Slide 7: CoCa
Visible camera system
Based on CaSSIS/TGO-JANUS/JUICE heritage
8 m/px from 1000 km
4 colour filter imaging
Framing rate of 1 image/s
Large redundant intermediate storage.
Telescope developed in CH industry.
Elements from D, H, E, (UK).
Stares at a Rotating Mirror Assembly (B and CH industry) to track the nucleus during the fly-by.
CoCa PFM Telescope delivered (Dec. 2025) to UBE

## Slide 8
This is all fine and good but it is old shit…..
…. so where could remote-sensing on planetary exploration missions go in the next 10+ years?
stuff
…. and where could we lead…..:

## Slide 9
Quasi-classical high-resolution imagers and spectrometers
Lightweight near-object systems
Landed systems for (mainly) non-destructive diagnostics
Mars (ZefERO/
CAIMAN)
Enceladus (COLIME)
Small bodies (SUBICE)

## Slide 10
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
Maintaining high resolution imaging capability at Mars is seen as crucial for future manned missions.
Dynamic processes on Mars also require monitoring.
Taking CaSSIS to the next scientific level.
TDI imaging extending into the infrared using a rotating mirror for stereo.
Monolithic mirror structure for improved stability and performance.
Need for substantial onboard pre-processing/compression.
Improve resolution x2
Double the wavelength range
Double the filter discrimination
Triple the swath width
At least x5 stereo coverage
10x the data rate

## Slide 11
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
Monolithic mirrors
Multi-detector FPA
CAIMAN – A concept for a “CaSSIS 2.0”
We are currently looking at developing this concept for the ZefERO mission in ESA/HRE.
Imaging at
2.5m/px in VIS and
7.5m/px out to >=1.9 μm

## Slide 12
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
ILLUMINATI – Nighttime processes
100 km
Dynamic processes on Mars at night and during permanent polar darkness are fundamentally interesting for numerous reasons.
Condensation on Martian volcanoes first detected by CaSSIS.
High power lasers to illuminate surfaces from orbit can allow targeting of specific areas of interest.

## Slide 13
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
Timescale
Next 10-15 years
ILLUMINATI – Nighttime processes
Study by Uni Bern and Beyond Gravity suggests that this is plausible.
SNR budgets are challenging but NOT ridiculous.
3-6 kW CW fibre lasers at 1060-1080 nm for short duty cycles.
  1550 nm and 2 micron lasers are also plausible.
Miniaturization and space qualification needs to be addressed.

## Slide 14
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
Other areas
Ultra-high resolution push-broom imaging (1 microrad) is still beyond what Europe can do for interplanetary flight today. (total instrument mass < 60 kg)
  There are instrumentation problems but also spacecraft stability issues!!
Planetary sciences needs 1-6 micron wavelength (small pixel) detector technologies for interplanetary flight – especially in imaging spectroscopy – CH teams have a real interest here.
HiRISE on MRO is still the state of the art 20 years after launch!
Lynred Snake detector and board from TASCH under test at UBE.

## Slide 15
Quasi-classical high-resolution imagers and spectrometers
CAIMAN – A concept for a “CaSSIS 2.0”
Other areas
LiDARs and high power lasers remain of extreme interest to the atmospheric sciences community.
  Some of the BepiColombo/BELA heritage remains relevant.
UV instrumentation has not been a major priority in Solar System missions in recent years but this might change. (Exoplanet astronomy is pushing this as seen in the Waltzer F-class proposal.)
Sub-mm wave instrumentation is pushed hard in Germany and CH has an interest.
ASIDE: Scientifically a European SAR development for Mars is also attractive.
BepiColombo Laser Altimeter

## Slide 16
CHANCES for RAMSES
Monolithic structure (including electronics)
Lightweight (CFRP + AlBeMet)
Vis-SWIR (InGaAs CMOS)
6 broadband filters (3 Vis, 3 NIR)
Linear polarisation (2 crossed filters)
Adjustable focus (through filter thickness)
400mm FL, 80mm aper., f/#=5, 1° FoV
~ 4 kg, 30x20x20 cm, 20W
Lightweight near-object systems
Specifically constructed for rendezvous imaging and maximizing information return for landing site selection on small bodies.
Launch to Apophis
in 2028

## Slide 17
Future evolution for PRIAMOS
See poster by Marschall, Pommerol et al. (this conference))
Larger field of view or a combined WAC
Continuous refocusing down to ~100s of metres distance
Filters and spectral range adapted to a D-type asteroid
Improved polarisation capabilities
Improved electronics: high cadence, fast compressor (lossless and lossy), on-board storage and processing
One of 10 missions down-selected for phase 2 in ESA’s M8 call
Lightweight near-object systems
Similar system could be envisaged for landing site identification on Enceladus (e.g. COLIME, NF Eagle proposal).

## Slide 18: Miniaturization and Implementation
Landed systems for (mainly) non-destructive diagnostics
There are strong desires in the science community to develop new for flight instrumentation.
There are now programmes available to support this (e.g. OSIP, MARVIS).
Work is on-going to test possible implementations.
Examples include
  THz TDS (see talk by Stoeckli)
  Miniaturized (bore-hole) spectrometers
  Scanning Electron Microscopy
There are challenges in how these devices can be brought to the surfaces/sub-surfaces to be examined.
  There are going to be opportunities to expand our capabilities in these areas.
Why?
Investigation of sub-surface (unprocessed) material to constrain Solar System formation.
Determination of the extent of sub-surface resources for future exploration.

## Slide 19
Quasi-classical high-resolution imagers and spectrometers
Lightweight near-object systems
Landed systems for (mainly) non-destructive diagnostics
Higher spatial resolution, improved discrimination between different mineralogical units, atmospheric remote sensing.
Driving mass down, data transfer/ processing rates up, extending the wavelength range and resolution.
Higher spatial resolution, improved discrimination between different mineralogical units, for landing site identification.
Maximizing performance of R-S systems with max. mass of <=10kg.
Expansion of the palette of diagnostic tools.
Growing knowledge of the properties of planetary surfaces, the sub-surface and local “atmospheres”.