## Slide 1: Superconducting RF for Higgs factories
Kellen McGee
FNAL
September 4, 2025

## Slide 2: Outline
Introduction to superconducting RF
Special SRF considerations for Higgs factories
  SRF for FCC
  SRF for ILC/LCF
  Muon collider

## Slide 3: Introduction to superconducting RF

## Slide 4: Introduction to SRF: theory
(...and practice)
© 2014 CERN: Daniel Dominguez, Arzur Catel Torres
Input RF, excite a resonant EM mode in a cavity
  Ideal case: high accelerating gradient (), with low losses (high quality factor, )
Performance limitations:
  Electric field strength () limited by input power couplers, peak surface fields, leading to field emission, electrical breakdown, or (in SC) thermal quench.
  limited by RF surface losses, , even in superconductors!
    induces an electric field penetrating
    ~40nm for superconducting niobium at 2 K.

## Slide 5: Introduction to SRF: theory
(...and practice)
© 2014 CERN: Daniel Dominguez, Arzur Catel Torres
Input RF, excite a resonant EM mode in a cavity
  Ideal case: high accelerating gradient (), with low losses (high quality factor, )
Performance limitations:
  Electric field strength () limited by input power couplers, peak surface fields, leading to field emission, electrical breakdown, or (in SC) thermal quench
  limited by RF surface losses, , even in superconductors!
    induces an electric field penetrating
    ~40nm for superconducting niobium at 2 K.

## Slide 6: Introduction to SRF: theory
(...and practice)
© 2014 CERN: Daniel Dominguez, Arzur Catel Torres
Input RF, excite a resonant EM mode in a cavity
  Ideal case: high accelerating gradient (), with low losses (high quality factor, )
Performance limitations:
  Electric field strength () limited by input power couplers, peak surface fields, leading to field emission, electrical breakdown, or (in SC) thermal quench
  limited by RF surface losses, , even in superconductors!
    induces an electric field penetrating
    ~40nm for superconducting niobium at 2 K.

## Slide 7: Introduction to SRF: theory
(...and practice)
© 2014 CERN: Daniel Dominguez, Arzur Catel Torres
Input RF, excite a resonant EM mode in a cavity
  Ideal case: high accelerating gradient (), with low losses (high quality factor, )
Performance limitations:
  Electric field strength () limited by input power couplers, peak surface fields, leading to field emission, electrical breakdown, or (in SC) thermal quench
  limited by RF surface losses, , even in superconductors!
    induces an electric field penetrating
    ~40nm for superconducting niobium at 2 K.
Flux “sensitivity,” is an unknown function of some Nb material properties, changes with surface treatment

## Slide 8: Production challenges
Cleanliness: Clean RF surfaces for zero-FE cavities not a well-controlled process at scale
  10-20%, or higher rework rate possible
Some high-Q treatments increase sensitivity to trapped flux...
Flux trapping degrades Q!
  Varies within Nb batches
  Highly correlated with Nb texture
  Difficult/impossible to control at the Nb vendor level
...and implications
Mid-T baking
~4x
S

## Slide 9: Cavity production statistics
LCLS-II-HE 1.3 GHz cavities (ILC-like)
  N-doped cavities
  Discovered magnetic flux sensitivity
  Mitigated with high-temperature heat treatment
  All cavities FE-free (clean)
PIP-II 650 MHz cavities (FCC-like)
  Mid-T and N-doped cavities
  Spec is for FE-free up to gradient
  In prototype and pre-production 650 cavities, FE-free performance is still inconsistent
    Clean-room and HPR techniques need more research and development to achieve production consistency
    PIP-II production will provide more insight into large sub-GHz cavity cleaning(FE)/performance statistics
…to keep in mind
167 9-cell 1.3 GHz
~20% rework rate
Q0 2.5-4x1010
LCLS-II-HE Cavity and Cryomodule Test Progress, J. Maniscalco, TTC 2023

## Slide 10: Superconducting RF for FCC-ee
02

## Slide 11: 800 MHz SRF for FCC-ee
400 MHz Nb/Cu, 66 CM (collider)
800 MHz bulk Nb, 214 CM (collider+booster)
Phase 1: Z,W, and H operating points
  High-current machine: higher-order mode excitation
  Reverse phase operation enables Z,W, and H OPs
Phase 2: TTb operating point
  High-gradient machine
Introduction
Booster | Z | W | ZH
 | RPO | RPO | 
Total RF voltage [MV] | 80 | 401.9 | 1961
Beam current [mA] | 16.2 | 6.2 | 2
RF Frequency [MHz] | 801.58 |  | 
Operating temp. [K] | 2 |  | 
Cavity voltage at extraction [MV] | 5.6 | 13.5 | 17.5
# cell/cavity | 6 |  | 
Eacc [MV/m] | 4.9 | 12 | 15.6
Q0 | 3E+10 |  | 
Max RF power [kW] | 42 |  | 
Coupling QL | 1E+07 |  | 
# CM (with 4 cav/CM) | 28 |  | 
# cavities | 112 |  | 
800 MHz Booster: 112 cavities/28 CM
448 booster + 408 collider
= 856 800 MHz cavities/214 CM
400 MHz Collider: 264 cavities/66 CM

## Slide 12: 800 MHz SRF for FCC-ee
400 MHz Nb/Cu, 66 CM (collider)
800 MHz bulk Nb, 214 CM (collider+booster)
Phase 1: Z,W, and H operating points
  High-current machine: higher-order mode excitation
  Reverse phase operation enables Z,W, and H OPs
Phase 2: TTb operating point
  High-gradient machine
Introduction
Booster | Z | W | ZH
 | RPO | RPO | 
Total RF voltage [MV] | 80 | 401.9 | 1961
Beam current [mA] | 16.2 | 6.2 | 2
RF Frequency [MHz] | 801.58 |  | 
Operating temp. [K] | 2 |  | 
Cavity voltage at extraction [MV] | 5.6 | 13.5 | 17.5
# cell/cavity | 6 |  | 
Eacc [MV/m] | 4.9 | 12 | 15.6
Q0 | 3E+10 |  | 
Max RF power [kW] | 42 |  | 
Coupling QL | 1E+07 |  | 
# CM (with 4 cav/CM) | 28 |  | 
# cavities | 112 |  | 
800 MHz Booster: 112 cavities/28 CM
448 booster + 408 collider
= 856 800 MHz cavities/214 CM
400 MHz Collider: 264 cavities/66 CM
370 CM, ~1,500 cavities

## Slide 13: FCC performance goals
ˆ

## Slide 14: Reaching high Q0
N-doping1
  2012-13 FNAL: Doubled Q, reversed RBCS dependence on Eacc
  Industrialized at 1.3 GHz to deliver LCLS-II
Medium temperature baking2,3
  Simple one-step chemical processing (FNAL)
  300C, 3-hour bake dissolves the native oxide layer and diffuses oxygen into the niobium bulk
    Mechanism not fully understood, but seems to have traits in common with N-doping, despite differences in diffusion depth: See H. Hu, Hu, Hannah. "Decoupling of Nitrogen and Oxygen Impurities in Nitrogen Doped SRF Cavities." , Jun. 2024.
Sensitivity to trapped magnetic flux increases in both cases
    “Sensitivity” measures the amount of residual resistance generated per unit of trapped magnetic flux
    “Increased sensitivity” means your accelerator is more vulnerable to the effects of trapped flux
      Mitigation strategies include fast cooldown, improved magnetic hygiene
Recent advances in high-Q high-gradient SRF cavities
Bulk EP, High T (degassing+stress release) 800-950C 3h, light EP, mid-T furnace bake 300C 3h, HPR, VT assembly, RF test.
“2/0” N-doping: Bulk EP, High T (degassing+stress release) bake, light EP, N-Doping (2min doping/0min annealing), Post-doping+cold EP, HPR+VT assembly, RF test.
1 A. Grassellino et al, Supercond. Sci. Technol. 26, 102001 (2013).
3 H. Ito, et al., Prog of Theor. and Exp. Phys., Volume 2021, Issue 7, July 2021
2 S. Posen, et al., Phys.Rev.Applied., Volume 13, Issue 1, Jan 2020 (FNAL)

## Slide 15: Technical perspective: SRF
PIP-II HB650: N-doping
PIP-II LB650: Mid-T
FRIB 644 MHz: various

## Slide 16: Technical perspective: SRF
PIP-II HB650: N-doping
PIP-II LB650: Mid-T
FRIB 644 MHz: various

## Slide 17: Technical perspective: SRF
PIP-II HB650: N-doping
PIP-II LB650: Mid-T
FRIB 644 MHz: various
1-cell 650 MHz
“Optimized EP”

## Slide 18: 800 MHz 5-cell cavity
Cavity fabricated at JLab, currently at FNAL
High-power RF cold-test baseline electropolish
  Q0~3x1010 at 25 MV/m
  Quench at 27 MV/m
Explore advanced techniques for >26% improvement in Q0
  Mid-T baking complete 7/2025!
    Cold-test expected Fall 2025
  N-doping?
  Nb3Sn (future)
1-cell 800 MHz (rapid iteration) tests underway in collaboration with CERN
First experiments
F. Marhauser et al. 802 MHz ERL Cavity Design and Development (cern.ch) IPAC 2018 THPAL146

## Slide 19: 3D Model and planned analysis
Progress on conceptual mechanical designs
  Complex higher order mode (HOM) port design
  Single cavity design for booster and collider
  Potential need for active cooling on the HOM ports, studies ongoing
Detailed weldmap, fabrication plans to be optimized
Mattia Parise, FNAL

## Slide 20: Preliminary design of FCC 800MHz Cryomodule
The FCC 800 MHz CM design is based on SSR2 and HB650 PIP-II CMs with the following main differences:
  Heat exchangers and valves are integrated into the Cryogenic Distribution System (CDS).
  A “Jumper” will be used to interface with CDS through welded connection into the tunnel (no u-tubes).
  Couplers are actively cooled with helium.
Vincent Roger, FNAL
PIP-II SSR2 cryomodule
PIP-II HB650 cryomodule
FCC 800 MHz cryomodule
“Final Design of the Pre-Production SSR2 Cryomodule for PIP-II Project at Fermilab”, V. Roger et al., Proceedings of LINAC 2022
“Design of the 650 MHz High Beta Prototype Cryomodule for PIP-II at Fermilab”, V. Roger et al., Proceedings of SRF 2021

## Slide 21: Superconducting RF for ILC/LC
02

## Slide 22: International Linear Collider
ILC TDR published 2013
  1.3 GHz bulk Nb SRF cavities
  Standard electropolishing recipe
  Baseline performance specs:
Inspired a generation of SRF R&D
  1.3 GHz standardization
  Leveraged by other facilities using 1.3 GHz operating today
Casting a long shadow in SRF…
Cavity shape+High RRR Nb
Nitrogen doping!
High pressure water rinse
EP+low-temperature baking
2-step baking/N infusion

## Slide 23: International Linear Collider
ILC TDR published 2013
  1.3 GHz bulk Nb SRF cavities
  Standard electropolishing recipe
  Baseline performance specs:
Inspired a generation of SRF R&D
  1.3 GHz standardization
  Leveraged by other facilities using 1.3 GHz operating today
Casting a long shadow in SRF…
Cavity shape+High RRR Nb
Nitrogen doping!
High pressure water rinse
EP+low-temperature baking
2-step baking/N infusion

## Slide 24: ILC and cost
ILC as a unit of cost

## Slide 25: LC facility at CERN
2025 study
Maintains ILC baseline, updates Q0 specification to 2x1010
Mid-T baking/Oxygen doping
  Not yet at scale
Cites XFEL and other stats
  3.9 GHz cavities
Future R&D: travelling-wave
  HELEN
Updated ILC…

## Slide 26: SRF for Muon collider
Proton driver e.g. SNS, ESS, PIP-II
  SRF challenges
    Fast acceleration - high gradient, large transverse beam size
    Low frequency – Depends on 6D cooling – 200 MHz,325 MHz, 20 MV/m, 650 MHz 25 MV/m, 975 MHz?
    Proximity to high field magnets (solenoids or quads)
  Effect of decay products (~15% muons lost in acceleration)?
LFD, microphonics – High stored energy?
Efficient cryomodules – High packing factor (how close can the magnets be to SRF?)
High power RF sources, modulators, components
Muon acceleration using SRF looks feasible
  Frequency choice strongly depends on 6D cooling
  Bulk Nb, Nb on Cu or other materials viable
  R&D needed (more on cost reduction than viability), test/demonstrator facilities needed
c/o R. Rimmer, JLab. Muon Cmte meeting

## Slide 27: FCC/LC Synergies in SRF R&D
Bulk Nb R&D
  High-Q/High-gradient advancements to reduce overall cost of construction (length of ILC) or cooling (both for LC concepts and for FCC)
  Moving away from complex N-doping process and exploring simpler and less costly low-(~120℃) and mid-(~300℃) temperature baking benefit FCC and LC concepts
  Modest R&D needed to bring sub-GHz bulk cavity performance to FCC 800 MHz spec
  R&D in low-temperature baking and two-step baking shows potential to significantly increase 1.3 GHz cavity gradient, but more development needed to reach 50 MV/m+
Current status of Nb3Sn at FNAL
  > 20 MV/m demonstrated in 1-cell, 15 MV/m demonstrated in multicell
  FCC gradient demonstrated in Nb3Sn sub-GHz cavities
  R&D needed to realize this performance in multicell cavities and the cryomodule context
  Significant further R&D is needed to reach high gradients in 1.3 GHz Nb3Sn cavities for potential use in ILC
  Nb3Sn cavity processing and handling techniques also require R&D to enable consistent quality in ~16,000 cavities for ILC.
Linear...circular...

## Slide 28: Summary
SRF has a large role to play in many promising future Higgs factory options!
Technical drivers:
  Circular machines benefit most from high-Q R&D, high current iterations suffer from higher-order mode damping concerns that must be thoroughly understood and mitigated at scale
  Linear machines benefit greatly from high-Gradient R&D, reducing the length of the machine
SRF has experienced a bright period of innovation
  N-doping, O-doping, Nb3Sn, other high-Q treatments have the potential to deliver a lot to Higgs factory applications IF SUFFICIENT R&D IS SUPPORTED CONSISTENTLY OVER TIME
In Praise of Boredom! In the technical/production context, you cannot afford to overlook “boring” challenges
  Cavity cleaning, processing, handling, shipping, tuning….