## Slide 1: DMRadio: A lumped-element, low-mass axion search
Andrew Kunwoo Yi
SLAC National Accelerator Laboratory
June 23rd, 2026
PASCOS 2026

## Slide 2: Axions

## Slide 3: Strong CP problem
The QCD Lagrangian has a -violating term
In Neutron EDM is not observed:
Current limit implies
C. Abel et al. Phys. Rev. Lett. 124, 081803 (2020)
should be of order unity but isn’t!

## Slide 4: Peccei-Quinn theory
The Peccei-Quinn mechanism implements a new symmetry to solve the strong CP problem
  Eliminates all effects of -violation for all orders
The spontaneous symmetry breaking of this symmetry implies the existence of a pseudo-Goldstone boson, the QCD axion
The axion is the result of the explicit determination of

## Slide 5: Dark matter
Dark matter was predicted due to difference between measurements between gravitational and luminous matter
Galaxy rotation curves and small-scale structures are among the plethora of evidence for (cold) dark matter (CDM)
M33 galaxy rotation curve
E. Corbelli and P. Salucci, RAS, MNRAS 311 (2000)
Bullet cluster distribution difference in normal matter (red) and total mass (blue)
Chandra X-Ray Observatory: 1E 0657-56
Dark matter constitutes 26.8% of energy budget
P. A. R. Ade et al. (Planck Collaboration), Astron. Astrophys. 594, A13 (2016).

## Slide 6: Searching for axions
The axion, like dark matter, is weakly interacting with normal matter, and can be produced cold
One of the ways to probe the axion is to use the axion-photon coupling
A strong magnetic field converts the axion into a photon through the inverse Primakoff effect (Sikivie effect)
Inverse Primakoff effect
Strong CP problem solution
Dark matter candidate
QCD Axions

## Slide 7: The current axion search landscape
from https://cajohare.github.io/AxionLimits/
The axion could be anywhere in the uncolored parameter space
The axion could solve the strong CP problem if found among this colored band
Mass of axion
(How long it takes to detect the axion)
Axion-photon coupling
Benchmark models
Wavelength Size of detector
Resonant microwave cavities
Wavelength > Size of detector
Lumped element resonators

## Slide 8: The axion haloscope
The axion haloscope is a resonant axion search probing axion-photon coupling
The axion frequency is unknown: the resonator must be tunable for a range of frequencies
The converted axion signal power is small: we want low loss resonators and under low noise (cryogenic, quantum amplified) environments
DAQ system
Low noise quantum amplifiers
Cryogenic conditions
High magnetic field region
Axion current as stiff voltage source
Resonator
Has a tunable resonant frequency

## Slide 9: The DMRadio program

## Slide 10: DMRadio suite of experiments
The DMRadio program uses lumped-element axion haloscopes to probe pre-inflationary axions at the kHz – MHz (neV mass) scale

## Slide 11: DMRadio Collaboration

## Slide 12: DMRadio-50L
Toroidal magnet with field creates current
creates magnetic field
induces which is enhanced by an LC resonator and quantum amplifiers

## Slide 13: DMRadio-50L
Search for pre-inflationary axions from 5 kHz – 5 MHz
The first search using a tunable LC resonator
Testbed for innovative quantum sensing techniques
Commissioning in progress at Stanford University

## Slide 14: DMRadio-50L Subsystems
Slides adapted from V. Ankel
Superconducting “1K” shield
(magnet + resonator inside)
Dilution Refrigerator
4K Cryostat
Four 9 Design
Base stage here
A conductive “cold finger” connects the dilution fridge to the inner stages of the 4K cryostat
The inductor, SQUID readout, and tuning mechanisms are at temperatures around 44 mK
The superconducting magnet is housed at the 4 K stage
A toroidal magnet has a low-field region in the center of the magnet
Magnet cools to 4.5 K, with a peak magnetic field of 0.9 T
SSI Inc.
Fixed capacitor
Inductor coil
R&D LC resonator achieved:
at
R. Kolevatov et al.,
Rev. Sci. Instrum. 97, 024503 (2026)
Princeton University

## Slide 15: SQUID readout development
Using two independent SQUID chains to cross correlate noise
Slides adapted from V. Ankel
A tunable transformer optimizes scan speed of experiment by modulating coupling between resonator and readout chain

## Slide 16: Data acquistion (DAQ) system
Software to acquire, store, and analyze data has been developed
Courtesy of P. Stark

## Slide 17: DMRadio-Core
A proposed design for a DFSZ-axion-sensitive search probing frequencies 30 MHz – 200 MHz
Solenoidal magnet geometry with superconducting coaxial pickups on the outside of solenoid
Supported by SLAC National Accelerator Laboratory
Slides adapted from N. Rapidis
Preprint - arXiv:2604.16602

## Slide 18: DMRadio-Core
Axion current produces ac magnetic field inside and outside the solenoidal magnet
Couple to Bax ~1/r outside of magnet by placing magnet inside the core of a coaxial pickup.
Design magnet such that this region is in low dc field  superconducting pickup and electronics
Slides adapted from N. Rapidis

## Slide 19: DMRadio-GUT
Proposed experiment to reach DFSZ sensitivity down to 100 kHz frequencies
Requires upgrades to all parts of system
Important connection to 50L: Sub-SQL quantum technology!
Possible configuration using Core geometry

## Slide 20: Radiofrequency Quantum Upconverter (RQU)
Coherently upconvert MHz signal frequencies to GHz frequencies where superconducting quantum metrology techniques are more mature
Implemented by embedding a Josephson-junction based flux-tunable inductor in a microwave resonator
Low frequency signal modulates the microwave resonant frequency
S. E. Kuenstner, et al.,
Phys. Rev. Research 7, 013281 (2025)
Fabricated Josephson junction example from Irwin group

## Slide 21: RQU capabilities and status
Phase-preserving mode: operates at the Standard Quantum Limit (SQL)
Phase-sensitive mode: A two-tone carrier signal measures one in-phase quadrature, and noise is moved to the other  beats SQL
3-Josephson junction aluminum RQU devices have demonstrated flux-tuning, frequency upconversion of MHz signals, and phase-sensitive measurement
Graphics and pictures by
E. C. van Assendelft, J. Corbin

## Slide 22: Non-Foster broadband matching network
Axion as a stiff voltage source
Pickup ( and ) from axion detector
“Negative inductance” could cancel out pickup reactance at all frequencies!
Bode-Fano limits
Matching networks designed to match complex loads will be limited by its bandwidth
Assuming: passive, linear, time invariant components
Removing some of the assumptions could bypass the Bode-Fano limits!

## Slide 23: Non-Foster broadband matching network
A Josephson junction loop is coupled in circuit to provide effective “negative inductance” that cancels out inductance for a broadband frequency range
Capacitive match
Non-Foster match
No match
where (b) is
A. K. Yi, P. Stark, C. Bartram
J. Appl. Phys. 139, 244401 (2026)
WRSPICE simulation results
Josephson junction ( ) inductance
where is the phase across the junction
Published yesterday!
Fabrication layout example

## Slide 24: Summary
DMRadio is a lumped-element axion haloscope probing axions at kHz – MHz frequencies
DMRadio-50L is the first tunable LC axion search, currently commissioning
DMRadio-Core extends search to DFSZ axions, leading to DMRadio-GUT
Quantum sensing technologies are being developed such as RQUs and broadband non-Foster impedance matching circuits
Non-Foster broadband matching network
Radiofrequency quantum upconverters
DMRadio-Core
DMRadio-50L Resonator
Featured papers

## Slide 25: The Standard Quantum Limit (SQL)
There is always uncertainty in a measurement
1/2 photon from zero-point fluctuations + 1/2 photon (minimum) from amplifier
Axion signal + thermal noise
Zero point fluctuation noise
Amplifier added noise

## Slide 26: Sources of noise
Weakly coupled
Imprecision noise: White noise from amplifier added noise
Backaction noise: Noise injected back into circuit, filtered by circuit impedance
Sensitivity bandwidth increases by adjusting relative contributions
Strongly coupled

## Slide 27: Does it work?
where our impedance match is
Current leads voltage
Both amplitudes are larger
When biased to :
frequency: 50 MHz
Plot measured at output
Current lags voltage
Normal inductive behavior
When not biased:

## Slide 28: The axion haloscope
The axion haloscope is a resonant axion search probing axion-photon coupling
The axion frequency is unknown – the resonant cavity must be tunable for a range of frequencies
Cavity has various resonant modes which enhances the signal power of converted photon
Tuning rods are required to change the resonant frequency of cavity, usually copper or dielectric
External static magnetic field allows axion to photon conversion
Signal is studied using a digitizer in the frequency domain
Quantum sensors and other amplifiers in and outside cryostat amplify the signal
Antenna used to pick up signal (Signal power depends on coupling)
Experiments are conducted inside a cryostat and dilution fridge at low temperatures to reduce noise power
Digitizer
Cryogenic conditions

## Slide 29: Axion signal conversion power
The axion signal conversion power depends on various factors
: Total energy of a specific mode
: Axion to photon coupling
(value varies depending on model)
: Axion density in galaxy halos
: Axion mass
: Cavity coupling parameter ()
: Cavity resonant frequency
: Average external magnetic field
: Cavity volume
*Uses natural units and assumes cavity is resonant to axion frequency
: Form factor, depends on internal electric field of mode and external magnetic field
: Loaded quality factor, including losses of cavity () and receiver ()
For an empty cylindrical cavity inside an external B-field in the -direction, the TM010 mode has the highest form factor at 0.69
*Assumes

## Slide 30: Geometries for lumped axion experiments
Various geometries are possible to pickup the induced axion field