## Slide 1
Timing Distribution Method via 10-km Optical Fibers
at the J-PARC for the Hyper-K Project
2026/05/28 25th IEEE Real Time Conference [OS_DataAcquisitionAndTriggerArchitectures_125]
Che-Sheng LinA,B,
Eitaro HamadaA, Ian Benjamin HeitkampC, Yota HinoA,B, Ryotaro HondaA,B, Ken SakashitaA,B
AKEK IPNS, BSOKENDAI, CTohoku University
This work is supported by the JST K-program
(Grant No. JPMJKP24J2).

## Slide 2: T2K (Tokai to Kamioka)/HK Experiment
Long-baseline neutrino oscillation experiment
- Neutrino Oscillation
- T2K Experiment
- Neutrino flavors change
after traveling some distance.
- Muon neutrino (νμ) beam is generated
from the J-PARC main-ring (MR) proton beam.
- The neutrino flavor is measured
by Super-Kamiokande after traveling 295 km.
- Super-Kamiokande
- Near Detectors
- J-PARC
Ref: Abe, K., et al., NIM A,
659.1 (2011): 106-135.
J-PARC generates
from proton.
Kamiokande measures the arriving flavor.
pure
most of
with a few of ,
neutrino
flavor
Notes: https://j-parc.jp/documents/pdf/2024/T2K_202408_J-Low.pdf
https://www.mdpi.com/2673-9984/8/1/38
https://www-sk.icrr.u-tokyo.ac.jp/~berns_s/RT99/ far

## Slide 3: J-PARC Site of T2K Experiment
Fast-extraction (FX) and beam kicking pulse signal
- Neutrino beam
- MR fast-extraction (FX) mode
- The MR delivers a beam kicker timing pulse signal.
beam kicker pulse signal
- The period of the fast-extraction (FX) mode is 1.3s.
Ref: Y. Sato, J-PARC MR,
MOA2I1, HB2023
Main ring
proton
pion
muon
neutrino
Notes: https://indico.cern.ch/event/1138716/contributions/5437848/attachments/2730099/4745819/MOA2I1_TALK.pdf

## Slide 4: Timing Distribution System
Distribute the beam trigger and spill number
- Neutrino beam
- Local time clock (LTC) at the J-PARC site
beam kicker pulse signal
beam trigger & spill number
- When receiving the kicker pulse signal,
the timing distribution system distributes
the beam trigger pulse signal and spill number
to each neutrino facility.
- Developed during the K2K era over 20 years ago.
- Several modules have exceeded their production lifespan
and are no longer available.
- The system occasionally suffers from signal dropouts.
We aim to develop a new transmission method
to replace the current system for the future Hyper-K experiment.
beam kicker
pulse signal
beam trigger
& spill number
- Beam trigger pulse signal
with spill number
- No trigger loss
- Requirements:
- Timing accuracy < 1 ns
- Transmission distance > 10km
- Transmission latency < 1 ms
beam trigger
pulse signal
beam kicker
pulse signal
fixed latency
Notes: https://indico.cern.ch/event/1138716/contributions/5437848/attachments/2730099/4745819/MOA2I1_TALK.pdf

## Slide 5: 1. Timing Distribution Method 2. Phase Compensation Method 3. Implementation

## Slide 6: Method of Timing Distribution System
Principle: digitize analog pulse signals for transmission
MIKUMARI
Link TX
MIKUMARI
Link RX
clock (125MHz)
recovered clock (125MHz)
Time
Counter
Time
Counter
Data
Encode
Data
Decode
pulse I/F
pulse I/F
data I/F
data I/F
time
time
Pulse
Sampler
Pulse
Generator
Kicker
Timing
Pulse
Spill
Counter
Spill Num.
Spill
Num.
Beam
Trigger
Pulse
optical
fiber
(1) Main board:
Digitalize the pulse signal.
Main board
Sub board
(1) Digitalize
pulse signal
(3) Generate
pulse signal
(2) Transmit the leading-edge timing
(2) MIKUMARI link protocol:
Transmit the leading-edge timing of pulse signal.
(3) Sub board:
Generate the pulse signal at the corresponding timing.
- Principle:
Digitize analog pulse signals
for transmission
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 7: Method of Timing Distribution System (0)
Prepare the synchronize time counter
MIKUMARI
Link TX
MIKUMARI
Link RX
clock (125MHz)
Time
Counter
Time
Counter
Data
Encode
Data
Decode
pulse I/F
pulse I/F
data I/F
data I/F
time
time
Pulse
Sampler
Pulse
Generator
Kicker
Timing
Pulse
Spill
Counter
Spill Num.
Spill
Num.
Beam
Trigger
Pulse
optical
fiber
Main board
Sub board
(0.1) MIKUMARI signal serves as a reference clock
to recover the synchronized clock on the Sub board.
(0.2) Periodically synchronize the time counter via pulse I/F
The time counter values have a fixed offset, which depends on the transmission latency of the pulse I/F.
(0) Prepare the synchronize time counters:
Ref: R. Honda, IEEE TNS,
70.6 (2023): 1102-1109
recovered clock (125MHz)
Note: interface (I/F) of MIKUMARI link protocol:
1) clock I/F:
- synchronous clock signal of 125 MHz (8 ns).
2) pulse I/F:
- pulse signal with fixed latency and 3-bit data width.
3) data I/F:
- DC-balanced data frame (a few 8-bit characters)
- transmission latency with slight uncertainty
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 8: Method of Timing Distribution System (1)
Digitalize the kicker timing pulse signal
MIKUMARI
Link TX
MIKUMARI
Link RX
clock (125MHz)
Time
Counter
Time
Counter
Data
Encode
Data
Decode
pulse I/F
pulse I/F
data I/F
data I/F
time
time
Pulse
Sampler
Pulse
Generator
Kicker
Timing
Pulse
Spill
Counter
Spill Num. (32bit)
Spill
Num.
Beam
Trigger
Pulse
optical
fiber
Main board
Sub board
TDC (1ns/3bit)
(8ns/16bit)
(1.1) Measure the leading-edge timing of the pulse signal.
(1 ns-resolution TDC implemented by the ISERDES primitive.)
(1.3) Spill number for identifying the beam trigger (32bit).
(1.2) Measured timing = timing counter + pulse sampler
(8ns/16bit) (1ns/3bit)
(1) Digitalize the kicker timing pulse signal:
clock (8 ns)
parallel data pattern (1 ns)
pulse signal
0
0
0
0
1
1
1
1
Note: 1ns TDC (1-to-8 ISERDES )
recovered clock (125MHz)
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 9: Method of Timing Distribution System (2)
Transmit the leading-edge timing and spill number
MIKUMARI
Link TX
MIKUMARI
Link RX
clock (125MHz)
Time
Counter
Time
Counter
Data
Encode
Data
Decode
pulse I/F
pulse I/F
data I/F
data I/F
time
time
Pulse
Sampler
Pulse
Generator
Kicker
Timing
Pulse
Spill
Counter
Spill Num.
Spill
Num.
Beam
Trigger
Pulse
optical
fiber
Main board
Sub board
(2.1) Transmit the information of pulse signal by data I/F
leading-edge timing + spill number
(16+3 bit) (16 bits)
(spill number: 32 bits(total)/16 bits (delivered))
(2) Transmit the leading-edge timing and spill number:
Ref: R. Honda, IEEE TNS,
70.6 (2023): 1102-1109
Note: interface (I/F) of MIKUMARI link protocol:
1) clock I/F:
- synchronous clock signal of 125 MHz (8 ns).
2) pulse I/F:
- pulse signal with fixed latency and 3-bit data width.
3) data I/F:
- DC-balanced data frame (a few 8-bit characters)
- transmission latency with slight uncertainty
recovered clock (125MHz)
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 10: Method of Timing Distribution System (3)
Generate the pulse signal at the corresponding timing
MIKUMARI
Link TX
MIKUMARI
Link RX
clock (125MHz)
Time
Counter
Time
Counter
Data
Encode
Data
Decode
pulse I/F
pulse I/F
data I/F
data I/F
time
time
Pulse
Sampler
Pulse
Generator
Kicker
Timing
Pulse
Spill
Counter
Spill Num.
Spill
Num.
Beam
Trigger
Pulse
optical
fiber
Main board
Sub board
corresponding timing
OSERDES
(3.1) Generate the pulse signal at the corresponding timing.
( leading-edge timing + pulse width)
Note: transmission latency: data I/F > pulse I/F  add an extra fixed latency to ensure receiving
of data from the data I/F.
(3) Generate the pulse signal at the corresponding timing:
(3.2) Use the OSERDES primitive to achieve 1ns accuracy.
- Parameters:
- pulse width
- extra fixed latency
Kicker timing
pulse signal
Time counter
(main board)
Beam trigger
pulse signal
Time counter
(sub board)
T1
T2
T3
T1
T2
T3
width
leading-edge timing
recovered clock (125MHz)
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 11: 1. Timing Distribution Method 2. Phase Compensation Method 3. Implementation

## Slide 12: Phase drift of 10km Optical Fiber Link
Phase shift caused by temperature
duplex optical fiber
MIKUMARI
Link TX
PLL
clock signal
recovered
clock signal
MIKUMARI
Link RX
MIKUMARI
Link RX
MIKUMARI
Link TX
- For a 10-km optical fiber link, temperature-dependent propagation delay variations cannot be neglected.
Main board
Sub board
temperature-dependent
propagation-delay variation
Pulse
Generator
beam
trigger
pulse
(1) Drift of beam trigger pulse signal:
Pulse signal generation is based
on the recovered clock signal
(2) Decoding error of MIKUMARI RX of main board:
Decoding by the MIKUMARI RX on the main board
relies on the main-board clock.
main board clock
sub board clock
beam trigger
pulse signal
main board clock
(DDR)
main board
MIKUMARI RX decode
(1)
(2)
Note:
low thermal coefficient standard optical fiber (SMF-28)
thermal coefficient ≈ 35 ps/km/K.
Ref: Slavík, R., et al.,
Sci Rep 5, 15447 (2015)
variation
variation

## Slide 13: Phase compensation of 10km Optical Fiber Link
Phase measurement and compensation
duplex optical fiber
MIKUMARI
Link TX
PLL
clock signal
recovered
clock signal
MIKUMARI
Link RX
MIKUMARI
Link RX
MIKUMARI
Link TX
(1) The temperature-dependent phase shift can be measured
by comparing the returned MIKUMARI modulated clock signal with the local main-board clock.
Main board
Sub board
temperature-dependent
propagation-delay variation
Pulse
Generator
beam
trigger
pulse
Phase
Detector
Data
Encode
(1)
(2)
(3)
(3) MIKUMARI RX of main board dynamically adjusts the IDELAY taps and bit slip
based on the measured phase shift to keep the sampling point centered.
(2) Leading-edge timing is added to the phase compensation
to mitigate the drift of beam trigger pulse signal.

## Slide 14: Phase Measurement
Digital dual mixer time difference (DDMTD)
generate
DDMTD
beat signal
detect
leading
(deglitcher)
compare
leading
timing
main board
clock signal
return modulated
clock signal
DDMTD reference
clock signal
generate
DDMTD
beat signal
detect
leading
(deglitcher)
average &
unit conv.
accumulate
measured
phase shfit
(1) The DDMTD reference clock signal with slightly lower frequency is used to sample the measured clock signals,
and generate the DDMTD beat signal with lower-frequency. ( )
- The DDMTD down-converts a high-frequency clock signal into a low-frequency beat signal.
(2) The DDMTD beat signal preserves the measured clock signal phase.
 The phase difference can be measured from the DDMTD beat signal phase difference.
(3) Multiple phase samples are averaged to obtain a stable phase estimate.
(4) The measured phase is accumulated to track long-range phase shift.
(1)
(2)
(3)
(4)
sampling moment

## Slide 15: Phase compensation
For leading-edge timing of pulse signal
Pulse
Sampler
Phase
Detector
Pulse
Generator
Phase
Compensation
Kicker timing
pulse signal
Main board
Sub board
Beam trigger pulse signal
w/ phase compensation
- Phase compensation
- Since the measured phase shift is round trip variation,
the leading-edge timing of pulse signal ()
compensates half of phase shift.
-
10km duplex optical fiber
- Pulse generator
- Achieve the fine compensation
- 8-to-1 OSERDES + ODELAY primitive
- unit interval: 78 ps
- Phase detector
- Measure the phase shift ()
- Pulse sampler
- 1 ns-resolution TDC
- 8-to-1 OSERDES
- unit interval: 1 ns

## Slide 16: 1. Timing Distribution Method 2. Phase Compensation Method 3. Implementation

## Slide 17: Testbench of Timing Distribution System
- AMANEQs
Tested by a 10km optical fiber
Kicker timing
pulse signal
Beam trigger
pulse signal
Main board
Sub board
10 km optical fiber
PC
- Main board measures phase shift.
- Thermo recorder records the room temperature.
- The testbench of timing distribution system
is implemented by AMAENQs.
- NIM input of Main board receives the pulse signal.
- NIM output of Sub board generates the pulse signal.
- Pulse information is transmitted by 10 km optical fiber
with MIKUMARI link protocol.
- AMANEQ: a general main electronics
for trigger-less data acquisition system
- FPGA: Kintex-7, XC7K-160T-2FFG676-2
- PLL: CDCE62002
- NIM_IN: SN65LVDS348PWR
- NIM_OUT: SN65CML100D
- SFP: SFP1G-LX-31 (1G/1310nm/20km)
- Optical fiber: 24F MTP-MTP trunk cable (1310nm/1km)
fiber patch cable (1310nm/2m)
- Fiber Optic Cassette: FHD-1MTP12LCOS2AF
- Oscilloscope: KEYSIGHT DSOS054A (2GHz Upgrade)
- Thermo recorder: TANDD TR-71nw
PC
- Fiber Optic Cassette
- Thermo recorder
Notes: There are too many flow charts. Real photos for the test bench could be more in your slide.

## Slide 18: Result of Phase Shift and Room Temperature
Tested by a 10km optical fiber
- The measured phase shift
clearly tracks the room temperature variation.
Temperature [°C]
2m optical fiber (1day)
10km optical fiber (13day)
Phase shift [ns]
Phase shift [ns]
Temperature [°C]
time
time
- Red : room temperature
- Block : measured phase shift
- The phase shift of the 10km optical fiber
are significantly larger than the 2m one.

## Slide 19: Measured signals on Oscilloscope
Tested by a 10km optical fiber
Pulse
Sampler
Pulse
Generator
Phase
Detector
Pulse
Generator
Pulse
Generator
Phase
Compensation
Kicker timing
pulse signal
Main board
Sub board
Beam trigger pulse signal
w/ phase compensation
Beam trigger pulse signal
w/o phase compensation
Reference
pulse signal
10km optical fiber
(1) Trigger the kicker timing pulse signal
- Evaluate the pulse signal transmission performance.
(2) Trigger the reference pulse signal
- Evaluate the phase compensation performance.
- Suppress sampling-timing uncertainty.
(1)
(2)

## Slide 20: Result of Time Synchronization System
Tested by a 10km optical fiber
3) Stability:
- Testing time ≈ 11 days
- Room temperature variation ≈ 12°C - Clock phase shift ≈ 5 ns
- The MIKUMARI RX on the main board
maintains the sampling point at the center
based on the measured phase shift.
1) Transmission latency & Timing accuracy :
unit: 1 ns
- Kicker timing pulse signal as trigger
- Transmission latency: (requirement <1 ms)
- Time interval: 54.934 μs (with extra latency of 5 μs)
- Timing accuracy:
- Range (Max-Min): 1.223 ns
2) Phase compensation performance:
Beam trigger pulse signal
w/ phase compensation
Beam trigger pulse signal
w/o phase compensation
unit: 200 ps
- Reference pulse signal as trigger
- Phase compensation performance :
- Range (Max-Min): 287.754 ps
- Std Dev: 34.996 ps
The testing results
confirmed requirements.
- # of transmitted pulse signal: 9,352,060,226
- No trigger loss was detected.
- Probability of trigger loss: < 3.2x10-10 @95%CL

## Slide 21: Conclusion
- Motivation: replace the current timing distribution system of T2K experiment at J-PARC site.
- Principle: digitize the analog pulse signal for transmission.
(1) Main board: digitalize the pulse signal.
(2) MIKUMARI link protocol: transmit the leading-edge timing of pulse signal.
(3) Sub board: generate the pulse signal at the corresponding timing.
- Test results using a 10-km optical fiber:
- Timing accuracy : 1.22 ns - Transmission latency: fixed 54.92 μs (with extra latency of 5 μs)
- Probability of trigger loss: < 3.2x10-10 @95%CL
 Confirmed requirements.
- Future: implement it for the timing distribution system of Hyper-K experiment.
- Advantage:
(1) Enables flexible transmission of multi-channel pulse signals or additional information
via a duplex optical fiber.
(2) Mitigates the drift of the pulse signal caused by ambient temperature variation.
Development of the new pulse signal transmission method

## Slide 22: Backup

## Slide 23: MIKUMARI
Ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023
Clock distribution system based on clock-duty-cycle-modulation (CDCM)
- MIKUMARI link
- MIKUMARI modulated clock signal:
- characteristic
- fixed leading-edge interval carrying clock reference.
- variable duty cycle embedding user data.
- transmitter
- modulated by OSERDES (Serializer) primitive of FPGA.
- receiver
- used as the PLL (Phase-Locked Loop) reference
to recover clock signal.
- decoded by IDELAY and ISERDES (Deserializer) primitive of FPGA.
optical fiber
MIKUMARI
Link RX
MIKUMARI
Link TX
PLL
clock signal
recovered
clock signal
pulse I/F
data I/F
pulse I/F
data I/F
clock reference content (fixed)
user data content (variable)
modulated
clock signal
recovered
clock signal
- MIKUMARI link interface (I/F):
- pulse I/F
- 3-bit data width.
- fixed transmission latency.
- data I/F
- DC-balance data frame (a few 8-bit characters)
- transmission latency with a few uncertainty

## Slide 24: Method of Time Synchronization System (2)
Sample and Generate the Kicker Timing
- I/O SERDES
OSERDES
clock
Output SERial/DESerializer
- Pulse Sampler (1ns TDC)
ISERDES
parallel
data pattern
clock
Inputput SERial/DESerializer
pulse signal
pulse signal
- Pulse Generator
clock (8 ns)
parallel data pattern (1 ns)
pulse signal
0
0
0
0
1
1
1
1
encode/decode data
- Serial/Deserial Convertor
- ISERDES samples the data pattern of pulse signal.
- Timing encoder converts the data pattern to leading-edge timing
Timing
Encoder
Timing
Decoder
leading-edge timing
leading-edge timing
pulse width
- Only the leading-edge timing is delivered by MIKUMARI link protocol.
- Timing decoder generates the data pattern
by the leading-edge timing and pulse width parameter.
- OSERDES generates the pulse signal.
- Converting ratio: 1-to-8
- Timing resolution: 8 ns1ns
I/O SERDES
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 25: Extra Fixed Latency
To ensure timely pulse generation.
- Transmission latency difference of MIKUMARI I/F
MIKUMARI data frame phase
Conflict with pulse I/F
- The maximum of transmission latency difference
is acceptable.
- Extract fixed latency > 1060 ns
Note:
1) The latency of the data I/F are longer than the pulse I/F,
and has a small uncertainty.
2) The pulse I/F has higher priority than the data I/F.
- To ensure timely pulse generation,
the added extra fixed latency must be enough long.
- Larger than the maximum of transmission latency difference
between the MIKUMARI data and pulse I/F.
Notes: ref: D. Calvet, IEEE TNS, vol. 67, no. 8, pp. 1912-1919, Aug. 2020
ref: R. Honda, IEEE TNS, vol. 70, no 6, pp. 1102-1109, June 2023

## Slide 26: AMANEQ
A Main Electronics for Network Oriented Trigger-less Data Acquisition System
XC7K160T
-2FFG
DDR3-SDRAM (DDR3-800, 2Gb)
SFP+
(Up to 10G)
NIM I/O
SFP+ (MIKUMARI)
Power
(DC 35V)
Mezzanine slot
(compatible with HUL)
Small mezzanine
for I/O extension
Main Input Ports
LVDS/PECLE/ECL
Main Mezzanine Slots
Compatible with HUL
Small Mezzanine Slot
for IO Extension
FPGA
SDRAM
SFP+
SFP+
SFP+
NIM-INs
NIM-OUTs
32
64 (32)
4 (2)
2
CDCE62002
Jitter Clear
Up to 10 Gbps
Differential
to Single-end
EEPROM
EEPROM
32
64 (32)
2
100 MHz
Clock Oscillator
Clock Synchronization
Signal Receiver
Data Communication
Memory
- The AMANEQ is generic electronic board for StrDAQ system.
- By modifying the FPGA firmware and exchanging the mezzanine card,
the AMANEQ can achieve various purposes.
FPGA
ref: https://openit.kek.jp/project/StrHRTDC
Main input
part
(Diff. signals)
(MIKUMARI)

## Slide 27: Evaluate DDMTD phase measurement
By ODELAY of MIKUMARI TX on sub board