## Slide 1: A High-Bandwidth, High-Framerate Integrated Ionizing Particle Detection System
Carl Grace, on behalf of the Advanced Accelerator Diagnostics Collaboration
Lawrence Berkeley National Laboratory
IEEE Real Time Conference, Elba, Italy 05/26/2026

## Slide 2: Advanced Accelerator Diagnostics Collaboration
Three University of California campuses and three US National Labs
  UC Santa Cruz (Santa Cruz Institute for Particle Physics), UC Davis, UC Santa Barbara
  Lawrence Berkeley National Lab, Los Alamos National Lab, SLAC National Accelerator Lab
Originally funded by the University of California, Office of the President. Current funding from the the US Department of Energy
Developing diagnostic systems for XFEL, synchrotron, and proton beams and performing basic diamond sensor R&D (transport properties, radiation tolerance). Focus of this talk is on beam position monitors for future XFELs.

## Slide 3: Per‑pulse XFEL beam diagnostics in the sub‑ns regime
Current 50 MHz electronics too slow and cannot resolve individual pulses
Remote digitizers smear signals
36 GS/s
< 250 fs Jitter
Minimal cables
Diamond + ASIC integration
Evolution
Tarun Prakash, IEEE NSS, 2025

## Slide 4: Beam Position Monitors
3.1mm
4.0mm
20µm
30-50 µm thick
Metallization: 25 nm Pt
A
B
C
D
Diamond Sensors
Low X-ray Absorption (can be used in beam path)
High Thermal Conductivity
Radiation Hardness
Large, indirect bandgap 5.5 eV  13.3 eV/eh-pair (~4X silicon)
High mobility (~2X e- and 4X holes compared to Si)
Fabricated at LANL

## Slide 5: Fast Diamond Sensor System Concept
  Charge Collection (LANL, SLAC)
    Diamond fast and efficient up to ~1016 charges/cm3
  Signal Path (UCSC, UCSB)
    How fast the signal can return to ground without ringing?
  Signal processing / amplification / buffering / digitization (LBNL and UC Davis)
    High speed electronics development
  Interfacing of signal path with signal processing features (LBNL)
    RF Engineering
Rene Padilla, Ulitima 2023

## Slide 6: 50 MHz Position-Sensitive Diagnostic (proof of concept)
4 quadrant diamond sensor
 20 ns pulse time
Sweep across 2 quadrants
Charge resolution  0.025 pC
~ 10 ns shaping network

## Slide 7: 50 MHz Position-Sensitive Diagnostic (proof of concept)
For 4 nJ pulse ~ Q of 0.025 pC yields to 2 μm centroid position resolution (pulse-by-pulse)
P
Asymmetry ranges only between -1 to 1
 Position Resolution
ASIC needed to extend speed by 20X +

## Slide 8: ASIC Specification
Timing Accuracy vs ENOB and analog BW (sampling at ~40 GS/s)
James McDaniel, UC Santa Cruz 2023

## Slide 9: First ASIC – FPS-0 (was LABFEES)
First ASIC submitted 04/2022
Intended to explore front end architectures
Designed for 11 GHz bandwidth
3 transimpedance (current mode input) amplifiers
3 voltage sensitive inputs
Included ring oscillator and internal bias network
Measured BW of 3.5 GHz. Limitation was use of active inductors in the front end to reduce silicon area
Implemented in 65nm CMOS

## Slide 10: First ASIC (FPS-0) performance
Fast pulse input ( 40 ps rise time)
Observed 100 ps rise time with Probe
Signals preserved to at least 3.5 GHz bandwidth
Preliminary HyperLynx (RF solver) simulation of PCB suggests > 5 GHz preserved at input to chip
Pulse input
Probed Signal
ASIC
Rene Padilla, Ulitima 2023

## Slide 11: Second ASIC – FastPulse Precision Sampler (FPS-1)
Input pulse
Concept: use array of capacitors to store fast pulse in “analog memory” and digitize slowly
Useful because sampling is a faster process than quantization
Switched-Capacitor array
Conrad Rowling, UC Davis MS Thesis

## Slide 12: Second ASIC – FastPulse Precision Sampler (FPS-1)
Second ASIC submitted 03/2023
Four-channel waveform digitizer with analog output
Externally-triggered sampling
Improved current-mode input amplifier
Implemented in 65 nm CMOS
FPGA
(ADC)
Specification | Value | Unit
Sample Rate | 50 | Gs/s
Capture Window | 1 | ns
Readout Rate | 500 | MHz
Resolution | 10 | bits

## Slide 13: Second ASIC - FastPulse Precision Sampler (FPS-1)
Transimpedance State
Gain Stage
Output Stage
Key changes to address UCFEES ASIC shortcomings:
Common-gate input with inductive peaking  key
Multi-stage, open-loop design
Dedicated low-gain output stage
Physical inductor
Tunable pseudo-resistors
Peaking for BW extension

## Slide 14: Second ASIC - FastPulse Precision Sampler (FPS-1)
Inductors for gain peaking
FPS Simulation Result
LVDS
trigger
Input pulse
Amplified
Measured Performance

## Slide 15: System Test at NLCTA at SLAC
FPS-1 – 65 nm CMOS
2 mm
2 mm
NLCTA = Next Generation Linear Collider Test Accelerator

## Slide 16: Zoom in on readout board
16
Readout Board

## Slide 17: July 16, 2025: Beam delivered to the system
Search for beam with slowest sampling rate (~18 GS/s)
Capture window ~2.5 ns
Courtesy: B. A. Schumm, UCSC/SCIPP
Notes: On July 16th, 2025, beam was first delivered to our system - this was a really exciting moment. We initially searched at 18 gigasamples per second with a 2.5 nanosecond window and successfully found the beam.

## Slide 18: July 16, 2025: Beam delivered to the system
With beam found, switch to fastest sampling rate (~36 GS/s)
Capture window ~1.25 ns
Read out SCA at 2 MHz (500 ns per capacitor)
Courtesy: B. A. Schumm, UCSC/SCIPP

## Slide 19: Measured beam pulse after averaging and fit
Cleanup: subtract pedestal, remove clock spikes, average ~1000 points → one value per cap
Align: use Δt calibration to map cells to time; reconstruct on 28 ps grid (~1.25 ns window)
Fit: Exponentially modified Gaussian fit to the samples; example pulse near top of linear range

## Slide 20: Third / Fourth ASIC (FPS2 / FPS3)
Key additions:
Delay Locked Loop to stabilize delays
Internal trigger capability
On-chip ADC to simplify interface (FPS3)

## Slide 21: FPS2 fabricated; characterization underway
Co-designed with compact signal path load (Spice level for now)
Preamp change: regulated common gate amplifier for predictable 8+ GHz BW
DLL from 1 GHz ref; low‑jitter multiphase sampling; replica path for pulse conditioning
90 cells → 2.25 ns window at 25 ps spacing
Improved routing/buffers to cut crosstalk;
ADC will be added for FPS3
2 mm
2 mm

## Slide 22: Comparison of FPS ASICs
ASIC | BW [GHz] | Max Sampling Rate [GS/s] | Memory locations | Noise [µV-rms] | Resolution (ENOB) | Process [nm] | Fab Date
UCFEES (FPS-0) | 3.5 | N/A | N/A | 750 | N/A | 65 | 2022
FPS-1 | 5 | 36 | 45 | 550 | ~ 8 | 65 | 2023
FPS-2 | 8 | 50 | 90 | TBD | ~ 9 | 65 | 2025 (under test)
FPS-3 | TBD | TBD | TBD | TBD | 10 (goal) | 65 | 2028 (expected)

## Slide 23: Future: Multi-GHz Position Sensing System
HFSS Simulation
10 Ohm back-contact sense resistor
50Ω traces on Rogers Material
FPS is 50Ω resistive load
3 mm
Input current pulse
Diamond Sensor (LANL)

## Slide 24: Conclusion
Developing high-speed diagnostics for next generation accelerators. End-goal is ease of use as well as performance
Successfully demonstrated in-situ beam position monitoring
Multi-GHz (5 – 10+ GHz) analog BW, 50+ GS/s, 10b+ readout generally useful
Have made progress on diamond sensor, readout ASIC, and signal path

## Slide 25: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231