## Slide 1: Real-time Monitoring of Virgo Super-Attenuators
Alberto Gennai

## Slide 2: Summary
VIRGO Gravitational Waves Detector
  Gravitational Waves
  Detector
Seismic Isolation
  Super Attenuator
Control System
  System in use
  Running upgrade
  Future upgrades

## Slide 3
https://www.ego-gw.it/

## Slide 4: Gravitational Waves
Einstein describes gravity as a property of space-time that is deformed by masses.
Acceleration of large masses on the ‘fabric’ of space-time produce tiny ripples, Gravitational Waves, that propagates at the speed of light alternately stretching and squeezing the fabric.

## Slide 5: Gravitational Waves (II)
How Small?
To detect a gravitational wave, we must measure displacements in the order of 10-18 m over a length of 3 km
Such displacement is so small that it is extremely difficult to figure out what does it mean. To give some hint, it is like:
  Detecting a variation in the order of one atom diameter in the Earth-Sun distance.
  Detecting a variation in the order of one human hair in the distance of Proxima Centauri (about 4 ly).
  Detecting the variation in the oceans level pouring in a glass of water.

## Slide 6: GW170814: 3 Detectors
Livingston (LA) & Hanford (WA) Detectors

## Slide 7: Dawn of multi-messanger era
Astronomical Observatories were triggered with the coordinates of the event
Starting from search area and using the additional information about event distance, astronomers could select a small set of galaxies to look at
About 80 observatories all over the world followed the birth a new star, a kilonova at ~130–140 million light-years from us

## Slide 8: Optical Layout
VIRGO interferometer is more complex than basic Michelson.
The two arms are Fabry Perot cavities 3km long
Makes use of Power Recycling technique to increase the total circulating power
Signal Recycling

## Slide 9
Source:
LIGO-T2500390-v1
Francesco Di Renzo

## Slide 10: Seismic Noise
Different sources:
  Tidal strain (about 200 µm peak-to-peak between input and end mirrors)
  Earthquakes
  Seismic noise
    Microseism: dominant between 0.1 and 1 Hz mainly due to sea waves
    Anthopogenic:
      between 1 and 5-10 Hz, due to heavy vehicles traveling along near roads and bridges
      Between 10 and 40 Hz, due to onsite ‘traffic’.

## Slide 11: Seismic Noise Reduction
Seismic noise limits sensitivity of ground-based detectors at low frequencies - “seismic wall”
Typical seismic noise at Virgo site at 10 Hz is ~ few x 10-10 m/√Hz - many orders of magnitude above target noise level
Solution: isolation system with a multistage pendulum: the Super-Attenuator
Isolation required in vertical direction as well as horizontal due to cross-coupling

## Slide 12: Super-Attenuator

## Slide 13: Seismic Filters
The Super-Attenuator is a chain of mechanical stages acting as filters for seismic noise
At the end of the chain of filters there is the Payload: Marionette and Mirror

## Slide 14: Super-Attenuator

## Slide 15: Virgo Control
Interferometer
Seismic Isolation System

## Slide 16: Feedback Control
Opto-Mechanical System
Control System
Environmental Disturbances
Seismic Noise
Tidal Displacement
...
Sensors
Global Sensors
  Photodiodes
Local Sensors
  Rel. Displacement
  Inertial
Measurement Noise
Actuation Noise
~400 signals
~600 signals

## Slide 17
Mechanical transfer functions between force applied on Super-Attenuator top stage.
High complexity and high dynamics

## Slide 18
Open loop (blue) vs closed loop (green) top stage acceleration spectra
Without local control of the normal modes of the Super-Attenuator, residual motion of suspended mirrors would be too large

## Slide 19: Control Hardware Evolution 10 Super Attenuators: 20 Local Control Units
1999-2009: VME Crate (10 Units)
2x Motorola DSP96002
2x PowerPC
60x Analog IO (16bit ADC – 20bit DAC)
NIM Crate for FE Electronics
2009-2014: VME Crate
2x Multi ADSP21160
2x PowerPC
60x Analog IO
NIM Cratefor FE Electronics
2015-2026: MTCA Crate (20 units)
Up to 12x TMS320C6678 DSPs
Up to 72x Analog IO including FE electronics

## Slide 20: Local Control Unit
MicroTCA (customized)
20 Control Units
130 UDSPT boards
Each board equipped with:
6ch ADC (24bit, 3.84MSPS)
6ch DAC (24bit 320 kSPS)
8 core DSP TMS3206678
Analog electronics
Up to 60 GFLOPS per board

## Slide 21: UDSPT Module
Customized (taller) MicroTCA
DSP <-> AD/DA PCIe
DSP <-> DSP SRIO

## Slide 22: Interconnections

## Slide 23: Digital To Analog Converters
AD1955 stereo digital audio converter 24bit operated at 320kSPS
Benchmark for linearity check (no up-conversion of low frequency components)
Due to high dynamics of mechanical systems, we need double precision

## Slide 24: Analog to Digital Converters
TI ADS1675, delta-sigma converter, 24bit 4MSPS
Local sensors that monitor the Super Attenuator movements are typically inductive (ironless LVDT) operating at 50 kHz

## Slide 25: AD  Processing  DA
Since we are dealing with feedback loops, delay must be kept low.
The minimum delay we can achieve is 42 us
50 us delay produce a 18deg phase shift at 1 kHz, therefore limiting the unity gain frequencies in the kHz range.

## Slide 26: Data Fluxes
10 Super-Attenuators, 20 LCU, ~130 boards
~600 input channels 24b 3.84MSPS
~600 output channels 24b 320kSPS
All conversions are synchronous triggered by the Virgo timing system
AD
FPGA
DSP
DA

## Slide 27: Software Architecture
Users act only on application layer
The hard real-time part of user's code run on two parallel task whose activation frequency is selectable between 10 and 320 kHz. Compiler checks if there are timing issues
Native programming language using a library of optimized functions

## Slide 28: Example: ScNE LCU Tasks List
9 user tasks are running. Activation frequency is 40 kHz for all of them except for the last one activated 320’000 times per second. Execution is parallel: each tusk runs on a dedicated DSP core.
24 system task are running simultaneously to user tasks (ADC decimation, DAC inputs interpolation, Data Acquisition signals pre-processing, communication, …)
Task Name | Activation Period (us) | Exec Time (us) | Digital IO | MFLOPS
NE_LN.hrd | 25 | 3.2 | 56 | 43
NE_Mar_LN.hrd | 25 | 5.2 | 50 | 64
NE_PSDf.hrd | 25 | 3.7 | 167 | 119
NE_PSDi.hrd | 25 | 3.3 | 40 | 46
NE_PSDm.hrd | 25 | 0.6 | 10 | 26
NE_PSDt.hrd | 25 | 0.6 | 104 | 26
NE_F7_CD.hrd | 25 | 1.9 | 32 | 34
NE_F7_LVDT | 25 | 0.7 | 20 | 25
NE_F7_LVDT_Demod | 3.125 | 1.9 | 0 | 134
 |  |  | Total | 516

## Slide 29: Example: Vertical Control
Four DSPs involved
Users develop only control algorithms using a simple text interface
Communication and synchronization transparent to users

## Slide 30: Data Flows
Each of the 20 LCU could handle continuously:
  More than 5000 high quality audio streams (320kbps)
  250 HD movies (3GB/hr)
  100 4K Ultra HD movies
Slot | kPkts/s RX | kPkts/s TX | MB/s RX | MB/s TX
AMC_1/8-11 | 160 | 120 | 44 | 33
AMC_2/8-11 | 0 | 80 | 0 | 22
AMC_3/8-11 | 0 | 80 | 0 | 22
AMC_4/8-11 | 0 | 160 | 0 | 44
AMC_6/8-11 | 120 | 120 | 33 | 33
InterSwitch_1 | 200 | 120 | 54 | 33
InterSwitch_3 | 240 | 40 | 65 | 11
AMC_7/8-11 | 200 | 80 | 54 | 22
AMC_11/8-11 | 120 | 80 | 33 | 22
AMC_12/8-11 | 160 | 40 | 44 | 11
 |  | Total | 207 | 207

## Slide 31: Upgrade running (prototypes ready soon)
The upgrade of existing system has been recently funded by the Virgo Collaboration for complete replacement of control electronics.
Virgo Subsystem Mirror Position Control
Main differences
  Fully compliant with MTCA.4
  Replace DSPs with TI 66AK2H14 Multicore DSP+ARM® KeyStone™ II System-on-Chip (SoC)
  Added flexibility with different rear modules
  In collaboration with INFN Bologna (Timing/DAQ Module)

## Slide 32: MicroTCA.4 (MTCA.4)
Functionalities that in old system are merged into a single board have been split into three different modules:
  DSP Front Module
  AD/DA Rear Module
  TimingDAQ Rear Module

## Slide 33: DSP Front Module

## Slide 34: AD/DA Rear Module
To speed up replacement, we keep same front end and data converters of system today in use
Any further improvement postponed.

## Slide 35: Future Upgrades
We are starting from existing VIRGO system and evolve gradually towards future architecture where presumably A.I. will play a key role.
Progress in Ethernet latency reduction will probably allow replacement of RapidIO.
DSP+FPGA architecture would presumably evolve in GPU+FPGA architecture but total latency cannot be larger than the 40 us we have today (minimum delay).
Key focusing is in high resolution converters and in lower low-frequency noise in general.
Improving total latency down to 3-4 us with solutions based on fast data converters and FPGA will allow extending feedback loops unity gain frequencies and therefore possible applications range.

## Slide 36: Einstein Telescope

## Slide 37: Real Time Systems Design
Real Time Systems
Control Theory
Programming Languages
Algorithms
Computers Architecture
Operating Systems
Signal Processing
High Resolution Data Converters
Low Noise Analog Electronics