## Slide 1: Aligning Data to Better Than one Picosecond
Erich Frahm, Roger Rusack, Rohith Saradhy, Yahya Tousi, Emily Vadnais.
The University of Minnesota
Rohith Saradhy

## Slide 2
One of the big problems of getting to ultra-precise timing is the distribution of the reference clock across the whole detector.
Current strategy is to send a clock encoded in the data stream from the off-detector electronics and monitor what comes back.
In this talk I will describe a new solution to monitor the reference clock on detector.

## Slide 3
Concentrate on this here.

## Slide 4
What are we doing now?

## Slide 5
From DRD7.3c Presentation by Louis D’Eramo Sept 25th 2025. — Here

## Slide 6
Primer on noise in clock signals:
A pure clock is a balanced sequence of zeroes and ones
An encoded clock is when a clock is encoded onto a date stream.
A clock data recovery (CDR) circuit is used to recover a pure clock from a data stream
Jitter, high-frequency phase variations.
Wander, Low frequency phase variations.

## Slide 7
What do you need to stabilize the clock on detector?
Something to detect the phase on-detector
Something to shift the phase if it is moves.
Jitter can be stabilized on detector with a PLL.
Wander cannot be corrected this way.
Wander can be caused by changes in the clock transmission system.
Eg 100 m fiber —> temperature change of 1C —> 16 ps drift.
To address this we need:

## Slide 8
Phase Shifter:
Two solutions:
Standard PLL with frequency adjustments.
Specialized ASIC with 300 fs steps — DCPS.

## Slide 9
Digitally Controller Phase Shifter
Low Delay
High Delay
and
Sequence of waveguide cells each with
62 cells with 300 fs steps — Max delay 20ps
Extended range with lumped delays to 250ps.
Temperature stable and rad tolerant.
0.8mm
1.3mm

## Slide 10
Demonstration: 1km stabilization

## Slide 11
DDMTD
The digital dual mean time difference (DDMTD) circuit used to measure phase difference between two same frequency clocks by measuring their beat times with a clock with a small frequency difference.

## Slide 12
DDMTD — Phase Detector
Length of the metastability interval as the phases align and un-align matters a lot!
FPGA implementation is limited by the setup-and-hold times of ~800 ps. This limits the phase detection resolution of the order of 2-3 ps.
Implemented the circuit with RF components with setup-and-hold times of ~20 ps and got resolutions of the order of 100~fs.

## Slide 13
On Detector Phase Stabilization

## Slide 14
DDMTD — ASIC
Rohith Saradhy designed a DDMTD ASIC in the TSMC 65nm LP process.
M. Maiti, A. Paul, S. K. Saw and A. Majumder, “A Dynamic Current Mode D-Flipflop for High Speed Application”
Designed in CML for speed and optimized for the DDMTD application.
Preliminary Cadence simulation (no added noise)

## Slide 15
DDMTD — ASIC
How to test it?

## Slide 16
DDMTD ASIC Test Setup:
40 MHZ Oven Controlled Crystal Oscillator
N = 100,000
717.000 MHz
716.993 MHz
7.17 kHz
Use PLL to adjust phase of test clock

## Slide 18
Clock 717 MHz
Frequency Offset
Standard Deviation of 76 femtoseconds

## Slide 19
Clock 717 MHz
Frequency Offset
Each point is average of ~2,000 collected at 7 kHz.
Standard Deviation of 28 femtoseconds

## Slide 20
Clock 717 MHz
Frequency Offset
Standard Deviation of 28 femtoseconds
Each point is average of ~2,000 collected at 7 kHz.

## Slide 21
On Detector Phase Stabilization

## Slide 22
This can now be less than 1 picosecond

## Slide 23
By detecting phase shifts at the front-end we can remove wander from our clock distribution systems and align the reference time across large subsets of a detector with sub-picosecond precision
With thanks to the DOE Office of Science, Division of HEP, who funded this research under award DE-SC0020185