## Slide 1: Axion Search with HAYSTAC Phase III Multi-Rod Cavity Upgrade
Claire Laffan (Yale University)
CPAD Workshop
October 8th, 2025
HAYSTAC is a collaboration between…
(host)
Located at…

## Slide 2: Axions as Dark Matter
Originally proposed axion field as solution to strong CP problem
Later found that axions are also dark matter candidates
One of the lightest DM candidates, making direct detection challenging
Inverse Primakoff Effect: Mixing between axion field & B-field induces E-field of frequency νa
νa ∝ ma
Coupling strength = gaγγ
ma & gaγγ both unknown
This interaction is a promising avenue for detection
Notes: Consolidate to 3-4 bullets

## Slide 3: HAYSTAC: Past, Present & Future

## Slide 4: A Brief History of HAYSTAC
Top: Xiran Bai et al. PRL 134, 151006 (2025)
Phase I (PI):
Jan. 2016 – Jul. 2017
23.15-24.00 μeV (5.6-5.8 GHz)
1 JPA
Phase II-ab & Phase II-cd (PII):
Sep. 2019 – Aug. 2024
16.96 – 19.46 μeV (4.1 – 4.7 GHz)
Quantum squeezing with 2 JPAs
Cavity:
Cu-plated stainless steel
Unfilled Vc = 1.545 L
1 tuning rod
(Haloscope At Yale Sensitive To Axion CDM)
HAYSTAC
HAYSTAC
HAYSTAC
Bottom left: M. Simanovskaia. Ph.D. thesis, UC,Berkeley (2019)
Bottom right: K. M. Backes. PhD thesis, Yale University (2021)

## Slide 5: Onto Higher Frequencies
Xiran Bai et al. PRL 134, 151006 (2025)
Here be dragons
Post-inflation axion models motivate high masses
Cavity frequency scales inversely with volume: Vc ∝ νc-3
Higher mass axion searches necessitate smaller cavities which have…
  Degraded signal power
  Higher intruder mode density
Electronic losses also increase with frequency
HAYSTAC plans to address these issues as we pursue higher frequencies

## Slide 6: HAYSTAC: Onto Higher Frequencies
Phase IIIb
Phase IV
Phase V
Phase IIIa
Xiran Bai et al. PRL 134, 151006 (2025)
7 tuning rods
5.5 – 7.3 GHz (22.75 – 30.19 μeV)
PIIIa: 7-Rod Cavity
Rev.Sci.Instrum. 96 094704 (2025)
PIIIb: 7-Rod + PBG
Y. Jiang et al., PRX Quantum 4 (2024)
PIV: CEASEFIRE
Rev.Sci.Instrum. 96 094704 (2025)
PV: Plasma Haloscope (ALPHA)

## Slide 7: Motivation for 7-Rod Cavity
Goal: Maximize cavity figure of merit (FOM) for given Vc
FOM = QC2Vc2
Many designs were simulated
Simulated Q & C, combined with V to calculate FOM
7-rod cavity configuration maximizes FOM for given volume
M. Simanovskaia et al, Rev. Sci. Instrum. 92, 033305 (2021)
Comparing Performance of 4 Cavity Configurations
(constant volume)
# Tuning Rods
1
1
7
7
Tuning Rod OD
2.00”
2.46”
0.625”
0.875”
Symbol
PI/II
PIIIa
Quality factor
Form factor
Notes: https://arxiv.org/pdf/2006.01248
Show predicted vs. realized FOM for PII maybe?

## Slide 8: 7-Rod Cavity Design

## Slide 9: PI & II vs. PIII: Cavity Design
Phases I & II
Δνc: 4.1 – 5.8 GHz
Single tuning rod
Asymmetrical mode structure
ID: 4”, height: 10”
Unfilled Vc ~1.545 L
Phase IIIa
Δνc: 5.5 – 7.3 GHz
7 tuning rods
6-fold symmetrical mode structure
ID: 4”, height: 10”
Unfilled Vc ~1.707 L
Maria Simanovskaia, Ph.D. thesis, UC Berkeley, 2019.
Simulated E-field density maps of TM010-like mode
Notes: Preserving (increasing!) volume while going to higher frequencies is cool

## Slide 10: Let’s take a closer look…
Top of cavity (with tophat)
Bottom of cavity
Bottom axles
Bottom endcap
Ball bearings
Drive shaft
Top axles
Gears
Top endcap
Antenna ports
(3 total)
Top of cavity (tophat removed)
Ball bearings
Collars

## Slide 11: 7-Rod Cavity Testing & Optimization

## Slide 12: Dedicated Cryogenic Testing Setup
First 7-rod cryo tests began at Yale in April
Testing at 15K in He fridge for fast turnarounds
Two critical functionalities need to work before data taking:
  Mechanical tuning
  Cryogenic Q
4K plate
1K plate
Tuning rod thermal braids
Tuning motor
Heat strap
Fridge with cavity testing setup, insulated with MLI

## Slide 13: Mechanical Tuning: Rod Design
Cu-plated Al, OD 0.625”, ~9.98” long
1/8” holes on both ends to insert axle
Dielectric joints between axle shaft & rod prevent RF leakage
Axles attached to rod with Stycast
Cure for 24hrs in alignment jig
Challenges:
Axles must be perfectly coaxial
Thermalization through dielectric joint
RF leakage through axles
Tuning rod cross-section
0.625”
Hole for axle
Ø 0.125”
↧ 0.5
0.125”
0.5”
9.98”
2.25”
1.00”
Dielectric “rolling pin”
Axle shaft
0.25”
0.125”
0.25”
Axle cross-section
Notes: Stycast 1266

## Slide 14: Mechanical Tuning: Optimization
Successful tuning requires perfect cooperation of all tuning rods & gears
Factors to optimize for tuning:
Smooth bearings
Radial tuning rod alignment
Gear engagement
Tuning rod axle-alignment
  Very challenging
  3 alignment jig iterations
Tuning rod thermalization
  Change axle shaft material
SS axle shaft
Copper axle shaft
3
Alignment Jig Iterations
1
2

## Slide 15: Mechanical Tuning: Success!
S21
TM010 mode
Achieved full cryogenic tuning range
5.5 - 7.5 GHz
Now to tackle cryogenic Q…
Mode map from first successful cryogenic tuning.
(Blank patches from interpolation)

## Slide 16: Cryogenic Q: The “Hot Rod” Problem
K. M. Backes. PhD thesis, Yale University (2021)
Cavity Spectra
Off-resonance
On-resonance
PSD
HAYSTAC has always observed excess cavity noise
Potential culprits:
  Vibrations (publication pending)
  RF leakage through tuning rod axles
  Tuning rod not thermalizing
Improved in PII:
  Copper stems inserted through alumina axles improved thermalization
  Did not fully fix problem
  Difficult to implement in 7-rod
Needs to be addressed for upgrade to multi-rod cavity
On-resonance power excess indicates cavity is not in thermal equilibrium

## Slide 17: Cryogenic Q: Optimization
Features to optimize:
Rod thermalization
  Switching to Cu axle shafts helped
  Could be further improved by changing dielectric joint material
RF leakage through axles
  Need dielectric joint that conducts heat well
Search for new dielectric joint material:
Promising candidate: 50/50 Stycast & copper powder (by volume)
Hypothesis: Stycast serves as dielectric, Cu improves thermal conductivity & acts as filter against RF leakage
Promising, but still being characterized
Stycast
Cu + Stycast

## Slide 18: Current Status & Outlook
Quality factor optimization studies still underway
  Testing full 7-rod assembly with Cu-Stycast dielectric joints
  Will move ahead with install if cryogenic Q is good
  Will continue investigating this problem with PII cavity
Cryogenic tuning is well understood & optimized
Installation by end of year

## Slide 19: Thank You!

## Slide 20: Backup Slides

## Slide 21: Thermal Conductivity Measurements
Thermal conductivity of samples measured in BlueFors dilution refrigerator
Cu-Stycast promising

## Slide 22: Cryogenic Q: Optimization
Features to optimize:
Rod thermalization
  Switching to Cu axle shafts helped
  Could be further improved by changing dielectric joint material
RF leakage through axles
  Need dielectric joint that conducts heat well
Search for new dielectric joint material:
Promising candidate: 50/50 Stycast & copper powder (by volume)
Stycast serves as dielectric, copper improves thermal conductivity
Suspended copper powder may also serve as filter against RF leakage
Stycast
Cu-Stycast
Copper
7.1 GHz Al cavity
3-axis micrometer
Sample
Cu-Stycast sample had promising results for Q retention