## Slide 1: EIC International Accelerator Collaboration Commissioning Tool Workgroup EIC Virtual Accelerator Updates
Yue Hao

## Slide 2: Plans for EIC VA
EIC Accelerator Complex
IOC
IOC
IOC
IOC
IOC
EIC Virtual Accelerator
Machine Portal / Database
Machine Model
MADX
Elegant
BMAD
Beam-Beam Sim.
...
USER Interface
(JupyterHub)
AI/ML applications
Control Room
Software, GUI
Deploy
Infer
Train

## Slide 3: July 2025 Updates, Overview
Current effort : Machine Portal
  Separate machine description
Adopt the concept of PALS
  Only small subset is implemented
  Parameter is grouped by parameter groups
  Define ControlP group
  Option fields: PV_names, str_limit, ramp_rates, …
Export and Load from Human readable file
  YAML is chosen
EIC Machine Portal
Design
Lattice
Import
Machine readable Machine Description file (YAML)
Control Interface, PVAccess

## Slide 4: July 2025 Updates, Code Status
Repo: git@github.com:yuehao/EICViBE.git
A short Example of FODO Description file
name: FODO
root_branch: FODO
elements:
- Bend:
name: Bend1
length: 2.0
BendP:
ANGLE: 0.15707963267948966
- Drift:
name: Drift1
length: 1.0
- Quadrupole:
name: Quad1
length: 0.6
MagneticMultipoleP:
K1: 1.2
ApertureP:
X:
- -0.05
- 0.05
…
FODO:
- Bend:
name: Bend1_1
length: 2.0
inherit: Bend1
BendP:
ANGLE: 0.15707963267948966
- Drift:
name: Drift1_1
length: 1.0
inherit: Drift1
- Quadrupole:
name: Quad1_1
length: 0.6
inherit: Quad1
…