## Slide 1: The RFX-mod2 experiment
CUP: B53C22003070006
L. Marrelli and the RFX-mod2-team
NEFERTARI Final Workshop
Padova, 22-25/3/2026

## Slide 2: RFX-mod2 is a Reversed Field Pinch
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)

## Slide 3: RFX-mod2: Toroidal field Coils
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)
  Toroidal Field Coils: Low Engineering Demand
    Reduced External Field: Plasma-generated bulk field.
    Moderate Mechanical Stress: Low Lorentz forces on windings

## Slide 4: RFX-mod2: Poloidal Field Coils
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)
  Toroidal Field Coils: Low Engineering Demand
    Reduced External Field: Plasma-generated bulk field.
    Moderate Mechanical Stress: Low Lorentz forces on windings
  Poloidal field coils: Air core high flux swing (15 Vs)
    Pure Ohmic Heating: No auxiliary heating required for RFP

## Slide 5: RFX-mod2: Power supplies
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)
  Toroidal Field Coils: Low Engineering Demand
    Reduced External Field: Plasma-generated bulk field.
    Moderate Mechanical Stress: Low Lorentz forces on windings
  Poloidal field coils: Air core high flux swing (15 Vs)
    Pure Ohmic Heating: No auxiliary heating required for RFP
    Versatile MW-class power plant featuring modular ac/dc units

## Slide 6: RFX-mod2: high power test facility
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)
  Toroidal Field Coils: Low Engineering Demand
    Reduced External Field: Plasma-generated bulk field.
    Moderate Mechanical Stress: Low Lorentz forces on windings
  Poloidal field coils: Air core high flux swing (15 Vs)
    Pure Ohmic Heating: No auxiliary heating required for RFP
    Versatile MW-class power plant featuring modular ac/dc units
      Qualification tests for ITER Fast Discharge Units FDU (70kA,24kV), JT-60SA Quench Protection Unit QPC (25 KA, 4kV) and development of next step reactors Magnetic Energy Storage and Transfer system (MEST)

## Slide 7: RFX-mod2: active control
RFX-mod2 is the second modification of the Reversed Field eXperiment which is a Reversed Field Pinch (RFP) (R=2m,a=0.49)
  Paramagnetism: Bulk B-field self-generated by plasma.
  Field Reversal: Inverted edge pitch (Cyan vs. Red lines)
  Toroidal Field Coils: Low Engineering Demand
    Reduced External Field: Plasma-generated bulk field.
    Moderate Mechanical Stress: Low Lorentz forces on windings
  Poloidal field coils: Air core high flux swing (15 Vs)
    Pure Ohmic Heating: No auxiliary heating required for RFP
    Versatile MW-class power plant featuring modular ac/dc units
  Active control of MHD instabilities; (J.D. Lawson 1977 proposal)
    3mm thick copper shell
    48x4 independent coils
J.D. Lawson, (1977) Reversed Field Pinch Reactor Studies. Part I., Physical Principles, CLM-R171
C.M. Bishop, (1989) Plas. Phys. Contr. Fus, 31, 1179

## Slide 8: RFX-mod results: multiple Resistive Wall Modes stabilization
RFX-mod proved that multiple RWMs can be simultaneously suppressed [1,2]
[1] S.Ortolani, Active MHD control experiments in RFX-mod. Plas Phys Contr Fus. 2006;48(12B):B371
[2] Bolzonella T, et al. Resistive-Wall-Mode Active Rotation in the RFX-Mod Device. Phys Rev Lett 2008; 101: 165003
Without Control
Controlled after 150ms
Fully controlled

## Slide 9: RFX-mod-results: highest plasma current for an RFP
Reversed-Field pinch 2 MA plasma current target level was achieved in RFX-mod thanks to
  Advanced mode control strategies [2]
  Power supplies configuration flexibility [1] (15.8 Vs flux swing)
No MHD control
Simple Virtual Shell [3]
Advanced ModeControl [2]
Power supply reconfiguration [1]
[1] Novello, et al (2011). "Enhancement of the power supply systems in RFX-mod towards 2 MA plasma current". ''Fusion Engineering and Design'' 86: 1393-1397,
[2] Zanca, Marrelli, Manduchi, Marchiori (2007). "Beyond the intelligent shell concept: the clean-mode-control". ''Nuclear Fusion'' 47: 1425-1436.
[3] Ortolani and RFX-mod team, (2006) Plasma Physics and Controlled Fusion 48, B371

## Slide 10: RFX-mod results: From Multiple Helicity
At low plasma currents many tearing modes are present, spooling performances and generating localized bulging of the plasma column.
RFX (and RFX-mod with non optimal control)

## Slide 11: RFX-mod results: From Multiple Helicity
At low plasma currents many tearing modes are present, spooling performances and generating localized bulging of the plasma column.
  RFX-mod was able to partially mitigate wall locking by slowly rotating the bulging
RFX (and RFX-mod with non optimal control)
RFX-mod with Advanced Mode Control

## Slide 12: RFX-mod results: From Multiple Helicity to Quasi single Helicity
At high plasma currents (Ip > 1MA) one tearing mode dominates and the core plasma becomes helical with internal transport barriers
Lorenzini, (2009). "Self-organized helical equilibria as a new paradigm for ohmically heated fusion plasmas". ''Nature Physics'' 5: 570-574.

## Slide 13: RFX-mod as a ohmic tokamak, Very Low q and Ultra Low q
Thanks to TF coils design (0.5T for 1 s) and active feedback
  RFX-mod also operated below the q(a)<2 limit [1]
  Performed disruption prevention studies [2]
  Performed runaway mitigation with RMP [3]
[1] Zanca P, et al.. Plasma Phys Control Fusion. 2012 Sep 1;54(9):094004
[2] Zanca P., et al. (2015). "An active feedback recovery technique from disruption events induced by m = 2, n = 1…, Nuclear Fusion 55: 043020.
[3] Gobbin, et al (2024). "Runaway electron mitigation by 3D fields application in ASDEX upgrade, COMPASS, and RFX-mod". ''Frontiers in Physics'' 12

## Slide 14: RFX-mod: shaped tokamak
Reconfigurable connections to field shaping coils allow shaping
  Positive and Negative Triangularity
  Single (upper and lower) Null, Double Null, Snow Flake
D. Abate, Plasma Phys. Control. Fusion 62, 085001 (2020)

## Slide 15: From RFX-mod
RFX-mod performances were limited by the highly resistive Inconel Vacuum Vessel, causing wall locking of multiple Tearing Modes and subsequent localized Plasma Wall Interaction
Mechanical support structure
Passive stabilizing Cu shell
Vacuum vessel
First wall (graphite)
RFX-mod

## Slide 16: From RFX-mod to RFX-mod2
RFX-mod performances were limited by the highly resistive Inconel Vacuum Vessel, causing wall locking of multiple Tearing Modes and subsequent localized Plasma Wall Interaction
Thanks to POR FESR regional funding «MIAIVO», RFX-mod have been modified to remove the Inconel Vessel
Mechanical support structure
Passive stabilizing Cu shell
Vacuum vessel
First wall (graphite)
RFX-mod
RFX-mod2

## Slide 17: RFX-mod2 expectations
With the new boundary the localized edge deformation decreases by a factor 3
Zuin, et al (2017). Nuclear Fusion 57: 102012.

## Slide 18: RFX-mod2 expectations
With the new boundary the edge deformation decreases by a factor 3
Wall locking is simulated to occur at 500-800 kA (instead of 100-150kA)
RFX-mod Inconel
RFX-mod2 Copper
Marrelli L, et al.,. Nuclear Fusion. 2019 Jul 1;59(7):076027
Zuin, et al (2017). Nuclear Fusion 57: 102012.

## Slide 19: RFX-mod2 expectations
With the new boundary the edge deformation decreases by a factor 3
Wall locking is simulated to occur at 500-800 kA (instead of 100-150kA)
25% reduction of tearing mode energy
RFX-mod Inconel
RFX-mod2 Copper
Marrelli L, et al.,. Nuclear Fusion. 2019 Jul 1;59(7):076027
Zuin, et al (2017). Nuclear Fusion 57: 102012.
RFX-mod
RFX-mod2

## Slide 20: RFX-mod2: status of vessel complex reassembly
RFX-mod2 Vessel Complex components in the assembly hall

## Slide 21: The NEFERTARI opportunity: plants revamping and key diagnostics
Revamped key auxiliary plants
  Vacuum system (WP1)
  Toroidal field power Supplies (WP1)
  Wall conditioning systems: Glow Discharge (WP1) Cleaning and Pulse Discharge Cleaning (WP1)
  Remote Manipulation (WP1)
  Electromagnetic measurements and model based control (WP2)
Revamped and enhanced existing diagnostics; allows applications of codes for experiment interpretations
  Edge diagnostics (WP3)
  Core diagnostics (WP4 & WP5)
Foster the integration of expertise and pave the way for future common research
  High Voltage Insulation (WP6)
  Plasma Wall Interaction (WP7)
  Neutron and SXR imaging diagnostics (WP8)
  Spectroscopic diagnostics & advanced modelling (WP9)

## Slide 22: RFX-mod2 research themes
Complete exploration of 2MA Reversed Field Pinch Exploit real-time control capabilities both for RFP and tokamak
  Model based (machine learning) control algorithms
    FEM, BEM of passive structures and plasma response
  Non magnetic real-time plasma position control with reflectometry
Explore 3D physics in high current Reversed Field Pinch plasmas
  Plasma Wall Interaction
  MHD dynamics with controlled 3D boundary
Explore 3D effects in ohmic tokamak
  Error fields
  Experimental characterization of disruptions
    electromagnetic induced forces direct measurements
Fundamental Plasma physics studies in multiple configurations
  Edge turbulence and microinstabilities
  Magnetic reconnection and particles accelerations
  Transport barriers characterization

## Slide 23
Spare Slides

## Slide 27: RFX @ Consorzio RFX
RFX was a toroidal device for magnetic confinement in Reversed Field Pinch (RFP) configurations
  (R=2m,a=0.457)
  Operated in 1991-1999
RFX was modified and became RFX-mod
  Operated in 2004-2015