## Slide 1: Trigger Happy Or How & why we analyse a really, very large amount of data really, very fast
Andy Rose, Imperial College, London
awr01@imperial.ac.uk
www.hep.ph.ic.ac.uk/~awr01

## Slide 2: Science: The basics
Science is the art of knowing what to record, and when

## Slide 3: Science: The basics
Science is the art of knowing what to record, and when
Or being cynical, it's being in the right place at the right time

## Slide 4: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate

## Slide 5: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
Ten orders of magnitude
Probability
100(100%)
10-2(1%)
10-4
10-8
10-10
10-12
Events per second at LHC
Beam Energy
10-6

## Slide 6: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building

## Slide 7: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 316 years, 324 days (5 hours, 6 minutes and 17 seconds give or take)

## Slide 8: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 316 years, 324 days (5 hours, 6 minutes and 17 seconds give or take)
And one Higgs boson is pretty much USELESS We need loads of them to be able to study them…

## Slide 9: This is why the LHC collides…
̴50 protons at a time × 40 million times a second

## Slide 10: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds

## Slide 11: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems

## Slide 12: One proton-proton collision

## Slide 13: Many proton-proton collisions
25 proton-proton collisions

## Slide 14: Many proton-proton collisions
25 proton-proton collisions
Even if you get a Higgs boson, the RUBBISH makes it hard to find

## Slide 15: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes problems too

## Slide 16: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 17: Big detectors for small particles

## Slide 18: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 19: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 20: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
500M Swiss Francs 10 years to build

## Slide 21: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
Covers 205m2
Most intense radiation environment on the planet Installation completed before release of 1st iPhone
And…

## Slide 22: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals
× 40 million snapshots per second

## Slide 23: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
× 40 million measurements per second

## Slide 24: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
What does that even mean?

## Slide 25: How much data?

## Slide 26: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
CMS Raw

## Slide 27: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
1× Home broadband
1,000,000× Home broadband
1,000× Home broadband
CMS Raw
CMS tape-store

## Slide 28: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
1× Home broadband
1,000,000× Home broadband
1,000× Home broadband
CMS Raw
CMS tape-store
But do we need to store it all?
The Higgs is rare, after all

## Slide 29: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep

## Slide 30: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep
Called Triggering

## Slide 31: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep
Called Triggering
uninteresting crossings to discard
The LHC is a discovery machine, after all

## Slide 32: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long

## Slide 33: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long
And that is a *really, really* expensive mistake

## Slide 34: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes other problems too

## Slide 35: A note on timescales
At 40MHz BX rate, a 4GHz CPU could perform 100 CPU operations before the next data arrives
  Not enough to be useful
Compare that to the O(100M) detector channels

## Slide 36: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 37: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 38: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid

## Slide 39: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid
But this is exactly what a PC does

## Slide 40: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 41: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
So why doesn’t my PC do this?

## Slide 42: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
Because writing code like this is *really, really* hard
So why doesn’t my PC do this?

## Slide 43: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 8.9 million logic cells & up to 12,000 “math” cells
  All clocked at ̴500MHz
Over O(1015) operations/second
  That is PetaBOps
Fully parallel and fully pipelineable

## Slide 44: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 8.9 million logic cells & up to 12,000 “math” cells
  All clocked at ̴500MHz
Over O(1015) operations/second
  That is PetaBOps
Fully parallel and fully pipelineable
and *really, really* hard to program efficiently

## Slide 45: Field-Programmable Gate Arrays
A chip needs to be attached to something!
Imperial’s latest platform: Serenity
  208 optical transmit links & 208 optical receive links @ 28.5Gbps =
  Skewable to
5.9 + 5.9 Tbps
7.0 + 4.8 Tbps

## Slide 46: The future: High-luminosity LHC
Averaging 250 proton-proton collisions per event
Really, really hard to find the interesting event under all that rubbish
Need to sift through 300Tbps to find the interesting events
150 proton-proton collisions

## Slide 47: But this is the 21st century…
How do you deal with hard problems and big data?

## Slide 48: But this is the 21st century…
How do you deal with hard problems and big data?

## Slide 49: But this is the 21st century…
How do you deal with hard problems and big data?
Ummm… It's not quite that simple

## Slide 50: Why can't you just use Machine Learning at HL-LHC?
The data is still only safe on the detector for ~10 microseconds
  Not much time
The trigger is receiving ~100Tbps from the tracker, ~100Tbps from the barrel calorimeter and ~100Tbps from the endcap calorimeter
  AKA 1 hellavalotta data
Recall, that you can't see the data the trigger throws away…
  You need to be *REALLY* sure you know what your algorithm is doing.
The detector environment is always changing, inference may not look anything like your training data

## Slide 51: Why can't you just use Machine Learning at HL-LHC?
The data is still only safe on the detector for ~10 microseconds
  Not much time
The trigger is receiving ~100Tbps from the tracker, ~100Tbps from the barrel calorimeter and ~100Tbps from the endcap calorimeter
  AKA 1 hellavalotta™ data
Recall, that you can't see the data the trigger throws away…
  You need to be *REALLY* sure you know what your algorithm is doing.
The detector environment is always changing, inference may not look anything like your training data

## Slide 52: That said… if it works, why wouldn't you use it?
For certain, well-defined sections of the trigger chain, machine-learning is a useful and powerful tool
  Tools developed for translating Neural Networks for use in high-throughput and low-latency systems
Work being done in the area of understandable AI
Work being done in the area of continual learning

## Slide 53: Conclusion
The hardware triggers at the LHC are some of the most computationally challenging problems on the planet
They are a great deal of responsibility

## Slide 54: Conclusion
The hardware triggers at the LHC are some of the most computationally challenging problems on the planet
They are a great deal of responsibility
And, if you like puzzles, a great deal of fun 