## Slide 1: A Hybrid Asymmetic Linear Higgs Factory
Brian Foster (Oxford/DESY)

## Slide 2: Hybrid Asymmetric Linear Higgs Factory (HALHF)
https://arxiv.org/2303.10150
ILC
CEPC

## Slide 3: Plasma Wave Acceleration

## Slide 4
SCRF Cavity
Plasma wakefield
Plasma vs SCRF Cavities

## Slide 5: Plasma vs SCRF Cavities
SCRF Cavity
Plasma wakefield
5

## Slide 6: Plasma vs SCRF Cavities
SCRF Cavity
Plasma wakefield

## Slide 7: Setting the scale
Notes: Contrast with conventional cavities….
Work at Lawrence Berkeley Laboratory. 40 TW laser pulse (3 * 10 18 W/cm2) – 1 GeV in 3.3 cm
produced 33 GV/m fields. Beam quality lousy! Florian is at forefront of this table top infra-red FELs.

## Slide 8: Plasma Acceleration 101
Non-linear (“Blow-out”)
Regime (nb/n0 >>1)
Linear Regime (nb/n0 << 1)
Non-linear (“Blow-out”)
Regime (nb/n0 >>1)
Ack. For next 3 slides: S. Deiderichs:
https://ediss.sub.uni-hamburg.de/bitstream/ediss/10403/1/SDiederichs-PhD-Thesis.pdf

## Slide 9: The problem with positrons

## Slide 10: Positron acceleration
e-
e+

## Slide 11: Positron acceleration
There are many schemes for e+ acceleration – but currently, none can be tested experimentally.
Most involve some
sort of shaping or
truncation of
plasma to inhibit
return flow of
electrons from
blowout.

## Slide 12: Positron Acceleration
Even if one of these schemes proves to work reliably and reproducibly, they are generally not close to
collider regime.

## Slide 13: Origin of HALHF
The basic idea is – there are enough problems with a PWFA e- accelerator; e+ is even more difficult. Bypass this for e+e- collider by using conventional linac for e+.
For this to be attractive financially, conventional linac must be low energy => asymmetric energy machine.
This requirement led to (at least for us) unexpected directions – the more asymmetric the machine became, the better!

## Slide 14: Relativistic Refresher
We thought that the optimum (see later) for Ecm = 250 GeV is to pick Ee = 500 GeV, Ep= 31 GeV, which gives a boost in the electron direction of g ~ 2.13.

## Slide 15: Power Efficiency
Asymmetric machines less energy efficient than symmetric – energy lost “in accelerating the C.o.M.” For equal bunch charges => 2.5 times more power required for same C.o.M. energy.
Can be reduced by introducing asymmetry into beam charges – increase charge of low-energy beam and decrease high-energy s.t. N2 = NeNp constant => L conserved.
P/P0 = (NeEe+NpEp)/(N*sqrt(s))
Optimum is to scale e+ charge by sqrt(s)/(2Ep), i.e. factor ~ 4.
Producing so many e+ problematic – compromise by scaling by factor 2 (2*e+, ½* e-).
Reduces power increase to 1.25. Also reduces bunch charge in PWFA arm.

## Slide 16: Emittance reduction
Geometric emittance of bunch scales with 1/E .
Lower-energy e+ beam must have smaller b function at I.P. – use bx /by = 3.3/0.1 mm c.f. CLIC 4.0/0.1 mm.
In contrast, high-energy e- beam - b function can be increased, which could reduce complexity of BDS.
More interesting is to increase the e- emittance AND reduce the b function => normalized emittance can be 16 times higher for the same L => increased tolerances in PWFA arm.
Beam-beam focusing effect on L must be simulated with Guinea Pig.

## Slide 17: HALHF Layout
e-
e+
e+ BDS
e- BDS

## Slide 18: But hang on…..
HALHF Collaboration “kick-off” meeting @ DESY 23/10/23. Attendance ~ 50.
HALHF Workshop @ Oslo 4-5/4/24. Attendance ~ 30 (physical+ Zoom).
https://indico.cern.ch/event/1370201/

## Slide 19: Second thoughts

## Slide 20: ABEL: The Adaptable Beginning-to-End Linac simulation framework
A start-to-end simulation framework, using OpenPMD
Adaptable implementations — choose fidelity versus speed for each subsystem
Running other codes via wrappers (also submits HPC jobs etc.) — HiPACE++, WakeT, ImpactX, GUINEAPIG, ELEGANT, CLICopti
Run simulations as experiments — run simulations with multiple shots, incl. random jitter — perform automated scans (one-liner) — perform parameter optimisations
“System code” (term borrowed from e.g. fusion) — integrated cost modelling — machine layouts
Chen et al., TUPS012, IPAC’25
Now released as open source - Repository: https://github.com/abel-framework/ABEL
Facility Optimisation

## Slide 21: Blow-out simulation
PIC simulation with HiPACE++, He @ 6 × 1014 cm−3 ; driver and main beam (orange) 8 & 1.6 nC. Excess ion density
on axis (green)

## Slide 22: Two-stage simulation

## Slide 23: ABEL: The Adaptable Beginning-to-End Linac simulation framework
Towards Full Simulation

## Slide 24: ABEL: The Adaptable Beginning-to-End Linac simulation framework
Facility Optimisation

## Slide 25: ABEL: The Adaptable Beginning-to-End Linac simulation framework
Facility Optimisation

## Slide 26: Second HALHF workshop
Facility Optimisation
2nd HALHF
Workshop,
Erice,
3-8 October,
2024

## Slide 27: HALHF New Baseline
Foster et al., Phys. Open 23, 100261 (2025)

## Slide 28: HALHF @ CERN

## Slide 29: HALHF New Baseline
Cost estimates for HALHF 2.0
Driver RF linac is a major cost driver for the machine (~30%; 50% incl. e+ linac)
    Drivers: ~22 CHF/watt beam power
    Positrons: ~167 CHF/watt beam power
PWFA linac is not a cost driver (~7%)
    Driver distribution is the cost driver
BDS and IP (~13%) adds
Civil engineering adds ~25% to the machine cost, other overheads ~30%
    Cooling and ventilation is expensive (~3.6 CHF/watt wall-plug power)
Based scaling from ILC and CLIC
E. Adli et al. “HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration”, arXiv:2503.19880

## Slide 30: Experimentation at HALHF
Boost is smaller than HERA - HERA detectors very similar to those at symmetric machines.
Also H & Z heavy, so anyway more homogeneous.
Measurement of L via Bhabha (e+e- -> e+e-) - rate reduced by 1/(qg)2 & e+ scattered into barrel – but not a problem. Singles rate good for machine optimisation

## Slide 31: Experimentation at HALHF
Simulation by M. Berggren, A. Laudrain (DESY) – extend ILC Barrel as proxy for forward detector;
“Proper” simulation needed and under discussion.

## Slide 32: Preparation for pre-CDR
Despite ~ 0 project funding (only a few FTEs from JAI general programme, DESY & CERN), HALHF is making rapid progress;
New baseline & costing carried out;
HALHF input to European Strategy: 10pager:https://arxiv.org/abs/2503.19880
Backup: https://arxiv.org/abs/2503.23489 ~ 15 year R&D programme before approval
Regular monthly HALHF meetings;
Longer-term goal: pre-CDR this year; & funding to start R&D programme;
Contribute to 10 TeV design

## Slide 33: The march of progress
NB – many of these issues, particularly transverse tolerances and instability mitigation are still work in progress!

## Slide 34: Path to construction
https://indico.cern.ch/event/1439855/contributions/6461458/attachments/3045828/5381747/HALHF_Input_ESPP_2025_Backup_submitted.pdf

## Slide 35: 10 TeV Wakefield Collider
Challenges
Inefficient acceleration of positrons in plasma
  Proposed solution: Take advantage of large VBF cross-section and utilize gamma-gamma or e-e- collisions instead.
Extreme beamstrahlung at high collision energies and beam densities
  Proposed solution: 1) Collide ultrashort bunches to mitigate beamstrahlung and 2) Embrace the broad luminosity spectrum so long as significant fraction of the colliding particles are close to 10 TeV CM.
Detector design and background modeling for high energy collisions
  Proposed solution: Development of new Particle-in-Cell codes, benchmarked against GUINEA-PIG and CAIN, to accurately model backgrounds for high-energy gamma-gamma, e-e-, and e-e+ collisions.
10 TeV Design Study sign up @ https://docs.google.com/forms/d/e/1FAIpQLScffLXDxF_8-TUYaWLznL7jAWUGfYOTEzBu4YrOnr8nRS-JQw/viewform

## Slide 37: 10 TeV Wakefield Collider
Simplified 10 TeV γ–γ collider with “two HALHFs”

## Slide 38
(April 2025)
Summary

## Slide 39: Summary & Outlook
Despite ~ 0 funding, HALHF is making rapid progress;
New baseline & costing carried out;
HALHF input to European Strategy: 10pager:https://arxiv.org/abs/2503.19880
Backup: https://arxiv.org/abs/2503.23489 - ~ 15 year R&D programme before approval
Regular monthly HALHF accelerator meetings;
Medium-term goal: pre-CDR in 2026 & funding to start R&D programme;
Contribute to 10 TeV design.
  PLEASE JOIN US: https://adams-institute.ac.uk/halhf

## Slide 40: Backup slides

## Slide 41: Running Costs
Dominated by power to produce drive beams.
(100*16*4.3nC + 6.4nC)*100 => 47.5 MW@50% eff.
Damping rings: 2*10 MW.
Cooling – assume similar to CLIC => 50% of RF power (corresponds to 20 kW/m).
For magnets and other conventional sources assume ~9 MW.
Gives total power requirement ~ 100 MW – somewhat smaller than other proposals.

## Slide 46: Bunch pattern

## Slide 47: R&D Topics

## Slide 48: R&D Topics - Staging

## Slide 49: R&D Topics - Beam-Delivery
Challenges: Emittances: Factor 10-100 larger than in previous designs;
𝜷x : Factor 2-4 smaller
=> Longer than current design beyond 250 GeV
See. R. Thomas talk
@ LCWS25

## Slide 50: R&D Topics - Plasma Cell

## Slide 51: Selected Updates
PWFA arm:
  Flat beams (essential to get required lumi at IP while minimising beamsstrahlung)
    “Resonant emittance mixing of flat beams in plasma accelerators”
    S. Diederichs et al., arXiv:2403:05871
    Issue: when ion motion present, non-linear focusing mixes planes
    => Flat beams don’t stay flat
    Possible solution: flat drive beams
    Seems to work – but need to evaluate ion-motion from witness beam

## Slide 52: Path to construction

## Slide 53: Path to construction

## Slide 54: Path to construction

## Slide 55: Upgrade Existing LC
Technology being developed for HALHF could also enhance a “conventional” LC design – part of “LCVision”:
Assume: ILC has been built, -> 2x125GeV linacs available
Goal: upgrade electron arm to 500GeV with plasma -> 125x500GeV -> 500GeV COM; g ~ 1.2 -> upgrade a Higgs factory to a tth / Zhh factory
Use electron linac for drive and witness beam: run a lower gradient but higher current, upgrade RF on electron arm
Use space for undulator source between electron ML and BDS to install plasma booster
Feed boosted electrons into existing BDS (laid out for 500GeV)
(B. List)
Space for plasma booster

## Slide 56
1
3
Diagram and image courtesy: F. Pena, J. Beinortaitė
[1] R. D’Arcy, BF, et al., Nature 603, 58-62 (2022)
Trailing bunch
Driver
63 ns
Accelerated bunch on the energy spectrometer
Rate limits in Plasma
Demonstrates >10 MHz repetition
Rate in Ar – lighter gases faster.
Notes: In principle, the plasma recovers quickly enough to enable MHz acceleration. However, there are also other mechanisms in play, such as cell heating and gas expulsion.
BRIDGE: Now we want to actually do acceleration at MHz
56

## Slide 57: HALHF results
Preliminary results for HALHF (simplified interstage, driver guiding assumed): With no ion motion, the BBU is large. With ion motion, the BBU is efficiently mitigated up 10-2 nm rad drive-beam jitter-emittance – “state of the art” FLASH@DESY - position jitter of ~30 nm. A halo of large amplitude particles has formed, driving up the rms emittance, while the 90%-percentile emittance is better preserved.
E. Adli, IPAC’25
At the end of the HALHF linac:

## Slide 58: Importance of driver guiding
Centre of cell
Centre of drive beam
Main beam trajectory
Driver injection angle:
may lead to large main beam offset
Mitigation: guiding driver with an external magnetic field,
here simulated in HiPACE++ (radially focusing field).
Driver guiding has been assumed in the following ABEL simulations
Without magnetic guiding-field
With magnetic guiding-field

## Slide 59: Positron Source
“Conventional” e+ sources are not trivial – that for ILC, which has relaxed requirements wrt HALHF, still under development.
e- accelerated to 5 GeV and then collide with target to produce e+ which are accumulated, bunched and accelerated to 3 GeV and then damped in 2 rings (~identical to CLIC but bigger e+ bunch charge (4*1010 e+).
May be possible to use spent e+ bunch after collision rather than dedicated e- bunch, with cost savings.

## Slide 60: Polarized e+
Produce e+ polarization via ILC-like scheme - ideas exist for E(e-) 500 GeV; wiggler probably longer and more expensive. Cost ~ 300 MILCU minus conventional source cost.