## Slide 1: On Electron Cloud Effects and Possible Mitigation Strategies
This work was performed under the auspices of, and with support from, the Swiss Accelerator Research and Technology (CHART) program (www.chart.ch).
Luca Sabato1, Lotta Mether2, Tatiana Pieloni1, Adam Furman1,2,
Cantún Karla3, Maury Humberto4, Yaman Fatih5
Acknowledgments: Oide Katsunobu, Zimmermann Frank, Zobov Mikhail , Iadarola Giovanni
1 2 3 4 5
IAS Program 12-15th January 2026, HONG KONG

## Slide 2: Outline
Introduction
Multipacting and Stability
Photoelectrons
Mitigation Techniques
Conclusions and Outlooks

## Slide 3: Outline
Introduction
Multipacting and Stability
Photoelectrons
Mitigation Techniques
Conclusions and Outlooks

## Slide 4: Motivation
Electron cloud (e-cloud) effects have been observed in several accelerators all over the world (LHC, KEKB, DAɸNE, …)
  more commonly in those operated with positively charged particles
Presently among the major performance limitations for high energy collider
  transverse beam instabilities
  incoherent beam effects
  vacuum degradation
  heat load
E-cloud effects have to be studied for FCC-ee
  to give input to chamber design and material properties to avoid e-cloud formation
  define beam parameters and identify performance limitations

## Slide 5: E-Cloud Formation
With the particle bunch passage
  primary electrons can be accelerated to energies up to hundreds of eV
  after impacting the wall, secondary electrons can be emitted
Secondary electrons have energies of tens of eV
  after impacting the wall, they can be either absorbed or elastically reflected
  if they survive until the passage of the following bunch, they can be accelerated, projected onto the wall and produce secondaries
Secondary electron emission can drive an avalanche multiplication effect
    electron cloud
    Bunch passage
    e- is emitted
    Secondary Electron Emission
Courtesy of
G. Iadarola
A circulating beam can produce primary electrons (seed)
  ionisation of the residual gas in the beam chamber
  photoemission from the chamber’s wall due to the synchrotron radiation emitted by the beam

## Slide 6: E-Cloud Parameters
Quadrupole
Dipole
Chamber geometry influences e- acceleration and time of flight
Surface properties have a primary role in the e- multiplication process
  The main quantity involved is the Secondary Electron Yield (SEY):
  depends on
    surface chemical properties
    history of the surface, in particular on accumulated electron dose
Bunch spacing  It determines how many electrons survive between consecutive bunch passages and has direct impact on multipacting threshold
  For FCC-ee: the strongest e-cloud effects are foreseen for the Z running mode due to the largest number of bunches (smallest bunch spacing)
Bunch intensity and bunch length  affect the acceleration received by the electrons
Magnetic fields  Electron trajectories are strongly influenced
Electron density 103 e-/mm3

## Slide 7: Outline
Introduction
Multipacting and Stability
Photoelectrons
Mitigation Techniques
Conclusions and Outlooks

## Slide 8: E-Cloud Build-up Studies for FCC-ee baseline
Extensive simulation campaign scanning all relevant parameters using Zimmerman-Rumolo model (PyEcloud)
Simulations have been benchmarked versus Furman-Pivi model  F. Yaman, “Electron cloud simulations using the Furman-Pivi model”, FCC-ee electron cloud meeting 18/03/2025
Important to understand the impact of lower bunch intensity (we will need to fill the ring and then top-up), chamber radius, magnetic fields of different elements
  “Electron cloud studies”, FCC week 2023
  “Electron Cloud Studies”, FCC week 2025
  “Update on the Electron Cloud Studies for FCC-ee”, FCC e-cloud meeting 12/09/2023
From Feasible Study Report
Bunch Intensity [x1011 ppb] | Bunch Spacing [ns] | Number bunches / Train | Number Trains | Gap Length [ns] (gap/bunch spacing)
2.15 | 25 | 280 | 40 | 575 (23)
Studies done for GHC Lattice by Ohmi-san
Main collider
Effects visible for positrons- electron beam effect negligible

## Slide 9: E-Cloud Build-Up Studies: multipacting
Bunch population | SEY multipacting thresholds
nominal | 1.4
below nominal | 1.0
  Starting from an initial random seed of uniformly distributed electrons of 107 e/m
  Avoid Multipacting:
   Compute the Average electron density for different SEY values and different magnetic elements (drift, dipole, quads, sextupoles)
   Repeat for intensities in the range from 0.2-2.5 1011 ppb to establish the intensity dependency and identify worse case during the accumulation phase
Secondary Emission Yield (SEY)
Nominal bunch intensity
Lower bunch intensity:
charge accumulation phase
Dipole case

## Slide 10: E-Cloud Build-Up Studies Baseline
Element | Field | Bunch population | Thresholds
Drift Space | - | nominal | 1.4
 |  | below nominal | 1.2
Dipole | 15.2 mT | nominal | 1.4
 |  | below nominal | 1.0
Quadrupole | 1.45 T/m | nominal | 1.1
 |  | below nominal | 1.0
Sextupole | 72.5 T/m2 | nominal | 1.1
 |  | below nominal | 1.0
Non monotonic behaviour versus intensity of the cloud formation (intensities [1.0-1.5] ∙ 1011 ppb most critical) problematic during top-up and accumulation!
The SEY multipacting thresholds are extremely tight for baseline parameters
  difficult to satisfy using the baseline copper chamber with thin NEG coating (SEY 1.0-1.2) might require more complex surface treatments
Dipole, Quadrupoles and sextupoles have the lowest SEY multipacting thresholds

## Slide 11: E-Cloud Stability Threshold
E-cloud could trigger instabilities, because the beams pass through the e-clouds and they receive transverse kicks
Is the central density above the stability threshold? Which is the e-cloud density stability threshold?
  Theoretical equation:
  Simulations by means of PyECLOUD-PyHEADTAIL in order to track the beams through the e-clouds and observe instability rise and parameter evaluations (emittances)
From K. Ohmi et al., “Study of Electron Cloud Instabilities in FCC-hh”, Proc. of IPAC2015
  Theoretical and numerical e-cloud density stability threshold have the same order of magnitude with strong vertical instability observed and with relevant emittance blow-up

## Slide 12: E-Cloud Stability: Summary
  Dipoles and Quadrupoles
  Above the SEY multipacting threshold, the central e-cloud density before the bunch passage is larger than the e-cloud stability threshold  leads to beam instabilities
Sextupoles
  The central e-cloud density before the bunch passage is smaller than the e-cloud stability threshold (element length dependence)
Above the SEY multipacting threshold, the e-cloud leads to beam instabilities, because the central density is above the stability threshold

## Slide 13: Outline
Introduction
Multipacting and Stability
Photoelectrons
Mitigation Techniques
Conclusions and Outlooks

## Slide 14: Photoelectron Emission
The circulating beam particles can produce primary electrons via photoemission from the chamber’s wall due to the synchrotron radiation emitted by the beam
The results presented in the previous slides do not take into account the photoemission
  What is the impact of the photoelectrons on the e-cloud formation process?
Material properties determine the conversion from radiation to electrons Absorber structures control where most of the radiation impacts the walls
The number of photoelectrons is determined by:
  the amount of photons scattered into the main beam chamber
  the Photoelectron Yield (PY)
    property of the beam chamber
    defined as the ratio between the emitted photoelectrons and the number of impinging photons
Simulations of photon flux with Synrad curtesy Marton Ady, Gabriel Saretti
Photon Flux

## Slide 15: Photoelectron Yield Limit
Dipole
  Number of photoelectrons generated per positron and per unit length
The central density could be larger than the stability threshold even below the SEY multipacting threshold
High values of npe should be avoided ( < 1.0 ∙ 10-4 (e+ m)-1 )
The PY and the number of photoelectrons are related through the following equation
  φ: realistic photon flux -> from ray tracing codes (e.g., SYNRAD+ Marton-Saretti) in the order of 1013 - 1014 photons/cm2 s (not in the absorber areas)
The constraint on the material is very tight with PY~ 2x10-3  incompatible with the expected PY of the foreseen chamber surface (0.1-0.25 for NEG coated!) (in the absorber areas the photon flux is expected to be even higher!)
A new design of the photon absorbers is under development and will reduce the photon flux inside the main beam chamber by a factor 100 !
A detailed photoelectron emission model based on synchrotron radiation simulations will be developed and studies extended to understand the impact of photoelectrons in realistic configurations  new PhD student Adam Furman
  I: beam current (1.27 A)
  L: chamber's perimeter (278 mm)
  e: elementary charge

## Slide 16: Outline
Introduction
Multipacting and Stability
Photoelectron Impacts
Mitigation Techniques
Conclusions and Outlooks

## Slide 17: Mitigation I: Non-Uniform Bootstrap Injection
During the charge accumulation phase: do not fill the bunches of the train uniformly, in this way the critical bunch intensities will be reached with a larger bunch spacing
  Hannes Bartosik, FCC week 2024
With special filling schemes during the charge accumulation phase, the SEY multipacting thresholds are higher and they tend to the SEY multipacting thresholds for the nominal bunch intensity

## Slide 18: Charge Accumulation Phase: Summary
Element | Field | Special filling schemes during charge accumulation phase | Uniform 25 ns | 
Drift Space | - | 1.4 | nominal | 1.4
 |  |  | below nominal | 1.2
Dipole | 15.2 mT | 1.3 | nominal | 1.4
 |  |  | below nominal | 1.0
Quadrupole | 1.45 T/m | 1.1 | nominal | 1.1
 |  |  | below nominal | 1.0
Sextupole | 72.5 T/m2 | 1.1 | nominal | 1.1
 |  |  | below nominal | 1.0
A major concern with this approach is having bunches of significantly different intensities in the collider at the same time, which makes difficult to find a working point that ensures stability for all bunches
Studies on the interplay between beam-beam effects and impedance show that the horizontal plane is dominated by the coherent x-z instability not enough tune space to accommodate the expected bunch-by-bunch intensity and voltage spread
Roxana Soos et al., FCC week 2025

## Slide 19: Mitigation II: 5ns non-uniform Bunch Spacing
Investigated possible filling schemes: reduced bunch spacing and small gaps after
Considering larger bunch spacing (20 ns and 15 ns), the gap lenght is not long enough to mitigate the e-cloud
  e-cloud after the bunch passages and the gap is larger than the initial e-cloud density
Considering very small bunch spacing (10 ns and 5 ns), the gap is long enough to mitigate the e-cloud
  e-cloud after the bunch passages and the gap is smaller than the initial e-cloud density
Bunch spacing 15 ns with 3 bunches and 2 empty
Bunch spacing 5 ns with 2 bunches and 8 empty

## Slide 20: Short Bunch Spacing: 10 ns vs 5 ns
Considering the passage a full train of 280 bunches and the following train gap
Higher SEY threshold for lower intensities is obtained using NON-uniform filling schemes with 5 ns bunch spacing
Bunch spacing 5 ns with 2 bunches and 8 empty
Multipacting
regime
Bunch spacing 25 ns uniform
Dipole case

## Slide 21: Non-uniform Bunch Spacing 5 ns
2b+8e
4b+16e
5b+20e
8b+32e
Considering the passage of a full train of 280 bunches and the following train gap, a better e-cloud mitigation is obtained using filling schemes with 5 ns bunch spacing
Electron average densitieas are reduced
SEY multipacting thresholds for critical bunch intensities are increased: could mitigate!
Dipole case

## Slide 22: Non-uniform Bunch Spacing 5 ns: Summary
Element | Field | Bunch population | Uniform 25 ns | 2b+8e | 4b+16e | 5b+20e | 8b+32e
Drift Space | - | nominal | 1.4 | 1.4 | 1.4 | 1.4 | 1.3
 |  | below nominal | 1.2 | 1.4 | 1.4 | 1.4 | 1.3
Dipole | 15.2 mT | nominal | 1.4 | 1.4 | 1.3 | 1.3 | 1.2
 |  | below nominal | 1.0 | 1.2 | 1.2 | 1.2 | 1.2
Quadrupole | 1.45 T/m | nominal | 1.1 | 1.3 | 1.3 | 1.3 | 1.3
 |  | below nominal | 1.0 | 1.2 | 1.3 | 1.3 | 1.3
Sextupole | 72.5 T/m2 | nominal | 1.1 | 1.4 | 1.5 | 1.5 | 1.4
 |  | below nominal | 1.0 | 1.3 | 1.5 | 1.5 | 1.4
Using filling schemes with non-uniform bunch spacing, the strict constraint on the SEY multipacting thresholds could be mitigated, for all the analysed magnetic elements
No tighter constrains during accumulation
Need to be further explored with photoelectrons
Investigating possible implementation (impedance, injectors…)

## Slide 23: Outline
Introduction
Secondary Electron and Photoelectron Emission
Electron Cloud Effects
Mitigation Techniques
Conclusions and Outlooks

## Slide 24: Conclusions and Outlooks
The material constraints in order to avoid e-cloud avalanche multiplication and to control photoelectrons are extremely tight for baseline parameters and planned 150nm NEG coating (SEY 1.0-1.2, PY~0.1-0.2)
  Above the SEY multipacting threshold (as low as below 1.0), the e-cloud leads to beam instabilities for central densities above 2x1010 m-3
  Considering the additional contribution of the photoemission on the e-cloud formation process, the beam could be unstable even below the SEY multipacting threshold: PY ~ 10-3 required for existing photon flux  New photo absorbers are underdevelopment to improve by factor 100 the photon absorption very challenging
  Further systematic studies and the development of a more detailed model describing the impact of photoelectrons on electron cloud effects have started
Incoherent ecloud effects have to be addressed Electron and positron beams will experience different electron-cloud effects  slightly different parameters for the two beams with consequences for other collective effects
Non-uniform 5ns bunch spacing filling schemes mitigates the e-cloud formation process
  Discussions and studies on-going to evaluate possible implementation
  Investigation of the effectiveness of various active mitigation strategies of the e-cloud instabilities, such as the use of a transverse feedback system in combination with chromaticity and octupole settings are also under going

## Slide 25: Thanks for your attention

## Slide 26: Mitigation techniques : Larger Bunch Spacing
Element | 25 ns | 30 ns | 40 ns | 50 ns
Drift Space | 1.2 | 1.3 | 1.5 | > 1.6
Dipole (15.2 mT) | 1.0 | 1.1 | 1.2 | 1.3
Quadrupole (1.45 T/m) | 1.0 | 1.0 | 1.1 | 1.3
Sextupole (72.5 T/m2) | 1.0 | 1.1 | 1.3 | 1.4
Larger bunch spacing
E-cloud could be mitigated using larger bunch spacing
Dipole 50 ns
From FCC Feasibility Study Report (March 2025)
Increasing the bunch spacing requires increasing the bunch intensity to maintain a constant beam current
 Larger bunch intensities could lead to problems due to other collective effects, such as beam-beam and beam-coupling impedance (Mauro Migliorati FCC week 2024)

## Slide 27: SEY Models
ECLOUD Model
Furman-Pivi Model
Courtesy of Fatih Yaman
Furman-Pivi model is more pessimistic:
  Multipacting occurs for lower SEY
  Larger e-cloud density
More details in: F. Yaman, “Electron cloud simulations using the Furman-Pivi model”, FCC-ee electron cloud meeting 18/03/2025
Simulations based on different parametrisations of the surface SEY

## Slide 28: Heat Loads: Drift Space
Filling scheme 1
Filling scheme 2
If multipacting (considering nominal bunch intensity and maximum simulated SEY=1.6):
  Filling scheme 1: ∼38.7 W/m -> full circumference ∼673 kW ∼1.35% of synchrotron radiation power
  Filling scheme 2: ∼25.3 W/m -> full circumference ∼439 kW ∼0.88% of synchrotron radiation power
If no multipacting (considering SEY smaller the SEY multipacting threshold, all simulated bunch intensities):
  Filling scheme 1 (SEY<=1.1) & 2 (SEY<=1.2): smaller than 0.01 W/m -> full circumference smaller than 200 W ∼0.0004% of synchrotron radiation power
  Ldrift = 17.4 km (Ldrift /L = 19.18%)
Synchrotron radiation power: ∼50 MW per beam

## Slide 29: Heat Loads: Summary
In case there is multipacting, the total heat loads are in the order of:
  5-7% of synchrotron radiation power for the filling scheme 1
Dipoles are the main contributors to the total heat loads
If there is no multipacting, the total heat loads are negligible compared to the synchrotron radiation power

## Slide 30: E-Cloud Stability Simulation Threshold
  considering only the drift length Ldrift = 17.4 km (Ldrift /L = 19.18%)
Stable
Very unstable
Horizontal
Vertical
Centroid/
Sigma
Unstable
Normalised emittance/
Normalised emittance [t=0]
  Theoretical and numerical e-cloud density stability threshold have the same order of magnitude: ⍴e,th = 9.53 ⋅1010 e-/m3
  Vertical plane is unstable
Drift Space case:

## Slide 31: 5 ns Uniform Bunch Spacing (56,000 bunches)
Sextupole
Quadrupole
Dipole
Drift
Analysed ranges
  Bunch spacing: from 25 ns down to 5 ns
  Total number of bunches per train: from 280 up to 1,400 (Number of trains 40)
  Nominal bunch intensity: from 0.43e11 ppb down to 4.3e10

## Slide 32: Comparison 25 and 5ns Uniform Bunch Spacing
Element | Field | Bunch population | 25 ns | 5 ns
Dipole | 15.2 mT | nominal | 1.4 | 1.2
 |  | below nominal | 1.0 | 
Drift Space | - | nominal | 1.4 | 1.1
 |  | below nominal | 1.2 | 
Quadrupole | 1.45 T/m | nominal | 1.1 | 1.0
 |  | below nominal | 1.0 | 
Sextupole | 72.5 T/m2 | nominal | 1.1 | 1.1
 |  | below nominal | 1.0 | 
5 ns uniform bunch spacing
e-cloud density are higher when there is multipacting
Considering the nominal case the SEY multipacting thresholds are lower

## Slide 33: Charge Accumulation Phase
Option 1
Option 2
Option: 1 Booster Cycle: 200
Courtesy of Hannes Bartosik (FCC week 2024)

## Slide 34: Mitigation: Non-Uniform reduced bunch spacing
Analysed trains with uniform bunch spacing
Trains with 25 ns bunch spacing
Trains with smaller bunch spacing and with small gaps in order to mitigate the e-cloud (keeping the same train duration):
Trains with 10 ns bunch spacing (2 bunches + 3 empty bunches)
Time [ns]
1 2 3 280
0 25 50
...
Time [ns]
1 2 3 280
0 10 20 30 40 50
...
e e e

## Slide 35: Outlooks: Nested Magnets
Quadrupole
Sextupole
Dipole
Dipole + Quadrupole
Nested Magnets under exploration by overlapping dipole fields with arc quadrupoles and sextupoles
  Thereby increasing the dipole filling factor and reducing the synchrotron radiation
On going development on HTS SSS magnets development (Koratzinos et al.)
On going studies on nested magnet alternative optics (more details in L. Van Riesen-Haupt presentation)
The configurations with nested magnets have to be studied from the e-cloud point of view
10.0
Dipole + Quadrupole + Sextupole