## Slide 1
Challenge Gravitational Wave Measurement with a Novel Mössbauer Spectrometer
Huaqiao ZHANG (IHEP)
张华桥 （高能所）
In collaborate with Yu GAO, Wei XU
Science Bulletin 2024; 69(18): 2795-2798
10.1016/j.scib.2024.07.038
IAS 2026 -remote

## Slide 2: Outline
Introduction
How to achieve precision and speed needed for gravitational wave use novel Mossbauer Spectrometer
Setup for Multi-band gravitational wave detection use this novel Mossbauer Spectrometer
Summary and proposals

## Slide 3: Gravitational Wave
ALi
Taiji，Tianqin
Lisa
PBH/SR
GW： a new way to explore our universe
PTA
(Fast)
Accuracy needed at the order of thickness of a paper over the diameter of solar system
Ligo,Virgo
Kargra,ET…

## Slide 4: Mössbauer effect
1961
Recoil-less emission and resonant absorption of nuclear transition photons
  Mössbauer active nucleus bound to solid state lattice
  Thermal vibration(~1013 Hz) much faster than nuclear transitions (lifetime ~>10-7 s)
    Effect averages to zero, no 1st Doppler broadening
    Recoil to the whole crystallite(>1014 atom)
    Without phonon excitations recoil free
recoil

## Slide 5: Doppler shift
Sound
Photon： E=hv
Red shift
Notes: 精密移动探针，来测量极小的能量变化

## Slide 6: “Traditional” Mössbauer Spectrometer
Change the recoil-less emission and absorption overlap with doppler effects
Strength of recoilless nuclear resonant absorption as determined by the “overlap” of emission and absorption lines when the emission line is shifted by Doppler modulation
High accuracy of the resonant absorption width w.r.t. photon energy
Widely used in material science, chemistry, and even on mars rovers
Notes: 穆斯堡尔谱仪原理
源，吸收体，计数探测器，运动控制： 简单可靠，精度高，灵敏度高

## Slide 7: Relativity test with Mössbauer effect
Gravitational redshift test with Mössbauer effect
Pound, Rebka & Snyder (1960-1965)
Observation of a height-induced frequency shift

## Slide 8: Mössbauer for Gravitational Wave
Idea since 1970
  Photon frequency varies when it propagates in an un-even space-time background.
  No experimental proposal till our work
Gave way to clock-based experiments in later tests of “static” gravity.
  See K. Hentschel, Annals of Science 53, 269–295 (1996)

## Slide 9: Issues in traditional Mössbauer Gravity tests
A cryogenic 65Zn measurement of the local g-value (Potzel et.al. 1992)
Differential measurement of the resonance with a sinusoidal oscillator
  Resonance is achieved
  g-value is off, possibly due to various line-shifts
  Take hours-days to achieve high acc.
“such solid-state effects might be difficult …… there might exist two exceptions. The first are null redshift experiments,
in particular measurements with stationary source and absorber”.
Can be improved with a stationary scheme：
Quoted from the paper

## Slide 10: Idea of the stationary measurement
Doppler shift ==> Gravitational shift
  V=1mm/s  ~10-12 = 1mm  ~10-19
<<r
Improve on sensitivity to energy shift

## Slide 11: Design of a gravitational shift Mössbauer Spectrometer
Replace Doppler shift with gravitational shift
Parallel readout the resonant absorption shape
Time dependent resonance’s height-shift （not absolute height）
  Frequency of resonance peak hight shift  GW frequency: multi-band
Radioactive source (intensity RS)
0
-h
h
distance (d)
Photon counters with proper Z resolution,
¼ cut view
x
Z
Resonance peak(s)
Energy loss ER is compensated by a slight height difference between absorber and source: can be calibrated in advance. --- the absolute height of resonance (Z0) is affected by large systematics: 2nd Doppler, chemical composition, etc. --- but its time-dependent shift under GW is not affected.
horizontal→
absorption layer
Demo. Only

## Slide 12: The choice of isotope source: 109Ag
Mössbauer database (DICP, CAS)
Narrow 88 keV linewidth: O(10-22) sensitivity
Workable ΔZ ~ 10μm under terrestrial (1 g) gravity field for
Long parent nuclei lifetime: 461 days allow for sufficient operation time
IC ~ 26, small fraction of gamma emitted
The quest of the 109Ag resonance:
, (W. Wildner and U. Gonser, 1979)
Improved resonance resolution, w broadening factors down to 16 (US) R. D. Taylor and G. R. Hoy, SPIE 875, 126 (1988).
S.RezaieSerej, G. R. Hoy, and R. D. Taylor, Laser Phys. 5, 240 (1995). Russian group: improvements with Grav. Effects V. G. Alpatov, et.al. Laser Physics 17, 1067–1072 (2007).
Yu. D. Bayukov, et.al. JETP Letters 90, 499–503 (2009).

## Slide 13: The transmission integral
Photon emission at source
  Fractional recoil-less : fs,
  Fractional recoiled:1-fs
Photon absorption at absorber
  Mass attenuation effect: all photons
  Resonant absorption: only resonant emitted photons
The transmission integral (textbook)
  Replaced the doppler shift with gravitational shift

## Slide 14: Accuracy from Pseudo experiments
Pseudo experiment simulation with reasonable parameter
  Ex: vertical z-position resolution 10 μm, detection efficiency ~100%
  Readout frequency ~10 fGW, Energy resolution exclude non-88 keV BG
Sensitivity extracted by fitting the resonance absorption peak
Accuracy compatible to the accuracy needed for GW strain
Silver alloy/compound with higher TdeBye helps improve fS e.g. AgB2 has a higher TdeBye and fS =0.2 (@ 4K)
Parallel measure of resonance absorption shape: fast enough for GW

## Slide 15: The GW signal: photon energy shifts
Consider a plain-wave strain perturbation
A particle’s 4-momentum response to GW strain after one-way propagation:
Estabrook and Wahlquist, Gen. Relat. Gravit. 6, 439–447 (1975);
Hellings, Phys. Rev. D 23, 832–843 (1981).
(figure from Hellings paper)
Energy diff. between and
Energy shift due to different space-time matrix for photon emission and absorption
source
absorber

## Slide 16: Stationary Mössbauer GW setup
Absorber+detectors are in the resonance plane around source
  At least two perpendicular directions relative to any GW incident θ angle.
  Enhance acceptance of resonances photons
* highest sensitive to GW wavelength ~d/2
* The distance d between source and absorber can be tabletop size

## Slide 17: Hypothetical GW signal “seen” by our experiment
Modulation of resonance peak shifts in the ring
  Allow GW direction and polarization reconstruction

## Slide 18: Expected sensitive on GWs
AC: 106 periods: table top
B: single period
Coherent GWs from NS, SR, PBHs, see N.Aggarwal et al., Living Rev. Rel. 24, 4 (2021) Inverse Gentsenshtein: also see: 2305.00877
Science Bulletin 2024; 69(18): 2795-2798
Max Freq. Reach: cutoffs at:
*3σ peak with ,
*
1011 Bq. 1m, ground
1014 Bq., 100m, 10-4g
Region of interests
Limited by photon counter and readout

## Slide 19: Summary
Conceptional design GW experiment use novel gravitational redshift Mössbauer spectrometer:
  Measure the spatial resonance absorption peak shift under GW.
  Allow direction and polarization reconstruction.
  Relatively small-scale setup (meter – 100 meter for your preference)
  109Ag source gives 10-22 strain sensitivity, long lived mother particle.
  Multiband sensitivity（Sensitive to fGW > kHz）
Possible extension on sensitivity
  low-g, focusing of photons…
Larger source-absorber distance:
  Aiming for lower frequency GWs

## Slide 20
Phase 0: Tabletop exotic/Axion(arXiv:2511.14851，arXiv:2512.18960） physics searches
Phase 1: Tabletop Ground based GW experiment
Phase 2: low-g GW experiment (higher sensitivity)
Space based experiment
Moon/Asteroid based experiment
saddle/Lagrangian point based experiment？