## Slide 1
AWAKE-UK collaboration
A flavour of our UK contributions to AWAKE
Dr Morgan Hibberd
Ernest Rutherford Fellow
morgan.hibberd@manchester.ac.uk
UK-CERN Accelerator Celebration Day
Daresbury Laboratory + CERN | 27th November 2025

## Slide 2
AWAKE-UK collaboration: Areas of research and development
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Discharge plasma source
Claudia Cobo
Lewis Kennedy
Louis Forrester
Zulfikar Najmudin
Plasma density step
Energy spectrometer
Fern Pannell
David Cooke
Matthew Wing
Beamline design
Beam position monitors
Eleonora Belli
Bethany Spear
Philip Burrows
Synchronisation
Joshua Gregory
Ben Wooley (CERN)
Ed Snedden (ASTeC)
Rob Apsimon
Amos Dexter
Single-shot emittance
Bunch length monitors
Debdeep Ghosal
Joseph Wolfenden
Carsten Welsch
Betatron radiation
Cherenkov diffraction
Hossein Saberi
Jack McGunigal
Guoxing Xia
Electro-optic monitors
Terahertz manipulation
Samuel Norman
Collette Pakuza (CERN)
David Walsh (ASTeC)
Morgan Hibberd
Two-pulse ionisation injection
Abigail James
Ramy Aboushelbaya
Robin Timmis
Peter Norreys

## Slide 3
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Discharge plasma source
Beamline design
Synchronisation
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 4
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Discharge plasma source
Beamline design
Synchronisation
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 5
K. V. Lotov, Physics of Plasmas 22, 103110 (2015)
Numerical simulation results
Uniform plasma
Low-amplitude wakefields after saturation
Density step plasma
Larger amplitude maintained after saturation
Energy gain
 Measurement of integrated longitudinal wakefield
Varying plasma length
 Measurement of accelerating gradient
Plasma density ne = 3.8 x 1014 cm-3
10m energy gain uniform: ~1 GeV
10m energy gain step: ~ 1.6 GeV
Larger accelerating gradient with density step
Strong agreement between numerical simulations and experimental measurements
Simulation using LCODE 2D
Preliminary
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Slides provided by Fern Pannel
Measure energy gain with varying plasma length

## Slide 6
Laser-ionised plasma 10.3m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
Diagram not drawn to scale
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 7
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
The plunger experiment
Slides provided by Fern Pannel

## Slide 7
Laser-ionised plasma 10.3m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 10
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 8
Standard
acceleration
Through
Laser dump
2
4
7
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 11
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
The plunger experiment
Slides provided by Fern Pannel

## Slide 9
Laser-ionised plasma 10.3m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 12
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 10
Laser-ionised plasma 9.5m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 13
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 11
Laser-ionised plasma 8.5m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 14
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 12
Laser-ionised plasma 7.5m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 15
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 13
Laser-ionised plasma 6.5m
Laser dump 2 (LBDP2)
Quadrupole doublet
Dipole
Scintillator screen
Camera array
Vapour source
Spectrometer
Plungers
1
2
3
4
5
6
7
8
9
10
10.3m
Protons
Injected electrons
0.5m
Accelerated electrons
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | 16
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Diagram not drawn to scale
The ‘plungers’ (laser dumps) allow us to study the acceleration as a function of the plasma length
We can attempt to perform a direct measurement on the accelerating gradient (dE/dz)
The plunger experiment
Slides provided by Fern Pannel

## Slide 14
K. V. Lotov, Physics of Plasmas 22, 103110 (2015)
Numerical simulation results
Uniform plasma
Low-amplitude wakefields after saturation
Density step plasma
Larger amplitude maintained after saturation
Experiment: Measure energy gain with varying plasma length
Energy gain
 Measurement of integrated longitudinal wakefield
Varying plasma length
 Measurement of accelerating gradient
Plasma density ne = 3.8 x 1014 cm-3
10m energy gain uniform: ~1 GeV
10m energy gain step: ~ 1.6 GeV
Larger accelerating gradient with density step
Strong agreement between numerical simulations and experimental measurements
Simulation using LCODE 2D
Preliminary
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Slides provided by Fern Pannel

## Slide 15
The main diagnostic to study the accelerated electrons
Quadrupole doublet  electron bunch focusing
C-shaped dipole  separate electrons from protons
Scintillator screen  electron impact causes scintillation
Camera systems  capture the scintillation light
Integrating current transformer  charge calibration
Measurements of the energy, energy spread, charge
Run 2a & 2b: Upgrades to the imaging systems for measurements of the transverse emittance
Camera array
Light to intensified camera
Quadrupole doublet
Beam current transformer
C-shaped dipole
Scintillator screen
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | B2
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
The magnetic spectrometer
Slides provided by Fern Pannel

## Slide 16
Camera array is the main imaging diagnostic for Run 2a & 2b acceleration
7 cameras cover entire screen, improved resolution over old system
The beam is rarely fully contained within a single camera
Need to view full beam  Capture full energy/charge distribution
Full screen  absolute position calibration
SPECTRO 1
SPECTRO 2
SPECTRO 3
SPECTRO 4
SPECTRO 5
SPECTRO 6
SPECTRO 7
STITCHED SPECTRO
F. Pannell | AWAKE Collaboration Meeting 15.10.25 | B3
AWAKE-UK collaboration: Plasma density step
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
The magnetic spectrometer – Imaging system

## Slide 17
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Discharge plasma source
Beamline design
Synchronisation
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 18
Plasma density step (+ spectrometer)
Discharge plasma source
Beamline design
Synchronisation
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Areas of research and development

## Slide 19
330 A
500 A
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Discharge plasma source
Discharge plasma source development
1 m argon arc discharge produced using 8 kV pulse generator
Discharge reproducibility improved with increased current
MHz rep rate operation of pulse generator tested on dummy load
Scale acceleration over longer distances (>100 m)
Require different plasma technology
Slides provided by Claudia Cobo

## Slide 20
Longitudinal interferometry
Reveals radial expansion of plasma during discharge pulse
Plasma emission spectroscopy
Provides information on plasma temperature and longitudinal uniformity
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Discharge plasma source
Discharge plasma source diagnostics
Acknowledgements: AWAKE scalable plasma sources R&D team
Slides provided by Claudia Cobo

## Slide 21
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Discharge plasma source
Beamline design
Synchronisation
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 22
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 23
1st plasma source
2nd plasma
source
Dipole
injection point
7.5 cm clearance around the proton beam required
Diagnostics
installation
Expansion volume
Proton beam
Electron beam
Focal point moved 21 cm upstream to maintain 30 cm gap between plasma sections
Full design ongoing
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Beamline design
Run 2c preparation and integration studies
Slides provided by Eleonora Belli
New 150 MeV electron line required for injection into plasma
Extremely complex region (electrons, protons, plasma, lasers)

## Slide 24
Proton line: horizontal correctors to inject the proton beam off-axis into the 1st plasma cell to compensate the bending of the dipole between the two plasma sections
  New configuration: two angled plasma sources
18 MeV electron line: mu‑metal shielding feasibility study ongoing to mitigate the influence of the Earth’s magnetic field
Commissioning plan to be integrated into LS3 master schedule
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Beamline design
Slides provided by Eleonora Belli

## Slide 25
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 26
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 27
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Synchronisation
Back in 2016 Lancaster developed the Booster Linac for Run 1
Issues locking lasers to RF  Provided a Mach Zehnder solution
Ultimately synchronisation and RF stability were not a limiting factor for Run 1
Bunch synchronisation for Run 2c
One of Run 2c key goals is to demonstrate high quality acceleration
  Preservation of emittance and energy spread
Requires witness bunch injection stability at < 50-100 fs level
Plasma wakefield phase locked to seed electrons
Need to synchronise seed and witness electron bunches
Slides provided by Joshua Gregory/Amos Dexter
Contributions to Run 1
Critical to monitor and improve bunch synchronisation/locking for Run 2c

## Slide 28
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Synchronisation
Slides provided by Joshua Gregory/Amos Dexter
Beam arrival time monitor using stabilised links
~150 MeV witness line linac
~18 MeV seeding line linac
Seeding bunch dump
Witness bunch energy spectrometer
400 GeV protons
Self modulation plasma cell
Acceleration plasma cell
BAM
BAM
RF master clock 3 GHz
IR Menlo Mode Locked laser 1560 nm, 88 MHz rep rate
Titanium Sapphire fibre amp.
UV lasers
Titanium Sapphire fibre amp.
Pulse selector
BOXC
length stabilised fibres carrying 88 MHz clock pulses
BAM: Beam arrival time monitor
BOXC: Balanced optical cross correlator
Arrival times are measured at the BAM with respect to the clock pulses
stretcher
stretcher
BOXC
780 nm

## Slide 29
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Synchronisation
Slides provided by Joshua Gregory/Amos Dexter
Balanced optical cross correlator (BOXC) design
mode locked fibre laser
1560 nm
HWP
QWP
Stabilised fibre link to Beam Arrival Time Monitor
Forward pulse
Reflected pulse
QWP
Beam Splitter Prism
Moveable mirror adjusts delay of reference pulses up to 11 ns so they are roughly co-incident with reflected pulses
QWP
Stretcher
Polarised reflected pulse
Polarised reference pulse
Optical Master Oscillator
Dichroic mirror
Dichroic mirror
780 nm
780 nm
Non-linear crystal generates second harmonic only when two signals co-propagate
Balanced photodiode output determines whether fibre link is stretched or unstretched
Nonlinear crystal for SHG
Development underway for Run 2c

## Slide 30
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 31
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 32
Proton bunches longer (250ps) than electron bunch (1-5ps)
Low frequency signal dominated by protons
Current stripline BPMs unable to measure electron beam position when protons are present
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Beam position monitors
High-frequency e-BPMs
Slides provided by Bethany Spear
Option 1: Cherenkov Diffraction based BPM
6 mm diameter, 86 mm long alumina rods angled at the Cherenkov angle (71°), 9.6 GHz cut-off
Options for testing
Option 2: High-frequency button BPM
Conical shaped high-frequency button BPM developed at DESY

## Slide 33
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Beam position monitors
High-frequency e-BPM R&D studies
Slides provided by Bethany Spear
Schematic of signal acquisition for ChDR (top) and HF BPM (bottom)
Single shot waveform of voltage response to electron beam passing in centre of beam pipe.
At low proton intensities, successful discrimination of electron signal
Sensitivity to electron signal is
  2%/mm for ChDR BPM
  0.8%/mm for HF Button
Contribution of proton signal in different frequency bands.
ChDR
Electron signals with (red) and without (blue) the proton bunch are well-matched

## Slide 34
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
Diagnostics
AWAKE-UK collaboration: Areas of research and development

## Slide 35
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 36
Optical pepper-pot
Full 4D transverse phase space reconstruction
Targeting ~1 mm.mrad resolution
Quadrupole scans as integrated benchmarking
OTR & OSR (non-invasive)
Integration studies for Run 2c advancing well
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Transition and synchrotron radiation diagnostics
OTR/OSR single-shot emittance
Slides: Joe Wolfenden/Debdeep Ghosal
Testing at CLEAR

## Slide 37
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Transition and synchrotron radiation diagnostics
Broadband CTR/CSR imaging for bunch length
Slides: Joe Wolfenden/Debdeep Ghosal
Prototype system installed and operational at MAX IV SPF
Design flexible to large range of bunch lengths
CTR (imaging and compression) & CSR (compression)
Machine learning studies to extract profile information

## Slide 38
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 39
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 40
  Plasma wakefields produces extremely strong accelerating and focusing fields
  Witness electrons in wakefield oscillate and emit betatron radiation
  Study BR for AWAKE and its feasibility as a diagnostic tool
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Betatron radiation diagnostics
Betatron radiation as a diagnostic tool
Slides provided by Hossein Saberi
  Simulation studies
  Particle-in-cell simulations to understand betatron radiation features.
  Spectral features: span from UVX to X-ray
  Machine learning
  Application of neural network to predict beam parameters from X-rays of betatron radiation.
  H. Saberi et al. Phys. Plasmas 30, 043104 (2023)
  L. Liang, H. Saberi et al. J. Plasma Phys. 89, 965890301 (2023)
  H. Saberi et al. Physics of Plasmas 31, 093104 (2024)
  H. Saberi et al. Data-driven betatron diagnostics, Submitted to Plasma Phys. Control. Fusion (2025)

## Slide 41
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 42
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 43
J. McGunigal, G. Xia, C. Davut, P. Karataev, S. Mazzoni, T. Lefevre, C. Pakuza, A. Schlögelhofer, R. Kieffer
Non-invasive and single-shot measurement
Calculated using the intensity ratio of coherent ChDR in two different frequency bands.
Calibrated with bunch profile reconstructed using a Martin-Puplett interferometer.
Tests were performed at CLEAR comparing with their RF deflector bunch length measurements
Zero-bias Schottky diode
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Cherenkov diffraction radiation
ChDR as a bunch length monitor
Slides provided by Jack McGunigal

## Slide 44
First results at CLEAR comparing single-shot ChDR with RF deflector
Polarization Current Approach simulations on detector frequency ranges.
Preliminary shadowing results at CLEAR using an EO modulator on the 1st and 3rd radiator. 1st peak corresponds to the CChDR intensity
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Cherenkov diffraction radiation
Results and publications
Slides provided by Jack McGunigal

## Slide 45
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 46
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 47
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
AWAKE-UK collaboration: Electro-optic monitors
Electro-optic spectral interferometry (EOSI)
Slides provided by Sam Norman/Dave Walsh
Live real bunch profile and arrival time monitoring (wrt to laser timing)
Non-invasive, single shot
Simple spectral readout
Measure bunches < 100 fs
D.A. Walsh et al. Demonstration of an electro-optic spectral interferometry longitudinal profile monitor at CLARA, IPAC’23, THPL171
Encode electron bunch profile directly into spectrum of laser pulse
Demonstrations at CLARA and CLEAR
CLEAR
CLARA
Developing instruments for integration on AWAKE
Witness electron bunch
Proton micro-bunches
Monitor profiles and timing synchronisation
S.N.O. Norman et al. Fibre-Coupled Oscillator-Driven Electro-Optic Spectral Interferometry as a Longitudinal Bunch Profile Monitor, IBIC’2025, WEPCO40

## Slide 48
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Areas of research and development

## Slide 49
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Plasma density step (+ spectrometer)
Beamline design
Synchronisation
Discharge plasma source
Beam position monitors
Diagnostics
Transition and synchrotron radiation
Betatron radiation
Cherenkov diffraction radiation
Electro-optic monitors
AWAKE-UK collaboration: Summary
UK contributions essential to help prepare for and deliver Run 2 (and beyond)

## Slide 50
AWAKE-UK collaboration: Acknowledgements
Dr Morgan Hibberd | AWAKE-UK collaboration | UK-CERN Accelerator Celebration Day | 27th Nov 2025
Discharge plasma source
Claudia Cobo
Lewis Kennedy
Louis Forrester
Zulfikar Najmudin
Plasma density step
Energy spectrometer
Fern Pannell
David Cooke
Matthew Wing
Beamline design
Beam position monitors
Eleonora Belli
Bethany Spear
Philip Burrows
Synchronisation
Joshua Gregory
Ben Wooley (CERN)
Ed Snedden (ASTeC)
Rob Apsimon
Amos Dexter
Single-shot emittance
Bunch length monitors
Debdeep Ghosal
Joseph Wolfenden
Carsten Welsch
Betatron radiation
Cherenkov diffraction
Hossein Saberi
Jack McGunigal
Guoxing Xia
Electro-optic monitors
Terahertz manipulation
Samuel Norman
Collette Pakuza (CERN)
David Walsh (ASTeC)
Morgan Hibberd
Two-pulse ionisation injection
Abigail James
Ramy Aboushelbaya
Robin Timmis
Peter Norreys