## Slide 1: Fermilab Accelerators and Demonstrator Concept
Robert Zwaska
Fermilab
October 28, 2025
* Thanks to Diktys Stratakis for Demonstrator Slides

## Slide 2: Summary
Fermilab operates an accelerator complex providing up to 1 MW of proton beam for neutrino and muon experiments
  A continuous campaign of improvements has pushed beam power and reliability
  Ageing infrastructure has impacted beam delivery
  Upgrades are underway for DUNE and future accelerator-based experiments
A Muon Collider Demonstrator Facility is desired
  The Muon Collider is very ambitious in several ways
  A concept for a cooling demonstrator is being studied for Fermilab

## Slide 3: Fermilab Accelerator Complex

## Slide 4: The Fermilab Linac
Linear (copper) Accelerator
Accelerates H- ions
  750 keV  400 MeV
    Thousands to millions of volts
Beam bunched at 200 MHz
  ~ 1.5 Billion ions / bunch
RF of 200 & 800 MHz
  Distance between drift tubes changes with beam velocity
Pulse length of ~ 80 ms
  Many particles for short periods of time – more efficient operation
To be retired Jan. 2028

## Slide 5
H- ions stripped and multi-turn injected onto the Booster
Protons are accelerated from 400 MeV to 8 GeV in 33 msec
Fast cycling synchrotron
  Fast magnet ramping
  Frequency of 15 Hz
Single turn extraction
Many systems upgraded over the decades
Booster | 
Circumference (m) | 474
Harmonic Number | 84
Kinetic Energy (GeV) | 0.4 - 8
Momentum (GeV/c) | 0.954 - 8.9
Revolution period (msec) | t(inj) 2.77 – t(ext) 1.57
Frequency (MHz) | 37.9 - 52.8
Batch size | 4.5 E12
Focussing period | FDooDFo (24 total)
Booster
Combined Function Magnets
Booster Overview

## Slide 6: Main Injector & Recycler
Main Injector: 120 GeV Fast-cycling synchrotron
360 main dipole magnets
200 main quadrupole magnets
108 sextupoles, 66 octupoles, corrector dipoles/ quads, specialty injection and extraction magnets
Twenty 53-MHz RF cavities to accelerate beam
170 DC and 360 ramped magnet supplies with total of 140 MVA, 40 specialty pulsed magnet supplies
Recycler: 8 GeV Storage Ring
Originally built for antiproton storage, repurposed for proton stacking
Combined function, permanent magnets
RF cavities for stacking proton beams

## Slide 7: Booster Neutrino Beam (BNB)
Uses 8 GeV beam from the Fermilab Booster, operating since 2002
  Up to ~ 30 kW of beam (5e12 ppp)
Beryllium target integrated with single focusing horn
Services a suite of experiments at Fermilab: the Short Baseline Neutrino (SBN) program
BNB capability with PIP-II will be preserved after the long shutdown

## Slide 8: SBN Program

## Slide 9: The NuMI Facility: “Neutrinos (ν –> Nu) at the Main Injector”
Intense muon-neutrino beam directed towards Minnesota
Main Injector supplies 50–70e12 120GeV protons every 1.2 seconds
  Designed for 400 kW, operated up to 900 kW
  Multiple upgrade projects to 1 MW
Each pulse produces about 2x1014 ν 
  ~ 20,000,000 Pulses per year
  Direct beam 3o down
Commissioned in 2005, expect to run to ~ 2027
Near Detectors
Far Detectors: 5400 tons & 14000 tons
5
Neutrino beam
“Long-baseline”

## Slide 10: The LBNF Beam
Facility designed for initial beam power of 1.2 MW, upgradeable to 2.4 MW

## Slide 11: Section View of Target Complex – Target Hall
Beam
Primary Beam Enclosure
Target Hall
Work Cell
Decay Pipe
Primary Beam Window
He Gas
Cooling
Panels
Horn A with Target
Horn B
Horn C
Baffle
N2 Gas
Hatch Covers
Decay Pipe Upstream Window
Steel Shielding

## Slide 12: The NuMI Beam “Neutrinos at the Main Injector”
400 kW design average power
700 kW upgrade for NOvA
1 Megawatt Upgrade 2021
s ~ 1 mm
1 meter long, C target
Produces p+, K+ mesons
Pulsed focusing horns
Toroidal magnetic field
Parabolic inner conductor profile
Focus meson momentum band
2 m diameter
Roughly decay length for 10 GeV p+
He-filled
Absorbs ~ 40 % of beam power
Allows high-energy muons to penetrate
Measure hadron & muon fluxes
Arrays measure distributions
Notes: Go light on horn description, other details

## Slide 13: Mu2e: Muon to Electron Conversion Experiment
Two transport solenoids and production solenoid were installed into the Mu2e experimental hall
  Looking forward to detector solenoid
Detectors components starting to install
Beamline has been commissioning
  Electrostatic septa operated for slow extraction
  AC Dipoles being installed for extinction
Plan to have a 4 month physics run before the long shutdown

## Slide 14: Accelerator Complex function - beam delivery to science users
Protons-On-Target Power × Runtime × Uptime
Multiple experiments operate concurrently

## Slide 15: 1 MW Test Run: June 26, 2024
AD was granted an 8-hr window for up to 4-hr of running exceeding One Megawatt
Summer temperatures necessitated work during a cool and calm period
Individual machines pushed their capabilities to near-MW the few days before
Full operations & machine teams reported at 4am along with technical department personnel at the appropriate locations
At 6:53 machine conditions stabilized to allow 1 MW running, so the 4-hr period started at 5:53 am
  Improvements were made over the next few hours and 1.018 MW (1-hr average) was achieved at 8:21 am.
  BNB ran at full intensity in this period. Experiment concluded at 9:30 am
Much was learned from the run in terms of machine tuning and vulnerabilities.

## Slide 16: Major Issues Impacting Beam Operations
Main Injector heat exchanger corrosion issue
Main Interconnecting duct bank between Master Sub Station and Kautz Rd.
Kautz Road transform failure
August of 2024
Master/Kautz Rd bushing recall/failure

## Slide 17: MI Heat Exchanger Corrosion
  At the end of the 2024 Summer Shutdown, the corrosion issue was found.
  Solution was to replace the end channels on the impacted heat exchangers.
  All heat exchangers have been repaired/replaced as of September 2025.
Before End Channel Repair.
After End Channel Replacement

## Slide 18: Proton Improvement Plan II (PIP-II)
Increase Main Injector beam power to 1.2 MW.
  Replace the existing 400 MeV linac with a new 800 MeV superconducting linac => increase in Booster intensity.
    Provide a platform to increase LBNF power to 2.4 MW
  Provide path for a 100 kW Mu2e-II
  Provide capability for 1.6 MW at 800 MeV, CW beam
  Platform for high duty-factor / power operations to multiple experiments

## Slide 19
19
19
PIP-II Linac & Upgrades (1.2 MW power on target)
Project started in 2016 (CD-0)
First beam in Booster: 2029 (plan)
MI 1.2 MW beam on target: 2031 (plan)
Notes: 19
19
19
19
19
19

## Slide 20: PIP-II Project construction
Magnets provided by
PIP-II received DOE CD-3 approval for start of construction/execution on April 18, 2023
  Linac complex construction is actively underway
Front end of PIP-II linac constructed and successfully tested with beam
PIP-II cryoplant building complete
Extensive in-kind and partner contributions arriving
PIP-II is the first particle accelerator built in the U.S. with significant international contributions

## Slide 21: Mid-Term Accelerator Plans

## Slide 22: Accelerator Complex Evolution (ACE) plan – beyond 1.2 MW
Our vision is centered on the ACE plan that has two components
The Main Injector reliability improvements, cycle time shortening, and target systems upgrade to be started in the 2020’s called ACE-MIRT – without construction of new machines after PIP-II
  Will accelerate the achievement of the DUNE science goals with respect to the original PIP-II plan
  Improve reliability and safety of the key machines for the future of accelerator complex
Further, design a Next Accelerator Upgrade that builds upon the existing complex and enables Muon Collider R&D, and potentially a path to the collider
  Enables the next set of experiments (beyond DUNE and Mu2e)
  Capability of Muon Collider R&D, including a demonstrator facility
  Provide a robust and reliable platform for the future evolution of the Fermilab accelerator complex
2+ MW
Multi-MW

## Slide 23: ACE-MIRT scope to enable 2+ MW Accelerator Complex Evolution
This component of ACE plan aims to develop the Fermilab accelerator complex capabilities beyond PIP-II, without new accelerator construction.
  Overall efficiency and reliability of operations
    Implement improvements aiming to reduce losses, radioactive activation
    Task 1) Improve MI reliability by replacing quadrupole magnets with robust design
  Machine capability: Maximum proton flux produced by the accelerator
    Task 2) Upgrade MI ramp power system to enable faster cycle time (1.20.6s)
    Task 3) Upgrade MI RF acceleration system to allow for more beam flux
  Ability of target station to convert protons to neutrinos
    Task 4) Upgrade LBNF Target and Horns to reliable 2+ MW capability

## Slide 24: Numerous concepts for future proton accelerators
Scenarios were developed informed by studies from the past and input to Snowmass/P5
  Robust and capable 2.4MW accelerator complex for LBNF.
  Opportunities for high-power experiments at 1, 2, 8 GeV
  A platform for accelerator test facilities and demonstrators for future accelerators and colliders
Community engagement and design studies will continue

## Slide 25: Muon Collider Demonstrator
Many challenges throughout the proposed complex
  Numerous technologies to be demonstrated
Ionization cooling is one of the more novel approaches, and requires a great deal of integration

## Slide 26: Concept of ionization cooling
x1000 cells!
Not identical
one cell (~ 1m)
Considerations for MuC cooling:
  Beam size must be small at the absorber to reduce scattering
  Absorbers with low Z and large energy loss must be selected
  Magnetic field has to increase in strength over distance to keep cooling
  The magnetic field, makes normal conducting (NC) cavities the only option

## Slide 27: Design & simulation studies for cooling
During the MAP-era a complete design of a Muon Collider cooling system was developed; further improved by the IMCC
Simulation findings look promising but more R&D is needed to benchmark assumptions

## Slide 28: Muon demonstrator staging
  Full demonstrator with beam
  Coils producing 7T axial fields
  Potential to achieve 50% 6D cooling
  Cell integration studies
  Cell resembles late 6D cooling stages
  Reuse components from Phase I
  RF studies in B-fields
  Material studies & cryogenic Cu
Detailed parameters will depend on available funding and resources
Phase-II
Phase-I
Phase-III

## Slide 29: Full demonstrator with beam
Design in progress
  Muon source, target and transport
  Beam transport
  Cooling channel
Investing commonalities with other applications
C. Rogers, Phys. Sci. Forum 2023, 8(1), 37
Fermilab with access to high-power proton beams and technological expertise, is a good candidate for a Cooling Demonstrator

## Slide 30: Candidate locations at Fermilab

## Slide 31: Summary
Fermilab operates an accelerator complex providing up to 1 MW of proton beam for neutrino and muon experiments
  A continuous campaign of improvements has pushed beam power and reliability
  Ageing infrastructure has impacted beam delivery
  Upgrades are underway for DUNE and future accelerator-based experiments
A Muon Collider Demonstrator Facility is desired
  The Muon Collider is very ambitious in several ways
  A concept for a cooling demonstrator is being studied for Fermilab

## Slide 32
Thank you!