## Slide 1
Tripling TRIUMF’s RIB capabilities with the ARIEL facility
Luca Egoriti
Target Physicists
ARIEL Target Stations Project Co-Lead

## Slide 2
Member Universities
University of Alberta University of British Columbia Carleton University
University of Calgary University of Guelph University of Manitoba McGill University
McMaster University
Université de Montréal
University of Northern British Columbia
Queen's University University of Regina
Saint Mary’s University
Université de Sherbrooke Simon Fraser University University of Toronto University of Victoria
University of Waterloo
Western University
University of Winnipeg York University
2
TRIUMF: Canada’s particle accelerator center
TRIUMF is a not-for-profit corporation owned by a consortium of 21 member universities

## Slide 3: TRIUMF’s Role in Canada
Notes: TRIUMF operates at the interface between academia, government, and industry – the three pillars of Canada’s research and innovation ecosystem.
Our multidisciplinary community uses its world-class accelerator infrastructure to drive leading-edge research that delivers impact in science, medicine, and industry

## Slide 5
TR: 13
TR: 30-1
TR: 30-2
TR: 24
Medical isotopes
TRIUMF accelerators
Muons for
material science
500 MeV – 400 μA
P+ Cyclotron
PIF
STF
T1
T2
82Sr medical production
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
ITW
ITE
AETE
ARIEL
(ISOL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL1A
BL2A
BL2C
Spectroscopy γ, β, n (GRIFFIN and DESCANT, LE)
Precision mass measurements (TITAN, LE)
β-NMR (LE)
Atomic laser trap (TRINAT, LE)
Recoil separator (DRAGON, ME)
Recoil detector (TUDA, ME)
Radiochemistry (ASPIRE, ME)
Gamma-ray spectrometer (TIGRESS, HE)
Recoil separator (EMMA, HE)
Recoil detector (IRIS, HE)
One-year long shutdown to focus on installing the ARIEL facility
LS 26

## Slide 6
ARIEL ultimate objectives
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
ITW
ITE
AETE
ARIEL
(ISOL)
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
Two new radioisotope production stations 50 kW protons and 100 kW electrons
Multi-user operation up to three simultaneous beams (9000 RIB hours)
More efficient post acceleration EBIS, RFQ, Nier-spectrometer and 1/20,000 mass separator.
Medical Isotopes production in proton target station beam dump and transfer to medical isotope research

## Slide 7
ARIEL program
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
ITW
ITE
AETE
ARIEL
(ISOL)
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
ARIEL-I (2012 - 2014): e-linac, beam tunnel, target building
ARIEL-II (2017 - 2028) target stations, shielding, hot cells, RIB distribution
CANREB (2014 - 2019) charge state breeding and purification
Therapeutic Isotopes (2020 - 2028) Parasitic 225Ac production
200 $M by federal and 6 provincial governments;

## Slide 8
ARIEL program
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
ITW
ITE
AETE
ARIEL
(ISOL)
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
Electron linac

## Slide 9
ARIEL e-linac
300 keV
10 MeV
30 MeV
NORTH
To “Driver tunnel”
E = 30 MeV (upgradable to 50 MeV); Current up to 10 mA; Power up to 100 kW
Early science enabled: AETE material developments, FLASH studies on mice, DarkLight
Status: Commissioned up to 10 kW (beam dump rating)
CTS
[1] Egoriti, L. et al., Material development towards a solid 100 kW electron-gamma converter for TRIUMF-ARIEL https://doi.org/10.1016/j.nimb.2019.05.031
[2] Esplen, N., et al., Dosimetric characterization of a novel UHDR megavoltage X-ray source for FLASH radiobiological experiments. Sci Rep 14, 822 (2024). https://doi.org/10.1038/s41598-023-50412-w
[3] Ford, N. et al., Respiratory-gated micro-computed tomography imaging to measure radiation-induced lung injuries in mice following ultra-high dose-rate and conventional dose-rate radiation therapy, J. Med. Imag. 12(1) 014002 (30 January 2025) 10.1117/1.JMI.12.1.014002
DarkLight
FLASH

## Slide 10
TRIUMF accelerators for RIB
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
ITW
ITE
AETE
ARIEL
(ISOL)
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
Driver beamline tunnel

## Slide 11
Driver beam line tunnel
AETE
APTW
BL4N Vault region
BL4N Proton Cave region
BL4N Pharoah’s tomb region
EHBT dogleg region
BL4N & EHBT
Straight Tunnel section
BL4N & EHBT
North Tunnel bend section
NORTH
One proton & one electron beam line, for transport, spaced by ~1 meter
Status: beam line & services (cables, piping) installation in progress

## Slide 12
TRIUMF accelerators for RIB
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
ITW
ITE
AETE
ARIEL
(ISOL)
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISAC
(ISOL)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
Target stations

## Slide 13
ISOL targets for RIB production
500 MeV – 100 μA
P+ Cyclotron
Extraction electrode
HV 60 kV
Target
T=2000 °C
2 kV
Ionizer
Radioactive
Ion
Beam
Low energy experiments
High energy experiments
Post-accelerator
Mass separator
Neutrals
Ions
Isobars only
Post-accelerated
18 m
20 cm
[pps]
10 - 50 m
Evaporation
t>10-18
*
Fission
t>10-20
*
500 MeV protons
Intra-nuclear cascade
t~10-22 s
p
n
μ,π,k
…
Nuclei: U, Th, Ta, Si, C, O, Zr, Nb, Ni, Al, Ca
Nuclei: U, Ta

## Slide 14
[1/s]
[1/s]
ISAC I and ISAC-II halls
ARIEL’s objective: Three parallel RIBs
500 MeV – 100 μA
P+ Cyclotron
ISAC
ARIEL - APTW
ARIEL - AETE
30 MeV – 10 mA
e- LINAC
x 2
γ
e-
Converter
Target
Ion Source

## Slide 15
ITE
BL1A
PIF
BL2A
BL2C
RIBs from electrons: How?
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
ITW
TR: 13
TR: 30-1
TR: 30-2
CP: 42
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISOL
(ISAC)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
[1/s]
Future AETE
[1/s]
Current ISAC Future APTW
γ
e-
Converter
Target
Ion Source

## Slide 16
RIBs from electrons: How?
Muons for
material science
500 MeV – 400 μA
P+ Cyclotron
PIF
T1
T2
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
ITW
ITE
TR: 13
TR: 30-1
TR: 30-2
CP: 42
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISOL
(ISAC)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL2A
BL2C
γ
e-
Converter
Target
Ion Source
[1/s]
Future AETE
[1/s]
Current ISAC Future APTW

## Slide 17
Compact, modular shielding approach – similar to ISAC
[µSv/h]
P+ beam on APTW at 100 µA
~2.5m tall
Steel “plugs”
~2m tall
Steel + Concrete
APTW target
AETE target

## Slide 18
ISAC target lifetime and sequence
Service connections
Front end
+
Target
Shielding
ISAC
Irradiation station
ISAC
Hot Cell
Front end
+
Target
Shielding
Three weeks irradiation
One week cooldown
Hands-on service disconnection
Move module to Hot Cell
Remote target exchange in Hot Cell
Move module to irradiation station
Hands-on service connection
Few days pump-down
Three weeks irradiation
Approx. two-three weeks without beam on one station
Vacuum volume
ITW
ITE
ISAC
RIB

## Slide 19
ARIEL target lifetime and sequence
Service connections
Front end
+
Shielding
ARIEL
Irradiation station
Three weeks irradiation
Few hours of cooldown
Remote vacuum disconnection
Move target to spent target vault
Move new target to irradiation station
Remote vacuum connection
Few hours pump-down
Three weeks irradiation
Approx. two days without beam on one station
Vacuum volume
Spent target vault
Target
Target
(New) Target
Target hall

## Slide 20
ISAC vs ARIEL target exchange
Three weeks irradiation
Few hours of cooldown
Remote vacuum disconnection
Move target to spent target vault
Move new target to irradiation station
Remote vacuum connection
Few hours pump-down
Three weeks irradiation
Approx. two days without beam on one station
Three weeks irradiation
One week cooldown
Hands-on service disconnection
Move module to Hot Cell
Remote target exchange in Hot Cell
Move module to irradiation station
Hands-on service connection
Few days pump-down
Three weeks irradiation
Approx. two-three weeks without beam on one station
ISAC
ARIEL
ITW
ITE
ISAC
RIBs
APTW
AETE

## Slide 21
Hermetic Target Vessel (HTV) capabilities
ISOLDE-style, high-power target vessel
Improved DC current delivery
  Increasing temperature
  Thicker target heaters to reduce likelihood of breaking
  Bigger diameters possible
  Compatible with beam rastering (rotating)
Mass markers for offline/pre-delivery tuning
Gas injection
  For plasma ion source (FEBIAD)
  To support radioactive molecule production
All-metal sealing solution is possible
Feet for landing
P+ beam window
HTV cup
HTV
back plate
Ion source
Target
Mass markers conductors
Gas injection
Gate valve
APTW HTV
50 kW protons @ 500 MeV

## Slide 22
AETE HTV, target and converter
25 kW e- beam power
γ
e-
Converter
Target
Ion Source
e-
AETE converter
100 kW electrons @ 30 MeV
AETE HTV
e-

## Slide 23
Medical facility for 225Ac production
ISOL vessel

## Slide 24
Medical facility for 225Ac production
Hundreds of co-produced isotopes including 225Ra, 225Ac, 224Ra, 223Ra, 213Bi, 212Pb, 212Bi
Few tens of GBq of 225Ac produced per week, 10d after EoB
Pneumatically transferred into hot cell for extraction
ISOL vessel
Medical module
APTW medical rabbit and enclosure
Th
pellets

## Slide 25
Timeline
Today
2026
Q1
Q2
Q3
Q4
LS 26
Proton station ready to receive modules
Electron station ready to receive modules
Driver beam lines installed
Target hall infrastructure ready to receive modules
2027
Q1
Q2
Q3
Q4
2028
Q1
Q2
Q3
Q4
2029
Q1
Q2
Ready to start commissioning with beam
Controls and safety systems installed
Ready to transition to operations
On track to deliver 5000 RIB-hours in 1 year

## Slide 26
Several contributors through the years

## Slide 27
Backup

## Slide 28
ISAC vs ARIEL target module – services
Service connections
Front end
+
Target
Shielding
Vacuum volume
All services routed within tall vacuum volume
All services routed in GN2
Service connections
Front end
+
Shielding
Vacuum volume
Target

## Slide 29
ARIEL target module – services
Ground services: roughing line, water cooling
Actuation: GND electrode movement, Gate Valves (x2)
High Voltage Feed Through (HVFT)
Front End:
  Beam lines connections
  Structural supports (HV breaks)
  “Last meter” service delivery
  Pneumatic target vessel engagement mechanism
Hermetic Target Vessel (HTV)

## Slide 30
Experimental hall – available hardware
TITAN
GRIFFIN
Spectroscopy γ, β, n (GRIFFIN and DESCANT, LE)
Precision mass measurements (TITAN, LE)
β-NMR (LE)
Atomic laser trap (TRINAT, LE)
Recoil separator (DRAGON, ME)
Recoil detector (TUDA, ME)
Radiochemistry (ASPIRE, ME)
Gamma-ray spectrometer (TIGRESS, HE)
Recoil separator (EMMA, HE)
Recoil detector (IRIS, HE)
TIGRESS + EMMA
β-NMR

## Slide 31
HVFT
Two concentric Al sheaths
  • inner held at HV
  • outer at GND
Interior services held at HV: design voltage 75kV
  Bus bars Al 6101 T64 (biased up to 3kV): 1000A, 2400A
  Mass Markers: 6 (3 pairs) biased up to 3kV, and 80A
  Water conduits: 4
  Gas pipes: 2
  Air lines: 6
    Piston RIB in
    Piston RIB out
    Piston converter in
    Piston converter out
    RIB pillow inflation
    Driver pillow inflation
  Spare lines: 5
  Vacuum lines (spares): 2
    RIB differential pumping
    Converter differential pumping
  Services Route: 1
Filled with S2 glass fibre reinforced CTD-403 resin (green/orange)

## Slide 32
Front End – front and back

## Slide 33: ISAC – The Highest Power ISOL Facility in the World
ISAC target module moved by remote handling crane
Target module transport to target station
Containment Box
Shielding
ISAC target module in hot cell

## Slide 34
ARIEL Hermetic Target Vessel - APTW
γ
e-
Converter
Target
Ion Source
AETE HTV
100 kW electrons @ 30 MeV
APTW HTV
50 kW protons @ 500 MeV
e-
Thin Ta layer (converter)
Thick Al body (e- absorption and heat removal fins)

## Slide 35: ISAC Radioisotope Beams Since 1998
Water-cooled heat
shields
target materials:
UCx
UO2
ThO
Nb
Ta
TaC
NiO
ZrC
TiC
SiC
target container ~2000 °C
(Ø 20 mm, 60 cm3)
ion sources:
surface
resonant lasers
FEBIAD
IG-LIS
500 MeV protons
Target ion source service connections
  → Corina Andreoiu, PS-1-3
  → Jens Lassen,
  Mon, oral
  → Fernando Maldonado,
  PS-1-19

## Slide 36: ARIEL Targetry: Green-Field ISOL Technology
ISAC inspired:
Module, crane, hot-cell-based handling paradigm
Compact shielding with radiation hard components at beam level and sensitive equipment on top of shielding
Externally inspired:
Hermetic target unit
Flexible and efficient direct target exchange
New:
GGy – level radiation hard technology
Consistent remote repair and decommissioning
Reduced material activation
Superior power management
Improved HV design and reliability
Prototype tests completed

## Slide 37: Electron-Driven ISOL Power Management
e-
Target
Converter
γ
Ion source
e- 30 MeV, 100 kW
Separator
magnet
A
++
++
A
A
++
A
++
A
++
A
++
A
++
A
++
A
++
++++
A
A
++
++
A
A
++
e- LINAC
γ
60 kV Target and ion source
2000 oC
Radioactive ion beams
→ Thinner target or change of orientation
→ ISAC target cooling fins not viable

## Slide 38
ARIEL Targetry Systems
module storage
spent target storage
AETE
APTW
drivers beam tunnel
RIB
RIB
ASTM
Hot cell facilities
Remote-controlled crane
2000 t of steel and concrete
Modular RH high-power infrastructure
Symbiotic medical target in APTW beam dump

## Slide 39
RIB path at target elevation (underground)
APTW
AETE
Destinations

## Slide 40
RIB path in CANREB and ISAC-I (ground floor)

## Slide 41
https://50stories.triumf.ca

## Slide 42: Proven Modular Design Paradigm for Target Station