## Slide 1: Optical Calibration of the SNO+ Scintillator Phase using a Laserball
June 22, 2026
Jamie Grove, Ph.D. Candidate
Supervisor: Dr. Alex Wright, Dr. Christine Kraus

## Slide 2: SNO+ Detector Overview
Detector is in SNOLAB, in Sudbury, Ontario Canada.
12m diameter acrylic vessel (AV), currently filled with 780 tonnes of liquid scintillator.
  LAB + 2.2g/L PPO + 2.2mg/L bis-MSB + 6.5mg/L BHT.
Viewed by ~9400 inward-facing photomultiplier tubes (PMTs) mounted on the 18m diameter stainless steel support structure (PSUP).
7000 tonnes of external ultrapure water (UPW).
AV hold-down ropes.
[1] SNO+ Collaboration

## Slide 3: SNO+ Phases and Physics Goals
Water Phase
May 2017 – July 2019
905 tonnes of UPW
Invisible nucleon decay
Solar neutrinos
Rector antineutrinos
Scintillator Phase
Started April 2022
780 tonnes of liquid scintillator
Solar neutrinos
Rector antineutrinos
Geo-neutrinos
Supernova neutrinos
Dark matter and axion-like particle searches
Tellurium Phase
4 tonnes of natural Te loaded into scintillator
Full scintillator physics program
Neutrinoless double beta decay in 130Te (0νββ)

## Slide 4: SNO+ Event Reconstruction
A key aspect of the physics program is the energy and position reconstruction.
The most important quantities for reconstruction are:
These quantities are influenced by the scintillator optics.
Number of PMTs hit (nhit)
PMT hit time

## Slide 5: SNO+ Scintillator Optics
Main takeaway: the complex scintillator absorption and re-emission spectrum is wavelength dependent. The number of PMTs hit will depend on this spectrum.
[Scaled for illustrative purposes]
Scintillator Cocktail
LAB (Linear Alkyl Benzene)
2.2 g/L PPO (2,5-diphenyloxazole)
2.2 mg/L bis-MSB (4-bis(2-methylstyryl)benzene)
Notes: Jamie it could be fun to make a little cocktail glass or bottle.

## Slide 6: SNO+ Calibration Deployment Systems
All new scintillator phase calibration hardware.
**Not an exhaustive list, further sources in commission.
Calibration Sources
Laserball, optical source
241Am- 9Be, neutron source [Session M2-9 (PPD) Anthony Allega, Contribution #856]
[Session R2-6 (PPD) Dr. Ryan Bayes, Contribution #804]
[1] SNO+ Collaboration

## Slide 7: SNO+ Laserball Calibration Systems
Photodiode
[1] SNO+ Collaboration
A nitrogen laser produces light pulses at 40Hz -> beamsplitter -> triggers detector.
Dye cells
Neutral Density Filters (not pictured)
Transmitted via fibre optic cables to the umbilical retrieval mechanism (URM).
Notes: A nitrogen laser, on the SNO+ deck, produces light pulses at 40Hz. The laser passes through a beam splitter, where the trigger from a photodiode is sent to the detector.
The light travels through one of a series of dye cells, before going through two neutral density filters, and out of an aperture coupled to one end of the umbilical fibres.

## Slide 8: SNO+ Laserball Calibration Systems
[1] SNO+ Collaboration
Umbilical Retrieval Mechanism (URM).
Attaches to universal interface (UI).
Pulley system for umbilical.
  Z-axis position.
Side-ropes for the x, and y axes position.
Side-rope motor boxes
Umbilical Retrieval Mechanism (URM).
Pulley system for umbilical.
Cross-section of the umbilical, the optical fibres (5)
Notes: A nitrogen laser, on the SNO+ deck, produces light pulses at 40Hz. The laser passes through a beam splitter, where the trigger from a photodiode is sent to the detector.
The light travels through one of a series of dye cells, before going through two neutral density filters, and out of an aperture coupled to one end of the umbilical fibres.

## Slide 9: SNO+ Laserball
[1] SNO+ Collaboration
The diffuser flask is filled with Silgel and suspended glass microspheres that provide necessary scattering.
[1] SNO+ Collaboration
Triggered light pulses.
Produces pulses at multiple, selectable wavelengths.
Deployed in multiple positions.
Ideal calibration source for measuring scintillator optics and PMT response.
Diffuse light throughout the detector.
Notes: A nitrogen laser, on the SNO+ deck, produces light pulses at 40Hz. The laser passes through a beam splitter, where the trigger from a photodiode is sent to the detector.
The light travels through one of a series of dye cells, before going through two neutral density filters, and out of an aperture coupled to one end of the umbilical fibres.

## Slide 10: SNO+ Laserball Deployment
First SNO+ internal scintillator deployment with the Laserball.

## Slide 11: SNO+ Laserball Occupancy
Occupancy describes the number of hits a PMT, j, is hit for a Laserball run, i.
Number of hits registered by PMT, j.
Total number of pulses emitted by the Laserball
The PMT Occupancy map displays expected polar anisotropy and detector components shadowing.
Occupancy can be used to extract the optical parameters for the optics model.
Central (0, 0, 0), 500nm Laserball run
Notes: Add link to the Laserball design paper

## Slide 12: SNO+ Laserball Occupancy
The occupancy is parameterized by,
[2] SNO+ Collaboration
** This talk
Problem: this leaves ~9400 PMT efficiencies, j , to fit.
Notes: Add link to the Laserball design paper

## Slide 13: SNO+ Laserball Occupancy
If we take the ratio of the occupancy of a given PMT, j, for a Laserball run, i, with PMT, j, for a central Laserball run, 0, we eliminate the PMT efficiency parameters.
Central (0, 0, 0), 500nm Laserball run
(0, 300cm, 0), 500nm Laserball run
The attenuation coefficients
(Scintillator, Acrylic, and External water)
[2] SNO+ Collaboration
Notes: Add link to the Laserball design paper

## Slide 14: SNO+ Laserball Fit Results
Short wavelengths are consistent with the Laserball measurement at the bisMSB dye (~420nm).
Scintillator absorption spectrum based on UV-VIS measurements, susceptible to variations in baseline subtractions at long wavelengths.
The Laserball measures that baseline and improves our optics model in this region.
Notes: Add link to the Laserball design paper

## Slide 15: Summary
Calibration campaign designed to measure and improve the energy and position reconstruction for the SNO+ physics program.
Deployed the SNO+ Laserball in the scintillator.
Preliminary measurements of the SNO+ scintillator optics.
Future improvements to scintillator optics model.

## Slide 16: References
[1] SNO+ Collaboration, The SNO+ Experiment, arXiv:2104.11687v3 (2021).
[2] SNO+ Collaboration, Optical calibration of the SNO+ detector in the water phase with deployed sources, JINST 16 P10021 (2021)

## Slide 17: Back-up Slides

## Slide 18: Hit Time Residuals, AV reflections, PMT response
The prompt peak represents a direct light path from the Laserball to the PMT.
Other paths, and PMT late pulsing features are seen in the late and early light in the PMTs.
[2] SNO+ Collaboration

## Slide 19: Hit Time Residuals, AV reflections, PMT response
The hit time residual is defined as,
tPMT, i is the hit time of PMT, i
t0, is the time of the event (triggered by laser light pulse)
tTOF, is the calculated time of flight from the Laserball position to the PMT.

## Slide 20: SNO+ Scintillator Optics Timing
Main takeaway: the scintillator has a scintillation and re-emission timing and will therefore impact the PMT hit time.
Time constant
Scintillator Cocktail
LAB (Linear Alkyl Benzene)
2.2 g/L PPO (2,5-diphenyloxazole)
2.2 mg/L bis-MSB (4-bis(2-methylstyryl)benzene)

## Slide 21: PMT Angular Response and Concentrator Efficiency
PMT Angular response and concentrator efficiency were monitored throughout SNO and the SNO+ water phase.
Observed degradation in the reflectivity of the concentrators.
[2] SNO+ Collaboration

## Slide 22: Laserball Filling
The 11cm diameter flask is filled with 600mL of SilGel suspended with glass microspheres (average ⌀ 40 μm). The microspheres provide the necessary light scattering, however the concentration is an optimization of pulse time width and isotropy.
[3] S. Valder, et. al.

## Slide 23: Laserball Filling
The light injection point defined as, z0, is the distance above the centre to the quartz rod end within the Laserball flask.
[3] S. Valder, et. al.

## Slide 24: Laserball Filling
The Laserball diffuser flask is filled with 600 mL SilGel with homogeneously suspended glass microspheres at a concentration ~1.5mg/mL.
Mixing/pouring SilGel
Successful testing fill
Final flask fill
Degas

## Slide 25: References (Back-up Slides)
[1] SNO+ Collaboration, The SNO+ Experiment, arXiv:2104.11687v3 (2021).
[2] SNO+ Collaboration, Optical calibration of the SNO+ detector in the water phase with deployed sources, JINST 16 P10021 (2021).
[3] S. Valder, et. al., A Laserball Calibration Device for the SNO+ Scintillator Phase, JINST (2024).
Notes: Jamie, separate these into the back-up slides references and the slides references.