## Slide 1: Developing Scalable Readout Electronics for Directional Sensitivity of the NEWS-G Dark Matter Experiment
Julia Redinger
University of Alberta
Supervisor: Dr. Marie-Cécile Piro
2026 CAP Congress
June 23, 2026
Globie

## Slide 2
Searching for light Dark Matter
NEWS-G assumes the WIMP model
  Weakly Interacting Massive Particle
NEWS-G (New Experiments with spheres – gas)
We know it’s there, but we don’t know what it is!
[1]
Notes: Focuses on ionization detection method. WIMP miracle – WIMPs match relic density very well!

## Slide 3: Detection Goals and obstacles
NEWS-G focuses on the smaller mass region (less than ~5 GeV)
WIMP experiments will soon reach the neutrino floor!
  Experiments will also detect the neutrinos
  For NEWS-G, CE𝜈NS (Coherent Elastic Neutrino Nucleus Scattering) from the sun
  Looks the same as WIMPs, can’t be shielded
→ How can we distinguish between these signals?
Directionality!
[2]
Neutrino Floor

## Slide 4: Directionality
Take advantage of “WIMP Wind”!
  Apparent flux of dark matter as the sun moves through the galaxy
Dark matter will come from a particular direction in the detector
→ Need detector to determine direction of incoming particles
[3]
Notes: Paper?

## Slide 5: Spherical proportional counter (SPC)
[1]
Copper spherical vessel, filled with noble gas
High voltage anode in center allows charge to be read out
Different spheres for data taking and R&D!
  The U of A has a 30 cm diameter sphere
Notes: Noble, low A gas - higher sensitivity to low mass DM
S30: Argon

## Slide 6: Detector operation
1. Incident particle interaction
  Primary ionization
2. Electron drift towards anode
3. Secondary electron/ion pair creation
  Townsend avalanche
4. Signal formation on sensor
  Current is induced by secondary ion drift
e-
ions
Notes: Current induced by secondary ions drifting away from the anode
Cathode: sphere walls

## Slide 7: Sensor Anode
ACHINOS:
11 anodes instead of 1!
Means “sea urchin” in Greek
[4]
[1]

## Slide 8: Directionality
Electrons from particle tracks will induce a signal on different anodes → provides directional information!
Requires individual anode readout
[5]
Simulations done by Keiran Nicholson:
Poster at 6 pm!
Notes: Plan: take data and compare

## Slide 9: Goal: Develop 11 Channel Readout System For ACHINOS!

## Slide 10: Signal Processing (single anode)
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)

## Slide 11: Single Anode S30 Setup

## Slide 12: Single anode S30 Setup
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
S30
Single anode currently installed!

## Slide 13
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
S30
Cremat charge-sensitive pre-amplifier
Commercially available
More expensive
Breakout board discontinued
[6]

## Slide 14
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
S30
Red Pitaya STEMlab 125-14
Commercially available
Features…
  an ADC (Analog to Digital Converter) for digitization
  an FPGA (Field Programmable Gate Array) for processing and dispatching
[7]

## Slide 15
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
Samba
Custom software used for the NEWS-G detector signals
Manages triggers/cuts and data storage

## Slide 16: Eleven Anode S30 Setup
[1]

## Slide 17: Eleven anode S30 Setup
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
S30
Need to install ACHINOS!
S30
To be completed this summer!

## Slide 18
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
Edge Amp
Designed in-house
Cheaper
Custom carrier board
Design by Dr. Adam Maunder and Michael Rangen
Multi-channel carrier board to be completed this summer!

## Slide 19
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
Red Pitaya Chaining
Two input channels per board
Chained for clock synchronization
  Allows synchronized data collection
Successful 4 channel test complete
Ethernet output cables
From Edge Amps

## Slide 20
Pre-amplification
High Voltage Bias
Digitization
Dispatching
Analysis & Storage
DAQ (Data Acquisition)
Samba Updates
Eleven channel functionality added
4 channel test results: perfect synchronization in time!
Many thanks to Michel Gros

## Slide 21: Conclusions
Development of 11-channel readout system in progress
  Enables directional information to be read out, to distinguish WIMPs from CE𝜈NS
Successful preliminary tests with 4 channels
Future work this summer:
  Install the ACHINOS!
  Design circuit board for 11 channel pre-amps
  Design the electronics enclosures
  End of summer 2026: Test full eleven channel readout with S30 signals!
  Thanks! Questions?
Globie
NEWS-G S30 mascot!
Notes: Photos?

## Slide 22: References
[1] M.-C. Piro, “Searching for Light Dark Matter with the NEWS-G Experiment”, Nov. 2025, https://indico.ijclab.in2p3.fr/event/11699/contributions/39006/attachments/26615/39485/MCPiro_Astrosymposium_2025.pdf (accessed Jun. 5, 2026).
[2] J. Billard et al., “Direct Detection of Dark Matter—APPEC Committee Report,” Reports on Progress in Physics, vol. 85, no. 5, p. 056201, Apr. 2022. doi:10.1088/1361-6633/ac5754
[3] Quantum diaries, https://www.quantumdiaries.org/2012/03/16/une-conference-qui-laisse-songeur/wimp-wind-3/ (accessed Jun. 15, 2026).
[4] D. Young, “Purple sea urchin,” vic high, https://vichighmarine.ca/purple-sea-urchin/ (accessed Jun. 5, 2026).
[5] K. Nicholson, Directionality Simulations
[6] “CR-11X charge sensitive preamplifier modules,” Cremat Inc, https://www.cremat.com/home/charge-sensitive-preamplifiers/ (accessed Jun. 5, 2026).
[7] STEMlab 125-14 4-input starter kit - red pitaya | mouser, https://www.mouser.com/new/red-pitaya/red-pitaya-stemlab-125-14-kit/ (accessed Jun. 5, 2026).
Notes: Maybe do summary and combine with this? Photo of sphere and achinos??