## Slide 1: Photo-detector R&D in the FCC era
Fabrice Retiere (TRIUMF) on behalf of the DRD4 collaboration
Although very much a personnal selection

## Slide 2: State of the art Ring Imaging Cerenkov
CAP 2026 · DRD4 photodetector R&D for the FCC
R. Preghenella (INFN Bologna)
Dual RICH (dRICH) detector with SiPM for ePIC (EIC)
  2 radiators: aerogel (n ~ 1.02) and C2F6 (n ~ 1.0008)
  4× matrix Hamamatsu (8×8 S13361
  Read-out board with front-end chip (ASIC), FPGA, and cooling
  Single-photon detection inside high B field (~ 1 T)
  Advanced design and prototype tests
Preamble

## Slide 3: State of the art?
Preamble

## Slide 4
ORGANISATION
Working Groups and Work Packages
Six WGs are open R&D forums; five WPs are funded, milestone-driven projects mapped to the ECFA roadmap — the same roadmap that defines detector needs for the FCC.
Spokesperson: M. Fiorini (INFN Ferrara), deputy spokesperson: F. Retiere (TRIUMF)
WORKING GROUPS
open forums · no committed resources
WORK PACKAGES
funded projects · goals, milestones, deliverables
WG1 Photon Detectors Retière, TRIUMF
Writing a 400 pages compendium about single photon detectors
WG2 Particle ID Easo, RAL
WG3 Technological activities Tessarotto, Trieste
WG4 Software Martinelli, Milano-Bicocca
WG5 SciFi & TR detectors Jakobsen, CERN
WG6 Novel / far-future R&D Özkorucuklu, Istanbul
WP1 Solid-state photodetectors Pestotnik, Ljubljana
WP2 Vacuum-based photodetectors Laktineh, Lyon
WP3 RICH & imaging detectors Cardinale, Genova
WP4 Time-of-Flight detectors Lapington, Leicester
WP5 SciFi tracking & TR Leverington, Heidelberg
CAP 2026 · DRD4 photodetector R&D for the FCC
Notes: WGs share know-how, samples, infrastructure; WPs carry the funded commitments. Note the leadership map. Canadian point: TRIUMF leads WG1. ~1 min.

## Slide 5: Vacuum Photo-Detector
Pros
  High gain and low dark noise
  Excellent timing resolution for MCP
  Good efficiency
Conventional PMT
Multi-Anode PMT
Micro-channel plates
Hybrid-Photodetector
WP2/WG1 – silicon photo-detector foundation
Cons
  Specialized manufacturing
    Limited suppliers
  Fragile
  Bulky

## Slide 6: Vacuum photo-detector moving towards enhanced integration
MCP fabrication over silicon substrate
3D printed MCP
Transmission dynode
All these technique enables integration with CMOS – TimePiX4, PICMIC
6
S. Frei (IEEE TNS Vol.70 No. 9 2226, 2023)
C. Ertley (Proc. of SPIE Vol.13093, 130935S)
J. Lapington (RICH 2025)
WP2/WG1 – silicon photo-detector

## Slide 7: Single Photon Avalanche Diode Arrays (SiPMs)
Pros:
  High gain (~106) and single photon separation
  Excellent time resolution
  Good granularity
  Insensitive to magnetic fields; low V operation
  Compact
Cons:
  High dark count rate. typ. ~100 kHz/mm2
  correlated avalanches (afterpulse, crosstalk) & emits light
  Very sensitive to neutrons and ionizing particles
WP1/WG1 – silicon photo-detector foundation
Notes: Dark counts are produced by thermal generation of carriers, trap assisted tunnelling or band gap tunnelling.
Optical cross-talk produced when photons emitted in avalanche initiate signal in neighbouring cell, reduced by screening – trenches.
After-pulses produced by trap-release of carriers or delayed.

## Slide 8: WP 1, task 3 radiation hardness
DCR highly depends on temperature and irradiation
Can be mitigated by cooling (and annealing after irradiation)
1011 neq/cm2
non irradiated
1012 neq/cm2
1013 neq/cm2
M. Calvi (NIM A 952 161788, 2020)
-30°C, after annealing
Hamamatsu S13360-1350CS, -30°C
Liquid nitrogen (77 K)
WP1/WG1 – silicon photo-detector radiation damage
Notes: Baselines of the same devices just after irradiation, and after 600 h of annealing up to 175 ◦C: operation in single photon regime is possible, but only for fluences up to 10^11 neq/cm^2.
Devices were then cooled down to 77 K: for Hamamatsu SiPMs of any cell size, a DCR of about 10 MHz∕cm2 was measured, which would allow single photon operation.
The device that was annealed shows an even lower DCR of about 10 kHz∕cm2, comparable to that of vacuum devices like MaPMTs and MCP-PMTs.

## Slide 9: CMOS SPAD
Pros
  “no” power dissipation when idling
  Tailor performances to needs. E.g. dynamic range, timing, imaging,…
  Less complex at system level
  Lower dark noise by SPAD elimination
Cons
  In 2D, some efficiency loss
  More complex at chip level
  Mass production not demonstrated (by HEP)
WP1/WG1 – silicon photo-detector electronics integration

## Slide 10: CMOS SPAD within DRD4
PLATON (EPFL, ETHZ – D. Sgalaberna)
  Scintillating fibres as active neutrino target
  Towards dedicated dSiPM: 272x192 SPAD pixels, per-cluster TDCs (200-800 ps LSB), low data rate (1-2 LVDS connections sufficient per chip)
WP1/WG1 – silicon photo-detector electronics integration

## Slide 11: Leveraging the nano-optics revolution
C. Bruschini
WP1/WG1 – silicon photo-detector optics

## Slide 12: 3D integration
Industry is leading:
  CANON, SONY for single photon imager
  STMicroelectronics and smaller companies for LIDAR
In HEP, University of Sherbrooke, Canada (S.Charlebois, J.-F. Pratte) is leading with Photon to Digital Converter
  Development driven by astro-particle physics, nEXO, ARGO
  SPAD array and CMOS readout 3D-stacked to form a single heterogeneous detector chip
  Made in Canada: SPAD array and 3D integration in Teledyne MEMS, Bromont, Quebec
S. Charlebois (PD 2025)
WP1/WG1 – silicon photo-detector electronics integration
Notes: NEXT: Search for neutrino-less Double Beta Decay

## Slide 13: Back-side illumination is the next step for versatility
CMOS
CMOS
p+
p
n+
n
SiO2
Poly
CMOS
p-epi
CMOS
Front side avalanche diode
Back side avalanche diode
Extended
80um
5-20um
5-50um
Ultra-thick
100-500 um
Geiger mode avalanche
VUV – Blue photon
Charged particle
Un-depleted
p-epi
depleted
Electron trajectories
Linear avalanche
Neutron or dark matter
Hole trajectories
Even dark matter search
WP1/WG1 – silicon photo-detector electronics integration

## Slide 14: Canada FCC and photo-detectors
Canadian effort can no longer be sustained only by astro-particle physics
Both TRIUMF and Sherbrooke are drifting to applied projects
  Neutron imaging. Sherbrooke - ORNL
  Air analysis. TRIUMF – SenseNet
  Neutron spectrometry. TRIUMF – General Fusion
  Expansion through non NSERC SAP grants
Canada photo-detector effort needs FCC interest
  DRD4 is LHCB biased. About 50% of the community
  And DRD4 is also fibers, optics,…
Canada has very strong industrial assets in photonic
  Teledyne-MEMS
  And broad industry
Strong opportunity to catch up with industry if we can create critical mass
Conclusion - outlook

## Slide 15: Merci / Thank you