## Slide 1: THE PHOTSAT MISSION Big science with a small satellite
Josep Manel Carrasco
Project Scientist
Ignasi Esteva
Project Manager
Josh Wilkinson
Systems Engineer
Ignasi Ribas
PI
Guillem Anglada-Escudé
co-PI
LIA7

## Slide 2: INTRODUCTION
PhotSat is the first astrophysical satellite developed from design to operations by the IEEC and the local industrial ecosystem
Objectives
All-sky monitoring of the 40 million brighter stars and other astrophysical objects, mainly to support high-precision programmes of all kinds (exoplanets, stellar physics, Solar System, cosmology, transients)
Develop the capability of executing science experiments from scratch, including preliminary design, construction, launch, and operations; using off-the-shelf #newspace technologies

## Slide 3
The mission
Parameter | Value
Telescopes | 1 Visible + 1 Ultraviolet
Diameters | 70 mm
WIDE passband | 500 – 840 nm
RED passband | 670 – 840 nm
UV passband | 245 – 310 nm
Detectors | 2 x EHD GSENSE2020BSI (2048x2048 pixels)
Exposure time | 3.125 seconds (frames) 50 seconds (coadded)
Pixel size | 14 arcsec/pix (6.5 μm)
Parameter | Value
Launch | 2026
Lifetime | 2 – 3 years
Full sky scan | 2 – 3 days
Field of view | 8 deg x 8 deg
Orbit | LEO SSO (>500 km)
Ground stations | Montsec & Svalbard
Cubesat | 16U
Number of observations | 100 - 1000 obs/source/yr
The payload
IN A NUTSHELL…

## Slide 4: SCIENTIFIC JUSTIFICATION
UV coverage – not accessible from a ground-based telescope
Homogeneous full-sky coverage – not accessible from a single ground-based telescope with a single instrument
High-cadence time-domain monitoring of bright sources – not observable with larger telescopes (saturation)
Broad wavelength coverage of all stellar types (white dwarfs, red giants, emission line stars, …)
Balmer jump measurement – not accessible from ground
SCIENCE CASES
Transient events: Supernovae, stellar flares, gamma-ray bursts, AGN, …
Periodic events: Pulsating stars, stellar activity, eclipsing binaries, ...
Solar System: Asteroids and near-Earth objects
Complete catalog of celestial objects in UV and VIS
Space debris: Monitoring MEO/LEO satellites

## Slide 5
SCIENCE CASES
Balmer jump for an A-type star
Expected number of transient events
Stellar flares

## Slide 6
PhotSat has great potential for debris and artificial satellite studies:
Large field of view (FoV=8º x 8º → 11.3º diagonal)
Full sky scan every 2 – 3 days (except 32º around the Sun)
Sources at the anti-Sun position observed every orbit (∼90 min)
All sources brighter than 14 – 15 mag
One full FoV observed during 50 seconds (16 frames of 3 s)
Half of the FoV observed again the following 50 seconds
Follow-up observations from IEEC telescopes at Montsec observatory (TRAC, TFRM, TJO)
Pathfinder to test methodology and improvements for a future fully-devoted SST satellite?
PHOTSAT FOR SST

## Slide 7
SYSTEM DEVELOPMENT

## Slide 8
PAYLOAD INSTRUMENT CONTROL UNIT (ICU)
ICU based on a backplane with cards that follow the VNX+ standard

## Slide 9
SIDEROSTAT
Foldable solar panels
Scanning of a given
great circle

## Slide 10: SIDEROSTAT Qualification campaign (Sep/Oct 2025)

## Slide 11
SCANNING LAW
1 year of survey
First days of mission
One year of mission

## Slide 12: OBSERVABLE SOURCES
Crowded field
Moon size comparison
(FoV = 8º = 16 x Moon)
Image from Montsec Observatory using PhotSat detector (Mar 2025)
FoV = 8º
Moon

## Slide 13
INSTRUMENT CONCEPT
VIS
UV
UV
VIS
WIDE
RED
WIDE
RED
VIS2
UV
CMOS detectors
UV
245–310 nm
WIDE
500–840 nm
RED
670–840 nm

## Slide 18
PHOTSAT PHOTOMETRIC PERFORMANCE

## Slide 19
ON-GROUND TESTS
Radiation campaign (Sevilla, April 2025)
Detector tests (Obs. Montsec, March 2025)
Centro Nacional de Aceleradores (CNA)
Orion nebula (left) and Pleiades (right)
EHD SCA2020-UV-TR detector

## Slide 20
ORBIT & COMMUNICATIONS
Download (X band) ∼9 GB/pass

## Slide 21
PHOTSAT OPERATIONS
Operations concept being defined ➔ Funding challenge
Ground station at Montsec (Sant Esteve de la Sarga Teleport) and Svalbard for redundancy
Science exploitation – The PhotSat catalog
    Data policy still TBD
    Most likely all data to be public either immediately or after short period
    Catalog published in VO/TAP (like Gaia)
    First prototype based on GAVO DaCHS using simulated data already available

## Slide 22
PROJECT STATUS

## Slide 23
FUTURE SPIN-OFF MISSION?
GAUDI mission concept submitted to ESA as mini-F
PI: Josep Manel Carrasco (ICCUB & IEEC)

## Slide 24
THANK YOU
Contact: ribas@ieec.cat
showcase/photsat/
@photsat_mission
@photsat-mission.bsky.social
photsat_mission
https://photsat.ieec.cat/

## Slide 25
Orbit | Maximum distance to PhotSat (km) | Magnitude difference mground-mPhotSat (mag) | FoV crossing time (s) | Number of satellites with V<15 mag | Observable satellites (illuminated by the Sun)
LEO | 9787 | 1.7 | 254.68 | 6768/6768 | 3926 (58%)
MEO | 27264 | 0.67 | 709.41 | 85/143 | 8 (5%)
GEO | 42721 | 0.38 | 1111.60 | 590/590 | 77 (13%)
PhotSat for SST
In 50 seconds, even LEO satellites are caught without leaving the FoV
60% of LEO satellites (about 4000) are observable with PhotSat
Also some MEO and GEO are observable
From PhotSat, LEO satellites are 1.7 magnitudes brighter than from ground

## Slide 26: INSTRUMENT AND OPERATIONS CONCEPT

## Slide 27
SIDEROSTAT
Spring (2N·mm/deg in rest at 60º)
Mirror rotation axis
Bearing
Microswitch
Mirror cover
Mirror
Rotation axis coupling (mirror+gear)
Nanorelease Nut mechanism
Gears
Reducer assembly support

## Slide 28: SIDEROSTAT: prototype
10 deg rotation test

## Slide 29: SIDEROSTAT: prototype

## Slide 30
SCANNING LAW
Great circle orientation change
Scanning of a given
great circle

## Slide 31
OPTICAL SYSTEM

## Slide 33: THE PHOTSAT CONSORTIUM

## Slide 34
PHOTSAT CONSORTIUM

## Slide 35
PHOTSAT CONSORTIUM

## Slide 36
PHOTSAT CONSORTIUM
Senior Board - IEEC (PI), +5 members ICE/CSIC, UAB, ICCUB, UPC
Project Office - IEEC, Project manager (full time), Systems Engineers (full time), Project Scientist (part time), communication, admin & legal
Science exploitation team - ICE, UB, UPC, UAB (+ partners, funding for operations)
Engineering development & advisory - IEEC, UPC, UAB, ICCUB
Payload assembly and QA - IEEC, IFAE, terms & contract to be negotiated
Contractor
Main contractor - Mission architecture, platform, launch, commissioning, operations, ground segment, with advice from consortium
Minor contracts for payload subsystems - Optics
PhotSat Exploitation Consortium
Science exploitation - pipelines, alerts, cosmic rays, compression, archival and dissemination- Institutes, not fully funded : national/international partners
Operations - IEEC (not fully funded). Requests to infrastructure support funding Gen.Cat & intl partner contributions.
PhotSat consortium
Mission definition, payload
Science modes and products
2023
PhotSat Exploitation Consortium
Operations and science exploitation (open to international partners)
2024
2025
2026+
Contractor
Mission architecture and platform & minor

## Slide 37
PROJECT STATUS